9/14 & 9/16

CS150

Section week 3

- Xilinx:  Lab manual ( How to use it to make your life easier )

a.  OK. Create a schematic consisting of a 16-bit binary counter with clock enable and synchronous reset. Go.

>> You could lay down 16 flip-flops and some gates and get some kind of counter  made and tested in a half an hour if you’re really quick… OR

>> You could click on “Add Component”, click on the ____________ library, and look for a suitable component ( In this case it’d be CB16RE ).

b. What kind of components are there?

>> __________, __________, ___________, ___________, __________, and others…

c. How do you find a component?

>> You can often figure out the name of the component if you know what you’re looking for. What would the name of a 16 bit, synchronous reset shift register with clock enable? ( P. 2-33: Shift registers ) ______________.

- Xilinx: The chip and board

- P. 2-3 : Board. Find I/O pins, clock, where additional

chips are placed, + & - terminals, dip switches…

- P. 4-10 : Chip...

- Xilinx: LUT ( Look Up Table )

- What is a look up table?

- Example of how one is used on the Xilinx chip.

How would the following function be implemented

In the Xilinx chip?

_ _ _     _                          _ _

Where:   F = ABC + ABD + ABC + ABD

ABCD 	      F

0000

0001

0010

0011

0100

0101

0110

0111

1000

1001

1010

1011

1100

1101

1110

1111

- Why do we use them?

4.	FSMs: Using a decoder for implementing logic… ( Kinda like a LUT… )

a. What’s a 3:8 decoder?

ABC	01234567

000	10000000

001  	01000000

010 	00100000

011 	00010000

100 	00001000

- 00000100

110 	00000010

111 	00000001

- Use an 3:8 decoder and a single gate ( you can use bubbles ) to implement the following circuit’s output and NSD. ( Note: This circuit uses a 4 state FSM. )

IN  PS0 PS1    OUT   NS1  NS0

0      0      0  	 0         1       0

0      0      1   	 1         1       1

0      1      0 	 1         1       0

0      1      1 	 0         0       0

1      0      0  	 0         1       0

1      0      1    	 0         1       0

1      1      0 	 0         0       1

1      1      1    	 1         1       0

- Serial to parallel converter ( Based on F97 HW #3, problem #3 )

Design a system which can convert 4 serial input bits ( SerialData ) to an 4 bit parallel output.

In the final circuit you should use a 4 bit shift register and a 2 bit counter from the Xilinx library and any other necessary logic. The serial data comes in MSB first.

Circuit timing is described in the timing diagram below.

# Text boxes

?          ?

?          ?

Xilinx

A

B

C

D

NS0

Done

SerialData

Start

Clk

NS1

OUT

0

1

2

3

4

5

6

7

CLK

SerialData

Start

Done

Counter

DataOut0           ?0          ?0          ?0        SD3       SD2      SD1       SD0      SD0

DataOut1           ?1          ?1          ?1         ?0         SD3      SD2       SD1       SD1

DataOut2           ?2          ?2          ?2         ?1          ?0        SD3       SD2       SD2

DataOut3           ?3          ?3          ?3         ?2          ?1         ?0          SD3       SD3

FSM1 State      Wait      Wait      Shift     Shift     Shift      Shift       Wait     Wait

FSM2 State         ?             ?        Run      Run       Run       Full         Run     Run

0

1

2

3

4

5

6

7

A

B

C

Bit3     Bit2     Bit1      Bit0       ?        ?        ?

F

0          1           2          3          0          1

IN

PS0

PS1

4

DataOut[3:0]