9/21 & 9/23

CS150

Section week 4

- T Flip Flops

1a) T Flip Flop truth table

T    Q

0

1

1b) What’s this circuit called?

1c) What might be a problem

with this circuit?

What’s Q?		What’s J & K?

2.	JK Flip Flop

J   K    Q

0   0

0   1

1   0

1   1

- Timing ( Statistics for Xilinx chip: 4-97 )

3a) Setup & hold time ( no clock skew ).

For both D flip flops:

5ns < Tcko < 10ns

What’s the maximum setup time possible?

What’s the equation to find the maximum possible setup time?

What’s the maximum hold time possible?

What’s the equation to find the maximum possible hold time?

Does finding the minimum setup and hold times have meaning?

3b) Setup and Hold times ( no clock skew – same circuit )

For both flip flops:

Tsetup = 15ns

Thold = 20ns

What’s the possible range for Tcko?

What’s the equation to find the minimum Tcko?

What’s the equation to find the maximum Tcko?

3c) Setup and Hold times when there is clock skew

For both flip flops:

Tsetup = 15ns

Thold = 20ns

Delay = 10ns

What’s the minimum Tcko possible?

What’s the equation to find the minimum Tcko?

What’s the maximum Tcko?

What’s the equation for the maximum Tcko?

3d) Setup and Hold times when there is feedback

For both flip flops:

Tsetup = 5ns	       5ns < Tcko < 15ns  		What’s the fastest clock where

Thold = 10ns	       8ns < Tp < 12ns   		this circuit will still work?

- Other stuff ( If there are no questions, here are some suggestions... )

- Difference in Mealy and Moore STT

- Controllers and datapaths ( May help with hw4 #1 )

- Loadable counters and loadable shift registers

- Go over some more components

- FSM design example

- FSM analysis example

- Cross coupled gates				h)    Random stuff

# Text boxes

Delay

D1          Q1

C

1

T Flip Flop

T

Q

C

D0         Q0

C

CLK

0ns			   25ns			    50ns			     75ns		       	     100ns

CLK

D0

CLK2

Q0/D1

D1          Q1

C

D0         Q0

C

CLK

0ns			   25ns			    50ns			     75ns		       	     100ns

CLK

D0

Q0/D1

0ns			   25ns			    50ns			     75ns		       	     100ns

1

1

CLK

T Flip Flop

T

Q

C

T Flip Flop

T

Q

C

Q0                                   Q1                             Q2

CLK

J

K

Q

CLK

D0

Q0

Q1

CLK

Q0

Q1

Q2

Q

D             Q

C

CLK

D1          Q1

C

CLK

D

Q

D0         Q0

C

CLK