10/26 & 10/28

CS150

Section week 9

This week: RTN ( Register Transfer Notation ) Review & Microoperations, Computer Data Path ( HW9 ),

- RTN review, (-operations

a. In the notes for the 5th section ( 6th week ), we saw what register transfers and control signals were

necessary to calculate (X+Y)*Z when using the datapath below.

What are the register transfers and control signals to add A & B and put the sum into TMP?

RTN				(-operations	        Control signals

b.     RTN describes transfers of data from one __________ component to _____________ component.

Each Register transfers takes __________ clock cycle(s).

For one register transfer there may be ______________ control signal(s) that may need to be set.

RTN				(-operations			Control signals

- Computer datapath ( Just another datapath like the one above... )

a. The three steps to carry out an instruction on a computer:

b. What are the differences between the model that the

book is basing its STD on and the handout given in lecture?

Four step handshake for book’s memory model:

Write			     Read

Cycle 1: Wait high.		Request

Request  asserted.

Put write data on bus.	Read/Write

Cycle 2: Wait goes low.

Read data latched by circuit.	Data

Cycle 3: Request goes low.

Cycle 4: Wait goes high.	Wait

c. Instructions.

Format:

OP Codes:	Instruction		Action:

00		LOAD XXX	 	Memory[XXX] ( ACC

01		STORE XXX 	 	ACC ( Memory[XXX]

10		ADD XXX	 	ACC + Memory[XXX] ( ACC

11		BRN XXX	 	If ACC < 0     ACC ( PC

Address: Address in memory.

What does the instruction   0x000F do?

d. Instructions & Memory contents

So... Let’s do X*Y = PRODUCT.

Use the code:

Mult( X, Y ) {

int i = X, minus1 = -1, product = 0, count = Y;

for ( ; count ( 0 ; count-- ) product += i;

}

| _i | data X | i = X | 40 | X |
| --- | --- | --- | --- | --- |
| _count | data Y | count = Y | 41 | Y |
| _minus1 | data 0xffff | minus1 = -1 | 42 | 0xffff |
| _product | data 0x0000 | product = 0 | 43 | 0 |
| _mult | LOAD _count | ACC = count | 44 | 0x0029 |
|  | ADD _minus1 | ACC = ACC – 1 | 45 | 0x802A |
|  | STORE _count | count = ACC | 46 | 0x4029 |
|  | BRN _done | if count < 0 goto “done” | 47 | 0xC035 |
|  | LOAD _i | ACC = X | 48 | 0x0028 |
|  | ADD _product | ACC = ACC + product | 49 | 0x802B |
|  | STORE _product | product = ACC | 50 | 0x402B |
|  | LOAD _minus1 | ACC = -1 | 51 | 0x002A |
|  | BRN _mult | if ACC < 0 then goto “mult” | 52 | 0xC02C |
| _done |  | … | 53 | ???? |

Problem started in Wednesday section:

What are the register transfers, (-operations, and signals for a new instruction:

ADDMEM XXX	RAM[XXX] + ACC ( RAM[XXX]

Use the datapath handed out in class.

There were already 4 instructions defined for the datapath handed out in class so adding this instruction would mean there would be a total of 5 instructions in the instruction set. In the instruction format we only have 2 bits in the opcode. This means that we’d need another bit in the opcode if we were to still implement the other 4 instructions in order to have a unique opcode for each instruction. I’m not going to worry about that here. Let’s just assume it’s replacing ADD. Assume instruction ahs already been fetched.

RTN				(-operations			signals

IR<13:0> ( MAR		IR ( ABUS			IROUT

ABUS( MAR			MARLOAD

RAM[MAR] ( MBRIN	RAM[MAR] ( DataBus	CS.L

DataBus ( MBRIN		MBRINLOAD

MBRIN + ACC ( MBROUT	MBUS ( RBUS		Y=A+B ( ALU Op

RBUS ( MBROUT		MBROUTLOAD

WE.L

MBROUT ( RAM[MAR]	MBROUT ( DataBus		MBROUT

DataBus ( RAM[MAR]	WE.L, CS.L

(finish write cycle. Avoid bus conflicts				WE.L

and wierd writes by turning off CS.L first

Another way:

RTN				(-operations			signals

IR<13:0> ( MAR		IR ( ABUS			IROUT

ABUS( MAR			MARLOAD

RAM[MAR] ( MBRIN	RAM[MAR] ( DataBus	CS.L

DataBus ( MBRIN		MBRINLOAD

MBRIN + ACC ( MBROUT	MBUS ( RBUS		Y=A+B ( ALU Op

RBUS ( MBROUT		MBROUTLOAD

WE.L, CS.L( ( OK since address

is already ready.)

MBROUT ( RAM[MAR]	MBROUT ( DataBus		MBROUT

DataBus ( RAM[MAR]	WE.L

PS.  CS.L( means falling edge transition.

# Text boxes

Data

Data

The model the book uses is for a memory that may not read/write in a consistent amount of clock cycles. The model that we’re using in lecture uses a RAM for its memory. RAM will always require the same amount of clock cycles for a read/write.

The way the book has the circuit deal with variable read/write times is by using a 4 step handshake  ( on next page ). The circuit and memory converse using this 4 step handshake.

Instruction fetch, decode, execute

T

A + B ( TMP 			     A + B ( BUS       	 T = 0 ( One signal for both tristate buffers )

BUS ( TMP		 ENTMP = 1

multiple

one

another memory

memory

Answers in red.

A + B ( TMP 			     A + B ( BUS       	 T+ = 0, T* = 1 ( = TTMP, TX = TY = TZ )

BUS ( TMP		 ENTMP = 1

Label            Operation                Comment                                                                                Address       Memory value

Address

OP Code

15        14       13      12       11        10       9         8         7         6        5          4         3         2         1         0

LOAD 0xF

*An aside:

Say we change the datapath to the one on the right. Note that the TBUF on the

output of the TMP register has been changed to an EBUF and assume TAZ<TZA for both tri-state buffers. Can we reduce the number of control signals for the same calculation?