# University of California at Berkeley

## College of Engineering

Department of Electrical Engineering and Computer Sciences

### EECS150								J. Wawrzynek

# Spring 2000								E. Caspi

#### Homework #10 – Solution

6.1	By pushing bubbles, we can convert the cross-coupled NAND pair into a cross-coupled OR pair (an RS latch!) with inverted inputs and outputs.  Thus the cross-coupled NAND behaves like an RS latch with inverted inputs and outputs.  Complementary inputs {0,1}, {1,0} set and reset the latch, respectively.  High inputs {1,1} hold the present value.  Low inputs {0,0} are forbidden.

| A | B | Q |
| --- | --- | --- |
| 0 | 0 | unstable |
| 0 | 1 | 1 |
| 1 | 0 | 0 |
| 1 | 1 | hold |

6.2	An RS latch can identify which of two signals falls 1(0 first.  The signals are attached to inputs {R,S}.  With both signals high, the output {Q,Q'} is {0,0} and stable.  When one signal falls, the input {0,1} or {1,0} forces the RS latch to set or reset.  When both signals have fallen, the input {0,0} makes the latch hold its output, "remembering" which signal fell first – {1,0} indicates that R fell first, and {0,1} indicates that S fell first.  Katz actually asks us to detect the opening of a switch, but it is easy to convert that into the falling of a signal.

To identify which of three signals falls first, we can use 3 RS latches to perform 3 pairwise comparisons.  Each signal participates in 2 pairwise comparisons.  The first signal to fall "wins" both of its comparisons.  The AND of a signal's 2 comparison results indicates whether it was the first to fall.

This method can be extended to identify which of n signals falls first.  Each signal participates in n-1 pairwise comparisons, once with every other signal.  The AND of a signal's comparison results indicates whether the signal was the first to fall.  This method requires a total of n(n-1) pairwise comparisons (RS latches) and n (n-1)-input AND gates.  The circuit area grows roughly quadratically with n.

Interestingly, this method can be extended to find the order of n falling signals.  The number of pairwise comparisons won by a signal indicates its rank.  The first signal to fall wins all n-1 of its comparisons.  The next signal to fall wins n-2 of its comparisons.  The last signal to fall wins none of its comparisons.  Thus, in place of AND gates, we can use adders to compute a signal's rank.

6.19	Implement a T flip-flop from a D flip-flop.
Both implementations shown here are derived by inspection from the behavior of a T flip flop:  T=0 retains Q, T=1 inverts Q.

Error Correction Codes (CRC)

The long division modulo 2 is as follows, yielding remainder 00000.
Recall that in modulo 2, addition and subtraction become XOR without carry or borrow.

110001010

110101 | 101000110101110

110101

0111011

110101

00111010

110101

00111110

110101

00101111

110101

0110101

110101

0000000

A trace of the corresponding LFSR computation follows:

FFFFF

Time  Bit  43210

----------------

0         00000

1     1   00001

2     0   00010

3     1   00101

4     0   01010

5     0   10100

6     0   11101

7     1   01110

8     1   11101

9     0   01111

10     1   11111

11     0   01011

12     1   10111

13     1   11010

14     1   00000

15     0   00000

# Text boxes

CLK

T

D       Q

Q

T

CLK

0

1

B fell first

D       Q

Q

A fell first

B

A

R       Q

S       Q

A fell first

C

B

A

R       Q

S       Q

R       Q

S       Q

R       Q

S       Q

B

A

Q

Q

B

A

Q

Q

B

A

Q

Q

B fell first

C fell first

Signal falls when switch opens

Large R