# University of California at Berkeley

## College of Engineering

Department of Electrical Engineering and Computer Sciences

### EECS150								J. Wawrzynek

# Spring 2000								E. Caspi

#### Quiz #4 – Solution

We implement a leftward bit rotator using tri-states.  Given a 4-bit input {x3 x2 x1 x0} and a one-hot-encoded rotation amount {s3 s2 s1 s0}, the bit rotator produces output {y3 y2 y1 y0} as follows:

| Rotation {s3 s2 s1 s0} | Output {y3 y2 y1 y0} |
| --- | --- |
| 0 0 0 1 | {x3 x2 x1 x0} |
| 0 0 1 0 | {x2 x1 x0 x3} |
| 0 1 0 0 | {x1 x0 x3 x2} |
| 1 0 0 0 | {x0 x3 x2 x1} |

Tri-state buffers are useful for implementing a shared bus, i.e. a line with many writers, only one of which may write at any given time.  For the bit rotator, we create a shared bus for each output, with the writers being tri-stated copies of the inputs.  The rotation amount {s3 s2 s1 s0} controls the tri-states to determine which input writes to which output.

# Text boxes

s0

s3

s2

s1

s2

s3

s0

s1

s3

s0

s1

s2

s0

s1

s2

s3

x3

x2

x1

x0

y3

y2

y1

y0