# University of California at Berkeley

## College of Engineering

## Department of Electrical Engineering and Computer Sciences

### EECS150								J. Wawrzynek

# Spring 2000								E. Caspi

#### Quiz #6 – Solution

The critical path remains in the COMPUTE_SUM state.  It is the path from NEXT through memory to SUM.  Some of the given components have a width mismatch with respect to the original design spec from lecture, but we must use them anyway.  We use a wastefully wide 16-bit adder to increment NEXT and a parallel pair of 8-wide multiplexors on the input to SUM.  Note that the parallel composition of 2 multiplexors has exactly the same delay as one multiplexor.  The total delay of COMPUTE_SUM, hence the minimum clock cycle, is either 111ns or 141ns, depending on your version of the quiz.  Two versions were distributed, each with different timing for components.

# Timing for quiz (A)	Timing for quiz (B)

| Component | Delay |
| --- | --- |
| 8-bit Register | Clk-to-Q=1ns Setup=1ns |
| 8-bit wide 2-1 Mux | 3ns |
| 16-bit Adder | 30ns |
| Memory | 40ns |
| Zero Compare | 5ns |
| Component | Delay |
| 8-bit Register | Clk-to-Q=1ns Setup=1ns |
| 8-bit wide 2-1 Mux | 3ns |
| 16-bit Adder | 40ns |
| Memory | 50ns |
| Zero Compare | 5ns |

# Text boxes

Timing diagram for COMPUTE_SUM state

1

3

3

1

Total, 111ns (A) / 141ns (B)

SUM setup, 1ns

SUM load mux, 3ns

SUM_SEL mux, 3ns

SUM adder,

30ns (A) / 40ns (B)

NEXT adder,

30ns (A) / 40ns (B)

NEXT Clk-to-Q, 1ns

CLOCK

SUM

NEXT

A_SEL mux, 3ns

3

memory,

40ns (A) / 50ns (B)