# University of California at Berkeley

## College of Engineering

Department of Electrical Engineering and Computer Sciences

### EECS150								J. Wawrzynek

# Spring 2000								E. Caspi

Quiz #8 – Solution

- The canonical sum-of-products or minterm expression for f is an OR (sum) of AND (product) terms, one AND term for each 1-valued entry in the truth table:

f = a’b’c’d’ + a’b’cd’ + a’bcd + ab’c’d’ + ab’cd’ + abc’d’ + abcd’ + abcd

We fill the Karnaugh map for ƒ using values from the truth table.  To find the reduced expression, we cover all 1’s in the map using the fewest, largest  rectangles of size (2n(2m).  The reduced expression is a sum of products, one product per rectangle:

f = b’d’ + ad’ + bcd

| cd ab | 00 | 01 | 11 | 10 |
| --- | --- | --- | --- | --- |
| 00 | 1 | 0 | 0 | 1 |
| 01 | 0 | 0 | 1 | 0 |
| 11 | 1 | 0 | 1 | 1 |
| 10 | 1 | 0 | 0 | 1 |