## Slide 1: 61C In the News
Jaguar's days as a CPU-only supercomputer are numbered. Over the next year, the 2.3 petaflop machine at the Oak Ridge National Lab (ORNL) will be upgraded by Cray with the new NVIDIA "Kepler" GPUs, […] The transformed supercomputer will be renamed Titan and should deliver in the neighborhood of 20 peak petaflops sometime in late 2012.
October 11, 2011
GPUs Will Morph ORNL's Jaguar Into 20-Petaflop Titan
Michael Feldman
The current Jaguar system … currently sits at number three on the TOP500 list...
www.hpcwire.com/hpcwire/2011-10-11/gpus_will_morph_ornl_s_jaguar_into_20-petaflop_titan.html
"It's all about power efficiency"

## Slide 2: CS 61C: Great Ideas in Computer Architecture (Machine Structures) Lecture 22 Thread Level Parallelism III
Instructors: Michael Franklin
Dan Garcia
http://inst.eecs.Berkeley.edu/~cs61c/Fa11

## Slide 3: Review
Sequential software is slow software
  SIMD and MIMD only path to higher performance
Multiprocessor (Multicore) uses Shared Memory (single address space)
Cache coherency implements shared memory even with multiple copies in multiple caches
  False sharing a concern
MOESI Protocol ensures cache consistency and has optimizations for common cases.

## Slide 4: Threads
thread of execution: smallest unit of processing scheduled by operating system
Threads have their own state or context:
  Program counter, Register file, Stack pointer,
Threads share: a memory address space
Note: A “process” is a heavier-weight construct, which has its own address space. A process typically contains one or more threads.
  Not to be confused with a processor, which is a physical device (i.e., a core)

## Slide 5: Memory Model for Multi-threading
CAN BE SPECIFIED IN A LANGUAGE WITH MIMD SUPPORT – SUCH AS OPENMP
Process

## Slide 6: Multithreading
On a single processor, multithreading occurs by time-division multiplexing:
  Processor switched between different threads
    may be “pre-emptive” or “non pre-emptive”
  Context switching happens frequently enough that user perceives threads as running at the same time
On a multiprocessor, threads run at the same time, with each processor running a thread

## Slide 7: Multithreading vs. Multicore
Basic idea: Processor resources are expensive and should not be left idle
For example: Long latency to memory on cache miss?
  Hardware switches threads to bring in other useful work while waiting for cache miss
  Cost of thread context switch must be much less than cache miss latency
Put in redundant hardware so don’t have to save context on every thread switch:
  PC, Registers, …
Attractive for apps with abundant TLP

## Slide 8: Data Races and Synchronization
Two memory accesses form a data race if from different threads, to same location, and at least one is a write, and they occur one after another
If there is a data race, result of program can vary depending on chance (which thread ran first?)
Avoid data races by synchronizing writing and reading to get deterministic behavior
Synchronization done by user-level routines that rely on hardware synchronization instructions

## Slide 9: Lock and Unlock Synchronization
Lock used to create region (critical section) where only one thread can operate
Given shared memory, use memory location as synchronization point: lock or semaphore
Thread reads lock to see if it must wait, or OK to go into critical section (and set to locked)
  0 => lock is free / open / unlocked / lock off
  1 => lock is set / closed / locked / lock on
Set the lock
Critical section (only one thread gets to execute this section of code at a time)
e.g., change shared variables
Unset the lock

## Slide 10: Possible Lock/Unlock Implementation
Lock (aka busy wait):
  addiu $t1,$zero,1 ; t1 = 1 means Locked
  Loop: lw $t0,lock($s0) ; load lock
  bne $t0,$zero,Loop ; loop if locked
  Lock: sw $t1,lock($s0) ; Unlocked, so lock
Unlock:
sw $zero,lock($s0)
Any problems with this?

## Slide 11: Peer Instruction: What Happens?
  addiu $t1,$zero, 1 ; t1 = 1 means locked
  Loop: lw $t0, lock($s0) ; load lock
  bne $t0, $zero, Loop ; loop if lock <> 0
  Lock: sw $t1, lock($s0) ; set lock and continue ; to critical section
It works great! Ensures that at most one thread enters the critical section at a time.
Infinite Loop, since no change to lock before bne
Doesn’t work because a different thread on another core could see lock == 0 before sw changes it to 1; so both go to critical section
Doesn’t work because a different thread on this same core could see lock == 0 before sw changes it to 1; so both go to critical section
(A) I only (B) II only (C) III only (D) IV only (E) III and IV

## Slide 12: Possible Lock Problem
Thread 1
addiu $t1,$zero,1
Loop: lw $t0,lock($s0)
bne $t0,$zero,Loop
Lock: sw $t1,lock($s0)
Thread 2
addiu $t1,$zero,1
Loop: lw $t0,lock($s0)
bne $t0,$zero,Loop
Lock: sw $t1,lock($s0)
Time
Both threads think they have set the lock
Exclusive access not guaranteed!

## Slide 13: Help! Hardware Synchronization
Hardware support required to prevent interloper (either thread on other core or thread on same core) from changing the value
  Atomic read/write memory operation
  No other access to the location allowed between the read and write
Could be a single instruction
  E.g., atomic swap of register ↔ memory
  Or an atomic pair of instructions

## Slide 14: Synchronization in MIPS
Load linked: ll rt,offset(rs)
Store conditional: sc rt,offset(rs)
  Succeeds if location not changed since the ll
    Returns 1 in rt (clobbers register value being stored)
  Fails if location has changed
    Returns 0 in rt (clobbers register value being stored)
Example: atomic swap (to test/set lock variable)
Exchange contents of reg and mem: $s4  ($s1)
  try: add $t0,$zero,$s4 ;copy exchange value
  ll $t1,0($s1) ;load linked
  sc $t0,0($s1) ;store conditional
  beq $t0,$zero,try ;branch store fails
  add $s4,$zero,$t1 ;put load value in $s4

## Slide 15: Test-and-Set
In a single atomic operation:
  Test to see if a memory location is set (contains a 1)
  Set it (to 1) If it isn’t (it contained a zero when tested)
  Otherwise indicate that the Set failed, so the program can try again
  No other instruction can modify the memory location, including another Test-and-Set instruction
Useful for implementing lock operations

## Slide 16: Test-and-Set in MIPS
Single atomic operation
Example: MIPS sequence for implementing a T&S at ($s1)
  Try: addiu $t0,$zero,1
  ll $t1,0($s1)
  bne $t1,$zero,Try
  sc $t0,0($s1)
  beq $t0,$zero,try
  Locked:
  critical section
  sw $zero,0($s1)

## Slide 17: What is OpenMP?
API used for multi-threaded, shared memory parallelism
  Compiler Directives
  Runtime Library Routines
  Environment Variables
Portable
Standardized
See http://www.openmp.org/, http://computing.llnl.gov/tutorials/openMP/

## Slide 18: OpenMP Specification

## Slide 19: Shared Memory Model with Explicit Thread-based Parallelism
Shared memory process consists of multiple threads, explicit programming model with full programmer control over parallelization
Pros:
  Takes advantage of shared memory, programmer need not worry (that much) about data placement
  Programming model is “serial-like” and thus conceptually simpler than alternatives (e.g., message passing/MPI)
  Compiler directives are generally simple and easy to use
  Legacy serial code does not need to be rewritten
Cons:
  Codes can only be run in shared memory environments!
  Compiler must support OpenMP (e.g., gcc 4.2)

## Slide 20: OpenMP Programming Model
Fork - Join Model:
OpenMP programs begin as single process: master thread; Executes sequentially until the first parallel region construct is encountered
  FORK: the master thread then creates a team of parallel threads
  Statements in program that are enclosed by the parallel region construct are executed in parallel among the various team threads
  JOIN: When the team threads complete the statements in the parallel region construct, they synchronize and terminate, leaving only the master thread

## Slide 21: OpenMP Directives
shares iterations of a loop across the team
each section executed by a separate thread
serializes the execution of a thread

## Slide 22: Building Block: C for loop
for (i=0; i<max; i++) zero[i] = 0;
Break for loop into chunks, and allocate each to a separate thread
  E.g., if max = 100, with two threads, assign 0-49 to thread 0, 50-99 to thread 1
Must have relatively simple “shape” for an OpenMP-aware compiler to be able to parallelize it
  Necessary for the run-time system to be able to determine how many of the loop iterations to assign to each thread
No premature exits from the loop allowed
  i.e., No break, return, exit, goto statements

## Slide 23: OpenMP Extends C with Pragmas
Pragmas are a mechanism C provides for language extensions
Commonly implemented pragmas: structure packing, symbol aliasing, floating point exception modes
Good mechanism for OpenMP because compilers that don't recognize a pragma are supposed to ignore them
  Runs on sequential computer even with embedded pragmas

## Slide 24: OpenMP: Parallel for pragma
#pragma omp parallel for
for (i=0; i<max; i++) zero[i] = 0;
Master thread creates additional threads, each with a separate execution context
All variables declared outside for loop are shared by default, except for loop index which is private per thread (Why?)
Implicit synchronization at end of for loop
Divide index regions sequentially per thread
  Thread 0 gets 0, 1, …, (max/n)-1;
  Thread 1 gets max/n, max/n+1, …, 2*(max/n)-1
  Why?

## Slide 25: Thread Creation
How many threads will OpenMP create?
Defined by OMP_NUM_THREADS environment variable (or in code procedure call)
Set this variable to the maximum number of threads you want OpenMP to use
Usually equals the number of cores in the underlying HW on which the program is run

## Slide 26: OMP_NUM_THREADS
Shell command to set number threads:
export OMP_NUM_THREADS=x
Shell command check number threads:
echo $OMP_NUM_THREADS
OpenMP intrinsic to set number of threads:
omp_num_threads(x);
OpenMP intrinsic to get number of threads:
num_th = omp_get_num_threads();
OpenMP intrinsic to get Thread ID number:
th_ID = omp_get_thread_num();

## Slide 27: Parallel Threads and Scope
Each thread executes a copy of the code within the structured block
#include <omp.h>
main () {
int nthreads, tid;
/* Fork a team of threads with each thread having a private tid variable */
#pragma omp parallel private(tid)
{
/* Obtain and print thread id */
tid = omp_get_thread_num();
printf("Hello World from thread = %d\n", tid);
/* Only master thread does this */
if (tid == 0)
{
nthreads = omp_get_num_threads();
printf("Number of threads = %d\n", nthreads);
}
} /* All threads join master thread and terminate */
}

## Slide 28: Matrix Multiply in OpenMP
start_time = omp_get_wtime();
#pragma omp parallel for private(tmp, i, j, k)
for (i=0; i<Ndim; i++){
for (j=0; j<Mdim; j++){
tmp = 0.0;
for( k=0; k<Pdim; k++){
/* C(i,j) = sum(over k) A(i,k) * B(k,j) */
tmp += *(A+(i*Ndim+k)) * *(B+(k*Pdim+j));
}
*(C+(i*Ndim+j)) = tmp;
}
}
run_time = omp_get_wtime() - start_time;
Note: Outer loop spread across N threads; inner loops inside a thread

## Slide 29: Notes on Matrix Multiply Example
More performance optimizations available
Higher compiler optimization (-O2, -O3) to reduce number of instructions executed
Cache blocking to improve memory performance
Using SIMD SSE3 Instructions to raise floating point computation rate

## Slide 30: And in Conclusion, …
Sequential software is slow software
  SIMD and MIMD only path to higher performance
Multiprocessor/Multicore uses Shared Memory
  Cache coherency implements shared memory even with multiple copies in multiple caches
  False sharing a concern; watch block size!
Data races lead to subtle parallel bugs
Synchronization via atomic operations:
  MIPS does it with Load Linked + Store Conditional
OpenMP as simple parallel extension to C
  Threads, Parallel for, private, critical sections, …

## Slide 31: Bonus Slides

## Slide 32: OpenMP Pitfall #1: Data Dependencies
Consider the following code:
  a[0] = 1;
  for(i=1; i<5; i++)
  a[i] = i + a[i-1];
There are dependencies between loop iterations
Sections of loops split between threads will not necessarily execute in order
Out of order loop execution will result in undefined behavior

## Slide 33: Open MP Pitfall #2: Avoiding Dependencies by Using Private Variables
Consider the following loop:
#pragma omp parallel for
{
for(i=0; i<n; i++){
temp = 2.0*a[i];
a[i] = temp;
b[i] = c[i]/temp;
}
}
Threads share common address space: will be modifying temp simultaneously; solution:
#pragma omp parallel for private(temp)
{
for(i=0; i<n; i++){
temp = 2.0*a[i];
a[i] = temp;
b[i] = c[i]/temp;
}
}

## Slide 34: OpenMP Pitfall #3: Updating Shared Variables Simultaneously
Now consider a global sum:
for(i=0; i<n; i++)
sum = sum + a[i];
This can be done by surrounding the summation by a critical section, but for convenience, OpenMP also provides the reduction clause:
#pragma omp parallel for reduction(+:sum)
{
for(i=0; i<n; i++)
sum = sum + a[i];
}
Compiler can generate highly efficient code for reduction

## Slide 35: OpenMP Pitfall #3: Parallel Overhead
Spawning and releasing threads results in significant overhead
Therefore, you want to make your parallel regions as large as possible
  Parallelize over the largest loop that you can (even though it will involve more work to declare all of the private variables and eliminate dependencies)
  Coarse granularity is your friend!