## Slide 1: 61C In the News
Rumors of the PC’s demise have been greatly exaggerated?
HP: We're keeping the PC unit
By Larry Dignan | October 27, 2011, 1:07pm PDT
Summary: HP CEO Meg Whitman decides the PC business isn’t so bad after all.
http://www.zdnet.com/blog/btl/hp-were-keeping-the-pc-unit/62081?tag=nl.e539
In the long run, HP’s decision to keep the PC unit isn’t a slam dunk. PCs are still a low-margin commodity business…

## Slide 2: CS 61C: Great Ideas in Computer Architecture (Machine Structures) Lecture 27: Single-Cycle CPU Datapath Design
Instructors: Mike Franklin
Dan Garcia
http://inst.eecs.Berkeley.edu/~cs61c/fa11

## Slide 3: Review
Use muxes to select among inputs
  S control bits selects from 2S inputs
  Each input can be n-bits wide, indep of S
Can implement muxes hierarchically
ALU can be implemented using a mux
  Coupled with basic block elements
N-bit adder-subtractor done using N 1-bit adders with XOR gates on input
  XOR serves as conditional inverter

## Slide 4: Agenda
Stages of the Datapath
Datapath Instruction Walkthroughs
Datapath Design

## Slide 5: Five Components of a Computer
Processor
Computer
Control
Datapath
Memory
(passive)
(where
programs,
data live
when
running)
Devices
Input
Output
Keyboard, Mouse
Display, Printer
Disk (where
programs,
data live when not running)

## Slide 6: The CPU
Processor (CPU): the active part of the computer that does all the work (data manipulation and decision-making)
Datapath: portion of the processor that contains hardware necessary to perform operations required by the processor (the brawn)
Control: portion of the processor (also in hardware) that tells the datapath what needs to be done (the brain)

## Slide 7: Stages of the Datapath : Overview
Problem: a single, atomic block that “executes an instruction” (performs all necessary operations beginning with fetching the instruction) would be too bulky and inefficient
Solution: break up the process of “executing an instruction” into stages, and then connect the stages to create the whole datapath
  smaller stages are easier to design
  easy to optimize (change) one stage without touching the others

## Slide 8: Five Stages of the Datapath
Stage 1: Instruction Fetch
Stage 2: Instruction Decode
Stage 3: ALU (Arithmetic-Logic Unit)
Stage 4: Memory Access
Stage 5: Register Write

## Slide 9: Stages of the Datapath (1/5)
There is a wide variety of MIPS instructions: so what general steps do they have in common?
Stage 1: Instruction Fetch
  no matter what the instruction, the 32-bit instruction word must first be fetched from memory (the cache-memory hierarchy)
  also, this is where we Increment PC (that is, PC = PC + 4, to point to the next instruction: byte addressing so + 4)

## Slide 10: Stages of the Datapath (2/5)
Stage 2: Instruction Decode
  upon fetching the instruction, we next gather data from the fields (decode all necessary instruction data)
  first, read the opcode to determine instruction type and field lengths
  second, read in data from all necessary registers
    for add, read two registers
    for addi, read one register
    for jal, no reads necessary

## Slide 11: Stages of the Datapath (3/5)
Stage 3: ALU (Arithmetic-Logic Unit)
  the real work of most instructions is done here: arithmetic (+, -, *, /), shifting, logic (&, |), comparisons (slt)
  what about loads and stores?
    lw $t0, 40($t1)
    the address we are accessing in memory = the value in $t1 PLUS the value 40
    so we do this addition in this stage

## Slide 12: Stages of the Datapath (4/5)
Stage 4: Memory Access
  actually only the load and store instructions do anything during this stage; the others remain idle during this stage or skip it all together
  since these instructions have a unique step, we need this extra stage to account for them
  as a result of the cache system, this stage is expected to be fast

## Slide 13: Stages of the Datapath (5/5)
Stage 5: Register Write
  most instructions write the result of some computation into a register
  examples: arithmetic, logical, shifts, loads, slt
  what about stores, branches, jumps?
    don’t write anything into a register at the end
    these remain idle during this fifth stage or skip it all together

## Slide 14: Generic Steps of Datapath
instruction
memory
+4
rt
rs
rd
registers
ALU
Data
memory
imm
1. Instruction
Fetch
2. Decode/
Register
Read
3. Execute
4. Memory
5. Register
Write
PC
Notes: missing: multiplexors or “data selectors” – where should they be in this picture and why?
also missing – opcode for control of what operations to perform
state elements vs combinational ones – combinational given the same input will always produce the same output – out depends only on the current input

## Slide 15: Datapath Walkthroughs (1/3)
add $r3,$r1,$r2 # r3 = r1+r2
  Stage 1: fetch this instruction, increment PC
  Stage 2: decode to determine it is an add, then read registers $r1 and $r2
  Stage 3: add the two values retrieved in Stage 2
  Stage 4: idle (nothing to write to memory)
  Stage 5: write result of Stage 3 into register $r3

## Slide 16: Example: add Instruction
instruction
memory
+4
registers
ALU
Data
memory
imm
2
1
3
add r3, r1, r2
reg[1]+ reg[2]
reg[2]
reg[1]
PC

## Slide 17: Datapath Walkthroughs (2/3)
slti $r3,$r1,17 # if (r1 <17 )r3 = 1 else r3 = 0
  Stage 1: fetch this instruction, increment PC
  Stage 2: decode to determine it is an slti, then read register $r1
  Stage 3: compare value retrieved in Stage 2 with the integer 17
  Stage 4: idle
  Stage 5: write the result of Stage 3 (1 if reg source was less than signed immediate, 0 otherwise) into register $r3

## Slide 18: Example: slti Instruction
instruction
memory
+4
registers
ALU
Data
memory
imm
3
1
x
slti r3, r1, 17
reg[1] <17?
17
reg[1]
PC

## Slide 19: Datapath Walkthroughs (3/3)
sw $r3,17($r1) # Mem[r1+17]=r3
  Stage 1: fetch this instruction, increment PC
  Stage 2: decode to determine it is a sw, then read registers $r1 and $r3
  Stage 3: add 17 to value in register $r1 (retrieved in Stage 2) to compute address
  Stage 4: write value in register $r3 (retrieved in Stage 2) into memory address computed in Stage 3
  Stage 5: idle (nothing to write into a register)

## Slide 20: Example: sw Instruction
instruction
memory
+4
registers
ALU
Data
memory
imm
3
1
x
SW r3, 17(r1)
reg[1] +17
17
reg[1]
MEM[r1+17]<=r3
reg[3]
PC

## Slide 21: Why Five Stages? (1/2)
Could we have a different number of stages?
  Yes, and other architectures do
So why does MIPS have five if instructions tend to idle for at least one stage?
  Five stages are the union of all the operations needed by all the instructions.
  One instruction uses all five stages: the load

## Slide 22: Why Five Stages? (2/2)
lw $r3,17($r1) # r3=Mem[r1+17]
  Stage 1: fetch this instruction, increment PC
  Stage 2: decode to determine it is a lw, then read register $r1
  Stage 3: add 17 to value in register $r1 (retrieved in Stage 2)
  Stage 4: read value from memory address computed in Stage 3
  Stage 5: write value read in Stage 4 into register $r3

## Slide 23: Example: lw Instruction
ALU
instruction
memory
+4
registers
Data
memory
imm
3
1
x
LW r3, 17(r1)
reg[1] +17
17
reg[1]
MEM[r1+17]
PC

## Slide 24: Peer Instruction
How many places in this diagram will need a multiplexor to select one from multiple inputs?
a) 0 b) 1 c) 2 d) 3 e) 4 or more

## Slide 25: Peer Instruction
How many places in this diagram will need a multiplexor to select one from multiple inputs
a) 0 b) 1 c) 2 d) 3 e) 4 or more

## Slide 26: Datapath and Control
Datapath based on data transfers required to perform instructions
Controller causes the right transfers to happen
PC
instruction
memory
+4
rt
rs
rd
registers
Data
memory
imm
ALU
Controller
opcode, funct

## Slide 27: What Hardware Is Needed? (1/2)
PC: a register that keeps track of address of the next instruction to be fetched
General Purpose Registers
  Used in Stages 2 (Read) and 5 (Write)
  MIPS has 32 of these
Memory
  Used in Stages 1 (Fetch) and 4 (R/W)
  Caches makes these stages as fast as the others (on average, otherwise multicycle stall)

## Slide 28: What Hardware Is Needed? (2/2)
ALU
  Used in Stage 3
  Performs all necessary functions: arithmetic, logicals, etc.
Miscellaneous Registers
  One stage per clock cycle: Registers inserted between stages to hold intermediate data and control signals as they travel from stage to stage
  Note: Register is a general purpose term meaning something that stores bits. Realize that not all registers are in the “register file”

## Slide 29: CPU Clocking (1/2)
For each instruction, how do we control the flow of information though the datapath?
Single Cycle CPU: All stages of an instruction completed within one long clock cycle
  Clock cycle sufficiently long to allow each instruction to complete all stages without interruption within one cycle
1. Instruction
Fetch
2. Decode/
Register
Read
3. Execute
4. Memory
5. Reg.
Write

## Slide 30: CPU Clocking (2/2)
Alternative multiple-cycle CPU: only one stage of instruction per clock cycle
  Clock is made as long as the slowest stage
  Several significant advantages over single cycle execution: Unused stages in a particular instruction can be skipped OR instructions can be pipelined (overlapped)
1. Instruction
Fetch
2. Decode/
Register
Read
3. Execute
4. Memory
5. Register
Write

## Slide 31: Processor Design
Analyze instruction set architecture (ISA) to determine datapath requirements
  Meaning of each instruction is given by register transfers
  Datapath must include storage element for ISA registers
  Datapath must support each register transfer
Select set of datapath components and establish clocking methodology
Assemble datapath components to meet requirements
Analyze each instruction to determine sequence of control point settings to implement the register transfer
Assemble the control logic to perform this sequencing

## Slide 32: Summary
CPU design involves Datapath, Control
  5 Stages for MIPS Instructions
    Instruction Fetch
    Instruction Decode & Register Read
    ALU (Execute)
    Memory
    Register Write
Datapath timing: single long clock cycle or one short clock cycle per stage

## Slide 33: Instruction Level Parallelism
P 1
Instr 1
IF
ID
ALU
MEM
WR
P 2
P 3
P 4
P 5
P 6
P 7
P 8
P 9
P 10
P 11
P 12
Instr 2
IF
ID
ALU
MEM
WR
IF
ID
ALU
MEM
WR
Instr 2
Instr 3
IF
ID
ALU
MEM
WR
IF
ID
ALU
MEM
WR
Instr 4
IF
ID
ALU
MEM
WR
Instr 5
IF
ID
ALU
MEM
WR
Instr 6
IF
ID
ALU
MEM
WR
Instr 7
IF
ID
ALU
MEM
WR
Instr 8