## Slide 1: OPTICAL COMPUTING realized
inst.eecs.berkeley.edu/~cs61c UCB CS61C : Machine Structures Lecture 34 – Virtual Memory II 2010-04-16
Researchers at Stanford have developed “nanoscale single-mode LED”, which can transmit chip-to-chip data at 10 Gbs (10x what is currently used) at 1/1000th the energy. Pretty cool! (get it?) 
Lecturer SOE Dan Garcia
http://news.stanford.edu/news/2011/november/data-transmission-breakthrough-111511.html

## Slide 2: Review
Next level in the memory hierarchy:
  Provides program with illusion of a very large main memory:
  Working set of “pages” reside in main memory - others reside on disk.
Also allows OS to share memory, protect programs from each other
Today, more important for protection vs. just another level of memory hierarchy
Each process thinks it has all the memory to itself
(Historically, it predates caches)

## Slide 3: Review: View of the Memory Hierarchy
Regs
L2 Cache
Memory
Disk
Tape
Instr. Operands
Blocks
Pages
Files
Upper Level
Lower Level
Faster
Larger
Cache
Blocks
Thus far
{
{
This week:
Virtual
Memory

## Slide 4: Mapping Virtual Memory to Physical Memory
Divide into equal sized chunks (about 4 KB - 8 KB)
Any chunk of Virtual Memory assigned to any chuck of Physical Memory (“page”)
0
Physical Memory
¥
Virtual Memory
Code
Static
Heap
Stack
64 MB
0

## Slide 5: Another Model: Base and Bound Reg
0
¥
OS
User A
User B
User C
$base
$base+ $bound
Want:
  discontinuous mapping
  Process size >> mem
Addition not enough!
 use Indirection!
Enough space for User D,
but discontinuous
(“fragmentation problem”)

## Slide 6: Paging Organization (assume 32B pages)
Addr
Trans
MAP
Page is unit of mapping
Page also unit of transfer from disk to physical memory
page 0
32B
32B
32B
00000000
00100000
11100000
Virtual Memory
Virtual
Address
page 1
page 7
32B
01000000
page 2
...
...
...
page 0
Physical
Address
Physical
Memory
32B
32B
32B
page 1
page 3
...
...
...
0000000
0100000
1100000

## Slide 7: Virtual Memory Mapping Function
Cannot have simple function to predict arbitrary mapping
Use table lookup of mappings
Use table lookup (“Page Table”) for mappings: Page number is index
Virtual Memory Mapping Function
  Physical Offset = Virtual Offset
  Physical Page Number = PageTable[Virtual Page Number]
  (P.P.N. also called “Page Frame”)
Page Number Offset

## Slide 8: Address Mapping: Page Table
Virtual Address:
page no.
offset
Page Table
Base Reg
Page Table located in physical memory
index
into
page
table
Physical
Memory
Address
Page Table
Val
-id
Access
Rights
Physical
Page
Address
.
V
A.R.
P. P. A.
...
...
offset
PPN

## Slide 9: Page Table
A page table is an operating system structure which contains the mapping of virtual addresses to physical locations
  There are several different ways, all up to the operating system, to keep this data around
Each process running in the operating system has its own page table
  “State” of process is PC, all registers, plus page table
  OS changes page tables by changing contents of Page Table Base Register

## Slide 10: Requirements revisited
Remember the motivation for VM:
Sharing memory with protection
  Different physical pages can be allocated to different processes (sharing)
  A process can only touch pages in its own page table (protection)
Separate address spaces
  Since programs work only with virtual addresses, different programs can have different data/code at the same address!
What about the memory hierarchy?

## Slide 11: Page Table Entry (PTE) Format
Contains either Physical Page Number or indication not in Main Memory
OS maps to disk if Not Valid (V = 0)
If valid, also check if have permission to use page: Access Rights (A.R.) may be Read Only, Read/Write, Executable
...
Page Table
Val
-id
Access
Rights
Physical
Page
Number
V
A.R.
P. P. N.
V
A.R.
P. P.N.
...
P.T.E.

## Slide 12: Paging/Virtual Memory Multiple Processes
User B: Virtual Memory
¥
Code
Static
Heap
Stack
0
Code
Static
Heap
Stack
A
Page
Table
B
Page
Table
User A: Virtual Memory
¥
0
0
Physical
Memory
64 MB

## Slide 13: Comparing the 2 levels of hierarchy
Cache version Virtual Memory vers.
Block or Line Page
Miss Page Fault
Block Size: 32-64B Page Size: 4K-8KB
Placement: Fully Associative Direct Mapped, N-way Set Associative
Replacement: Least Recently Used LRU or Random (LRU)
Write Thru or Back Write Back

## Slide 14: Notes on Page Table
Solves Fragmentation problem: all chunks same size, so all holes can be used
OS must reserve “Swap Space” on disk for each process
To grow a process, ask Operating System
  If unused pages, OS uses them first
  If not, OS swaps some old pages to disk
  (Least Recently Used to pick pages to swap)
Each process has own Page Table
Will add details, but Page Table is essence of Virtual Memory

## Slide 15: Why would a process need to “grow”?
A program’s address space contains 4 regions:
  stack: local variables, grows downward
  heap: space requested for pointers via malloc() ; resizes dynamically, grows upward
  static data: variables declared outside main, does not grow or shrink
  code: loaded when program starts, does not change
code
static data
heap
stack
For now, OS somehow prevents accesses between stack and heap (gray hash lines).
~ FFFF FFFFhex
~ 0hex

## Slide 16: Virtual Memory Problem #1
Map every address  1 indirection via Page Table in memory per virtual address  1 virtual memory accesses = 2 physical memory accesses  SLOW!
Observation: since locality in pages of data, there must be locality in virtual address translations of those pages
Since small is fast, why not use a small cache of virtual to physical address translations to make translation fast?
For historical reasons, cache is called a Translation Lookaside Buffer, or TLB

## Slide 17: Translation Look-Aside Buffers (TLBs)
TLBs usually small, typically 128 - 256 entries
Like any other cache, the TLB can be direct mapped, set associative, or fully associative
Processor
TLB
Lookup
Cache
Main
Memory
VA
PA
miss
hit
data
Trans-
lation
hit
miss
On TLB miss, get page table entry from main memory

## Slide 18: Another Analogy
Book title like virtual address
Library of Congress call number like physical address
Card catalogue like page table, mapping from book title to call #
On card for book, in local library vs. in another branch like valid bit indicating in main memory vs. on disk
On card, available for 2-hour in library use (vs. 2-week checkout) like access rights

## Slide 19: Peer Instruction
Locality is important yet different for cache and virtual memory (VM): temporal locality for caches but spatial locality for VM
VM helps both with security and cost
12
a) FF
b) FT
c) TF
d) TT
Notes: Answer: [correct=5, TFF] Individual (6, 3, 6, 3, 34, 37, 7, 4)% & Team (9, 4, 4, 4, 39, 34, 0, 7)%
A: T [18/82 & 25/75] (The game breaks up very quickly into separate, independent games -- big win to solve separated & put together)
B: F [80/20 & 86/14] (The game tree grows exponentially! A better static evaluator can make all the difference!)
C: F [53/57 & 52/48] (If you're just looking for the best move, just keep theBestMove around [ala memoizing max])

## Slide 20: Peer Instruction Answer
Locality is important yet different for cache and virtual memory (VM): temporal locality for caches but spatial locality for VM
VM helps both with security and cost
F A L S E
1. No. Both for VM and cache
2. Yes. Protection and a bit smaller memory
T R U E
12
a) FF
b) FT
c) TF
d) TT

## Slide 21: And in conclusion…
Manage memory to disk? Treat as cache
  Included protection as bonus, now critical
  Use Page Table of mappings for each user vs. tag/data in cache
  TLB is cache of Virtual  Physical addr trans
Virtual Memory allows protected sharing of memory between processes
Spatial Locality means Working Set of Pages is all that must be in memory for process to run fairly well