UNIVERSITY OF CALIFORNIA

College of Engineering

Department of Electrical Engineering and Computer Sciences

EE 130/230M	Prof. Liu and Dr. Xu

Spring 2013

Homework Assignment #5

Due at the beginning of class on Thursday, 2/28/13

Problem 1: pn Junction Electrostatics

Consider a silicon pn step junction with NA = 1×1018 cm-3 and ND = 1×1017 cm-3, maintained at T = 300K.

- Calculate the built-in potential (Vbi), the depletion layer width (W), and maximum electric field (E(0)) for zero bias (i.e. under thermal equilibrium conditions).

- Sketch the energy band diagram, charge density distribution, electric field distribution, and potential distribution as a function of position x for both zero bias and 1V reverse bias.  Indicate how the values for Vbi, W, and E(0) change with reverse bias.

Problem 2: p-i-n Diode

A p-i-n diode is a semiconductor diode with a wide, lightly doped intrinsic region between a p-type region and an n-type region.  P-i-n diodes are used as fast switches, photodetectors, and for high-voltage power electronics applications.  Consider a silicon p-i-n diode with a doping profile as shown below.  Assume T = 300K.

- Applying the depletion approximation (i.e. assuming that the electron and hole concentrations are zero within the depletion region), sketch the charge density distribution, electric field distribution, and potential distribution as a function of position x, for zero bias.

- Find the built-in potential, Vbi, and the lengths of the depletion regions in the n-type region and the p-type region.

- How does the maximum electric field in this p-i-n diode compare to that for a pn diode which contains no intrinsic region but has the same dopant concentrations in the n-type and p-type regions (i.e. as in Problem 1)?

- How does the small-signal capacitance of the p-i-n diode compare to that of a pn diode which contains no intrinsic region but has the same dopant concentrations in the n-type and p-type regions (i.e. as in Problem 1)?

Problem 3: pn Junction Diode Current Components

Consider a silicon pn step junction diode with NA = 1×1018 cm-3 and ND = 1×1017 cm-3, maintained at T = 300K.  The minority carrier lifetimes in the p-side and n-side are τn=10-8 s and τp=10-7 s, respectively.

- Calculate the minority carrier densities at the edges of the depletion region when the applied voltage (VA) is 0.6 V.

- Sketch the electron and hole current density components as a function of distance on both sides of the junction, for the applied bias voltage of part (a).

- Calculate the location of the plane (i.e. value of x) at which the electron and hole current densities are equal in magnitude, for the applied voltage of part (a).

Problem 4: Comparison of Schottky Diode and pn Junction Diode I-V Characteristics

- Calculate the reverse-bias current for a Schottky contact between nickel silicide (Bn = 0.65 eV) and n-type Si (ND = 1×1017 cm-3), of area A = 1 mm2, maintained at T = 300K:

- Calculate the reverse-bias current for a p+n diode with ND = 1×1017 cm-3 and minority carrier lifetime τp=10-7 s on the n side, of area A = 1 mm2, maintained at T = 300K:

- Qualitatively sketch the I-V curve for the Schottky diode and the pn diode on the same plot.

- Compare the forward bias voltages for each diode at a forward current of 1 A.