University of California at Berkeley

College of Engineering

Department of Electrical Engineering and Computer Science

EECS 150									R. H. Katz

Fall 2000

Problem Set # 4 - Solution

1a) Inputs: n_of_d[1:0]

n_of_n[2:0]

Outputs: d_out[1:0]

n_out[2:0]

no_change

- The d_out bits tell how many dimes should be given: 00 for none, 01 for one, and 10 for two. Three dimes should never be given so 11 is undefined.

The n_out bits are similar to dimes_out: 000 for none, 001 for one, 010 for two,  011 for three, 101 for four, and 110 for five. Anything else is undefined.

no_change will be 1 if it is not possible to return change and 0 if it is. If no_change is 1, we don’t care about all the other outputs. I’m assuming that the larger system will ignore the other output signals when no_change is 1.

c)

| n_of_d1 | n_of_d0 | n_of_n2 | n_of_n1 | n_of_n0 | d_out1 | d_out0 | n_out2 | n_out1 | n_out0 | no_change |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0 | 0 | 0 | 0 | 0 | x | x | x | x | x | 1 |
| 0 | 0 | 0 | 0 | 1 | x | x | x | x | x | 1 |
| 0 | 0 | 0 | 1 | 0 | x | x | x | x | x | 1 |
| 0 | 0 | 0 | 1 | 1 | x | x | x | x | x | 1 |
| 0 | 0 | 1 | 0 | 0 | x | x | x | x | x | 1 |
| 0 | 0 | 1 | 0 | 1 | x | x | 1 | 0 | 1 | 0 |
| 0 | 0 | 1 | 1 | 0 | x | x | 1 | 0 | 1 | 0 |
| 0 | 0 | 1 | 1 | 1 | x | x | 1 | 0 | 1 | 0 |
| 0 | 1 | 0 | 0 | 0 | x | x | x | x | x | 1 |
| 0 | 1 | 0 | 0 | 1 | x | x | x | x | x | 1 |
| 0 | 1 | 0 | 1 | 0 | x | x | x | x | x | 1 |
| 0 | 1 | 0 | 1 | 1 | 0 | 1 | 0 | 1 | 1 | 0 |
| 0 | 1 | 1 | 0 | 0 | 0 | 1 | 0 | 1 | 1 | 0 |
| 0 | 1 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 1 | 0 |
| 0 | 1 | 1 | 1 | 0 | 0 | 1 | 0 | 1 | 1 | 0 |
| 0 | 1 | 1 | 1 | 1 | 0 | 1 | 0 | 1 | 1 | 0 |
| 1 | 0 | 0 | 0 | 0 | x | x | x | x | x | 1 |
| 1 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 1 | 0 |
| 1 | 0 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 1 | 0 |
| 1 | 0 | 0 | 1 | 1 | 1 | 0 | 0 | 0 | 1 | 0 |
| 1 | 0 | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 |
| 1 | 0 | 1 | 0 | 1 | 1 | 0 | 0 | 0 | 1 | 0 |
| 1 | 0 | 1 | 1 | 0 | 1 | 0 | 0 | 0 | 1 | 0 |
| 1 | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 1 | 0 |
| 1 | 1 | 0 | 0 | 0 | x | x | x | x | x | 1 |
| 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 1 | 0 |
| 1 | 1 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 1 | 0 |
| 1 | 1 | 0 | 1 | 1 | 1 | 0 | 0 | 0 | 1 | 0 |
| 1 | 1 | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 |
| 1 | 1 | 1 | 0 | 1 | 1 | 0 | 0 | 0 | 1 | 0 |
| 1 | 1 | 1 | 1 | 0 | 1 | 0 | 0 | 0 | 1 | 0 |
| 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 1 | 0 |

| d_out1: |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
|  |  | n_of_d0¦n_of_n2 n_of_n1¦n_of_n0 | 00 | 01 | 11 | 10 |
|  |  | 00 | x | x | x | x |
|  | n_of_d1=0 | 01 | x | x | x | x |
|  |  | 11 | 0 | 0 | 0 | 0 |
|  |  | 10 | x | x | 0 | x |
|  |  | n_of_d0¦n_of_n2 n_of_n1¦n_of_n0 | 00 | 01 | 11 | 10 |
|  |  | 00 | x | 1 | 1 | 1 |
|  | n_of_d1=1 | 01 | 1 | 1 | 1 | 1 |
|  |  | 11 | 1 | 1 | 1 | 1 |
|  |  | 10 | x | 1 | 1 | 1 |
| d_out1 = n_of_d1 |  |  |  |  |  |  |

| d_out0: |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
|  |  | n_of_d0¦n_of_n2 n_of_n1¦n_of_n0 | 00 | 01 | 11 | 10 |
|  |  | 00 | x | x | x | x |
|  | n_of_d1=0 | 01 | x | x | x | x |
|  |  | 11 | 1 | 1 | 1 | 1 |
|  |  | 10 | x | x | 1 | x |
|  |  | n_of_d0¦n_of_n2 n_of_n1¦n_of_n0 | 00 | 01 | 11 | 10 |
|  |  | 00 | x | 0 | 0 | 0 |
|  | n_of_d1=1 | 01 | 0 | 0 | 0 | 0 |
|  |  | 11 | 0 | 0 | 0 | 0 |
|  |  | 10 | x | 0 | 0 | 0 |
| d_out0 = n_of_d1' |  |  |  |  |  |  |

| n_out2: |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
|  |  | n_of_d0¦n_of_n2 n_of_n1¦n_of_n0 | 00 | 01 | 11 | 10 |
|  |  | 00 | x | x | x | x |
|  | n_of_d1=0 | 01 | x | 1 | 1 | 1 |
|  |  | 11 | 0 | 0 | 0 | 0 |
|  |  | 10 | x | x | 0 | x |
|  |  | n_of_d0¦n_of_n2 n_of_n1¦n_of_n0 | 00 | 01 | 11 | 10 |
|  |  | 00 | x | 0 | 0 | 0 |
|  | n_of_d1=1 | 01 | 0 | 0 | 0 | 0 |
|  |  | 11 | 0 | 0 | 0 | 0 |
|  |  | 10 | x | 0 | 0 | 0 |
| n_out2 = n_of_d1'n_of_d0 |  |  |  |  |  |  |

| n_out1: |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
|  |  | n_of_d0¦n_of_n2 n_of_n1¦n_of_n0 | 00 | 01 | 11 | 10 |
|  |  | 00 | x | x | x | x |
|  | n_of_d1=0 | 01 | x | 0 | 0 | 0 |
|  |  | 11 | 1 | 1 | 1 | 1 |
|  |  | 10 | x | x | 1 | x |
|  |  | n_of_d0¦n_of_n2 n_of_n1¦n_of_n0 | 00 | 01 | 11 | 10 |
|  |  | 00 | x | 1 | 1 | 1 |
|  | n_of_d1=1 | 01 | 1 | 1 | 1 | 1 |
|  |  | 11 | 1 | 1 | 1 | 1 |
|  |  | 10 | x | 1 | 1 | 1 |
| d_out1 = n_of_d1 + n_of_d0 |  |  |  |  |  |  |

| n_out0: |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
|  |  | n_of_d0¦n_of_n2 n_of_n1¦n_of_n0 | 00 | 01 | 11 | 10 |
|  |  | 00 | x | x | x | x |
|  | n_of_d1=0 | 01 | x | 1 | 1 | 1 |
|  |  | 11 | x | x | x | x |
|  |  | 10 | x | x | x | x |
|  |  | n_of_d0¦n_of_n2 n_of_n1¦n_of_n0 | 00 | 01 | 11 | 10 |
|  |  | 00 | x | 1 | 1 | 1 |
|  | n_of_d1=1 | 01 | 1 | 1 | 1 | 1 |
|  |  | 11 | 1 | 1 | 1 | 1 |
|  |  | 10 | x | 1 | 1 | 1 |
| n_out0 = 1 |  |  |  |  |  |  |

| no_change: |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
|  |  | n_of_d0¦n_of_n2 n_of_n1¦n_of_n0 | 00 | 01 | 11 | 10 |
|  |  | 00 | 1 | 1 | 1 | 1 |
|  | n_of_d1=0 | 01 | 1 | 0 | 0 | 0 |
|  |  | 11 | 1 | 1 | 1 | 1 |
|  |  | 10 | 1 | 1 | 1 | 1 |
|  |  | n_of_d0¦n_of_n2 n_of_n1¦n_of_n0 | 00 | 01 | 11 | 10 |
|  |  | 00 | 1 | 0 | 0 | 0 |
|  | n_of_d1=1 | 01 | 0 | 0 | 0 | 0 |
|  |  | 11 | 0 | 0 | 0 | 0 |
|  |  | 10 | 1 | 0 | 0 | 0 |
| no_change = n_of_d1'n_of_d0 + n_of_d1'n_of_n2' + n_of_d1'n_of_n1n_of_n0 + n_of_n2'n_of_n1'n_of_n0' |  |  |  |  |  |  |

2) This is the way I am labeling the display:

LED6

LED5                                   LED4

LED3

LED2                                    LED1

LED0

| A | B | C | D | L6 | L5 | L4 | L3 | L2 | L1 | L0 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0 | 0 | 0 | 0 | 1 | 1 | 1 | 0 | 1 | 1 | 1 |
| 0 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |
| 0 | 0 | 1 | 0 | 1 | 0 | 0 | 1 | 0 | 0 | 0 |
| 0 | 0 | 1 | 1 | 1 | 0 | 0 | 1 | 0 | 0 | 1 |
| 0 | 1 | 0 | 0 | 0 | 1 | 1 | 1 | 0 | 0 | 0 |
| 0 | 1 | 0 | 1 | 0 | 0 | 0 | 1 | 1 | 1 | 0 |
| 0 | 1 | 1 | 0 | 0 | 0 | 1 | 1 | 1 | 0 | 0 |
| 0 | 1 | 1 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 |
| 1 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 1 | 1 | 0 |
| 1 | 0 | 0 | 1 | 0 | 1 | 1 | 1 | 1 | 1 | 0 |
| 1 | 0 | 1 | 0 | X | X | X | X | X | X | X |
| 1 | 0 | 1 | 1 | X | X | X | X | X | X | X |
| 1 | 1 | 0 | 0 | X | X | X | X | X | X | X |
| 1 | 1 | 0 | 1 | X | X | X | X | X | X | X |
| 1 | 1 | 1 | 0 | X | X | X | X | X | X | X |
| 1 | 1 | 1 | 1 | X | X | X | X | X | X | X |

L6:

| AB CD | 00 | 01 | 11 | 10 |
| --- | --- | --- | --- | --- |
| 00 | 1 | 1 | 1 | 1 |
| 01 | 0 | 0 | 0 | 0 |
| 11 | X | X | X | X |
| 10 | 0 | 0 | X | X |

L6 = A’B’

L5:

| AB CD | 00 | 01 | 11 | 10 |
| --- | --- | --- | --- | --- |
| 00 | 1 | 0 | 0 | 0 |
| 01 | 1 | 0 | 1 | 0 |
| 11 | X | X | X | X |
| 10 | 1 | 1 | X | X |

L5 = A + C’D’ + BCD

L4:

| AB CD | 00 | 01 | 11 | 10 |
| --- | --- | --- | --- | --- |
| 00 | 1 | 0 | 0 | 0 |
| 01 | 1 | 0 | 0 | 1 |
| 11 | X | X | X | X |
| 10 | 1 | 1 | X | X |

L4 = A + C’D’ + BCD’

L3:

| AB CD | 00 | 01 | 11 | 10 |
| --- | --- | --- | --- | --- |
| 00 | 0 | 0 | 1 | 1 |
| 01 | 1 | 1 | 1 | 1 |
| 11 | X | X | X | X |
| 10 | 0 | 1 | X | X |

L3 = C + B + AD

L2:

| AB CD | 00 | 01 | 11 | 10 |
| --- | --- | --- | --- | --- |
| 00 | 1 | 0 | 0 | 0 |
| 01 | 0 | 1 | 0 | 1 |
| 11 | X | X | X | X |
| 10 | 1 | 1 | X | X |

L2 = A + B’C’D’ + BC’D + BCD’

L1:

| AB CD | 00 | 01 | 11 | 10 |
| --- | --- | --- | --- | --- |
| 00 | 1 | 0 | 0 | 0 |
| 01 | 0 | 1 | 1 | 0 |
| 11 | X | X | X | X |
| 10 | 1 | 1 | X | X |

L1 = A + BD + B’C’D

L0:

| AB CD | 00 | 01 | 11 | 10 |
| --- | --- | --- | --- | --- |
| 00 | 1 | 0 | 1 | 0 |
| 01 | 0 | 0 | 0 | 0 |
| 11 | X | X | X | X |
| 10 | 0 | 0 | X | X |

L0 = A’B’C’D’ + B’CD				L5 AND L6

A	B	 C 	D

3a)

Z = AB’C’D0’D1’ + BCD1’ + B’CD0 + BC’D0D1 + ABD1 + BCD0’ + ACD1

b, c)

d) In terms of logic gates, the implementation in part a) will be the best.

# Text boxes

L6

L0

L1

L2

L3

L4

L5

0         0          1         0

0          0         1         1

0          0         1         1

1          0         1         0

CD0

AB

00        01       11       10

11

10

01

01

D1=0

0          0         1         0

0          1         0         1

1          1         1         1

0          0         1          1

00        01       11       10

D1=1

00

00

11

10

CD0

AB

Z

0

0

D0

D0

0

D0

1

D0’

D0’

0

D0

1

0

1

1

1

0

D0

D0 AND D1

D0 NAND D1

D0 NOR D1

D0 OR D1

D1

1

Z

A   B   C   D1