University of California at Berkeley

College of Engineering

Department of Electrical Engineering and Computer Science

EECS 150									R. H. Katz

Fall 2000

Homework Quiz # 4 Solution

Your job is to design a BCD-to-4 Segment Display controller to the following specification. The inputs are the decimal digits 0 through 9 encoded as 0000 through 1001 on the inputs A,B,C,D. The 4 Segment display has driver signals S0, S1, S2, S3 that when driven cause the indicated LED segment to illuminate. The encoding of the BCD digits is as follows:

Fill in the K-maps got S0, S1, S2, S3 and develop an implementation with the fewest possible products considered across all four functions (i.e., an implementation suitable for a PLA).

1	1	X      1                                            1        0  	X      1

0       1 	X      0                                            1        0	X      1

1       1	X      X	                                          0        1 	X      X

0       0	X      X	                                          1        1 	X      X

1        0 	X      0                                             1      1 	X       1

0        1	X      1                                             0      0	X       1

0        1     	X	X	                                           0      0	X	X

1        0  	X	X                                          0      1  	X	X

S0=  C’D’ + BD + CD					S2=  A’B’D’ + AD + BD

S1=  B’C’ + BC + CD’					S3=  AD + BD’ + C’D’

How many unique product terms in your solution?

9 : C’D’, BD, CD, B’C’, BC, CD’, A’B’D’, AD, BD’

# Text boxes

B

9

4

8

7

6

5

D

3

2

1

0

S2

S1

S3

S0

A

C

S0

B

D

A

C

S1

B

D

A

C

S2

B

D

A

C

S3