EECS150 Homework #8 Solutions:

1)

module counter16-1 (RST, CE, CLK, TC, Q)

input RST, CE, CLK;

output TC;

output[15:0] Q;

wire w0,w1,w2,w3,w4,w5,w6,w7,

w8,w9,w10,w11,w12,w13,w14,w15,w16;

wire c0,c1,c2,c3,c4,c5,c6,c7

c8,c9,c10,c11,c12,c13,c14;

XOR x0(CE, Q[0], w0),

x1(c0, Q[1], w1),

x2(c1, Q[2], w2),

x3(c2, Q[3], w3),

x4(c3, Q[4], w4),

x5(c4, Q[5], w5),

x6(c5, Q[6], w6),

x7(c6, Q[7], w7),

x8(c7, Q[8], w8),

x9(c8, Q[9], w9),

x10(c9, Q[10], w10),

x11(c10, Q[11], w11),

x12(c11, Q[12], w12),

x13(c12, Q[13], w13),

x14(c13, Q[14], w14),

x15(c14, Q[15], w15);

AND a0(CE, Q[0], c0),

a1(c0, 	Q[1], c1),

a2(c1, 	Q[2], c2),

a3(c2, 	Q[3], c3),

a4(c3, 	Q[4], c4),

a5(c4, 	Q[5], c5),

a6(c5, 	Q[6], c6),

a7(c6, 	Q[7], c7),

a8(c7, 	Q[8], c8),

a9(c8, 	Q[9], c9),

a10(c9, Q[10], c10),

a11(c10, Q[11], c11),

a12(c11, Q[12], c12),

a13(c12, Q[13], c13),

a14(c13, Q[13], c14),

a15(c14, Q[15], TC);

DFF q0(Q[0], w0, CLK, RST),

q1(Q[1], w1, CLK, RST),

q2(Q[2], w2, CLK, RST),

q3(Q[3], w3, CLK, RST),

q4(Q[4], w4, CLK, RST),

q5(Q[5], w5, CLK, RST),

q6(Q[6], w6, CLK, RST),

q7(Q[7], w7, CLK, RST),

q8(Q[8], w8, CLK, RST),

q9(Q[9], w9, CLK, RST),

q10(Q[10], w10, CLK, RST),

q11(Q[11], w11, CLK, RST),

q12(Q[12], w12, CLK, RST),

q13(Q[13], w13, CLK, RST),

q14(Q[14], w14, CLK, RST),

q15(Q[15], w15, CLK, RST);

endmodule

2)

module counter16-2 (RST, CE, CLK, TC, Q)

input RST, CE, CLK;

output TC;

output [15:0] Q;

reg [15:0] Q;

assign TC = CE & Q[15] & Q[14] & Q[13] & Q[12] & Q[11] & Q[10] &

# Q[9] &  Q[8] & Q[7] & Q[6] & Q[5] & Q[4] & Q[3] & Q[2] &

Q[1] & Q[0];

always @ (posedge CLK or CE or RST)

if (RST)

Q = 16’b0000000000000000;

else

if (CE)

Q = Q + 16’b0000000000000001;

endmodule

3)

module counter32 (RST, CE, CLK, TC, Q)

input RST, CE, CLK;

output TC;

output [31:0] Q;

wire TC1, TC2;

counter16-2 c1(RST, CE, CLK, TC1, Q[15:0]);

counter16-2 c2(RST, TC1, CLK, TC2, Q[31:16]);

assign TC = TC1 & TC2;

endmodule

4)

6-18)

If both up and down are 1, the counter counts up.

6-26)

Use a 2 bit counter.

6-28)

d1 = A xor B

d2 = AB’ + C

d3 = A’B’C’

5)

6)

7)

Calinx has two by-16 parts in parallel, providing 32 bit wide interface.
The maximum read bandwidth will occur when the burst length is maximized (a complete row). Rows are 512 32-bit words. From page 42 of the spec, the time for a burst read is 4+L cycles for a burst of L words.
Therefore the average max read bandwidth is:

(512 x 32 bits / 516 cycles) x 100MHz = 3.175 Gb/s.

8)