University of California at Berkeley

College of Engineering

Department of Electrical Engineering and Computer Science

(SOLUTIONS)

EECS 150									R. H. Katz

Fall 2005

Problem Set # 9 (Assigned 2 November, Due 18 November)

- Derive a table to show the coverage of various stuck-at-0 and stuck-at-1 faults by the eight possible input combinations. What is the minimum test set for this circuit?

| Out | Test | Fault Detected |
| --- | --- | --- |
|  | W1 | W2 | W3 | A0 | A1 | B0 | B1 | C0 | C1 | D0 | D1 | F0 | F1 |
| 1 | 0 | 0 | 0 |  |  |  |  |  |  |  | X | X |  |
| 0 | 0 | 0 | 1 |  |  |  |  | X |  | X |  |  | X |
| 1 | 0 | 1 | 0 |  |  |  |  |  |  |  | X | X |  |
| 0 | 0 | 1 | 1 |  | X |  |  | X |  | X |  |  | X |
| 1 | 1 | 0 | 0 |  |  |  |  |  |  |  | X | X |  |
| 0 | 1 | 0 | 1 |  |  |  | X | X |  | X |  |  | X |
| 1 | 1 | 1 | 0 |  |  |  |  |  |  |  |  | X |  |
| 1 | 1 | 1 | 1 | X |  | X |  |  | X |  |  | X |  |

2.	In the following circuit, are all single stuck-at-0 and stuck-at-1 faults in the circuit detectable? If not, explain why?

No, for example:

W1 = 1, W2 = 1, W3 = 0, regardless of d = 0 or 1, f will be 1.  This is just one example of how stuck at 0, and stuck at 1 faults can be undectable.

3.  Given the following MOORE MACHINE State Transition Table, use the Implication Chart method to minimize the number of states. Draw the resulting minimized state diagram.

By inspection, we see that B=E, C = F, A = D

| Current State | Next State | Output |
| --- | --- | --- |
|  | 0 | 1 |  |
| A | A | B | 1 |
| B | A | C | 0 |
| C | B | C | 0 |

- Given your minimized state diagram for Problem 4, perform three alternative state assignments:

- Assign your states sequentially (e.g., A=0, B=1, C=2, …);

A=00, B = 01, C = 10, D = 11

- Assign your states using a 1 Hot Encoding (e.g., A=001, B=010, C=100);
A=0001, B=0010, C = 0100, D=1000

- Assign states using the heuristics presented in lecture.
A = 00, B = 10, C = 11

- Implement your three assignments using K-maps. Which yields the best implementation and why?

Part A IMPLEMENTATION

| I | Q1 | Q0 | Q1+ | Q0+ |
| --- | --- | --- | --- | --- |
| 0 | 0 | 0 | 1 | 1 |
| 0 | 0 | 1 | 0 | 0 |
| 0 | 1 | 0 | 0 | 1 |
| 1 | 0 | 0 | 0 | 1 |
| 1 | 0 | 1 | 1 | 0 |
| 1 | 1 | 0 | 1 | 0 |

Q0+

|  | Q1Q0 |
| --- | --- |
|  | 00 | 01 | 11 | 10 |
| I | 0 | 1 | 0 | X | 1 |
|  | 1 | 1 | 0 | X | 0 |

Q0+ = Q0’Q1’ + IQ1

Q1+

|  | Q1Q0 |
| --- | --- |
|  | 00 | 01 | 11 | 10 |
| I | 0 | 1 | 0 | X | 0 |
|  | 1 | 0 | 1 | X | 0 |

Q1+ = IQ0 + I’Q0’Q1’

PART B IMPLEMENTATION

| I | Q2 | Q1 | Q0 | Q2’ | Q1’ | Q0’ |
| --- | --- | --- | --- | --- | --- | --- |
| 0 | 0 | 0 | 1 | 0 | 1 | 0 |
| 0 | 0 | 1 | 0 | 0 | 0 | 1 |
| 0 | 1 | 0 | 0 | 0 | 1 | 0 |
| 1 | 0 | 0 | 1 | 0 | 1 | 0 |
| 1 | 0 | 1 | 0 | 1 | 0 | 0 |
| 1 | 1 | 0 | 0 | 1 | 0 | 0 |

Q0’ = I’Q2’Q1Q0

Q1’=  I’Q2’Q1’Q0’ + I’Q2Q1’Q0’ + IQ2’Q1’Q0 + IQ2Q1Q0

Q2’ = I Q2’Q1Q0 + IQ2Q1’Q0

PART C IMPLEMENTATION

| I | Q1 | Q0 | Q1+ | Q0+ |
| --- | --- | --- | --- | --- |
| 0 | 0 | 0 | 0 | 1 |
| 0 | 0 | 1 | 0 | 1 |
| 0 | 1 | 0 | 0 | 0 |
| 0 | 1 | 1 | 1 | 0 |
| 1 | 0 | 0 | 1 | 0 |
| 1 | 0 | 1 | 1 | 0 |
| 1 | 1 | 0 | 1 | 1 |
| 1 | 1 | 1 | 1 | 1 |

Q0+

|  | Q1Q0 |
| --- | --- |
|  | 00 | 01 | 11 | 10 |
| I | 0 | 1 | X | 0 | 0 |
|  | 1 | 0 | X | 1 | 1 |

Q0+ = I’Q1 + IQ1

Q1+

|  | Q1Q0 |
| --- | --- |
|  | 00 | 01 | 11 | 10 |
| I | 0 | 0 | X | 0 | 1 |
|  | 1 | 1 | X | 1 | 1 |

Q1+ = I

PART C yields the simplest implementation

# Text boxes

1

0

0

1

0

0

1

B

C

C

E

F

C

0

D

A

B

D

A

E

Current State

A

B

C

D

E

F

Next State

Output