University of California at Berkeley

College of Engineering

Department of Electrical Engineering and Computer Science

Lab 0

Chips, Scopes, and Analyzers

| Assigned: | Week of 8/27 |
| --- | --- |
| Due: | Week of 9/2, 10 minutes after start of your assigned lab section. |

# 1.0 Motivation

In this lab you will gain hands-on experience with simple combinational gates (the real version of what you met in simulation on 61C) breadboarding simple circuits and using the basic tools of hardware design – signal generators and oscilloscopes.

In future labs, you will be “wiring up” circuits by programming your FPGA.  This lab will give you a little bit of experience with traditional gates and insight toward what is going on inside the FPGA.  Also, in debugging hardware you will often resort of using (or building) tools that generate certain patterns and observing how your hardware behaves when presented with those patterns.

# 2.0 Introduction to TTL

In this lab you will use a single 74C00 quad NAND gate in a Dual Inline Package (DIP).

# 3.0 Prelab

- There is no prelab preparation for this lab.

Materials

- Breadboard

- HP 8116A Pulse/Function Generator

- HP 54645D Mixed Signal Oscilloscope

- HP E3630A DC Power Supply

- 74C00 quad NAND chip

- Probes

# 4.0 Lab Procedure

Logical Behavior

- Go on the web and find the datasheet for the chip that you are using.  Identify the pins used for power and ground, as well as the inputs and outputs of the gates.

- Use a 5V DC Power Supply and ground (the red com plug for these power supplies is the ground, and not the black plug) to connect to the NAND chip.

- Connect the 5V power supply to the 2 inputs of the NAND gate and capture the output using the oscilloscope or multimeter. Repeat for the other 3 combinations of high and low inputs for the NAND gate and draw the truth table. Verify that it is the NAND function. Have your TA come by take a look and initial the checkoff below.

- Using multiple NAND gates, configure them to implement a 2-input XOR function.  Draw the circuit.  Draw the truth table.  Have your TA initial your checkoff.

Timing behavior

- Wire your NAND gates to form a sequence of inverters.

- Use the pulse/function generator to create a square wave as input to the series of NAND gates. You may need to play around a little with the amplitude and offset for some of the function generators to get a proper square wave oscillating from 0V to 5V.

- Capture the input, the output of the first gate and the output of the last gate using the oscilloscope.

- Use the oscilloscope to measure the rise and fall times and the propagation delays in your circuit. For the oscilloscope, it will be helpful to use the time and voltage cursors (press the cursors button, and then select the time/measurement cursors before using the entry knob to move them to their proper location) to get these measured times.

- Find the rise and fall times and the propagation delays described in your datasheet?  How do these compare to your measurements?

- Reconfigure your circuit to have a single NAND gate driving three gates.  How do the propagation times change?

Simple Circuit with Feedback

- Configure your circuit to form a ring containing three NAND gates.

- Explain the expected behavior of this circuit.

- Estimate the period and frequency of the output

- Capture the waveform and compare with your estimate. Have you TA initial your checkoff.

Simple Latch

- Configure your circuit to form a gated SR latch with cross-coupled NAND gates. hint: http://en.wikipedia.org/wiki/Latch_(electronic)

- What is the behavior when the “Clock” input is high?

- What is the behavior when the “Clock” input is low?

- Capture the waveform showing that it works as a latch.

# 5.0 HP54645D Mixed Signal Oscilloscope (Logic Analyzer)

Figure 6: HP54645D Mixed Signal Oscilloscope

Shown in Figure 6 above, is the HP54645D Mixed Signal Oscilloscope, which we will generally refer to as simply “the oscilloscope” or “the logic analyzer.”  It is in fact a combination of these instruments, both of which are design to graph waveforms (analog and digital respectively) over time.  In this class we will almost exclusively use the logic analyzer portion of these devices, since this is a digital systems class.

Using the logic analyzer is significantly less complicated than it appears and it is an invaluable debugging tool.  The logic analyzer allows us to examine signals over time at various scales, you can zoom in to see events on different clock cycles, or zoom out to see how a signal behaves over the course of seconds.

## 5.1 Front Panel Controls

This section will explain at least a little bit about all of the buttons and controls on the front panel of the logic analyzer.

Figure 7: HP54645D Front Panel Controls

### 5.1.1 Display & Brightness Control

Of course this is the screen, where you will see your waveforms and other such information.  At the bottom left of the screen is a brightness control.  If your screen appears blank, try the brightness.

Notice the row of softkeys across the bottom of the screen.

### 5.1.2 Softkeys

In order to provide more advanced controls without cluttering the front panel, there are six softkeys, whose meaning changes as you navigate the controls menus or change operating modes.  If we mention a button that does not appear on the front panel, check the softkeys.

### 5.1.3 Calibration Output

This is used to calibrate the analog oscilloscope probes.  If you are in doubt as to whether the probe is behaving correctly, hook it to the calibration output and hit Autoscale.  You should see a nice clean 0-5V square wave at ~1.2kHz.

### 5.1.4 Autoscale

Located in the Measurement Keys section of the front panel, this is one of the most used buttons.  It will cause the oscilloscope/logic analyzer to automatically search for signals on its inputs.  When it finds signals it will attempt to place them in the middle of the screen and set the triggering to that they are stable and ready for use.

If you lose the signal, Autoscale may help.

### 5.1.5 Measurement Controls

Consists of three buttons; Voltage, Time, and Cursors.  Voltage and Time will display options for types of measurements (Vavg, Vp-p, Freq, etc.) on the softkeys.  When selected, the measurements will be displayed at bottom of screen.  The Source softkey can be used to select the correct analog source channel.

The Cursors button is used to display or clear time and voltage measurement cursors which are selected with softkeys and moved with the Entry knob.  Note that you can have the time cursors print out the value (in Hex, Binary or Decimal) of the 16 digital channels.

### 5.1.6 Analog Controls

The Volts/Div knob can be used to change the vertical (voltage) scaling of the two analog channels.  Notice that there are two knobs: the scaling for each of the two channels are separate (1 division may be 1V on A1 and 2V on A2).

The A1 and A2 keys will turn the respective analog channel on or off while bringing up a softkey menu allowing you to select AC or DC coupling and Noise Filtering.  The ± button will allow you to see sum and difference waveforms.

### 5.1.7 Horizontal

The Delay knob will allow you to scroll the screen left or right.

Main Delayed:  Horizontal mode should be set as normal with softkeys, the Time Ref softkey controls what reference to use when zooming in with Time/Div knob.  Vernier is used to minimize time steps in Time/Div knob.

Time/Div changes the time per grid block.  The time/div scaling is displayed at the top of the screen.

### 5.1.8 Digital

The Label/Threshold button allows you to label any of the 16 probe leads of the logic analyzer.  The threshold menu and softkeys let you choose what type of logic you are using, MOS or TTL should work fine.

The D0-D15 button allows you to select which logic analyzer probes will be displayed.  Individual signals can be selected with Select knob and turned on or off with the softkeys.

The Position knob will let you reorder the signal on the display.  Notice that this will affect the value readout produced by the time cursors (see 5.1.5 Measurement Controls).

### 5.1.9 Trigger

The Edge button will select edge triggering mode, where the scope will wait for a rising or falling edge (selectable with softkeys) on the channel you select using the softkeys.

The Pattern button will let you modify the pattern triggering mode pattern, where the scope will trigger on a pattern of High, Low, Rising, Falling or Don’t Cares on the various inputs.  Use the Select knob and softkeys to set the pattern.

The Analog Level knob will let you set the analog voltage at which to trigger (applies to the analog signals only).  The Holdoff knob will allow you to set the amount of time before the screen is redrawn; you will want to set this to the minimum.

The Mode/Coupling button will bring up a softkey menu of triggering modes: Auto Level, Auto and Normal.  While Auto may be useful for analog work, you will always want Normal for using the logic analyzer.

The Advanced button brings up a softkey menu of the various triggering modes.

### 5.1.10 Storage

The Run/Stop button starts and stops the refresh on the display.  This is useful when you want to freeze the screen to examine it more closely.

The Single button can be used to set the scope to single mode, where it will trigger once, remember the data and then freeze the screen.  This is perfect for capturing a one time event, like something that happens at reset.

Erase will clear the screen; measurement should be restarted with the Run/Stop button.

## 5.2 Triggering

Triggering the logic analyzer properly is key to being able to actually see the waveforms you are interested in.  We recommend that you become intimately familiar with the various triggering modes, but perhaps the most useful for digital work is pattern mode.  This section is a brief tutorial on how to set up and use pattern triggering mode.

- Make sure the logic analyzer is on

- Make sure the channels you are interested in are showing

  - The A1 and A2 buttons can be used to enable or disable the analog channels.

  - The D0-D15 button and Select knob will let you select specific digital signals.  You can then use the softkeys to enable or disable them.

- Switch the logic analyzer to Normal triggering mode.

  - Press Mode/Coupling in the Trigger Box

  - Select Normal under Trigger Mode on the softkey menu

- Switch the logic analyzer to Pattern advanced triggering mode.

  - Press Advanced in the Trigger Box

  - Select Pattern under Advanced Trigger Mode on the softkey menu

- Set up a triggering pattern

  - Press Pattern in the Trigger Box

  - Use the Select knob to select a signal

    - Select the value that signal should have

    - Note that each signal is compared against its bit in the pattern, when all 18 (16 digital, 2 analog) channels match, the scope will trigger

    - L: Logic Low

    - H: Logic High

    - X: Don’t Care (Ignore this signal for the pattern)

    - ↑: Rising Edge

    - ↓: Falling Edge

- Set the Time/Div

  - Play with the Time/Div knob until the time per division is approximately what you need.

  - Remember a 27MHz clock cycle is 37ns from rising edge to rising edge.

- Start the logic analyzer running

  - To trigger once and save the waveforms press Single

    - If you want to trigger again you will need to press Single again

  - To trigger every time the pattern is matched press Run/Stop

# 6.0 Lab 0 Checkoff

Name: ____________________________

Section: ___________________________

| Assigned: | Week of 8/27 |
| --- | --- |
| Due: | Week of 9/2, 10 minutes after start of your assigned lab section. |

NAND truth table/waveform	__________

XOR truth table/waveform	__________

Tr, Tf, Tp0-1, Tp1	__________ __________ __________ __________

Ring oscillator	__________

D-Latch	__________

Hours Spent:	__________

Total:	__________

TA:	__________

| RevB – 8/27/2007 | Udam Saini | Updated to explain/modify some of the lab steps. Copied a detailed description of the Oscilloscope that was in an old lab. |
| --- | --- | --- |
| RevA | Culler | Draft of basic lab |

# Text boxes

C