CS150

Week 5, lecture 2

Covers:

- Glitches

- Solutions to glitch problems

- Converting to NAND

- Counters

- Glitches

Glitch: uninvited pulse at output.

Hazard – circuit with potential for glitches

Simple examples:

A				Should always be 1, but could glitch to 0: Static 1 hazard.

F

A

__

A

F				     Glitch!!!

A				     Should always be 0, but could glitch to 1: Static 0 hazard

F

How does a hazard look on a K-map?

_

F = AB + AC

In SOP form:

- 1-1 correspondence between implicant (circled groups on K-map) and AND gates.

- The “job” of each AND gate is to represent a piece of the ON set.

- “Most” implicants/AND gates output 0

- Moving inside the circle:

- No change on inputs to implicant

- No change on outputs

- In the ON set, worry about glitching to 0.

- In the OFF set, worry about glitching to 1.

2)	Solutions to glitch problems

SOP:

_

F = AB + AC + BC

POS:

_

F = ( A + C )( A + B )( B + C )

3)	Converting to NAND

Say you had a circuit like this:

And someone told you to implement it with only NAND gates. What should you do?

Answer:

Replace   		with 			and bubble push…

Now this circuit can be built with just inverters and NAND gates. (You can also build inverters from NAND gates and completely convert the circuit to a NAND circuit. NAND:                                       )

SOP AND/OR to NAND/NAND (as above)

and

POS OR/AND to NOR/NOR:

DON’T USE RULES. Understand bubble pushing.

4)	Counters

Offset and limit counters covered in first lecture of week 5.

The truth table for a binary counter:

Do you need the midterm review stuff?

# Text boxes

PS2

PS1

PS0

D0 Q0

D1 Q1

D2 Q2

NS

Logic

___            ___    ___

NS2 = PS2 PS0 + PS2 PS1 + PS2 PS1 PS0

___    ___

NS1 = PS1 PS0 + PS1 PS0 = PS1( PS0

___

NS0 = PS0

NS0

1      1      1     1

0      0      0     0

PS2PS1

PS0

00     01      11      10

0

1

NS1

0      1      1     0

1      0      0     1

PS2PS1

PS0

00     01      11      10

0

1

NS2

00     01      11      10

0

1

0      0      1     1

0      1      0     1

(

(

PS2PS1

PS0

PS	     NS

2   1   0      2   1   0

0   0   0      0   0   1

0   0   1      0   1   0

0   1   0      0   1   1

0   1   1      1   0   0

1   0   0      1   0   1

1   0   1      1   1   0

1   1   0      1   1   1

1   1   1      0   0   0

0      0      1     0

1      1      1     0

AB

C

00     01      11      10

0

1

0

F

A

B

C

F

A

B

C

(

0      0      1     0

1      1      1     0

AB

C

00     01      11      10

0

1

B

C

F

A

C

B

1

F

A

(

00     01      11      10

0

1

0      0      1     0

1      1      1     0

AB

C

F

A

C

B

(

(

F

A

F

A

1

1