CS150

Week 6, lecture 2

Covers:

- RAM

- Multi-input gates

- ROM

- Decoder/Demux

- Multiplexers

- Tristate buffers

- ROM based logic

- RAM

Control Lines

Timing for READing from a RAM (CS can be turned on all the time)

Timing for WRITing from a RAM (Doing WRITE using CS)

SRAM –Static RAM

2X3 SRAM

?

____________________

2)	Multi-input gates:   Alternative N-input NOR:	F(I0, I1, I2, I3, … IN) = (I0 + I1 + I2 + I3 + … + IN)

RBIG

_____________

Alternative N-input NAND: 		G(I0, I1, I2, I3, … IN) = (I0 I1 I2 I3 … IN)

NOR/NOR/Inverter = AND/OR with inverted inputs:

_

A	A	B

Pi

- ROM

N 							2N

Address							Word lines

Lines							(Internal)

Bit lines (M)

8X1 ROM

-Hard-wired AND array generates all minterms

4)	Decoder/Demux

n inputs, 1 of 2n outputs.

2n   outputs

How to make a Demux with a decoder:

Decoder creates minterms (Maxterms)

Remember:

5)	Multiplexers					How to make a multiplexer out of a decoder:

2n   inputs				    1 output

6)	Tri-state buffers

To select between multiple input lines to put on a single output line:

S3        S2      S1      S0	(Only one select line can be on at a time.)

OUT

Open collector

7)	ROM based logic

K x N ROM implements N different functions of log2K variables.

The table above is for a 8x4 ROM. The 3-bit address (A, B, and C) addresses a data record in the ROM. For an address of 000, you’ll get the outputs of  functions F1, F2, F3, and F4 for the input input 000.

64K Serial EEPROMs ( $3

# Text boxes

A  B  C     F1  F2  F3  F4

0   0   0      0    0    0    1

0   0   1      1    0    1    1

0   1   0      1    1    1    1

0   1   1      0    1    0    1

1   0   0      0    0    1    1

1   0   1      1    0    1    1

1   1   0      0    0    0    1

1   1   1      0    1    0    1

IN3

IN2

IN1

IN0

E

IN		       OUT

BUF-E tri-state truth table

T   OUT

0    Hi-Z (High impedence.

Open circuit.)

1    IN

T

IN		       OUT

I3  I2  I1  I0

S1  S0

## Decoder

BUFT tri-state truth table

T   OUT

0    IN

1    Hi-Z (High impedence.

Open circuit.)

S2S1 S0

=

0

1

2

3

4

5

6

7

A   B  C

## Decoder

F1

(Minterm)

F2

(Minterm)

F3

(Maxterm)

A  B  C      F1    F2    F3

0   0   0       1     0     1

0   0   1       0     1     1

0   1   0       0     1     1

0   1   1       0     1     0

1   0   0       1     0     1

1   0   1       0     0     1

1   1   0       0     0     0

1   1   1       1     0     1

IN

A   B

## Decoder

A0

A1

A2

A3

Decoder truth table

A  B  C     A0 A1 A2 A3 A4 A5 A6 A7

0   0   0      IN   0    0    0    0    0    0    0

0   0   1       0    IN  0    0    0    0    0    0

0   1   0       0     0   IN  0    0    0    0    0

0   1   1       0     0    0  IN   0    0    0    0

1   0   0       0     0    0    0  IN   0    0    0

1   0   1       0     0    0    0    0  IN   0    0

1   1   0       0     0    0    0    0    0  IN   0

1   1   1       0     0    0    0    0    0    0  IN

IN is the value of the input, “I”

IN

A B C

A   B  C

A   B  C

## Decoder

Decoder truth table

## Decoder

A0

A1

A2

…

A  B  C     A0 A1 A2 A3 A4 A5 A6 A7

0   0   0       1     0    0    0    0    0    0    0

0   0   1       0     1    0    0    0    0    0    0

0   1   0       0     0    1    0    0    0    0    0

0   1   1       0     0    0    1    0    0    0    0

1   0   0       0     0    0    0    1    0    0    0

1   0   1       0     0    0    0    0    1    0    0

1   1   0       0     0    0    0    0    0    1    0

1   1   1       0     0    0    0    0    0    0    1

VCC

VCC

VCC

VCC

VCC

VCC

VCC

VCC

VCC

GND

I0	I1	I2	I3	I4	I5	I6	I7	   …	   IN

VCC

I0	I1	I2	I3	I4	I5	I6	I7	   …	   IN

SA

___

WE

_

dj        			dj

bit lines

Word lines

(from decoder)

Address    1

__     0

CS    1

__     0

WE   1

0

Data 0   1

0

Data 1   1

0

Address    1

__     0

CS    1

__     0

WE   1

0

Data 0   1

0

Data 1   1

0

Address

Data

__	      __

CS	      WE

((

I/O

Actual

Storage

Decode