10/26 & 10/28

CS150

Section week 9

This week: RTN ( Register Transfer Notation ) Review & Microoperations, Computer Data Path ( HW9 ),

- RTN review, (-operations

a. In the notes for the 5th section ( 6th week ), we saw what register transfers and control signals were

necessary to calculate (X+Y)*Z when using the datapath below.

What are the register transfers and control signals to add A & B and put the sum into TMP?

RTN				(-operations			Control signals

b.     RTN describes transfers of data from one __________ component to _____________ component.

Each Register transfers takes __________ clock cycle(s).

For one register transfer there may be ______________ control signal(s) that may need to be set.

*For one control signal there may be ______________ (-operation(s) that may be done.

RTN				(-operations			Control signals

- Computer datapath ( Just another datapath like the one above... )

a. The three steps to carry out an instruction on a computer:

b. What are the differences between the model that the

book is basing its STD on and the handout given in lecture?

Four step handshake for book’s memory model:

Write			     Read

Cycle 1:			Request

Cycle 2:			Read/Write

Cycle 3:			Data

Cycle 4:			Wait

c. Instructions.

Format:

OP Codes:	Instruction		Action:

00		LOAD XXX	 	Memory[XXX] ( ACC

01		STORE XXX 	 	ACC ( Memory[XXX]

10		ADD XXX	 	ACC + Memory[XXX] ( ACC

11		BRN XXX	 	If ACC < 0     ACC ( PC

Address: Address in memory.

What does the instruction   0x000F do?

d. Instructions & Memory contents

So... Let’s do X*Y = PRODUCT.

Use the code:

Mult( X, Y ) {

int i = X, minus1 = -1, product = 0, count = Y;

for ( ; count ( 0 ; count-- ) product += i;

}

| _i | data X | i = X | 40 |  |
| --- | --- | --- | --- | --- |
| _count | data Y | count = Y | 41 |  |
| _minus1 | data 0xffff | minus1 = -1 | 42 |  |
| _product | data 0x0000 | product = 0 | 43 |  |
| _mult |  | ACC = count | 44 |  |
|  |  | ACC = ACC – 1 | 45 |  |
|  |  | count = ACC | 46 |  |
|  |  | if count < 0 goto “done” | 47 |  |
|  |  | ACC = X | 48 |  |
|  |  | ACC = ACC + product | 49 |  |
|  |  | product = ACC | 50 |  |
|  |  | ACC = -1 | 51 |  |
|  |  | if ACC < 0 then goto “mult” | 52 |  |
| _done |  | … | 53 |  |

# Text boxes

Label            Operation                Comment                                                                                Address       Memory value

Address

OP Code

15        14       13      12       11        10       9         8         7         6        5          4         3         2         1         0

*An aside ( (-instructions ) :

Say we change the datapath to the one on the right. Note that the TBUF on the

output of the TMP register has been changed to an EBUF and assume TAZ<TZA for both tri-state buffers. Can we reduce the number of control signals for the same calculation?