CS150

Section week 3

- Xilinx:  Lab manual ( How to use it to make your life easier )

a.  OK. Create a schematic consisting of a 16-bit binary counter with clock enable and synchronous reset. Go.

>> You could lay down 16 flip-flops and some gates and get some kind of counter  made and tested in a half an hour if you’re really quick… OR

>> You could click on “Add Component”, click on the ____________ library, and look for a suitable component ( In this case it’d be CB16RE ).

b. What kind of components are there?

>> __________, __________, ___________, ___________, __________, and others…

c. How do you find a component?

>> You can often figure out the name of the component if you know what you’re looking for. What would the name of a 16 bit, synchronous reset shift register with clock enable? ( P. 2-33: Shift registers ) ______________.

- Xilinx: The chip and board

- P. 2-3 : Board. Find I/O pins, clock, where additional

chips are placed, + & - terminals, dip switches…

- P. 4-10 : Chip...

- Xilinx: LUT ( Look Up Table )

- What is a look up table?

- Example of how one is used on the Xilinx chip.

How would the following function be implemented

In the Xilinx chip?

_ _ _     _                          _ _

Where:   F = ABC + ABD + ABC + ABD

ABCD 	      F

0000

0001

0010

0011

0100

0101

0110

0111

1000

1001

1010

1011

1100

1101

1110

1111

- Why do we use them?

4.	FSMs: Using a decoder for implementing logic… ( Kinda like a LUT… )

a. What’s a 3:8 decoder?

ABC	01234567

000	10000000

001  	01000000

010 	00100000

011 	00010000

100 	00001000

- 00000100

110 	00000010

111 	00000001

- Use an 3:8 decoder and a single gate ( you can use bubbles ) to implement the following circuit’s output and NSD. ( Note: This circuit uses a 4 state FSM. )

IN  PS0 PS1    OUT   NS1  NS0

0      0      0  	 0         1       0

0      0      1   	 1         1       1

0      1      0 	 1         1       0

0      1      1 	 0         0       0

1      0      0  	 0         1       0

1      0      1    	 0         1       0

1      1      0 	 0         0       1

1      1      1    	 1         1       0

- Serial to parallel converter ( Based on F97 HW #3, problem #3 )

Design a system which can convert 4 serial input bits ( SerialData ) to an 4 bit parallel output.

In the final circuit you should use a 4 bit shift register and a 2 bit counter from the Xilinx library and any other necessary logic. The serial data comes in MSB first.

Circuit timing is described in the timing diagram below.

Solution:							Step 2: Timing Diagram

Step 1: Identify Inputs and Outputs   			 		GIVEN:

GIVEN:

Step3: Decide whether to make it a Mealy or a Moore… Since your homework’s a Mealy, let’s make this a Moore.

Step 4: State Transiton Diagram

Two possibilities:

Possibility 1:

Possibilty 2:

We’re doing the same thing in 4 separate states ( 4 x Shift State ) in the above STD. Let’s, instead, make one state that does what the shift states above do and stay in it for 4 cycles. We’ll need a signal that’ll tell us when 4 clock cycles have gone by. To make this signal let’s make a separate FSM that counts to 4 and outputs a high signal when it’s counted to 4.

FSM1:

FSM2:

Step 5: State Transition Tables ( Working with “Possibility 2” ):

Let’s do FSM 2 first:

Skipping numerous steps, I see that it looks like a counter that counts to 4, and that there’s a component in the Xc4000e library that does exactly that: CB2RE. Attaching the Start signal to the RESET input of the counter sets the counter to zero when the START goes high. The TC output goes high when the counter has reached it’s maximum value, 3, which is when we want COUNT4 to go high… So, ignoring inputs and outputs that we don’t use the second FSM is just:

This is the complete implementation of FSM 2.

FSM 1: To design FSM 1 you need to go thru all the steps.

STT:

INPUTS		OUTPUTS

START	PS    COUNT4	         DONE    NS

0	0	X		1	0

1	0	X		1	1

X	1	0		0	1

X	1	1		0	0

Step 6:  Equations:

__

DONE = PS   __     ________

NS = START PS + COUNT4 PS

Step 7: Circuit:

# Text boxes

?          ?

?          ?

Xilinx

A

B

C

D

NS0

Done

SerialData

Start

Clk

NS1

OUT

0

1

2

3

4

5

6

7

CLK

SerialData

Start

Done

Counter

DataOut0           ?0          ?0          ?0        SD3       SD2      SD1       SD0      SD0

DataOut1           ?1          ?1          ?1         ?0         SD3      SD2       SD1       SD1

DataOut2           ?2          ?2          ?2         ?1          ?0        SD3       SD2       SD2

DataOut3           ?3          ?3          ?3         ?2          ?1         ?0          SD3       SD3

FSM1 State      Wait      Wait      Shift     Shift     Shift      Shift       Wait     Wait

FSM2 State         ?             ?        Run      Run       Run       Full         Run     Run

0

1

2

3

4

5

6

7

A

B

C

Bit3     Bit2     Bit1      Bit0       ?        ?        ?

F

0          1           2          3          0          1

IN

PS0

PS1

4

DataOut[3:0]

Xc4000e

Answers in RED

Flip Flops, Counters, Decoders, MUXs, Adders, Encoders, Shift Registers    RAM, ROM

SR16RE

1

1

0

0

0

1

0

1

1

0

1

0

0

0

1

1

This table is what is put into the LUTs ( look up tables ) on your Xilinx chip. Not the gates that you draw with ViewDraw.  The above function would be put into a table like the one on the left and the table would be put into the Xilinx chip LUTs.

>> Any 4 input, 3 input, 2 input or 1 input ( 1 output ) function can be implemented in a 4 input LUT.

>> Delay thru the LUT will be the same for any function.

Something to think about… Which of these ( OUT, NS1, NS0 ) is following the sum of products pattern? Which is following the product of sums pattern?

Wait

0

DONEE

Shift

1

DONE

Shift

2

DONE

Shift

3

DONE

Shift

4

DONE

______

START

START

Wait

0

DONE

Shift

1

DONE

Count

0

COUNT4

Count

1

COUNT4

Count

2

COUNT4

Count

3

COUNT4

______

START

The rest of the problem uses this design.

CB2RE

TC

CLK

RESET

START

START

DONE

NS			STATE			         OD

START

RESET

CLK

TC

CB2RE

Entire Circuit

FSM 1

FSM 2

NS = 	 __

START PS +

________

COUNT4 PS

__

DONE = PS

COUNT4

COUNT4

FDR

NS			PS

GND      R

SR4RE

SerialIn

DataOut[3:0]

CLK

CLK

ENABLE

PS

GND	   R

VCC          ENABLE