9/21 & 9/23

CS150

Section week 4

- T Flip Flops

1a) T Flip Flop truth table

T    Q

0     Q

1     Q

1b) What’s this circuit called?

Down counter

1c) What might be a problem

with this circuit?

The output of the first flip flop is the

clock to the second. There’s some

propogation delay through the first FF

so the output of the first FF (clock to the

second FF) will show up slightly behind the

clock to the first FF. In other words, there

will be clock skew on the clock to

to the second FF. There will be even more

skew on the clock to the third FF .

What’s Q?		What’s J & K?

2.	JK Flip Flop

J   K    Q

0   0     Q        Hold

0   1     0         “K”ill

1   0     1         “J”am

1   1     Q        Toggle

- Timing ( Statistics for Xilinx chip: 4-97 )

3a) Setup & hold time ( no clock skew ).

For both D flip flops:

5ns < Tcko < 10ns

What’s the maximum setup time possible?

What’s the equation to find the maximum possible setup time?

What’s the maximum hold time possible?

What’s the equation to find the maximum possible hold time?

Does finding the minimum setup and hold times have meaning?

3b) Setup and Hold times ( no clock skew – same circuit )

For both flip flops:

Tsetup = 15ns

Thold = 20ns

What’s the possible range for Tcko?

What’s the equation to find the minimum Tcko?

What’s the equation to find the maximum Tcko?

3c) Setup and Hold times when there is clock skew

For both flip flops:

Tsetup = 15ns

Thold = 20ns

Delay = 10ns

What’s the minimum Tcko possible?

What’s the equation to find the minimum Tcko?

What’s the maximum Tcko?

What’s the equation for the maximum Tcko?

3d)  Setup and Hold times when there is feedback

For both flip flops:

Tsetup = 5ns	       5ns < Tcko < 15ns  	  What’s the fastest clock where

Thold = 10ns	       8ns < Tp < 12ns   	  this circuit will still work?

# Text boxes

Delay

D1          Q1

C

1

T Flip Flop

T

Q

C

D0         Q0

C

CLK

0ns			   25ns			    50ns			     75ns		       	     100ns

CLK

D0

CLK2

Q0/D1

D1          Q1

C

D0         Q0

C

CLK

0ns		tsetup	   25ns	  thold		    50ns		    tsetup	     75ns	       thold	       	     100ns

CLK

D0

Q0/D1

0ns			   25ns			    50ns			     75ns		       	     100ns

1

1

CLK

T Flip Flop

T

Q

C

T Flip Flop

T

Q

C

Q0                                   Q1                             Q2

CLK

J

K

Q

CLK

D0

Q0

Q1

CLK

Q0

Q1

Q2

Q

0       7	      6        5         4        3         2         1         0        7

D             Q

C

CLK

Answers in RED

D1          Q1

C

CLK

D

Q

D0         Q0

C

Don’t

Care

Don’t     Don’t

Care       Care

CLK

Don’t

Care

40ns

Tsumax = Period – Tckomax

5ns

Tholdmax = Tckomin

I meant to remove this question... I guess the answer is no...

Can change any

where in this range

D0 can’t change in the                  area...   20ns < Tcko < 60ns

Tckomin = Thold

Tckomax = Period - Tsetup

Q0/D1 can’t change in the                area.  > 30ns

Tckomin > Thold + Delay

Tckomax  < 45ns

Tckomax < Period – Tsetup + Delay

Tsetup		Thold

Tsetup		Thold

Tckomin

Tckomax

Tpmin

Tpmax

When looking for the fastest clock, you look for the shortest period. If you shorten the period too much you could create a setup time violation ( why? ). To find the minimum clock/period first find the minimum period that won’t violate the setup time...

Period = Tckomax + Tpmax + Tsetup = 15ns + 12ns + 5ns = 32ns    Clock = 1/Period