11/2 & 11/4

Section week 10

This week: Synchronous design rules ( HW10 ), Microprogramming ( HW10 )

- Synchronous design rules

What are they ( Right off of the handout ):

1.	Use only one clock ( Tcko & skew )

2.	Synchronize inputs ( May bounce up to 100 ms. Use FFs. )

3.	Never gate clock ( Glitches & delays )

4.	Avoid clock skew ( BUFGS )

- Avoid asynchronous control signals ( Asynchronous RESET, etc. )

6.	Don’t use coupled Mealeys ( Don’t build own latches )

7.	Avoid set-up violations. ( Slow clock, reduce logic… )

2.	Microcode for CPU control.

Using the micro-programmed control unit on the next page as a starting point, design a MCU for controlling the above datapath for the following instructions ( You don’t need to program the control unit ):

LOAD X ( TMP	LOAD Y ( TMP

MOVE TMP ( A	MOVE TMP ( B

A + B ( TMP

Things we need to find: Jump conditions, output, ROM width, ROM depth, CTR bits, MUX select lines.

##### To find: Output

**Goal: To make the microcode instruction as narrow as possible.

To do this:

First, group datapath control signals. ( Look for groups of signals that can only have member asserted at a time. )

Sources ( Values put ON bus ): ( TX, TY, T+, TTMP (

Destinations ( Where values from bus are put ): ( ENA, ENB, ENTMP (

So, since only one of each group will be asserted at a time, let’s use decoders ( The same idea as the MCU that prof. Fearing designed in lecture for the computer datapath. ):

To find DO instruction format/width:

This tells you how many bits you’ll need for a DO instruction. You’ll need 4 for the decoders and one for the enable line ( total: 5 bits ):

| Enable | Soucre bit 1 | Source bit 0 | Destination bit 1 | Destination bit 0 |
| --- | --- | --- | --- | --- |

But until we find the format for the JUMP instruction we won’t know if this is a sufficient width for the ROM or not ( the maximum possible width of an instruction is the minimum width of the ROM ).

To find JUMP instruction format/width:

We need to find the number of selector bits needed and the bits in the counter.

To find the number of condition selector lines:

We need to find what jumps we may need to do. So, let’s

Do two things: Give the instructions for the datapath opcodes and then

Plan our jumps using a branch diagram like the one on the next problem.

Assume there’s an IR someplace with the datapath instruction in it.

Datapath Instruction  	OpCodes ( In IR<15:13> )

LOAD X ( TMP	000

LOAD Y ( TMP	001

MOVE TMP ( A	010

MOVE TMP ( B	011

A + B ( TMP		100

So, it looks like we want to be able to branch on:

IR<15>, IR<14>, IR<13>, and always. That means there

Are 4 inputs to the MUX and 2 selector lines are necessary.

To find the number of bits for the counter:

The number of bits in the counter is the same as the number of address lines to the ROM. The next information gives you the depth of the ROM:

Next, figure out how wide each microcode instruction needs to be ( In other words, how wide the ROM needs to be. ) assuming a maximum of 64 total (-instructions. Also, assume there’s an IR someplace and instructions fetched by datapath are 16 bits.

If there are a maximum of 64 (-instructions then the depth of the ROM will be 64 ( = 26 ) and have 6 address lines.

To find JUMP instruction format/width revisited:

Now you have enough information to figure out how many bits you’ll need for a JUMP instruction. You’ll need 2 bits for the MUX selector, 6 bits for the counter and one for the enable line ( total: 9 bits ):

| Enable | MUX selector bit 1 | MUX selector bit 2 | Addr 5 | Addr 4 | Addr 3 | Addr 2 | Addr 1 | Addr 0 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

This ( 9 bits ) is wider than the DO instruction ( 5 bits ) so this becomes the minimum width of the ROM. 9 bits isn’t a real popular width for ROMs so in this case let’s say we combine a 64x1 ROM and a 64x8 ROM to give us our 9 bits… ( Don’t worry about this. It’s OK to assume it behaves in a way that is indiscernable (sp?) from a 64x9 ROM. hmmmm. “MS Word” doesn’t like that spelling... Anyway, it’s not discernable from a 64x9 ROM ). So, now our final (-controller unit!

PS. The DO instruction format:

| Enable | spare | Spare | spare | spare | Source bit 1 | Source bit 0 | Destination bit 1 | Destination bit 0 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

- Microprogramming

Microprogram the control unit below to implement a rising edge detector. Emulate a Moore type FSM. The clock to the control unit is twice the clock of IN ( IN clock and the controller clock are synchronized. )

Some questions before we start:

Where is the (-program located? In the ROM

Can this be reused for different (-programs? It’s in a ROM. It can’t be re-written. In other words, the micro-controller will run a fixed program and can’t be re-programmed ( easily anyways… ).

What are the instructions for this microcode control unit?

Instruction			Bit:   7   6   5   4   3   2   1   0

DO  OUTPUT  OUT		         0  X  X  X  X  X  X  OUT

LOAD(IN) Address		         1   0  X  X  X    Address

LOAD(IN) Address		         1   1  X  X  X    Address

Remember the decode stage in the STD for the computer datapath we did in class. It branches 5 ways. How many directions can this controller branch on one instruction?   Only 2

What would it need to do if it had to go to multiple destinations on one instruction?

Can’t. You have to use multiple (-instructions to take care of multiple branches.

Write the microcode:

STD

| Address | Mnemonic form | O7 | O6 | O[5:0] |
| --- | --- | --- | --- | --- |
| 0 | DO OUTPUT 0 | 0 | X | XXXXX0 |
| 1 | JMP(IN) 0 | 1 | 1 | XXX000 |
| 2 | DO OUTPUT 1 | 0 | X | XXXXX1 |
| 3 | JMP(IN) 0 | 1 | 1 | XXX000 |
| 4 | DO OUTPUT 0 | 0 | X | XXXXX0 |
| 5 | JMP(IN) 0 | 1 | 1 | XXX000 |
| 6 | DO OUTPUT 0 | 0 | X | XXXXX0 |
| 7 | JMP(IN) 6 | 1 | 0 | XXX110 |

Possible problems with this program:

OUT will be asserted after one

(-controller clock cycle. Maybe not

a problem but something to notice.

The problems that I presented it with

in section are all solved by adding a

forth state. I don’t see any problems

with the 4 state based program.

# Text boxes

1

0

11

“1”

[0]

00

“0”

[0]

Micro

Program

counter

CLK

Width of buses & depth & width of ROM.

LOAD

D2_4

Jump conditions.

Condition

selector.

CLK

Condition

selector.

Jump conditions.

RESET

?x? ROM

LOAD

Output

Width of buses & depth & width of ROM.

EN

RESET

State 11     State 00

State 00      State 11

State 01

State 00

State 00

State 01

State 10

State 11

Branch diagram:

Left child is branch. Right child is natural path when counter counts up without branch.

State 00      State 10

State 00

0

CLK

CLK

Output Register

CE

O0                  D0     Q0               OUT

RESET

8x8 ROM

A2      O7

A1

O[6:0]

A0

LOAD

O2            D2      Q2

O1            D1      Q1

O0            D0      Q0

O6

1

0

BRNtaken   BRNnot taken

IN

__

IN

EN

STORE

LOAD

0

1

1

ADD

Solutions are in red.

01

“01”

[1]

10

“11”

[0]

?x? ROM

RESET

0

1

EN

TX

TY

T+

TTMP

ENA

ENB

ENTMP

NOOP

D2_4

EN

EN

2

2

0       1

0       1

0       1

1       0

1       0

IF

1          0	              1            0

1       0

Move TMP          Move TMP

( B                    ( A

JMP(Always)IF   JMP(Always)IF

Load Y    Load X

( TMP     ( TMP

JMP(Always)IF   JMP(Always)IF

JMP(IR<14>)

JMP(IR<15>)

JMP(IR<13>) JMP(IR<13>)

A+B(TMP

JMP(Always)IF

IF

IF

IF

IF

EN

IR<15>

IR<14>

IR<13>

“1”

2

2

EN

EN

ENA

ENB

ENTMP

NOOP

D2_4

TX

TY

T+

TTMP

D2_4

2

IR<15>

IR<14>

IR<13>

“1”

Width of buses & depth & width of ROM.

LOAD

CLK

RESET

64x? ROM

6

EN

6

6

6

2

IR<15>

IR<14>

IR<13>

“1”

EN

2

2

EN

EN

ENA

ENB

ENTMP

NOOP

D2_4

TX

TY

T+

TTMP

D2_4

8

LOAD

CLK

RESET

64x9 ROM

O8

O[7:0]

2

O[5:0]

O[7:6]

O[3:2]

O[1:0]