New instruction:

What are the register transfers, (-operations, and signals for a new instruction:

ADDMEM XXX	RAM[XXX] + ACC ( RAM[XXX]

Use the datapath handed out in class.

There were already 4 instructions defined for the datapath handed out in class so adding this instruction would mean there would be a total of 5 instructions in the instruction set. In the instruction format we only have 2 bits in the opcode. This means that we’d need another bit in the opcode if we were to still implement the other 4 instructions in order to have a unique opcode for each instruction. I’m not going to worry about that here. Let’s just assume it’s replacing ADD. Assume instruction ahs already been fetched.

RTN				(-operations			signals

IR<13:0> ( MAR		IR ( ABUS			IROUT

ABUS( MAR			MARLOAD

RAM[MAR] ( MBRIN	RAM[MAR] ( DataBus	CS.L

DataBus ( MBRIN		MBRINLOAD

MBRIN + ACC ( MBROUT	MBUS ( RBUS		Y=A+B ( ALU Op

RBUS ( MBROUT		MBROUTLOAD

WE.L

MBROUT ( RAM[MAR]	MBROUT ( DataBus		MBROUT

DataBus ( RAM[MAR]	WE.L, CS.L

(finish write cycle. Avoid bus conflicts				WE.L

and weird writes by turning off CS.L first

Another way:

RTN				(-operations			signals

IR<13:0> ( MAR		IR ( ABUS			IROUT

ABUS( MAR			MARLOAD

RAM[MAR] ( MBRIN	RAM[MAR] ( DataBus	CS.L

DataBus ( MBRIN		MBRINLOAD

MBRIN + ACC ( MBROUT	MBUS ( RBUS		Y=A+B ( ALU Op

RBUS ( MBROUT		MBROUTLOAD

WE.L, CS.L( ( OK since address

is already ready.)

MBROUT ( RAM[MAR]	MBROUT ( DataBus		MBROUT

DataBus ( RAM[MAR]	WE.L

PS.  CS.L( means falling edge transition.