MT1 practice questions. These questions aren’t to test your reasoning capabilities, just your knowledge of the basics.

- 3 Bit Up Counter ( Moore FSM Design, Setup/Hold Time, Logic Simplification )

1a)  Build a 3 bit up counter Moore machine using only AND, OR, NOT, and XOR gates. Simplify all logic. ( Use the fewest number of gates possible. )

1b)  Will the circuit have any problems if:

2ns < TpINV < 4ns

3ns < TpAND < 6ns

3ns < TpOR < 5ns

3ns < TpXOR < 4ns

3ns < Tcko < 8ns

Tsetup = 4ns

Thold = 6ns

CLK = 40 MHz

- Timing problem… (All questions use homework 5, problem 2)

2a) (HW5, 2b) Without doing any math, do you think increasing TDELAY will increase (T1-T0)MAX or decrease it.

2b) (HW5, 2c) Without doing any math, do you think increasing TDELAY will increase (T1-T0)MIN or decrease it.

2c) What is the formula for finding a setup time violation on HW #5’s 2b? Use ‘T’ for the period.

2d) What is the formula for finding a setup time violation on HW #5’s 2c? Use ‘T’ for the period.

- BUFEs and timing

(Note: EXAZ means the time it takes the

output of EX to go from active to tristated.

The turn-off time.)

The controller sends the following signals to the above datapath:

Are there any problems when:

3a) EXAZ = 10ns, EYZA = 5ns, Tsetup = 10ns, Thold = 4ns, Period = 30ns?

3b) EXAZ = 9ns, EYZA = 10ns, Tsetup = 10ns, Thold = 10ns, Period = 30ns?

3c) EXAZ = 10ns, EYZA = 12ns, Tsetup = 10ns, Thold = 4ns, Period = 20ns?

3d) EXAZ = 14ns, EYZA = 6ns, Tsetup = 12ns, Thold = 8ns, Period = 25ns?

- Clock divider (FSM Design, Counters, Clocks and Glitches )

Design a clock divider which runs on a 200MHz clock and produces a 1MHz clock. Make the duty cycle of the 1MHz clock 50%. Should you design this to be a Moore or a Mealy machine?

- FSM Analysis

What does this circuit do? ( Is it a Mealy or Moore? Where are the NSD, OD & State FFs. )

- STD & STT

Draw a Moore STD for a circuit that does the same thing as the circuit in problem 5 and then make it’s STT.

- Gate Delay Timing Diagram ( Cross Coupled Gates, Gate Delays )

It’s too much to try create a problem like the one on last year’s MT. Try to do last year’s ( and if you can get it, the year before’s timing problem might be good practice ).

- Toggle Flip Flops ( FSM Design )

Design a 2 Bit Down Counter that is implemented with T FFs.

- JK Flip Flops ( FSM Design )

Design a 2 Bit Up Counter that is implemented with JK FFs.

- Use 3 BUFTs and 3 BUFEs to build a 4-1 MUX.

Also review asserted high, asserted low, & equation simplfication.

Solutions:

- a) STT:

Equations:

NS0 = PS0

NS1 = PS1      PS0

NS2 = PS2 PS0 + PS2 PS1 + PS2 PS1 PS0

b) Any problems?

Check for hold time violations ( Can value from flip-flop output propagate back to the flip-flop inputs so quickly that the hold time is violated? ):

>  Find the shortest propagation path: Looks like NS0 ( XOR gates have bigger delay

than inverters ).

Tckpmin + Tinvmin > Thold

3ns        + 2ns        > 6ns		This isn’t true ( hold time violation possible.

Check for setup time violations ( Can value from flip-flop output propagate back to the flip-flop inputs so slowly that the next clock’s setup time is violated? )

>  Find the longest propagation path: Looks like NS2.

Tckomax + Tinvmax + Tandmax + Tormax + Tsetup < Period ( 1/40MHz = 25ns )

8ns         +  4ns       + 6ns         +  5ns     + 4ns      < 25ns     False ( setup time

violation possible.

2.     2a) By increasing the delay, you’re delaying the change in D1’s value. Which means that you can increase T1-T0.

2b) The delay won’t affect the minimum T1-T0.

2c) Tckomax + INVTpmax + Tsumax < T – (T1-T0).

2d) Tckomax + Tdelaymax + Tsumax < T – (T1-T0).

- 3a) Bus conflict (X & Y both on bus at same time).

3b) Hold time violation. Turn-off time (EXAZ) is less than Thold of flip-flop.

3c) Setup time violation. EYZA + Tsetup > Period.

3d) Setup time violation, hold time violation & bus conflict.

- This should be a Moore machine with two states and no logic on the output – the output should come directly from the state bits. Because... any combinational logic, no matter how simple may cause glitches. It should change states when a counter counts up to 100. Since the output of this circuit is a clock, we have to make especially sure that there aren’t glitches on the output. Moore is safer than a Mealy in this case. Why?

- It’s a Mealy pattern detector ( 1011 ).

Equations:

NS1 = R ( PS0 Z + PS1 PS0 Z )

NS0 = Z R

OUT = Z PS1 PS0

STT:

STD:

- The Moore STD has 5 states. 1 is output in the 5th state.

On the STT, make sure that the output is the same for the same PS even though the input changes.

- ------

- STT:						Equations found for T1 and T0:

9.	STT:						Equations:

J1 = PS0

K1 = PS0

J0 = PS0

K0 = PS0

X means “don’t care”.

10.

(

# Text boxes

S1

OUT

S1

S0

S0

S0

S0

A

B

C

D

T

E

T

E

T

A

B

OUT

C

D

S1      S0

00

01

10

11

A

B

OUT

C

D

S1      S0

00

01

10

11

E

CLK 1

0

Ex     1

0

Ey     1

0

LOADA  1

0

LOADA

EA

register

Y

X

EY

EX

Bookkeeping

PS1	PS0	J1K1	J0K0	NS1	NS0

0	0	0X	1X	0	1

0	1	1X	X1	1	0

1	0	X0	1X	1	1

1	1	X1	X1	0	0

OUT1

OUT0

1

T1        Q1

T0       Q0

Bookkeeping

PS1	PS0	T1	T0	NS1	NS0

0	0	1	1	1	1

0	1	0	1	0	0

1	0	1	1	0	1

1	1	0	1	1	0

00	           01	       10	                 11

0/0		1/0			     0/0

0/0		1/1

RESET	          1/0	        0/0	                 1/0

RESET	PS1	PS0	Z	NS1	NS0	OUT

0	0	0	0	0	0	0

0	0	0	1	0	1	0

0	0	1	0	1	0	0

0	0	1	1	0	1	0

0	1	0	0	0	0	0

0	1	0	1	1	1	0

0	1	1	0	1	0	0

0	1	1	1	0	1	1

1	0	0	0	0	0	0

1	0	0	1	0	0	0

1	0	1	0	0	0	0

1	0	1	1	0	0	0

1	1	0	0	0	0	0

1	1	0	1	0	0	0

1	1	1	0	0	0	0

1	1	1	1	0	0	1

S0

S1

?

?

?

?

PS2 	PS1 	PS0  	NS2 	NS1 	NS0

0	0	0	0	0	1

0	0	1	0	1	0

0	1	0	0	1	1

0	1	1	1	0	0

1	0	0	1	0	1

1	0	1	1	1	0

1	1	0	1	1	1

1	1	1	0	0	0

Z

RESET

OUT