9/27 & 9/29

CS150

Section week 5

Glitches, tri-state buffers, data path, generating control signals, RTN, tri-state timing analysis.

- Timing skew & glitches

During the _Routing_ phase of compilation the paths/wires which connect the CLBs are selected.

The length of the path chosen by the compiler can cause __Delays__ in signals.

The signal that we have to be most careful about is usually the ___Clock____.

To reduce any delay or _skew_ on that signal we normally pass it through a _BUFG or BUFGS_ component.

Say you have a 2-bit counter that you’ve built:

And say it’s part of a pretty big circuit.

And let’s say that when the compiler routes this

thing, it puts one of the flip-flops in the upper right

corner CLB and one in the lower left hand corner

because there’s no space left to put them nearby. And

let’s say that you forgot to put the clock signal through

a BUFGS.

What could happen?

First, figure out what it should do:

Does glitching occur due to the clock skew? If so, which transition(s) would be affected?

What if the S1 flip-flop rather than the S0 flip-flop received the delayed clock signal? Would this fix the problem? If so, why? If not, which transition(s) would be affected?

- Tri-state buffers

A tri-state buffer has 3 states: 0, 1, Hi-z ( high impedance ).

There are two kinds of tri-state buffers: Enabled high (BUFE) and enabled low (BUFT).

BUFE								BUFT

E	IN	OUT					T	IN	OUT

0	0						0	0

0	1						0	1

1	0						1	0

1	1						1	1

3.	Data path, generating control signals, RTN, tri-state timing analysis

Components:

Tri-state buffers, D Flip-flops, ALU ( Arithmetic Logic Unit ), Bus, Registers

Control signals

Values from memory

Problem:   TMP = ( X + Y ) * Z      (For this problem assume tristates turn off quicker than they turn on.)

In		RTN ( Register				Control Signals

Words	          Transfer Notation )        TX     TY      TZ     T+      T*    TTMP  ENA  ENB  ENC  END   ENTMP

Load X		A ( X		           0       1        1        1       1        1        1       0       0        0          0

Into A

Load Y 	B ( Y		           1       0        1        1       1        1        0       1       0        0          0

Into B

Load A+B	C ( A+B	           1       1        1        0       1        1        0       0       1        0          0

Into C

Load Z		D ( Z		           1       1        0        1       1        1        0       0       0        1          0

Into D

Load C*D	TMP ( C*D	           1       1        1        1       0        1        0       0       0        0          1

Into TMP

TAZ & TZA

TAZ is the time it takes for the output of a BUFT to go to Hi-z after select line goes high. ( Or the time it takes the output of a BUFE to go to Hi-z after the select line has gone low. )

TZA ...

Write timing diagram for putting X into A and Y into B if TAZ and TZA are 0. Assume the control signals change on the same clock as the datapath and Thold = 0.

What would happen if you used this timing when TAZ is not zero?

There would be two BUFTs putting a value on the bus at the same time for the time TAZ – TZA at the transition at the second rising edge...

Draw the timing if you didn’t know which was larger, TAZ or TZA, and wanted to be safe.

# Text boxes

IN

IN

OUT

OUT

T

E

You’d still have glitches. And they’ll occur at the same places: When more than one state/output bit changes on a state/output transition.

Yes. Glitches occur when more than one state/output bit changes on a state/output transition.

00                  01	                   11     10                                11                     01      00                               01

Glitch					Glitch

The clocks might not arrive at both FFs at the same time. There might be some clock skew.

Answers in RED

CLK1

TX

TY

ENA

ENB

CLK1

TX

TY

ENA

ENB

8

CLK

ENTMP

TTMP

T*

CLK

CLK

ENC

END

*

D

C

T+

CLK

TX      TY     TZ

### X    Y      Z

ENB

+

TMP

Hi-Z

Hi-Z

0

1

CLK

ENA

B

A

CLK1

S1

CLK2

S0

STATE

“11”

“10”

“01”

“00”

S0

S1

D           Q

R

FDR

RESET

CLK2

D           Q

R

FDR

RESET

CLK1

0

1

Hi-Z

Hi-Z

If you know that TAZ is always less than TZA then the timing in the upper diagram would work.