# University of California at Berkeley

## College of Engineering

Department of Electrical Engineering and Computer Sciences

### EECS150								J. Wawrzynek

# Spring 2000								E. Caspi

#### Quiz #10 – Solution

The carry-select scheme splits the 16-bit adder into four 4-bit quarters.  Each quarter except the least-significant one is duplicated, computed once with a carry-in of 0 and once with a carry-in of 1.  The critical path is 10 cycles:  4 cycles to the carry-out of the least-significant quarter, plus 2 cycles for each of 3 cascaded multiplexor pairs on the way to S[15:12] and Cout.

Carry-Lookahead Adder	Multiplexer	Build this:
S:	3 gate delays	2 gate delays	S:	_10__  gate delays
C4:	4 gate delays		Cout:	_10__  gate delays

# Text boxes

S[11:8]

S1[11:8]

S1[15:12]

S[3:0]

S0[15:12]

S0[11:8]

S[7:4]

1

1    0

B[15:12]

A[15:12]

S[15:12]

4-bit CLA

1    0

1

1    0

B[11:8]

A[11:8]

4-bit CLA

1

0

S0[7:4]

B[7:4]

A[7:4]

4-bit CLA

0

Cin

S[3:0]

B[3:0]

A[3:0]

4-bit CLA

0

S1[7:4]

B[7:4]

A[7:4]

4-bit CLA

1    0

B[11:8]

A[11:8]

4-bit CLA

Cout

1    0

B[15:12]

A[15:12]

4-bit CLA

1    0