# University of California at Berkeley

## College of Engineering

Department of Electrical Engineering and Computer Sciences

### EECS150								J. Wawrzynek

# Spring 2000								E.Caspi

#### Quiz #12  – Solution

The counter FSM will represent the gray-code directly in 3 state bits.  The next-state function will be the “next gray-code” function, and the counter output will be the state registers.

| State | Next State |
| --- | --- |
| S2 | S1 | S0 | NS2 | NS1 | NS0 |
| 0 | 0 | 0 | 0 | 0 | 1 |
| 0 | 0 | 1 | 0 | 1 | 1 |
| 0 | 1 | 0 | 1 | 1 | 0 |
| 0 | 1 | 1 | 0 | 1 | 0 |
| 1 | 0 | 0 | 0 | 0 | 0 |
| 1 | 0 | 1 | 1 | 0 | 0 |
| 1 | 1 | 0 | 1 | 1 | 1 |
| 1 | 1 | 1 | 1 | 0 | 1 |

State Transition Diagram	State Transition Table

| S1 S0 S2 | 00 | 01 | 11 | 10 |  |  |
| --- | --- | --- | --- | --- | --- | --- |
| 0 | 1 | 1 | 0 | 0 |  | NS0 = S’2S’1+S2S1 = (S2(S1)’ |
| 1 | 0 | 0 | 1 | 1 |  |  |
| S1 S0 S2 | 00 | 01 | 11 | 10 |  |  |
| 0 | 0 | 1 | 1 | 1 |  | NS1 = S’2S0+S1S’0 |
| 1 | 0 | 0 | 0 | 1 |  |  |
| S1 S0 S2 | 00 | 01 | 11 | 10 |  |  |
| 0 | 0 | 0 | 0 | 1 |  | NS2 = S2S0+S1S’0 |
| 1 | 0 | 1 | 1 | 1 |  |  |

Karnaugh Maps for Next State	Reduced Logic Eqns

# Text boxes

011

110

000

101

001

100

111

010