# UC Berkeley

## College of Engineering

EECS Department

### EECS150								J. Wawrzynek

# Spring 2002

#### Quiz #9

##### Name: ________________________Solution________________________

SID: ____________________________________Lab section number: _____________

For the Hamming code with four data bits, D3, D5, D6, and D7, along with three parity bits, P1, P2, and P4:

- Form the code word for the data word 1011:

The code word is P1 P2 D3P4D5D6D7

|  | P4 P2 P1 |
| --- | --- |
| 1 | 0 0 1 |
| 2 | 0 1 0 |
| 3 | 0 1 1 |
| 4 | 1 0 0 |
| 5 | 1 0 1 |
| 6 | 1 1 0 |
| 7 | 1 1 1 |

P1 P2 D3P4D5D6D7 =

- Assume an error in bit D6 during reading from the memory.  Evaluate the three check bits C1, C2, C3.  Show your computation:

An error in bit D6 ( P1 P2 D3P4D5D6D7 = 0110001

C1 = P1 ( D3 ( D5 ( D7 = 0 ( 1 ( 0 ( 1 = 0

C2 = P2 ( D3 ( D6 ( D7 = 1 ( 1 ( 0 ( 1 = 1

C3 = P4 ( D5 ( D6 ( D7 = 0 ( 0 ( 0 ( 1 = 1

# Text boxes

C3C2C1 = 110 ( error in bit D6 √

0110011

P1 = {3, 5, 7} = D3 ( D5 ( D7 = 1 ( 0 ( 1 = 0

P2 = {3, 6, 7} = D3 ( D6 ( D7 = 1 ( 1 ( 1 = 1

P4 = {5, 6, 7} = D5 ( D6 ( D7 = 0 ( 1 ( 1 = 0