University of California at Berkeley

College of Engineering

Department of Electrical Engineering and Computer Science

SOLUTIONS

EECS 150									R. H. Katz

Spring 2007

Problem Set #1: Combinational Logic forms

Assigned 16 January 2007, Due 26 January at 2 PM

- Use Boolean algebra to simplify into two-level sum of products form the following Boolean expressions. Show your intermediate steps of applying Boolean algebra axioms and theorems!

  - F(A,B,C) = A’ B’ C’ + A B C’ + A B’ C’

= A’B’C’ + AB’C’ + AB’C’ + ABC’

= B’C’(A’ + A) + AC’(B’ + B)

= B’C’ + AC’

  - F(A, B, C, D) = A’ B’ C’ D’ + A’ B’ C’ D + A’ B’ C D + A’ B C D + 
A B’ C’ D’ + A B’ C’ D + A B C’ D + A B C D

= A’B’C’(D’ + D) + A’CD (B’ + B) + AB’C’(D’ + D) + ABD (C’ + C)

= A’B’C’ + A’CD + AB’C’ + ABD

= B’C’(A’ + A) + A’CD + ABD

= B’C’ + A’CD + ABD

- Given the following minimized two-level sum of products expressions, describe the functions in “little m” notation:

  - F(A,B,C) = A’ B’ + A B

| A | B | C | Minterms | F(A,B,C) |  |
| --- | --- | --- | --- | --- | --- |
| 0 | 0 | 0 | A’B’C’ | 1 | m0 |
| 0 | 0 | 1 | A’B’C | 1 | m1 |
| 0 | 1 | 0 | A’BC’ | 0 | m2 |
| 0 | 1 | 1 | A’BC | 0 | m3 |
| 1 | 0 | 0 | AB’C’ | 0 | m4 |
| 1 | 0 | 1 | AB’C | 0 | m5 |
| 1 | 1 | 0 | ABC’ | 1 | m6 |
| 1 | 1 | 1 | ABC | 1 | m7 |

= (m(0,1,6,7)

  - F(A,B,C,D) = C + A B  + A’ B C

| A | B | C | D | Minterms | F(A,B,C,D) |  |
| --- | --- | --- | --- | --- | --- | --- |
| 0 | 0 | 0 | 0 | A’B’C’D’ | 0 | m0 |
| 0 | 0 | 0 | 1 | A’B’C’D | 0 | m1 |
| 0 | 0 | 1 | 0 | A’B’C D’ | 1 | m2 |
| 0 | 0 | 1 | 1 | A’B’C D | 1 | m3 |
| 0 | 1 | 0 | 0 | A’B C’D’ | 0 | m4 |
| 0 | 1 | 0 | 1 | A’B C’D | 0 | m5 |
| 0 | 1 | 1 | 0 | A’B C D’ | 1 | m6 |
| 0 | 1 | 1 | 1 | A’B C D | 1 | m7 |
| 1 | 0 | 0 | 0 | A B’C’D’ | 0 | m8 |
| 1 | 0 | 0 | 1 | A B’C’D | 0 | m9 |
| 1 | 0 | 1 | 0 | A B’C D’ | 1 | m10 |
| 1 | 0 | 1 | 1 | A B’C D | 1 | m11 |
| 1 | 1 | 0 | 0 | A B C’D’ | 1 | m12 |
| 1 | 1 | 0 | 1 | A B C’D | 1 | m13 |
| 1 | 1 | 1 | 0 | A B C D’ | 1 | m14 |
| 1 | 1 | 1 | 1 | A B C D | 1 | m15 |

= (m(2,3,6,7,10,11,12,13,14,15)

- Given the following minimized two-level product of sums expressions, describe the functions in “big M” notation:

  - F(A, B, C) = (A’ + C) (B + C’)

| A | B | C | Maxterms | F(A,B,C) |  |
| --- | --- | --- | --- | --- | --- |
| 0 | 0 | 0 | A+B+C | 1 | M0 |
| 0 | 0 | 1 | A+B+C’ | 0 | M1 |
| 0 | 1 | 0 | A+B’+C | 1 | M2 |
| 0 | 1 | 1 | A+B+C’ | 1 | M3 |
| 1 | 0 | 0 | A’+B+C | 0 | M4 |
| 1 | 0 | 1 | A’+B+C’ | 0 | M5 |
| 1 | 1 | 0 | A’+B’+C | 0 | M6 |
| 1 | 1 | 1 | A’+B’+C’ | 1 | M7 |

=( M(1,4,5,6)

  - F(A, B, C, D) = (A’ + B’) (A’ + C’) (B + D’)

| A | B | C | D | Maxterms | F(A,B,C,D) |  |
| --- | --- | --- | --- | --- | --- | --- |
| 0 | 0 | 0 | 0 | A+B+C+D | 1 | M0 |
| 0 | 0 | 0 | 1 | A+B+C+D’ | 0 | M1 |
| 0 | 0 | 1 | 0 | A+B+C’+D | 1 | M2 |
| 0 | 0 | 1 | 1 | A+B+C’+D’ | 0 | M3 |
| 0 | 1 | 0 | 0 | A+B’+C+D | 1 | M4 |
| 0 | 1 | 0 | 1 | A+B’+C+D’ | 1 | M5 |
| 0 | 1 | 1 | 0 | A+B’+C’+D | 1 | M6 |
| 0 | 1 | 1 | 1 | A+B’+C’+D’ | 1 | M7 |
| 1 | 0 | 0 | 0 | A’+B+C+D | 1 | M8 |
| 1 | 0 | 0 | 1 | A’+B+C+D’ | 0 | M9 |
| 1 | 0 | 1 | 0 | A’+B+C’+D | 0 | M10 |
| 1 | 0 | 1 | 1 | A’+B+C’+D’ | 0 | M11 |
| 1 | 1 | 0 | 0 | A’+B’+C+D | 0 | M12 |
| 1 | 1 | 0 | 1 | A’+B’+C+D’ | 0 | M13 |
| 1 | 1 | 1 | 0 | A’+B’+C’+D | 0 | M14 |
| 1 | 1 | 1 | 1 | A’+B’+C’+D’ | 0 | M15 |

=( M(1,3,9,10,11,12,13,14,15)

- Use K-maps to simplify the following logical expressions into minimized two-level forms. Show how you have used K-maps to obtain your answers!

  - F(A, B, C) = A C + A B C’ + A B’ C’ + A’ B’ C’ (answer in sum of products form)

|  | A’B’ | A’B | AB | AB’ |
| --- | --- | --- | --- | --- |
| C’ | 1 | 0 | 1 | 1 |
| C | 0 | 0 | 1 | 1 |

= A + B’C’

  - F(A, B, C) = M(2, 4, 6)  (answer in product of sums form)

| A | B | C | Maxterms | F(A,B,C) |  |
| --- | --- | --- | --- | --- | --- |
| 0 | 0 | 0 | A+B+C | 1 | M0 |
| 0 | 0 | 1 | A+B+C’ | 1 | M1 |
| 0 | 1 | 0 | A+B’+C | 0 | M2 |
| 0 | 1 | 1 | A+B’+C’ | 1 | M3 |
| 1 | 0 | 0 | A’+B+C | 0 | M4 |
| 1 | 0 | 1 | A’+B+C’ | 1 | M5 |
| 1 | 1 | 0 | A’+B’+C | 0 | M6 |
| 1 | 1 | 1 | A’+B’+C’ | 1 | M7 |

|  | A’B’ | A’B | AB | AB’ |
| --- | --- | --- | --- | --- |
| C’ | 1 | 0 | 0 | 0 |
| C | 1 | 1 | 1 | 1 |

= (B’ + C) (A’ + C)

  - F(A, B, C, D) = m(0, 4, 5, 8, 11, 12, 13) (answer in sum of products form)

| A | B | C | D | Minterms | F(A,B,C,D) |  |
| --- | --- | --- | --- | --- | --- | --- |
| 0 | 0 | 0 | 0 | A’B’C’D’ | 1 | m0 |
| 0 | 0 | 0 | 1 | A’B’C’D | 0 | m1 |
| 0 | 0 | 1 | 0 | A’B’C D’ | 0 | m2 |
| 0 | 0 | 1 | 1 | A’B’C D | 0 | m3 |
| 0 | 1 | 0 | 0 | A’B C’D’ | 1 | m4 |
| 0 | 1 | 0 | 1 | A’B C’D | 1 | m5 |
| 0 | 1 | 1 | 0 | A’B C D’ | 0 | m6 |
| 0 | 1 | 1 | 1 | A’B C D | 0 | m7 |
| 1 | 0 | 0 | 0 | A B’C’D’ | 1 | m8 |
| 1 | 0 | 0 | 1 | A B’C’D | 0 | m9 |
| 1 | 0 | 1 | 0 | A B’C D’ | 0 | m10 |
| 1 | 0 | 1 | 1 | A B’C D | 1 | m11 |
| 1 | 1 | 0 | 0 | A B C’D’ | 1 | m12 |
| 1 | 1 | 0 | 1 | A B C’D | 1 | m13 |
| 1 | 1 | 1 | 0 | A B C D’ | 0 | m14 |
| 1 | 1 | 1 | 1 | A B C D | 0 | m15 |

|  | A’B’ | A’B | AB | AB’ |
| --- | --- | --- | --- | --- |
| C’D’ | 1 | 1 | 1 | 1 |
| C’D | 0 | 1 | 1 | 0 |
| CD | 0 | 0 | 0 | 1 |
| CD’ | 0 | 0 | 0 | 0 |

= C’D’ + BC’ + AB’CD

  - F(A, B, C, D) = (A + C + D’) (A + B + D) (A’ + C + D’) (B’ + C + D’) (answer in product of sums form)

|  | A’B’ | A’B | AB | AB’ |
| --- | --- | --- | --- | --- |
| C’D’ | 0 | 1 | 1 | 1 |
| C’D | 0 | 0 | 0 | 0 |
| CD | 1 | 1 | 1 | 1 |
| CD’ | 0 | 1 | 1 | 1 |

= (C + D’) (A + B + D)

- Given that the Boolean function F(A, B, C) = A C’ + A’ B, answer the following questions. Show the intermediate work to arrive at the answer!

  - What is the corresponding expression in minimized product of sums form?

F(A,B,C) = (A + B) (A’ + C’)

  - What is the corresponding expression for the complement of F in minimized sum of products form?

F’(A,B,C) = ((A + B) (A’ + C’))’ = A’B’ + AC

  - What is the corresponding expression for the complement of F in minimized product of sums form?

F’(A,B,C) = ( AC’ + A’B )’ = (A’ + C) (A + B’)

- F(A,B,C,D) = B(C’ + D’) in minimized product of sums form. Answer the following questions, showing your intermediate steps:

  - Show a K-map for F.

|  | A’B’ | A’B | AB | AB’ |
| --- | --- | --- | --- | --- |
| C’D’ | 0 | 1 | 1 | 0 |
| C’D | 0 | 1 | 1 | 0 |
| CD | 0 | 0 | 0 | 0 |
| CD’ | 0 | 1 | 1 | 0 |

  - What is F in Big M notation?

| A | B | C | D | Maxterms | F(A,B,C,D) |  |
| --- | --- | --- | --- | --- | --- | --- |
| 0 | 0 | 0 | 0 | A+B+C+D | 0 | M0 |
| 0 | 0 | 0 | 1 | A+B+C+D’ | 0 | M1 |
| 0 | 0 | 1 | 0 | A+B+C’+D | 0 | M2 |
| 0 | 0 | 1 | 1 | A+B+C’+D’ | 0 | M3 |
| 0 | 1 | 0 | 0 | A+B’+C+D | 1 | M4 |
| 0 | 1 | 0 | 1 | A+B’+C+D’ | 1 | M5 |
| 0 | 1 | 1 | 0 | A+B’+C’+D | 1 | M6 |
| 0 | 1 | 1 | 1 | A+B’+C’+D’ | 0 | M7 |
| 1 | 0 | 0 | 0 | A’+B+C+D | 0 | M8 |
| 1 | 0 | 0 | 1 | A’+B+C+D’ | 0 | M9 |
| 1 | 0 | 1 | 0 | A’+B+C’+D | 0 | M10 |
| 1 | 0 | 1 | 1 | A’+B+C’+D’ | 0 | M11 |
| 1 | 1 | 0 | 0 | A’+B’+C+D | 1 | M12 |
| 1 | 1 | 0 | 1 | A’+B’+C+D’ | 1 | M13 |
| 1 | 1 | 1 | 0 | A’+B’+C’+D | 1 | M14 |
| 1 | 1 | 1 | 1 | A’+B’+C’+D’ | 0 | M15 |

=( M(0,1,2,3,7,8,9,10,11,15)

  - What is F in Little M notation?

| A | B | C | D | Minterms | F(A,B,C,D) |  |
| --- | --- | --- | --- | --- | --- | --- |
| 0 | 0 | 0 | 0 | A’B’C’D’ | 0 | m0 |
| 0 | 0 | 0 | 1 | A’B’C’D | 0 | m1 |
| 0 | 0 | 1 | 0 | A’B’C D’ | 0 | m2 |
| 0 | 0 | 1 | 1 | A’B’C D | 0 | m3 |
| 0 | 1 | 0 | 0 | A’B C’D’ | 1 | m4 |
| 0 | 1 | 0 | 1 | A’B C’D | 1 | m5 |
| 0 | 1 | 1 | 0 | A’B C D’ | 1 | m6 |
| 0 | 1 | 1 | 1 | A’B C D | 0 | m7 |
| 1 | 0 | 0 | 0 | A B’C’D’ | 0 | m8 |
| 1 | 0 | 0 | 1 | A B’C’D | 0 | m9 |
| 1 | 0 | 1 | 0 | A B’C D’ | 0 | m10 |
| 1 | 0 | 1 | 1 | A B’C D | 0 | m11 |
| 1 | 1 | 0 | 0 | A B C’D’ | 1 | m12 |
| 1 | 1 | 0 | 1 | A B C’D | 1 | m13 |
| 1 | 1 | 1 | 0 | A B C D’ | 1 | m14 |
| 1 | 1 | 1 | 1 | A B C D | 0 | m15 |

= (m(4,5,6,12,13,14)

  - What is F in minimized two-level sum of products form?

|  | A’B’ | A’B | AB | AB’ |
| --- | --- | --- | --- | --- |
| C’D’ | 0 | 1 | 1 | 0 |
| C’D | 0 | 1 | 1 | 0 |
| CD | 0 | 0 | 0 | 0 |
| CD’ | 0 | 1 | 1 | 0 |

= BC’ + BD’

  - Apply DeMorgan’s Law to derive the complement of F, starting with the original product of sums expression.

F’(A,B,C,D) = (B(C’ + D’))’ = B’ + CD

  - Apply DeMorgan’s Law to derive the complement of F given your answer to part d.

F’(A,B,C,D) = (BC’ + BD’)’ = (B’ + C) (B’ + D)

  - Using the K-map you filled in for part a, show how to derive the minimized complement of F in product of sums form. Is your answer the same as in part f? If not, why not?

|  | A’B’ | A’B | AB | AB’ |
| --- | --- | --- | --- | --- |
| C’D’ | 1 | 0 | 0 | 1 |
| C’D | 1 | 0 | 0 | 1 |
| CD | 1 | 1 | 1 | 1 |
| CD’ | 1 | 0 | 0 | 1 |

F’ = (B’ + C) (B’ + D)

Yes, it is the same as part f.

  - Using the K-map you filled in for part a, show how to derive the minimized complement of F in sum of products form. Is your answer the same as in part e? If not, why not?

|  | A’B’ | A’B | AB | AB’ |
| --- | --- | --- | --- | --- |
| C’D’ | 1 | 0 | 0 | 1 |
| C’D | 1 | 0 | 0 | 1 |
| CD | 1 | 1 | 1 | 1 |
| CD’ | 1 | 0 | 0 | 1 |

F’ = B’ + CD

Yes, it is the same as part e.