NAME: _____________________________________________________ SID: ______________

University of California at Berkeley

College of Engineering

Department of Electrical Engineering and Computer Science

##### EECS 150										         R. H. Katz

Spring 2007									            1 February 2007

Quiz #2: Multiplexer Logic

Closed Book! Open Neighbor!

F(A,B,C,D) = m(1,5,9,11,12,14). Fill in the K-map for this function:

Show how to implement F with an 8:1 multiplexer with A,B,C on the selection inputs and 0, 1, D, or D’ connected to the data inputs:

Show how to implement F with a 4:1 muliplexer with A,D on the selection inputs and 0. 1. B, B’, C, C’ connected to the data inputs (0, 1, or literals only – no product terms!):

# Text boxes

0

C’

B

B’

D

0

D

0

D

D

D’

D’

0       0         1         0

0       0         0         1

1       1         0         1

0       0         1         0

A  D

S1 S0

F

0

1

2

3

A  B  C

S2 S1 S0

F

0

1

2

3

4

5

6

7