# University of California at Berkeley

# College of Engineering

# Department of Electrical Engineering and Computer Science

EECS 150	R. H. Katz, Instructor

Spring 2007

# Quiz #8: Booth Step Sequential Multiplier

Thursday, 26 April 2007

Open Neighbor! Closed Book!

Consider the design of a 4-bit twos complement multiplier that takes two 4-bit operands and produces an 8-bit product. Suppose that you want to multiply 5 by 7.

- Using a conventional sequential multiplier, assuming 5 (0101) is the multiplicand and 7 (0111) is the multiplier, how many shift and how many add operations will be executed?

Number of shifts: ________4__________	Number of adds: ________3___________

(b) 	Using a sequential multiplier that implements the Booth multiplier step, with the same multiplicand and multiplier, how many shift and how many add operations will be executed?

Number of shifts: ________4___________	Number of adds/subs: ________2_______

(c)	Show the step-by-step, add/subtract, skip, and shift operations that take place to multiply 5 by 7 using a Booth multiplier. Fill in the Product/Multiplier/Extra Digit boxes with the RESULTS of applying the operation you select for the Op column:

| Step | Op (Add/Sub, Skip, or Shift) | Multiplicand | Product | Multiplier | Extra Digit |
| --- | --- | --- | --- | --- | --- |
| Initial | --------------- | 0101 | 0000 | 0111 | 0 |
| 1a. | Sub 0101 |  | 1011 | 0111 | 0 |
| 1b. | Shift |  | 1101 | 1011 | 1 |
| 2a. | Skip |  | 1101 | 1011 | 1 |
| 2b. | Shift |  | 1110 | 1101 | 1 |
| 3a. | Skip |  | 1110 | 1101 | 1 |
| 3b. | Shift |  | 1111 | 0110 | 1 |
| 4a. | Add 0101 |  | 0100 | 0110 | 1 |
| 4b. | Shift |  | 0010 | 0011 | 0 |