|  | University of California at Berkeley College of Engineering Department of Electrical Engineering and Computer Science |  |
| --- | --- | --- |
| EECS 150 Spring 2008 |  | P. C. McGeer K. S. J. Pister |
|  | Problem Set #5: Datapath Elements Assigned 3/7/2008, Due 3/14/2008 at 2 PM |  |

- Suppose (there is actually sometimes a good reason to do this, though it is often not worth the additional hardware) you have sign-and-magnitude representation for numbers in the registers.  Design a sign-and-magnitude to two’s-complement converter and a two’s-complement to sign-and-magnitude converter.

- Use the circuits you designed in #1, together with the ALU discussed in class, to build a sign-and-magnitude ALU.   When you build this, check: do the logical operations (bitwise or, and, negation, xor, equality) work properly?

- Design a 0-3 bit right shifter for 4-bit unsigned words using exactly 5 two-input muxes and three AND gates. (The specification of this shifter   is that 0’s are shifted in to the high-order bits) Extend this to a 0-7 bit right shifter for 8-bit unsigned words using exactly 17 two-input muxes and seven AND gates.  Estimate the number of AND gates and MUXES required to implement a 2n bit shifter.

- A BCD adder consists of  blocks with two four-bit inputs, one one-bit input (carry-in), one four-bit output  and a one-bit output (carry-out).  Design a BCD adder block that works for single BCD digits.  Show how to array these to make a BCD adder design.