University of California at Berkeley

College of Engineering

Department of Electrical Engineering and Computer Science

| Assigned: | Week of 2/11 |
| --- | --- |
| Due: | Week of 2/18, 10 minutes after start (xx:20) of your assigned lab section. |

Lab 3

Verilog Synthesis & FSMs

# 1.0 Motivation

In Lab1, you became acquainted with Synplify as well as the Xilinx Place and Route tools.  In Lab3, you worked with ModelSim and Verilog to produce a working design.  This lab is designed to give you a chance to bring those skills together to design, specify and then implement a fully working Finite State Machine in Verilog, using a combination lock as an example.

For this lab we have given you all of the support modules and design necessary, your job is to take our high level design and translate it into working Verilog.  In order to do this you will need to force yourself to use good Verilog coding style, acquaint yourself with the Verilog language and become at least somewhat proficient with the CAD tools.

# 2.0 Introduction

In this lab you will be making a 2bit, 2 digit combination lock such as those sometimes found on secure doors.  The inputs to the lock consist of two code switches and three buttons.  The code switches (SW9[2:1]) are used to enter the digits in the combination.  The three buttons are Reset (SW1) which is used to reset the lock, Enter (SW2) which is used to enter a digit of the combination and ResetCombo (SW6) which would not be accessible normally and which will reset the combination that will open the lock to a default value.

To operate the lock, a user would:

- Set the code on SW9[2:1] to the first digit and press enter (SW2).

- Set the code on SW9[2:1] to the second digit and press enter (SW2).

- The lock will Open.

- The user would then press enter (SW2).

- Set the code on SW9[2:1] to the new first digit and press enter (SW2).

- Set the code on SW9[2:1] to the new second digit and press enter (SW2).

- Cycle back to step 3 above…

When someone gets the combo wrong it would go like this:

- Set the code on SW9[2:1] to a wrong digit and press enter (SW2).

- Set the code on SW9[2:1] to any digit (right or wrong) and press enter (SW2).

- The lock will show Error

- The lock will stay in this state until the user presses Reset (SW1).

# 3.0 Prelab

Please make sure to complete the prelab before you attend your lab section.  You will not be able to finish this lab in 3hrs otherwise!

- Read this handout thoroughly.  Pay particular attention to section 4.0 Lab Procedure as it describes in detail the circuits you must create.

- Examine the Verilog provided for this weeks lab.

  - Most of the modules you have seen before.

  - Make sure you understand FPGA_TOP2 as it instantiates your module, and handles the I/O.

- Write your Verilog ahead of time.

  - Lab3Lock.v

    - Your lock FSM, which instantiates the comparator

  - Lab3Testbench.v

    - A testbench/Code Breaker for the lock FSM

    - The testbench will function as a code breaker that goes through all of the lock inputs until it finds the correct one and displays that.

    - Make sure that this tests as much of the lock and comparator as possible.

    - Refer to past testbenches as a starting point.

- You will need the entire 3hr lab to test and debug your Verilog!

  - Remember it has to pass simulation and synthesis

# 4.0 Lab Procedure

Since we expect you to write your verilog ahead of time, and Verilog is nothing more than a bunch of standard text in a file with a *.v extension you can do this part of the lab entirely from home in your favorite text editor or by connecting to Kramnik for remote access to Xilinx tools:

(http://inst.eecs.berkeley.edu/~cs150/fa06/Kramnik/tutorial.php).

Or you can come into the lab and use the tools there.  For those of you who like maintaining a single Xilinx Project Navigator project for each lab, you can even create the project ahead of time and write your Verilog from within Project Navigator.

Remember to manage your Verilog, projects and folders well.  Doing a poor job of managing your files can cost you hours of rewriting code, if you accidentally delete your files.

## 4.1 Lab3Top

The Lab3Top module is very simple and does not need to contain any behavioral Verilog.  The Lab3Top module simply instantiates the Lab3Lock FSM and Lab3Compare modules, and ties them together with the appropriate signals.

Figure 1: Lab3Top Block Diagram

In order to simplify the Lab3Lock FSM and make the whole lock design more flexible we have separated the FSM and the comparator, which compares the value on the switches to the digits of the combination.  Essentially the code input from the switches is fed into the Lab3Compare module which determines the Decode1 and Decode2 signals needed by the Lab3Lock FSM.  Based on these and the Enter and Reset buttons the Lab3Lock tracks its state and generates the appropriate outputs.

Table 1 below shows the inputs and outputs from the Lab3Top module.

| Signal | Width | Dir | Description |
| --- | --- | --- | --- |
| Code | 2 | I | The code value from dipswitch SW9[2:1] |
| Enter | 1 | I | The Enter button (SW2) |
| ResetCombo | 1 | I | Reset the combination to the default (SW6) |
| Clock | 1 | I | The Clock signal |
| Reset | 1 | I | Reset the FSM to the Init state (SW1) |
| Open | 1 | O | Indicates that the lock is open (OK2 state) |
| Error | 1 | O | Indicates that the wrong combo was entered (BAD2 state) |
| Prog1 | 1 | O | Indicates that the lock will accept a new 1st digit |
| Prog2 | 1 | O | Indicates that the lock will accept a new 2nd digit |
| LED | 8 | O | Debug outputs, for your use on the board |

Table 1: Port Specification for Lab3Top

## 4.2 Lab3Lock

In this lab you will be building primarily the Lab3Lock module, a relatively simple FSM.  This module is responsible for maintaining the state of the lock and generating the outputs to show the lock’s status to the user.

Below are: a table of the inputs and outputs from the Lab3Lock module and a bubble-and-arc diagram of the finite state machine.

| Signal | Width | Dir | Description |
| --- | --- | --- | --- |
| Decode1 | 1 | I | Indicates that the switches match the 1st digit of the combo |
| Decode2 | 1 | I | Indicates that the switches match the 2nd digit of the combo |
| Enter | 1 | I | The Enter button (SW2) |
| Clock | 1 | I | The Clock signal |
| Reset | 1 | I | Reset the FSM to the Init state (SW1) |
| Open | 1 | O | Indicates that the lock is open (OK2 state) |
| Error | 1 | O | Indicates that the wrong combo was entered (BAD2 state) |
| Prog1 | 1 | O | Indicates that the lock will accept a new 1st digit |
| Prog2 | 1 | O | Indicates that the lock will accept a new 2nd digit |
| LED | 8 | O | Debug outputs, for your use on the board |

Table 2: Port Specification for Lab3Lock

Figure 2: Bubble-and-Arc Diagram for Lab3Lock

Notice that in Figure 2, there are a number of bits of shorthand notation.  First off, there are no arcs labeled Reset.  That is because a high on the Reset input will ALWAYS return the FSM to the Init state.  Also of note is the output specifications in []s, where only the outputs which are actually asserted in a given state are shown.

As a note on optimization, you should examine the relationship between state changes and the Enter signal.  You may be able to simplify your Verilog if you are clever.

## 4.3 Lab3Compare

You should keep in mind that this module has been built for you.  We are providing this documentation to make the operation of this module very clear.

It is the responsibility of the Lab3Compare module to generate the Decode1 and Decode2 signals, which indicate that the Code input matches the 1st and 2nd digits of the combination respectively.  Therefore the Lab3Compare module is essentially a pair of combinational comparators.

However in order to make the combination on our lock programmable, this module has a pair of registers to remember what the 1st and 2nd digits of the combination actually are.  In order to set up a default combination the ResetCombo input will forcibly set these registers to 2’b11 and 2’b01 respectively.

In order to program new combinations, when the Prog1 and Enter signals are high, the register for the 1st digit will store whatever value is on the Code input as the new 1st digit.  Similarly, when the Prog2 and Enter signals are high the register for the 2nd digit will store the new 2nd digit.

| Signal | Width | Dir | Description |
| --- | --- | --- | --- |
| Code | 2 | I | The code value from dipswitch SW9[2:1] |
| Decode1 | 1 | O | Indicate that that Code matches the 1st digit of the lock |
| Decode2 | 1 | O | Indicate that that Code matches the 2nd digit of the lock |
| Prog1 | 1 | I | Indicates that the lock will accept a new 1st digit |
| Prog2 | 1 | I | Indicates that the lock will accept a new 2nd digit |
| Enable | 1 | I | Enable the loading of new combination digits (driven by the Enter button, SW2) |
| Clock | 1 | I | The Clock signal |
| ResetCombo | 1 | I | Reset the combination to 2’b11, 2’b01 (SW6) |

Table 3: Port Specification for Lab3Compare

| 5.0 Lab 3 Check-off |
| --- |
| Assigned: | Week of 2/4 |
| Due: | Week of 2/11, 10 minutes after start (xx:20) of your assigned lab section. |
| Man Hours Spent | Total Points | TA Initial | Date | Time |
|  | / 100 |  | / / 06 |  |
| NAME |  | SID |  | SECTION |  |
| Quality of Verilog Lab3Top __________ (8%) Lab3Lock __________ (12%) Full Simulation with Code Breaker __________ (40%) Working Synthesized Lock __________ (40%) |
| RevC – 1/18/2004 | Greg Gibeling | Added errata from Fall 2004 Migrated to Lab3 |
| RevB – 7/10/2004 | Greg Gibeling | Complete Rewrite of Lab3 Based on the old Lab3 |
| RevA | Multiple | Original Lab3 from Fa02-Sp04 Spring 2004: Greg Gibeling Fall 2003: Greg Gibeling Spring 2003: Sandro Pintz Fall 2002: John Wawrzynek & L.T. Pang |