## Slide 1: CS 152 Computer Architecture and Engineering Lecture 11 - Out-of-Order Issue, Register Renaming, & Branch Prediction
John Wawrzynek
Electrical Engineering and Computer Sciences
University of California at Berkeley
http://www.eecs.berkeley.edu/~johnw
http://inst.eecs.berkeley.edu/~cs152

## Slide 2: CS152 Administrivia
Quiz 2 Results posted
PS3 posted

## Slide 3: Last time in Lecture 12
Pipelining is complicated by multiple and/or variable latency functional units
Out-of-order and/or pipelined execution requires tracking of dependencies
  RAW
  WAR
  WAW
Dynamic issue logic can support out-of-order execution to improve performance
  Last time, looked at simple scoreboard to track out-of-order completion
Hardware register renaming can further improve performance by removing hazards.

## Slide 4: Register Renaming
Decode does register renaming and adds instructions to the issue-stage instruction reorder buffer (ROB)
 renaming makes WAR or WAW hazards impossible
Any instruction in ROB whose RAW hazards have been satisfied can be issued.
 Out-of-order or dataflow execution
IF
ID
WB
ALU
Mem
Fadd
Fmul
Issue

## Slide 5: Renaming Structures
Renaming
table &
regfile
Reorder
buffer
Load
Unit
FU
FU
Store
Unit
< t, result >
Ins# use exec op p1 src1 p2 src2
t1
t2
.
.
tn
Instruction template (i.e., tag t) is allocated by the
Decode stage, which also associates tag with register in regfile
When an instruction completes, its tag is deallocated
Replacing the
tag by its value
is an expensive
operation

## Slide 6: Reorder Buffer Management
Instruction slot is candidate for execution when:
  It holds a valid instruction (“use” bit is set)
  It has not already started execution (“exec” bit is clear)
  Both operands are available (p1 and p2 are set)
t1
t2
.
.
.
tn
ptr2
next to
deallocate
ptr1
next
available
Ins# use exec op p1 src1 p2 src2
Destination registers are renamed to the instruction’s slot tag
ROB managed circularly
  “exec” bit is set when instruction begins execution
  When an instruction completes its “use” bit is marked free
  ptr2 is incremented only if the “use” bit is marked free

## Slide 7: IBM 360/91 Floating-Point Unit R. M. Tomasulo, 1967
Mult
1
1
2
3
4
5
6
load
buffers
(from
memory)
1
2
3
4
Adder
1
2
3
Floating-Point
Regfile
store buffers
(to memory)
...
instructions
Common bus ensures that data is made available immediately to all the instructions waiting for it.
Match tag, if equal, copy value & set presence “p”.
Distribute
instruction
templates
by
functional
units
< tag, result >
p
tag/data
p
tag/data
p
tag/data
p
tag/data
p
tag/data
p
tag/data
p
tag/data
p
tag/data
p
tag/data
p
tag/data
p
tag/data
p
tag/data
p
tag/data
2
p
tag/data
p
tag/data
p
tag/data
p
tag/data
p
tag/data
p
tag/data
p
tag/data
p
tag/data
p
tag/data
p
tag/data

## Slide 8: Effectiveness?
Renaming and Out-of-order execution was first
implemented in 1969 in IBM 360/91 but did not show up in the subsequent models until mid-Nineties.
Why ?
Reasons
    1. Complex logic / cost
    2. Memory latency a much bigger problem
    3. Exceptions not precise!
    One more problem needed to be solved
Control transfers

## Slide 9: Precise Interrupts
It must appear as if an interrupt is taken between two instructions (say Ii and Ii+1)
  the effect of all instructions up to and including Ii is
  totally complete
  no effect of any instruction after Ii has taken place
The interrupt handler either aborts the program or
restarts it at Ii+1 .

## Slide 10: Effect on Interrupts Out-of-order Completion
I1 DIVD f6, f6, f4
I2 LD f2, 45(r3)
I3 MULTD f0, f2, f4
I4 DIVD f8, f6, f2
I5 SUBD f10, f0, f6
I6 ADDD f6, f8, f2
out-of-order comp 1 2 2 3 1 4 3 5 5 4 6 6
restore f2 restore f10
Consider interrupts
Precise interrupts are difficult to implement at high speed
- want to start execution of later instructions before
exception checks finished on earlier instructions

## Slide 11: Exception Handling (In-Order Five-Stage Pipeline)
Hold exception flags in pipeline until commit point (M stage)
Exceptions in earlier pipe stages override later exceptions
Inject external interrupts at commit point (override others)
If exception at commit: update Cause and EPC registers, kill
all stages, inject handler PC into fetch stage
Asynchronous Interrupts
Exc
D
PC
D
PC
Inst. Mem
D
Decode
E
M
Data Mem
W
+
Exc
E
PC
E
Exc
M
PC
M
Cause
EPC
Kill D Stage
Kill F Stage
Kill E Stage
Illegal Opcode
Overflow
Data Addr Except
PC Address Exceptions
Kill Writeback
Select Handler PC
Commit Point

## Slide 12: Phases of Instruction Execution
Fetch: Instruction bits retrieved from cache.
I-cache
Fetch Buffer
Issue Buffer
Functional Units
Architectural
State
Execute: Instructions and operands issued to execution units.
When execution completes, all results and exception flags are available.
Decode: Instructions dispatched to appropriate issue-stage buffer
Result Buffer
Commit: Instruction irrevocably updates architectural state (aka “graduation”).
PC
Commit
Decode/Rename

## Slide 13: In-Order Commit for Precise Exceptions
Instructions fetched and decoded into instruction
reorder buffer in-order
Execution is out-of-order (  out-of-order completion)
Commit (write-back to architectural state, i.e., regfile &
memory, is in-order
Temporary storage needed to hold results before commit (shadow registers and store buffers)
Fetch
Decode
Execute
Commit
Reorder Buffer
In-order
In-order
Out-of-order
Exception?
Kill
Kill
Kill
Inject handler PC

## Slide 14: Extensions for Precise Exceptions
Reorder buffer
ptr2
next to
commit
ptr1
next
available
add <pd, dest, data, cause> fields in the instruction template
commit instructions to reg file and memory in program
order  buffers can be maintained circularly
on exception, clear reorder buffer by resetting ptr1=ptr2
(stores must wait for commit before updating memory)
Inst# use exec op p1 src1 p2 src2 pd dest data cause

## Slide 15: Rollback and Renaming
Register file does not contain renaming tags any more.
How does the decode stage find the tag of a source register?
Search the “dest” field in the reorder buffer
Register File
(now holds only committed state)
Reorder
buffer
Load
Unit
FU
FU
FU
Store
Unit
< t, result >
t1
t2
.
.
tn
Ins# use exec op p1 src1 p2 src2 pd dest data
Commit

## Slide 16: Renaming Table
Register File
Reorder
buffer
Load
Unit
FU
FU
FU
Store
Unit
< t, result >
t1
t2
.
.
tn
Ins# use exec op p1 src1 p2 src2 pd dest data
Commit
Rename
Table
Renaming table is a cache to speed up register name look up. It needs to be cleared after each exception taken.
When else are valid bits cleared?
Control transfers
r1
t
v
r2
tag
valid bit

## Slide 17: Control Flow Penalty
I-cache
Fetch Buffer
Issue
Buffer
Func.
Units
Arch.
State
Execute
Decode
Result
Buffer
Commit
PC
Fetch
Branch executed
Next fetch started
Modern processors may have > 10 pipeline stages between next PC calculation and branch resolution !
How much work is lost if pipeline doesn’t follow correct instruction flow?
~ Loop length x pipeline width

## Slide 18: Mispredict Recovery
In-order execution machines:
  Assume no instruction issued after branch can write-back before branch resolves
  Kill all instructions in pipeline behind mispredicted branch
  Multiple instructions following branch in program order can complete before branch resolves
Out-of-order execution?

## Slide 19: In-Order Commit for Precise Exceptions
Instructions fetched and decoded into instruction
reorder buffer in-order
Execution is out-of-order (  out-of-order completion)
Commit (write-back to architectural state, i.e., regfile &
memory, is in-order
Temporary storage needed in ROB to hold results before commit
Fetch
Decode
Execute
Commit
Reorder Buffer
In-order
In-order
Out-of-order
Kill
Kill
Kill
Exception?
Inject handler PC

## Slide 20: Branch Misprediction in Pipeline
Fetch
Decode
Execute
Commit
Reorder Buffer
Kill
Kill
Kill
Branch
Resolution
Inject correct PC
Can have multiple unresolved branches in ROB
Can resolve branches out-of-order by killing all the
instructions in ROB that follow a mispredicted branch
Branch
Prediction
PC
Complete

## Slide 21: Recovering ROB/Renaming Table
t
v
t
v
t
v
Register File
Reorder
buffer
Load
Unit
FU
FU
FU
Store
Unit
< t, result >
t1
t2
.
.
tn
Ins# use exec op p1 src1 p2 src2 pd dest data
Commit
Rename
Table
r1
t
v
r2
Take snapshot of register rename table at each predicted branch, recover earlier snapshot if branch mispredicted
Rename
Snapshots
Ptr2 next to commit
Ptr1 next available
rollback next available

## Slide 22: Important Points on OOO Execution
Precise interrupts are provided by committing (graduating) instructions in-order.
Any instruction not yet committed is considered “speculative” because it might be killed because of:
  Interrupt on an older instruction
  Branch misprediction
Instructions (and their result values) are held in ROB waiting to commit

## Slide 23: “Data-in-ROB” Design (HP PA8000, Pentium Pro, Core2Duo, Nehalem)
On dispatch into ROB, ready sources can be in regfile or in ROB dest (copied into src1/src2 if ready before dispatch)
On completion, write to dest field and broadcast to src fields.
On issue, read from ROB src fields
Instructions are committed to the register file in order
Instruction slots (i.e. tags) are recycled after commit
Register File
holds only committed state
Reorder
buffer
Load
Unit
FU
FU
FU
Store
Unit
< t, result >
t1
t2
.
.
tn
Ins# use exec op p1 src1 p2 src2 pd dest data
Commit

## Slide 24: Data Movement in Data-in-ROB Design
ROB
Architectural Register File
Read operands during decode
Src Operands
Write sources after decode
Read operands at issue
Functional Units
Write results at completion
Read results at commit
Bypass newer values at decode
Result Data

## Slide 25: Unified Physical Register File (MIPS R10K, Alpha 21264, Intel Pentium 4 & Sandy Bridge)
Rename all architectural registers into a single physical register file during decode, no register values read
Functional units read and write from single unified register file holding committed and temporary registers in execute
Commit only updates the mapping of architectural register to physical register, no data movement
Unified Physical Register File
Read operands at issue
Functional Units
Write results at completion
Committed Register Mapping
Decode Stage Register Mapping

## Slide 26
Pipeline Design with Physical Regfile
Fetch
Decode & Rename
Reorder Buffer
PC
Branch
Prediction
Commit
Branch
Resolution
Branch
Unit
ALU
MEM
Store Buffer
D$
Execute
In-Order
In-Order
Out-of-Order
Physical Reg. File
kill
kill
kill
kill

## Slide 27: Lifetime of Physical Registers
ld x1, (x3)
addi x3, x1, #4
sub x6, x7, x9
add x3, x3, x6
ld x6, (x1)
add x6, x6, x3
sd x6, (x1)
ld x6, (x11)
ld P1, (Px)
addi P2, P1, #4
sub P3, Py, Pz
add P4, P2, P3
ld P5, (P1)
add P6, P5, P4
sd P6, (P1)
ld P7, (Pw)
Rename
When can we reuse a physical register?
When next write of same architectural register commits
Physical regfile holds committed and speculative values
Physical registers decoupled from ROB entries (no data in ROB)

## Slide 28: Physical Register Management
op
p1
PR1
p2
PR2
ex
use
Rd
PRd
LPRd
<x6>
P5
<x7>
P6
<x3>
P7
P0
Pn
P1
P2
P3
P4
x5
P5
x6
P6
x7
x0
P8
x1
x2
P7
x3
x4
ROB
Rename Table
Physical Regs
Free List
ld x1, 0(x3)
addi x3, x1, #4
sub x6, x7, x6
add x3, x3, x6
ld x6, 0(x1)
p
p
p
P0
P1
P3
P2
P4
(LPRd requires third read port on Rename Table for each instruction)
<x1>
P8
p

## Slide 29: Physical Register Management
op
p1
PR1
p2
PR2
ex
use
Rd
PRd
LPRd
ROB
ld x1, 0(x3)
addi x3, x1, #4
sub x6, x7, x6
add x3, x3, x6
ld x6, 0(x1)
Free List
P0
P1
P3
P2
P4
<x6>
P5
<x7>
P6
<x3>
P7
P0
Pn
P1
P2
P3
P4
Physical Regs
p
p
p
<x1>
P8
p
x ld p P7 x1 P0
x5
P5
x6
P6
x7
x0
P8
x1
x2
P7
x3
x4
Rename Table
P0
P8

## Slide 30: Physical Register Management
op
p1
PR1
p2
PR2
ex
use
Rd
PRd
LPRd
ROB
ld x1, 0(x3)
addi x3, x1, #4
sub x6, x7, x6
add x3, x3, x6
ld x6, 0(x1)
Free List
P0
P1
P3
P2
P4
<x6>
P5
<x7>
P6
<x3>
P7
P0
Pn
P1
P2
P3
P4
Physical Regs
p
p
p
<R1>
P8
p
x ld p P7 x1 P0
x5
P5
x6
P6
x7
x0
P8
x1
x2
P7
x3
x4
Rename Table
P0
P8
P7
P1
x addi P0 x3 P1

## Slide 31: Physical Register Management
op
p1
PR1
p2
PR2
ex
use
Rd
PRd
LPRd
ROB
ld x1, 0(x3)
addi x3, x1, #4
sub x6, x7, x6
add x3, x3, x6
ld x6, 0(x1)
Free List
P0
P1
P3
P2
P4
<x6>
P5
<x7>
P6
<x3>
P7
P0
Pn
P1
P2
P3
P4
Physical Regs
p
p
p
<x1>
P8
p
x ld p P7 x1 P0
x5
P5
x6
P6
x7
x0
P8
x1
x2
P7
x3
x4
Rename Table
P0
P8
P7
P1
x addi P0 x3 P1
P5
P3
x sub p P6 p P5 x6 P3

## Slide 32: Physical Register Management
op
p1
PR1
p2
PR2
ex
use
Rd
PRd
LPRd
ROB
ld x1, 0(x3)
addi x3, x1, #4
sub x6, x7, x6
add x3, x3, x6
ld x6, 0(x1)
Free List
P0
P1
P3
P2
P4
<x6>
P5
<x7>
P6
<x3>
P7
P0
Pn
P1
P2
P3
P4
Physical Regs
p
p
p
<x1>
P8
p
x ld p P7 x1 P0
x5
P5
x6
P6
x7
x0
P8
x1
x2
P7
x3
x4
Rename Table
P0
P8
P7
P1
x addi P0 x3 P1
P5
P3
x sub p P6 p P5 x6 P3
P1
P2
x add P1 P3 x3 P2

## Slide 33: Physical Register Management
op
p1
PR1
p2
PR2
ex
use
Rd
PRd
LPRd
ROB
ld x1, 0(x3)
addi x3, x1, #4
sub x6, x7, x6
add x3, x3, x6
ld x6, 0(x1)
Free List
P0
P1
P3
P2
P4
<x6>
P5
<x7>
P6
<x3>
P7
P0
Pn
P1
P2
P3
P4
Physical Regs
p
p
p
<x1>
P8
p
x ld p P7 x1 P0
x5
P5
x6
P6
x7
x0
P8
x1
x2
P7
x3
x4
Rename Table
P0
P8
P7
P1
x addi P0 x3 P1
P5
P3
x sub p P6 p P5 x6 P3
P1
P2
x add P1 P3 x3 P2
x ld P0 x6 P4
P3
P4

## Slide 34: Physical Register Management
op
p1
PR1
p2
PR2
ex
use
Rd
PRd
LPRd
ROB
x ld p P7 x1 P0
x addi P0 x3 P1
x sub p P6 p P5 x6 P3
x ld p P7 x1 P0
ld x1, 0(x3)
addi x3, x1, #4
sub x6, x7, x6
add x3, x3, x6
ld x6, 0(x1)
Free List
P0
P1
P3
P2
P4
<x6>
P5
<x7>
P6
<x3>
P7
P0
Pn
P1
P2
P3
P4
Physical Regs
p
p
p
<x1>
P8
p
x5
P5
x6
P6
x7
x0
P8
x1
x2
P7
x3
x4
Rename Table
P0
P8
P7
P1
P5
P3
P1
P2
x add P1 P3 x3 P2
x ld P0 x6 P4
P3
P4
Execute & Commit
p
p
p
<x1>
P8
x

## Slide 35: Physical Register Management
op
p1
PR1
p2
PR2
ex
use
Rd
PRd
LPRd
ROB
x sub p P6 p P5 x6 P3
x addi P0 x3 P1
x addi P0 x3 P1
ld x1, 0(x3)
addi x3, x1, #4
sub x6, x7, x6
add x3, x3, x6
ld x6, 0(x1)
Free List
P0
P1
P3
P2
P4
<x6>
P5
<x7>
P6
<x3>
P7
P0
Pn
P1
P2
P3
P4
Physical Regs
p
p
p
P8
x x ld p P7 x1 P0
x5
P5
x6
P6
x7
x0
P8
x1
x2
P7
x3
x4
Rename Table
P0
P8
P7
P1
P5
P3
P1
P2
x add P1 P3 x3 P2
x ld P0 x6 P4
P3
P4
Execute & Commit
p
p
p
<x1>
P8
x
p
p
<x3>
P7

## Slide 36: Acknowledgements
These slides contain material developed and copyright by:
  Arvind (MIT)
  Krste Asanovic (MIT/UCB)
  Joel Emer (Intel/MIT)
  James Hoe (CMU)
  John Kubiatowicz (UCB)
  David Patterson (UCB)
MIT material derived from course 6.823
UCB material derived from course CS252