CS152 Quiz 1 Answer Guide

Distributed 2/25/2008

# Problem Q.1:  Microprogramming Bus-Based Architectures

# [28 points]

In this problem, we explore microprogramming by writing microcode for the bus-based implementation of the MIPS machine described in Handout #1 (Bus-Based MIPS Implementation), which we have included at the end of this quiz for your reference. In order to further simplify this problem, ignore the busy signal, and assume that the memory is as fast as the register file. The final solution should be elegant and efficient.

You are to implement in microcode a double indirect addressing mode, as described below. In this addressing mode, the source register contains a pointer to a location in memory whose value is a pointer to the location in memory whose value is to be loaded. The instruction has the following format:

LWmm  rd, rs

LWmm performs the following operation:

rd  ( M[ M[ rs ] ]

Fill in Worksheet Q1-1 with the microcode for LWmm.  Use don’t cares (*) for fields where it is safe to use don’t cares.  Study the hardware description well, and make sure all your microinstructions are legal.

Please comment your code clearly. If the pseudo-code for a line does not fit in the space provided, or if you have additional comments, you may write in the margins as long as you do it neatly.  Your code should exhibit “clean” behavior and not modify any registers (except rd) in the course of executing the instruction.

Finally, make sure that the instruction fetches the next instruction (i.e., by doing a microbranch to FETCH0 as discussed in the Handout).

| State | PseudoCode | ld IR | Reg Sel | Reg W | en Reg | ld A | ld B | ALUOp | en ALU | ld MA | Mem W | en Mem | Ex Sel | en Imm | (Br | Next State |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| FETCH0: | MA <- PC; A <- PC | 0 | PC | 0 | 1 | 1 | * | * | 0 | 1 | * | 0 | * | 0 | N | * |
|  | IR <- Mem | 1 | * | * | 0 | 0 | * | * | 0 | 0 | 0 | 1 | * | 0 | N | * |
|  | PC <- A+4 | 0 | PC | 1 | 1 | 0 | * | INC_A_4 | 1 | * | * | 0 | * | 0 | D | * |
| . . . |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| NOP0: | microbranch back to FETCH0 | 0 | * | * | 0 | * | * | * | 0 | * | * | 0 | * | 0 | J | FETCH0 |
| LWMM0: | MA <- R[ rs ] | * | rs | 0 | 1 | * | * | * | 0 | 1 | * | 0 | * | 0 | N | * |
|  | MA <- Mem | * | * | * | 0 | * | * | * | 0 | 1 | 0 | 1 | * | 0 | N | * |
|  | R[ rd ] <- Mem; ubranch back to fetch | * | rd | 1 | 1 | * | * | * | 0 | * | 0 | 1 | * | 0 | J | FETCH0 |

Worksheet Q1-1

Problem Q2: Dual ALU Pipeline				[33 points]

| Problem Q2.A | ALU Usage |
| --- | --- |

|  | ALU1 or ALU2? |
| --- | --- |
| add r1, r2, r3 | ALU1 |
| lw r4, 0(r1) |  |
| add r5, r4, r6 | ALU2 |
| add r7, r5, r8 | ALU2 |
| add r1, r2, r3 | ALU1 |
| lw r4, 0(r1) |  |
| add r5, r1, r6 | ALU1 |

The following timeline diagrams the execution of the instructions, with the stage where each instruction produces its result highlighted in bold, and the bypassing between instructions shown by arrows.

| add1 | IF | ID | EX1 | EX2 | WB |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| lw1 |  | IF | ID | EX1 | MEM | WB |  |  |  |  |  |
| add2 |  |  | IF | ID | EX1 | EX2 | WB |  |  |  |  |
| add3 |  |  |  | IF | ID | EX1 | EX2 | WB |  |  |  |
| add4 |  |  |  |  | IF | ID | EX1 | EX2 | WB |  |  |
| lw2 |  |  |  |  |  | IF | ID | EX1 | MEM | WB |  |
| add5 |  |  |  |  |  |  | IF | ID | EX1 | EX2 | WB |

The pipeline is initially idle, so the first add reads its operands from the register file   in ID and uses ALU1.  The second add uses the result of the lw which is not available by the end of ID; therefore the add uses ALU2, and the load data is bypassed to it at the end of EX1.  The third add uses the result of the second, so its data is not available by the end of ID; it also uses ALU2, allowing the data to be bypassed to it at the end of EX1.  The fourth add has no dependencies on the previous instructions; it reads its operands from the register file in ID and uses ALU1.  The fifth add uses the result of the fourth add.  This value is bypassed to it at the end of ID from EX2/MEM, and it uses ALU1.

| Problem Q2.B | Instruction Sequences Causing Stalls |
| --- | --- |

|  | stall? (yes/no) | explanation |
| --- | --- | --- |
| add r1, r2, r3 lw r4, 0(r1) | No | The add (in EX1) uses ALU1 and bypasses its result to the LW (in ID). |
| lw r1, 0(r2) add r3, r1, r4 lw r5, 0(r1) | No | The first LW (in EX2/MEM) bypasses its result to the add (in EX1) which will use ALU2, and also to the second LW (in ID). |
| lw r1, 0(r2) lw r3, 0(r1) | Yes | The result of the first LW (in EX1) is not available in time for the second LW (in ID), so the second LW must stall. |
| lw r1, 0(r2) sw r1, 0(r3) | No | The LW (in EX2/MEM) bypasses its result to the SW (in EX1) in time for it to store the data in EX2/MEM. |
| lw r1, 0(r2) add r3, r1, r4 sw r5, 0(r3) | Yes | The LW (in EX2/MEM) bypasses its result to the add (in EX1) which will use ALU2. But, the result of the add (in EX1) is not available in time for the SW (in ID), so the SW must stall. |
| lw r1, 0(r2) add r3, r1, r4 | No | The LW (in EX2/MEM) bypasses its result to the add (in EX1) which will use ALU2. |

Note that the base address operand for both LW and SW must be available by the end of ID, but the data operand for SW must only be available by the end of EX1.

Problem Q3: Processor Design (Short Yes/No Questions)

[10 points]

The following questions describe two variants of a processor which are otherwise identical.  In each case, circle "Yes" if the variants might generate different results from the same compiled program, and circle "No" otherwise.  You must also briefly explain your reasoning.  Ignore differences in the time each machine takes to execute the program.

| Problem Q3.A | Interlock vs. Bypassing |
| --- | --- |

No. Data dependencies are preserved with either interlocks or bypassing, so the processors always generate the same results.  Bypassing improves performance by eliminating stalls.

| Problem Q3.B | Delay Slot |
| --- | --- |

Yes. The instruction following a taken branch is executed on processor A, but killed on processor B; so, the processors can generate different results.

| Problem Q3.C | Structural Hazard |
| --- | --- |

No.  Both processors retrieve the same data values.  There is only a performance difference because processor A must stall an instruction fetch to allow a load instruction to access memory.

| Problem Q3.D | Microcode size |
| --- | --- |

No. A wide variety of possible microded machines can implement the same user-level ISA semantics and generate the same results for all programs.

| Problem Q3.E | Register Size |
| --- | --- |

Either answer, depending on assumptions about microcode & ISA changes.

No: With appropriate microcode, both machines could generate identical results for a 32-bit ISA.  Also, machine A could implement a 64-bit ISA using two 32-bit registers for each 64-bit value and carefully handling overflow conditions.

Yes:  Assuming microcode was literally unchanged, the machines would generate different results due to the different overflow properties of 32-bit and 64-bit registers.  For example, if a value is shifted left, bits are lost using 32-bit registers that are retained with 64-bit registers.

Problem Q.4: Iron Law of Processor Performance (Short Answer) 				 [8 points]

Mark whether the following modifications will cause each of the categories to increase, decrease, or whether the modification will have no effect.  Explain your reasoning to receive credit.

|  | Instructions / Program | Cycles / Instruction | Seconds / Cycle | Reasoning? |
| --- | --- | --- | --- | --- |
| Combining two pipeline stages | No effect. No change is made to the ISA, so the program remains the same. | Decrease. Fewer possible pipeline hazards between instructions. | May increase. If combined stage makes critical path longer, cycle time may have to increase. |  |
| Removing a complex instruction | May increase. If program used this instruction, the compiler will have to replace it with several simple ones | May decrease. If complex instruction took more cycles than the others, overall CPI will decrease | May decrease. Complicated hardware may be removed as well |  |
| Running the machine at a higher clock frequency | No effect. ISA is unchanged | No effect. Pipeline is unchanged | Decrease. Clock frequency increase means each cycle takes fewer seconds |  |
| Using a better compiler | Usually decrease as improved compiler will generate more concise code, but could increase if more, simpler instructions reduced hazards | May decrease as better compiler scheduling can avoid hazards from load-use delay slots, and branch delay slots. | No effect. Underlying hardware is unchanged. |  |