## Slide 1: CS 152 Computer Architecture and Engineering Lecture 4 - Pipelining
Krste Asanovic
Electrical Engineering and Computer Sciences
University of California at Berkeley
http://www.eecs.berkeley.edu/~krste
http://inst.eecs.berkeley.edu/~cs152

## Slide 2: Last time in Lecture 3
Microcoding became less attractive as gap between RAM and ROM speeds reduced
Complex instruction sets difficult to pipeline, so difficult to increase performance as gate count grew
Load-Store RISC ISAs designed for efficient pipelined implementations
  Very similar to vertical microcode
  Inspired by earlier Cray machines (more on these later)
Iron Law explains architecture design space
  Trade instructions/program, cycles/instruction, and time/cycle

## Slide 3: An Ideal Pipeline
All objects go through the same stages
No sharing of resources between any two stages
Propagation delay through all pipeline stages is equal
The scheduling of an object entering the pipeline is not affected by the objects in other stages
stage
1
stage
2
stage
3
stage
4
These conditions generally hold for industrial assembly lines, but instructions depend on each other!

## Slide 4: Pipelined RISC-V
To pipeline RISC-V:
First build RISC-V without pipelining with CPI=1
Next, add pipeline registers to reduce cycle time while maintaining CPI=1

## Slide 5: Lecture 3: Unpipelined Datapath for RISC-V
0x4
RegWriteEn
Add
Add
clk
WBSel
MemWrite
addr
wdata
rdata
Data
Memory
we
WASel
Op2Sel
ImmSel
OpCode
FuncSel
clk
clk
addr
inst
Inst.
Memory
PC
rd1
GPRs
rs1
rs2
wa
wd
rd2
we
Imm
Select
ALU
ALU
Control
1
PCSel
br
rind
jabs
pc+4
Bcomp?
Br Logic

## Slide 6: Lecture 3: Hardwired Control Table
Opcode | ImmSel | Op2Sel | FuncSel | MemWr | RFWen | WBSel | WASel | PCSel
ALU |  |  |  |  |  |  |  | 
ALUi |  |  |  |  |  |  |  | 
LW |  |  |  |  |  |  |  | 
SW |  |  |  |  |  |  |  | 
BEQtrue |  |  |  |  |  |  |  | 
BEQfalse |  |  |  |  |  |  |  | 
J |  |  |  |  |  |  |  | 
JAL |  |  |  |  |  |  |  | 
JALR |  |  |  |  |  |  |  | 
Op2Sel= Reg / Imm WBSel = ALU / Mem / PC
WASel = rd / X1 PCSel = pc+4 / br / rind / jabs
*
*
*
no
yes
rind
PC
rd
jabs
*
*
*
no
yes
PC
X1
jabs
*
*
*
no
no
*
*
pc+4
BrType12
*
*
no
no
*
*
br
BrType12
*
*
no
no
*
*
pc+4
BsType12
Imm
+
yes
no
*
*
pc+4
*
Reg
Func
no
yes
ALU
rd
IType12
Imm
Op
pc+4
no
yes
ALU
rd
pc+4
IType12
Imm
+
no
yes
Mem
rd

## Slide 7: Pipelined Datapath
Clock period can be reduced by dividing the execution of an instruction into multiple cycles
tC > max {tIM, tRF, tALU, tDM, tRW} ( = tDM probably)
However, CPI will increase unless instructions are pipelined
write
-back
phase
fetch
phase
execute
phase
decode & Reg-fetch
phase
memory
phase
addr
wdata
rdata
Data
Memory
we
ALU
Imm
Select
0x4
Add
addr
rdata
Inst.
Memory
rd1
GPRs
rs1
rs2
wa
wd
rd2
we
IR
PC

## Slide 8: “Iron Law” of Processor Performance
Instructions per program depends on source code, compiler technology, and ISA
Cycles per instructions (CPI) depends on ISA and µarchitecture
Time per cycle depends upon the µarchitecture and base technology
Time = Instructions Cycles Time
Program Program * Instruction * Cycle
Microarchitecture | CPI | cycle time
Microcoded | >1 | short
Single-cycle unpipelined | 1 | long
Pipelined | 1 | short
Lecture 2
Lecture 3
Lecture 4

## Slide 9: CPI Examples
Time
Inst 3
7 cycles
Inst 1
Inst 2
5 cycles
10 cycles
Microcoded machine
3 instructions, 22 cycles, CPI=7.33
Unpipelined machine
3 instructions, 3 cycles, CPI=1
Inst 1
Inst 2
Inst 3
Pipelined machine
3 instructions, 3 cycles, CPI=1
Inst 1
Inst 2
Inst 3
5-stage pipeline CPI≠5!!!

## Slide 10: Technology Assumptions
Thus, the following timing assumption is reasonable
A small amount of very fast memory (caches)
backed up by a large, slower memory
Fast ALU (at least for integers)
Multiported Register files (slower!)
tIM tRF tALU tDM  tRW
A 5-stage pipeline will be focus of our detailed design
- some commercial designs have over 30 pipeline stages to do an integer add!

## Slide 11: 5-Stage Pipelined Execution
time t0 t1 t2 t3 t4 t5 t6 t7 . . . .
instruction1 IF1 ID1 EX1 MA1 WB1
instruction2 IF2 ID2 EX2 MA2 WB2
instruction3 IF3 ID3 EX3 MA3 WB3
instruction4 IF4 ID4 EX4 MA4 WB4
instruction5 IF5 ID5 EX5 MA5 WB5
Write
-Back (WB)
I-Fetch (IF)
Execute (EX)
Decode, Reg. Fetch (ID)
Memory (MA)
addr
wdata
rdata
Data
Memory
we
ALU
Imm
Select
0x4
Add
addr
rdata
Inst.
Memory
rd1
GPRs
rs1
rs2
wa
wd
rd2
we
IR
PC

## Slide 12: 5-Stage Pipelined Execution Resource Usage Diagram
time t0 t1 t2 t3 t4 t5 t6 t7 . . . .
IF I1 I2 I3 I4 I5
ID I1 I2 I3 I4 I5
EX I1 I2 I3 I4 I5
MA I1 I2 I3 I4 I5
WB I1 I2 I3 I4 I5
Resources
Write
-Back (WB)
I-Fetch (IF)
Execute (EX)
Decode, Reg. Fetch (ID)
Memory (MA)
addr
wdata
rdata
Data
Memory
we
ALU
0x4
Add
addr
rdata
Inst.
Memory
rd1
GPRs
rs1
rs2
ws
wd
rd2
we
IR
PC
Imm
Select

## Slide 13: Pipelined Execution: ALU Instructions
IR
IR
IR
1
PC
A
B
Y
R
MD1
MD2
addr
inst
Inst
Memory
0x4
Add
IR
Imm
Select
ALU
rd1
GPRs
rs1
rs2
wa
wd
rd2
we
wdata
addr
wdata
rdata
Data
Memory
we
Not quite correct!
We need an Instruction Reg (IR) for each stage

## Slide 14: Pipelined RISC-V Datapath without jumps
IR
IR
IR
1
PC
A
B
Y
R
MD1
MD2
addr
inst
Inst
Memory
0x4
Add
IR
Imm
Select
ALU
rd1
GPRs
rs1
rs2
wa
wd
rd2
we
Data
Memory
wdata
addr
wdata
rdata
we
FuncSel
ImmSel
Op2Sel
WBSel
MemWrite
WASel
RegWriteEn
F
D
E
M
W
Control Points Need to Be Connected

## Slide 15: Instructions interact with each other in pipeline
An instruction in the pipeline may need a resource being used by another instruction in the pipeline  structural hazard
An instruction may depend on something produced by an earlier instruction
  Dependence may be for a data value  data hazard
  Dependence may be for the next instruction’s address  control hazard (branches, exceptions)

## Slide 16: Resolving Structural Hazards
Structural hazard occurs when two instructions need same hardware resource at same time
  Can resolve in hardware by stalling newer instruction till older instruction finished with resource
A structural hazard can always be avoided by adding more hardware to design
  E.g., if two instructions both need a port to memory at same time, could avoid hazard by adding second port to memory
Our 5-stage pipeline has no structural hazards by design
  Thanks to RISC-V ISA, which was designed for pipelining

## Slide 17: Data Hazards
...
x1 x0 + 10
x4 x1 + 17
...
x1 is stale. Oops!
x1 …
x4  x1 …
IR
IR
IR
1
PC
A
B
Y
R
MD1
MD2
addr
inst
Inst
Memory
0x4
Add
IR
Imm
Select
ALU
rd1
GPRs
rs1
rs2
wa
wd
rd2
we
wdata
addr
wdata
rdata
Data
Memory
we

## Slide 18: Resolving Data Hazards (1)
Strategy 1:
Wait for the result to be available by freezing earlier pipeline stages  interlocks

## Slide 19: Feedback to Resolve Hazards
Later stages provide dependence information to earlier stages which can stall (or kill) instructions
FB1
stage
1
stage
2
stage
3
stage
4
FB2
FB3
FB4
Controlling a pipeline in this manner works provided the instruction at stage i+1 can complete without any interference from instructions in stages 1 to i
  (otherwise deadlocks may occur)
Notes: Real designs will seldom provide full feedback nor will they be able to stop on a dime.

## Slide 20: Interlocks to resolve Data Hazards
IR
IR
IR
1
PC
A
B
Y
R
MD1
MD2
addr
inst
Inst
Memory
0x4
Add
IR
Imm
Select
ALU
rd1
GPRs
rs1
rs2
wa
wd
rd2
we
wdata
addr
wdata
rdata
Data
Memory
we
bubble
...
x1 x0 + 10
x4 x1 + 17
...
Stall Condition

## Slide 21: Stalled Stages and Pipeline Bubbles
stalled stages
  time
  t0 t1 t2 t3 t4 t5 t6 t7 . . . .
IF I1 I2 I3 I3 I3 I3 I4 I5
ID I1 I2 I2 I2 I2 I3 I4 I5
EX I1 - - - I2 I3 I4 I5
MA I1 - - - I2 I3 I4 I5
WB I1 - - - I2 I3 I4 I5
      time
      t0 t1 t2 t3 t4 t5 t6 t7 . . . .
(I1) x1 (x0) + 10 IF1 ID1 EX1 MA1 WB1
(I2) x4 (x1) + 17 IF2 ID2 ID2 ID2 ID2 EX2 MA2 WB2
(I3) IF3 IF3 IF3 IF3 ID3 EX3 MA3 WB3
(I4) IF4 ID4 EX4 MA4 WB4
(I5) IF5 ID5 EX5 MA5 WB5
Resource
Usage
-  pipeline bubble

## Slide 22: Interlock Control Logic
IR
IR
IR
1
PC
A
B
Y
R
MD1
MD2
addr
inst
Inst
Memory
0x4
Add
IR
Imm
Select
ALU
rd1
GPRs
rs1
rs2
wa
wd
rd2
we
wdata
addr
wdata
rdata
Data
Memory
we
bubble
Compare the source registers of the instruction in the decode stage with the destination register of the uncommitted instructions.
stall
Cstall
wa
rs2
rs1
?

## Slide 23: Interlock Control Logic ignoring jumps & branches
Cdest
Should we always stall if an rs field matches some rd?
IR
IR
IR
PC
A
B
Y
R
MD1
MD2
addr
inst
Inst
Memory
0x4
Add
IR
ALU
rd1
GPRs
rs1
rs2
wa
wd
rd2
we
wdata
addr
wdata
rdata
Data
Memory
we
1
bubble
stall
Cstall
wa
rs1
rs2
?
we
re1
re2
Cre
wa
we
wa
Cdest
Cdest
we
not every instruction writes a register we
not every instruction reads a register re
Imm
Select

## Slide 24: Source & Destination Registers
source(s) destination
ALU rd  rs1 func10 rs2 rs1, rs2 rd
ALUI rd  rs1 op imm rs1 rd
LW rd M [rs1 + imm] rs1 rd
SW M [rs1 + imm]  rs2 rs1, rs2 -
Bcond rs1,rs2 rs1, rs2 -
true: PC  PC + imm
false: PC  PC + 4
J PC  PC + imm - -
JAL x1  PC, PC  PC + imm - x1
JALR rd  PC, PC  rs1 + imm rs1 rd
ALUI/LW/JALR
opcode
func3
Imm[11:0]
rd
rs1
func3
opcode
func10
rd
rs1
rs2
ALU
opcode
Imm[6:0]
Imm[11:7]
rs1
rs2
SW/Bcond
opcode
Jump offset[24:0]

## Slide 25: Deriving the Stall Signal
Cdest
  ws = Case opcode
    JAL X1
    else rd
  we = Case opcode
    ALU, ALUi, LW,JALR (ws  0)
  JAL on
    ... off
Cre
  re1 = Case opcode
    ALU, ALUi,
    on
    off
  re2 = Case opcode
    on
    off
LW, SW, Bcond,
JALR
J, JAL
ALU, SW,Bcond
...
Cstall stall = ((rs1D =wsE).weE +
(rs1D =wsM).weM +
(rs1D =wsW).weW) . re1D +
((rs2D =wsE).weE +
(rs2D =wsM).weM +
(rs2D =wsW).weW) . re2D
This is not
the full story !

## Slide 26: Hazards due to Loads & Stores
...
M[x1+7]  x2
x4  M[x3+5]
...
IR
IR
IR
1
PC
A
B
Y
R
MD1
MD2
addr
inst
Inst
Memory
0x4
Add
IR
Imm
Select
ALU
rd1
GPRs
rs1
rs2
wa
wd
rd2
we
wdata
addr
wdata
rdata
Data
Memory
we
bubble
Stall Condition
Is there any possible data hazard
in this instruction sequence?
What if
x1+7 = x3+5 ?

## Slide 27: Load & Store Hazards
However, the hazard is avoided because our memory system completes writes in one cycle !
Load/Store hazards are sometimes resolved in the pipeline and sometimes in the memory system itself.
More on this later in the course.
...
M[x1+7]  x2
x4  M[x3+5]
...
x1+7 = x3+5  data hazard

## Slide 28: CS152 Administrivia
Quiz 1 on Feb 19 will cover PS1, Lab1, lectures 1-5, and associated readings.

## Slide 29: Resolving Data Hazards (2)
Strategy 2:
Route data as soon as possible after it is calculated to the earlier pipeline stage  bypass

## Slide 30: Bypassing
Each stall or kill introduces a bubble in the pipeline
         CPI > 1
  time t0 t1 t2 t3 t4 t5 t6 t7 . . . .
(I1) x1 x0 + 10 IF1 ID1 EX1 MA1 WB1
(I2) x4 x1 + 17 IF2 ID2 ID2 ID2 ID2 EX2 MA2 WB2
(I3) IF3 IF3 IF3 IF3 ID3 EX3 MA3
(I4) stalled stages IF4 ID4 EX4
(I5) IF5 ID5
time t0 t1 t2 t3 t4 t5 t6 t7 . . . .
(I1) x1 x0 + 10 IF1 ID1 EX1 MA1 WB1
(I2) x4  x1 + 17 IF2 ID2 EX2 MA2 WB2
(I3) IF3 ID3 EX3 MA3 WB3
(I4) IF4 ID4 EX4 MA4 WB4
(I5) IF5 ID5 EX5 MA5 WB5
A new datapath, i.e., a bypass, can get the data from
the output of the ALU to its input

## Slide 31: Adding a Bypass
ASrc
...
(I1) x1 x0 + 10
(I2) x4 x1 + 17
x4  x1...
x1 ...
IR
IR
IR
PC
A
B
Y
R
MD1
MD2
addr
inst
Inst
Memory
0x4
Add
IR
Imm
Select
ALU
rd1
GPRs
rs1
rs2
wa
wd
rd2
we
wdata
addr
wdata
rdata
Data
Memory
we
1
bubble
stall
D
E
M
W
When does this bypass help?
x1 M[x0 + 10]
x4 x1 + 17
JAL 500
x4 x1 + 17
yes
no
no

## Slide 32: The Bypass Signal Deriving it from the Stall Signal
ASrc = (rs1D=wsE).weE.re1D
we = Case opcode
  ALU, ALUi, LW, JALR (ws  0)
JAL on
  ... off
No because only ALU and ALUi instructions can benefit from this bypass
Is this correct?
Split weE into two components: we-bypass, we-stall
stall = ( ((rs1D =wsE).weE + (rs1D =wsM).weM + (rs1D =wsW).weW).re1D
+((rs2D =wsE).weE + (rs2D =wsM).weM + (rs2D =wsW).weW).re2D )
ws = Case opcode
  JAL X1
  else rd
Notes: We can’t bypass on memory or JAL* instructions.

## Slide 33: Bypass and Stall Signals
we-bypassE = Case opcodeE
  ALU, ALUi  (ws  0)
... off
ASrc = (rs1D =wsE).we-bypassE . re1D
Split weE into two components: we-bypass, we-stall
stall = ((rs1D =wsE).we-stallE +
(rs1D=wsM).weM + (rs1D=wsW).weW). re1D
+((rs2D = wsE).weE + (rs2D = wsM).weM + (rs2D = wsW).weW). re2D
we-stallE = Case opcodeE
  LW, JALR  (ws  0)
JAL on
  ... off

## Slide 34: Fully Bypassed Datapath
ASrc
IR
IR
IR
PC
A
B
Y
R
MD1
MD2
addr
inst
Inst
Memory
0x4
Add
IR
ALU
Imm
Select
rd1
GPRs
rs1
rs2
wa
wd
rd2
we
wdata
addr
wdata
rdata
Data
Memory
we
1
bubble
stall
D
E
M
W
PC for JAL, ...
BSrc
Is there still
a need for the
stall signal ?
stall = (rs1D=wsE). (opcodeE=LWE).(wsE0 ).re1D
+ (rs2D=wsE). (opcodeE=LWE).(wsE0 ).re2D

## Slide 35: Pipeline CPI Examples
Time
3 instructions finish in 3 cycles
CPI = 3/3 =1
Inst 1
Inst 2
Inst 3
3 instructions finish in 4 cycles
CPI = 4/3 = 1.33
Inst 1
Inst 2
Inst 3
Bubble
Inst 1
Inst 2
Inst 3
Bubble 1
Bubble 2
Measure from when first instruction finishes to when last instruction in sequence finishes.
3 instructions finish in 5cycles
CPI = 5/3 = 1.67
Inst 3

## Slide 36: Resolving Data Hazards (3)
Strategy 3: Speculate on the dependence!
Two cases:
Guessed correctly  do nothing
Guessed incorrectly  kill and restart
…. We’ll later see examples of this approach in more complex processors.

## Slide 37: Speculation that load value=zero
ASrc
IR
IR
IR
PC
A
B
Y
R
MD1
MD2
addr
inst
Inst
Memory
0x4
Add
IR
ALU
Imm
Select
rd1
GPRs
rs1
rs2
wa
wd
rd2
we
wdata
addr
wdata
rdata
Data
Memory
we
1
bubble
stall
D
E
M
W
PC for JAL, ...
BSrc
Guess_zero
Guess_zero= (rs1D=wsE). (opcodeE=LWE).(wsE0 ).re1D
0
Also need to add circuitry to remember that this was a guess and flush pipeline if load not zero!
Not worth doing in practice – why?

## Slide 38: Control Hazards
What do we need to calculate next PC?
For Jumps
  Opcode, PC and offset
For Jump Register
  Opcode, Register value, and PC
For Conditional Branches
  Opcode, Register (for condition), PC and offset
For all other instructions
  Opcode and PC ( and have to know it’s not one of above )

## Slide 39: PC Calculation Bubbles
      time
      t0 t1 t2 t3 t4 t5 t6 t7 . . . .
(I1) x1 x0 + 10 IF1 ID1 EX1 MA1 WB1
(I2) x3 x2 + 17 IF2 IF2 ID2 EX2 MA2 WB2
(I3) IF3 IF3 ID3 EX3 MA3 WB3
(I4) IF4 IF4 ID4 EX4 MA4 WB4
  time
  t0 t1 t2 t3 t4 t5 t6 t7 . . . .
IF I1 - I2 - I3 - I4
ID I1 - I2 - I3 - I4
EX I1 - I2 - I3 - I4
MA I1 - I2 - I3 - I4
WB I1 - I2 - I3 - I4
Resource
Usage
-  pipeline bubble

## Slide 40: Speculate next address is PC+4
I1 096 ADD
I2 100 J 304
I3 104 ADD
I4 304 ADD
kill
A jump instruction kills (not stalls)
the following instruction
stall
How?
I2
I1
104
IR
IR
PC
addr
inst
Inst
Memory
0x4
Add
bubble
IR
E
M
Add
Jump?
PCSrc (pc+4 / jabs / rind/ br)

## Slide 41: Pipelining Jumps
I1 096 ADD
I2 100 J 304
I3 104 ADD
I4 304 ADD
kill
I2
I1
104
stall
IR
IR
PC
addr
inst
Inst
Memory
0x4
Add
bubble
IR
E
M
Add
Jump?
PCSrc (pc+4 / jabs / rind/ br)
IRSrcD = Case opcodeD
  J, JAL bubble
  ... IM
To kill a fetched instruction -- Insert a mux before IR
Any interaction between stall and jump?
bubble
IRSrcD
I2
I1
304
bubble
Notes: Kill takes precedence over stall.

## Slide 42: Jump Pipeline Diagrams
  time
  t0 t1 t2 t3 t4 t5 t6 t7 . . . .
IF I1 I2 I3 I4 I5
ID I1 I2 - I4 I5
EX I1 I2 - I4 I5
MA I1 I2 - I4 I5
WB I1 I2 - I4 I5
      time
      t0 t1 t2 t3 t4 t5 t6 t7 . . . .
(I1) 096: ADD IF1 ID1 EX1 MA1 WB1
(I2) 100: J 304 IF2 ID2 EX2 MA2 WB2
(I3) 104: ADD IF3 - - - -
(I4) 304: ADD IF4 ID4 EX4 MA4 WB4
Resource
Usage
-  pipeline bubble

## Slide 43: Pipelining Conditional Branches
I1 096 ADD
I2 100 BEQ x1,x2 +200
I3 104 ADD
I4 304 ADD
BEQ?
I2
I1
104
stall
IR
IR
PC
addr
inst
Inst
Memory
0x4
Add
bubble
IR
E
M
Add
PCSrc (pc+4 / jabs / rind / br)
bubble
IRSrcD
Branch condition is not known until the execute stage
  what action should be taken in the
  decode stage ?
A
Y
ALU
Taken?

## Slide 44: Pipelining Conditional Branches
I1 096 ADD
I2 100 BEQ x1,x2 +200
I3 104 ADD
I4 304 ADD
stall
IR
IR
PC
addr
inst
Inst
Memory
0x4
Add
bubble
IR
E
M
Add
PCSrc (pc+4 / jabs / rind / br)
bubble
IRSrcD
A
Y
ALU
Taken?
If the branch is taken
  - kill the two following instructions
  - the instruction at the decode stage is not valid  stall signal is not valid
I2
I1
108
I3
Bcond?
?

## Slide 45: Pipelining Conditional Branches
I1: 096 ADD
I2: 100 BEQ x1,x2 +200
I3: 104 ADD
I4: 304 ADD
stall
IR
IR
PC
addr
inst
Inst
Memory
0x4
Add
bubble
IR
E
M
PCSrc (pc+4/jabs/rind/br)
bubble
A
Y
ALU
Taken?
I2
I1
108
I3
Bcond?
Jump?
IRSrcD
IRSrcE
If the branch is taken
  - kill the two following instructions
  - the instruction at the decode stage is not valid  stall signal is not valid
Add
PC

## Slide 46: Branch Pipeline Diagrams (resolved in execute stage)
  time
  t0 t1 t2 t3 t4 t5 t6 t7 . . . .
IF I1 I2 I3 I4 I5
ID I1 I2 I3 - I5
EX I1 I2 - - I5
MA I1 I2 - - I5
WB I1 I2 - - I5
      time
      t0 t1 t2 t3 t4 t5 t6 t7 . . . .
(I1) 096: ADD IF1 ID1 EX1 MA1 WB1
(I2) 100: BEQ +200 IF2 ID2 EX2 MA2 WB2
(I3) 104: ADD IF3 ID3 - - -
(I4) 108: IF4 - - - -
(I5) 304: ADD IF5 ID5 EX5 MA5 WB5
Resource
Usage
-  pipeline bubble

## Slide 47: Acknowledgements
These slides contain material developed and copyright by:
  Arvind (MIT)
  Krste Asanovic (MIT/UCB)
  Joel Emer (Intel/MIT)
  James Hoe (CMU)
  John Kubiatowicz (UCB)
  David Patterson (UCB)
MIT material derived from course 6.823
UCB material derived from course CS252