## Slide 1: CS 152 Computer Architecture and Engineering Lecture 12 - Advanced Out-of-Order Superscalars
Dr. George Michelogiannakis
EECS, University of California at Berkeley
CRD, Lawrence Berkeley National Laboratory
http://inst.eecs.berkeley.edu/~cs152

## Slide 2: Last time in Lecture 11
Register renaming removes WAR, WAW hazards
In-order fetch/decode, out-of-order execute, in-order commit gives high performance and precise exceptions
Need to rapidly recover on branch mispredictions
Unified physical register file machines remove data values from ROB
  All values only read and written during execution
  Only register tags held in ROB

## Slide 3: Question of the Day
How many in-order cores do you think take up the same area as an out-of-order core?

## Slide 4
Reminder
Fetch
Decode & Rename
Reorder Buffer
PC
Commit
Branch
Unit
ALU
MEM
Store Buffer
D$
Execute
In-Order
In-Order
Out-of-Order
Physical Reg. File

## Slide 5: Separate Pending Instruction Window from ROB
Reorder buffer used to hold exception information for commit.
The instruction window holds instructions that have been decoded and renamed but not issued into execution. Has register tags and presence bits, and pointer to ROB entry.
op
p1
PR1
p2
PR2
PRd
use
ex
ROB#
ROB is usually several times larger than instruction window – why?
Rd
LPRd
PC
Except?
Ptr2 next to commit
Ptr1 next available
Done?
Instructions that committed are not in the instruction window any more

## Slide 6: Reorder Buffer Holds Active Instructions (Decoded but not Committed)
…
ld x1, (x3)
add x3, x1, x2
sub x6, x7, x9
add x3, x3, x6
ld x6, (x1)
add x6, x6, x3
sd x6, (x1)
ld x6, (x1)
…
(Older instructions)
(Newer instructions)
Cycle t
…
ld x1, (x3)
add x3, x1, x2
sub x6, x7, x9
add x3, x3, x6
ld x6, (x1)
add x6, x6, x3
sd x6, (x1)
ld x6, (x1)
…
Commit
Fetch
Cycle t + 1
Execute

## Slide 7: Issue Timing
i1 | Add R1,R1,#1 | Issue1 | Execute1 |  | 
i2 | Sub R1,R1,#1 |  |  | Issue2 | Execute2
How can we issue earlier?
Using knowledge of execution latency (bypass)
What makes this schedule fail?
If execution latency wasn’t as expected
i1 | Add R1,R1,#1 | Issue1 | Execute1 |  | 
i2 | Sub R1,R1,#1 |  | Issue2 | Execute2 | 

## Slide 8: Issue Queue with latency prediction
Fixed latency: latency included in queue entry (‘bypassed’)
Predicted latency: latency included in queue entry (speculated)
Variable latency: wait for completion signal (stall)
Issue Queue (Reorder buffer)
ptr2
next to
commit
ptr1
next
available
Inst# use exec op p1 lat1 src1 p2 lat2 src2 dest
BEQZ
Speculative Instructions

## Slide 9: Improving Instruction Fetch
Performance of speculative out-of-order machines often limited by instruction fetch bandwidth
  speculative execution can fetch 2-3x more instructions than are committed
  mispredict penalties dominated by time to refill instruction window
  taken branches are particularly troublesome

## Slide 10: Increasing Taken Branch Bandwidth (Alpha 21264 I-Cache)
Fold 2-way tags and BTB into predicted next block
Take tag checks, inst. decode, branch predict out of loop
Raw RAM speed on critical loop (1 cycle at ~1 GHz)
2-bit hysteresis counter per block prevents overtraining
Cached Instructions
Line Predict
Way Predict
Tag
Way
0
Tag
Way
1
=?
=?
fast fetch path
PC Generation
PC
Branch Prediction
Instruction Decode
Validity Checks
4 insts
Hit/Miss/Way

## Slide 11: Tournament Branch Predictor (Alpha 21264)
Choice predictor learns whether best to use local or global branch history in predicting next branch (best in each case)
Global history is speculatively updated but restored on mispredict
Claim 90-100% success on range of applications
Local history table (1,024x10b)
PC
Local prediction (1,024x3b)
Global Prediction (4,096x2b)
Choice Prediction (4,096x2b)
Global History (12b)
Prediction

## Slide 12: Taken Branch Limit
Integer codes have a taken branch every 6-9 instructions
To avoid fetch bottleneck, must execute multiple taken branches per cycle when increasing performance
This implies:
  predicting multiple branches per cycle
  fetching multiple non-contiguous blocks per cycle

## Slide 13: Branch Address Cache (Yeh, Marr, Patt)
PC
k
Entry PC
=
match
Valid
valid
predicted
target#1
target #1
len
len#1
predicted
target#2
target #2
Extend BTB to return multiple branch predictions per cycle

## Slide 14: Fetching Multiple Basic Blocks
Requires either
  multiported cache: expensive
  interleaving: bank conflicts will occur
Merging multiple blocks to feed to decoders adds latency increasing mispredict penalty and reducing branch throughput

## Slide 15: Trace Cache
Key Idea: Pack multiple non-contiguous basic blocks into one contiguous trace cache line
BR
BR
BR
Single fetch brings in multiple basic blocks
Trace cache indexed by start address and next n branch predictions
Used in Intel Pentium-4 processor to hold decoded uops
BR
BR
BR

## Slide 16: Superscalar Register Renaming
During decode, instructions allocated new physical destination register
Source operands renamed to physical register with newest value
Execution unit only sees physical register numbers
Rename Table
Op
Src1
Src2
Dest
Op
Src1
Src2
Dest
Register Free List
Op
PSrc1
PSrc2
PDest
Op
PSrc1
PSrc2
PDest
Update
Mapping
Does this work?
Inst 1
Inst 2
Read Addresses
Read Data
Write Ports
Issue multiple instructions per cycle

## Slide 17: Superscalar Register Renaming
Rename Table
Op
Src1
Src2
Dest
Op
Src1
Src2
Dest
Register Free List
Op
PSrc1
PSrc2
PDest
Op
PSrc1
PSrc2
PDest
Update
Mapping
Inst 1
Inst 2
Read Addresses
Read Data
Write Ports
=?
=?
Must check for RAW hazards between instructions issuing in same cycle. Can be done in parallel with rename lookup.
MIPS R10K renames 4 serially-RAW-dependent insts/cycle
Notes: Doesn’t show that update reflects last dest. (jse)

## Slide 18: Speculative Loads / Stores
Just like register updates, stores should not modify
the memory until after the instruction is committed
- A speculative store buffer is a structure introduced to hold speculative store data.

## Slide 19: Speculative Store Buffer
Just like register updates, stores should not modify the memory until after the instruction is committed. A speculative store buffer is a structure introduced to hold speculative store data.
During decode, store buffer slot allocated in program order
Stores split into “store address” and “store data” micro-operations
“Store address” execute writes tag
“Store data” execute writes data
Store commits when oldest instruction and both address and data available:
  clear speculative bit and eventually move data to cache
On store abort:
  clear valid bit
Data
Tags
Store Commit Path
Speculative Store Buffer
L1 Data Cache
Tag
Data
S
V
Tag
Data
S
V
Tag
Data
S
V
Tag
Data
S
V
Tag
Data
S
V
Tag
Data
S
V
Store Address
Store Data

## Slide 20: Load bypass from speculative store buffer
If data in both store buffer and cache, which should we use?
  Speculative store buffer
If same address in store buffer twice, which should we use?
  Youngest store older than load
Data
Load Address
Tags
Speculative Store Buffer
L1 Data Cache
Load Data
Tag
Data
S
V
Tag
Data
S
V
Tag
Data
S
V
Tag
Data
S
V
Tag
Data
S
V
Tag
Data
S
V

## Slide 21: Memory Dependencies
sd x1, (x2)
ld x3, (x4)
When can we execute the load?

## Slide 22: In-Order Memory Queue
Execute all loads and stores in program order
=> Load and store cannot leave ROB for execution until all previous loads and stores have completed execution
Can still execute loads and stores speculatively, and out-of-order with respect to other instructions
Need a structure to handle memory ordering…

## Slide 23: Conservative O-o-O Load Execution
sd x1, (x2)
ld x3, (x4)
Can execute load before store, if addresses known and x4 != x2
Each load address compared with addresses of all previous uncommitted stores
  can use partial conservative check i.e., bottom 12 bits of address, to save hardware
Don’t execute load if any previous store address not known
(MIPS R10K, 16-entry address queue)

## Slide 24: Address Speculation
Guess that x4 != x2
Execute load before store address known
Need to hold all completed but uncommitted load/store addresses in program order
If subsequently find x4==x2, squash load and all following instructions
=> Large penalty for inaccurate address speculation
sd x1, (x2)
ld x3, (x4)

## Slide 25: Memory Dependence Prediction (Alpha 21264)
sd x1, (x2)
ld x3, (x4)
Guess that x4 != x2 and execute load before store
If later find x4==x2, squash load and all following instructions, but mark load instruction as store-wait
Subsequent executions of the same load instruction will wait for all previous stores to complete
Periodically clear store-wait bits

## Slide 26
Fetch
Decode & Rename
Reorder Buffer
PC
Branch
Prediction
Commit
Datapath: Branch Prediction and Speculative Execution
Branch
Resolution
Branch
Unit
ALU
Reg. File
MEM
Store Buffer
D$
Execute
kill
kill
kill
kill

## Slide 27: Instruction Flow in Unified Physical Register File Pipeline
Fetch
  Get instruction bits from current guess at PC, place in fetch buffer
  Update PC using sequential address or branch predictor (BTB)
Decode/Rename
  Take instruction from fetch buffer
  Allocate resources to execute instruction:
    Destination physical register, if instruction writes a register
    Entry in reorder buffer to provide in-order commit
    Entry in issue window to wait for execution
    Entry in memory buffer, if load or store
  Decode will stall if resources not available
  Rename source and destination registers
  Check source registers for readiness
  Insert instruction into issue window+reorder buffer+memory buffer

## Slide 28: Memory Instructions
Split store instruction into two pieces during decode:
  Address calculation, store-address
  Data movement, store-data
Allocate space in program order in memory buffers during decode
Store instructions:
  Store-address calculates address and places in store buffer
  Store-data copies store value into store buffer
  Store-address and store-data execute independently out of issue window
  Stores only commit to data cache at commit point
Load instructions:
  Load address calculation executes from window
  Load with completed effective address searches memory buffer
  Load instruction may have to wait in memory buffer for earlier store ops to resolve

## Slide 29: Issue Stage
Writebacks from completion phase “wakeup” some instructions by causing their source operands to become ready in issue window
  In more speculative machines, might wake up waiting loads in memory buffer
Need to “select” some instructions for issue
  Arbiter picks a subset of ready instructions for execution
  Example policies: random, lower-first, oldest-first, critical-first
Instructions read out from issue window and sent to execution

## Slide 30: Execute Stage
Read operands from physical register file and/or bypass network from other functional units
Execute on functional unit
Write result value to physical register file (or store buffer if store)
Produce exception status, write to reorder buffer
Free slot in instruction window

## Slide 31: Commit Stage
Read completed instructions in-order from reorder buffer
  (may need to wait for next oldest instruction to complete)
If exception raised
  flush pipeline, jump to exception handler
Otherwise, release resources:
  Free physical register used by last writer to same architectural register
  Free reorder buffer slot
  Free memory reorder buffer slot

## Slide 32: Question of the Day
How many in-order cores do you think take up the same area as an out-of-order core?

## Slide 33: How Many In-Order In The Same Area?

## Slide 34: Performance?

## Slide 35: Acknowledgements
These slides contain material developed and copyright by:
  Arvind (MIT)
  Krste Asanovic (MIT/UCB)
  Joel Emer (Intel/MIT)
  James Hoe (CMU)
  John Kubiatowicz (UCB)
  David Patterson (UCB)
MIT material derived from course 6.823
UCB material derived from course CS252