## Slide 1: CS 152 Computer Architecture and Engineering Lecture 15: Vector Computers
Dr. George Michelogiannakis
EECS, University of California at Berkeley
CRD, Lawrence Berkeley National Laboratory
http://inst.eecs.berkeley.edu/~cs152

## Slide 2: Last Time Lecture 14: Multithreading
Time (processor cycle)
Superscalar
Fine-Grained
Coarse-Grained
Multiprocessing
Simultaneous
Multithreading
Thread 1
Thread 2
Thread 3
Thread 4
Thread 5
Idle slot

## Slide 3: Question of the Day
Can Vector and VLIW combine?

## Slide 4: Supercomputers
Definition of a supercomputer:
Fastest machine in world at given task
  Performs at or near the currently highest operational rate for computers
A device to turn a compute-bound problem into an I/O bound problem
Any machine costing $30M+
Any machine designed by Seymour Cray
CDC6600 (Cray, 1964) regarded as first supercomputer

## Slide 5: CDC 6600 Seymour Cray, 1963
A fast pipelined machine with 60-bit words
  128 Kword main memory capacity, 32 banks
Ten functional units (parallel, unpipelined)
  Floating Point: adder, 2 multipliers, divider
  Integer: adder, 2 incrementers, ...
Hardwired control (no microcoding)
Scoreboard for dynamic scheduling of instructions
Ten Peripheral Processors for Input/Output
  a fast multi-threaded 12-bit integer ALU
Very fast clock, 10 MHz (FP add in 4 clocks)
>400,000 transistors, 750 sq. ft., 5 tons, 150 kW, novel freon-based technology for cooling
Fastest machine in world for 5 years (until 7600)
  over 100 sold ($7-10M each)

## Slide 6: IBM Memo on CDC6600
Thomas Watson Jr., IBM CEO, August 1963:
  “Last week, Control Data ... announced the 6600 system. I understand that in the laboratory developing the system there are only 34 people including the janitor. Of these, 14 are engineers and 4 are programmers... Contrasting this modest effort with our vast development activities, I fail to understand why we have lost our industry leadership position by letting someone else offer the world's most powerful computer.”
To which Cray replied: “It seems like Mr. Watson has answered his own question.”

## Slide 7: Top 500 Systems
LINPACK & LAPACK: Software libraries for performing linear algebra

## Slide 8: Oak Ridge Titan
560,640 cores
LinkPack performance 17,590 TFlop/s
Theoretical peak 27,112.5 TFlop/s
8,209.00 kW
710,144 GB
Opteron 6274 16C 2.2GHz

## Slide 9: NERSC (LBNL) Cori
Cray XC40 supercomputer
Theoretical Peak performance 1.92 Petaflops/sec
1,630 computes nodes, 52,160 cores in total
Cray Aries high-speed interconnect with Dragonfly topology as on Edison (0.25 μs to 3.7 μs MPI latency, ~8GB/sec MPI bandwidth)
Aggregate memory: 203 TB
Scratch storage capacity: 30 PB

## Slide 10: CDC 6600: A Load/Store Architecture
Separate instructions to manipulate three types of reg.
      8 60-bit data registers (X)
      8 18-bit address registers (A)
      8 18-bit index registers (B)
All arithmetic and logic instructions are reg-to-reg
Only Load and Store instructions refer to memory!
Touching address registers 1 to 5 initiates a load
6 to 7 initiates a store
        - very useful for vector operations
opcode i j k Ri  (Rj) op (Rk)
opcode i j disp Ri M[(Rj) + disp]
6
3
3
3
6
3
3
18

## Slide 11: CDC 6600: Datapath
Address Regs Index Regs
8 x 18-bit 8 x 18-bit
Operand Regs
8 x 60-bit
Inst. Stack
8 x 60-bit
IR
10 Functional
Units
Central
Memory
128K words,
32 banks,
1µs cycle
result
addr
result
operand
operand
addr

## Slide 12: CDC6600 ISA designed to simplify high-performance implementation
Use of three-address, register-register ALU instructions simplifies pipelined implementation
  No implicit dependencies between inputs and outputs
Decoupling setting of address register (Ar) from retrieving value from data register (Xr) simplifies providing multiple outstanding memory accesses
  Software can schedule load of address register before use of value
  Can interleave independent instructions inbetween
CDC6600 has multiple parallel but unpipelined functional units
  E.g., 2 separate multipliers
Follow-on machine CDC7600 used pipelined functional units
  Foreshadows later RISC designs

## Slide 13: CDC6600: Vector Addition
    B0 <- - n
loop: JZE B0, exit
    A0 <- B0 + a0 load X0
    A1 <- B0 + b0 load X1
    X6 <- X0 + X1
    A6 <- B0 + c0 store X6
    B0 <- B0 + 1
    jump loop
Ai = address register
Bi = index register
Xi = data register

## Slide 14: Supercomputer Applications
Typical application areas
  Military research (nuclear weapons, cryptography)
  Scientific research
  Weather forecasting
  Oil exploration
  Industrial design (car crash simulation)
  Bioinformatics
  Cryptography
All involve huge computations on large data sets
In 70s-80s, Supercomputer  Vector Machine

## Slide 15: VLIW vs Vector
VLIW takes advantage of instruction level parallelism (ILP) by specifying instructions to execute in parallel
Vector architectures perform the same operation on multiple data elements
  Data-level parallelism
+
+
+
+
+
+
[0]
[1]
[VLR-1]
Vector Arithmetic Instructions
ADDV v3, v1, v2
v3
v2
v1
Int Op 2
Mem Op 1
Mem Op 2
FP Op 1
FP Op 2
Int Op 1

## Slide 16: Vector Programming Model
+
+
+
+
+
+
[0]
[1]
[VLR-1]
Vector Arithmetic Instructions
ADDV v3, v1, v2
v3
v2
v1
Scalar Registers
r0
r15
Vector Registers
v0
v15
[0]
[1]
[2]
[VLRMAX-1]
VLR
Vector Length Register
v1
Vector Load and Store Instructions
LV v1, r1, r2
Base, r1
Stride, r2
Memory
Vector Register

## Slide 17: Control Information
VLR limits the highest vector element to be processed by a vector instruction
  VLR is loaded prior to executing the vector instruction with a special instruction
Stride for load/stores:
  Vectors may not be adjacent in memory addresses
  E.g., different dimensions of a matrix
  Stride can be specified as part of the load/store

## Slide 18: Vector Code Example
# Scalar Code
LI R4, 64
loop:
L.D F0, 0(R1)
L.D F2, 0(R2)
ADD.D F4, F2, F0
S.D F4, 0(R3)
DADDIU R1, 8
DADDIU R2, 8
DADDIU R3, 8
DSUBIU R4, 1
BNEZ R4, loop
# Vector Code
LI VLR, 64
LV V1, R1
LV V2, R2
ADDV.D V3, V1, V2
SV V3, R3
# C code
for (i=0; i<64; i++)
C[i] = A[i] + B[i];

## Slide 19: Flynn’s Taxonomy
Single instruction, single data (SISD)
  E.g., our in-order processor
Single instruction, multiple data (SIMD)
  Multiple processing elements, same operation, different data
  Vector
  Multiple processing units execute the same instruction on different data in a lockstep. Either all complete or none do. Therefore, all units have to execute the same instruction at a given time
Multiple instruction, multiple data (MIMD)
  Multiple autonomous processors executing different instructions on different data
  Most common and general parallel machine
Multiple instruction, single data (MISD)
  Why would anyone do this?
Notes: MISD: Not really existant, but maybe for redundancy.

## Slide 20: More Categories
Single program, multiple data (SPMD)
  Multiple autonomous processors execute the program at independent points
  Difference with SIMD: SIMD imposes a lockstep
  Programs at SPMD can be at independent points
  SPMD can run on general purpose processors
  Most common method for parallel computing
Multiple program, multiple data (MPMD)
  Multiple autonomous processors simultaneously operating at least 2 independent programs

## Slide 21: Vector Supercomputers
Epitomy: Cray-1, 1976
Scalar Unit
  Load/Store Architecture
Vector Extension
  Vector Registers
  Vector Instructions
Implementation
  Hardwired Control
  Highly Pipelined Functional Units
  Interleaved Memory System
  No Data Caches
  No Virtual Memory

## Slide 22: Cray-1 (1976)
Single Port
Memory
16 banks of 64-bit words
+
8-bit SECDED
80MW/sec data load/store
320MW/sec instruction
buffer refill
4 Instruction Buffers
64-bitx16
NIP
LIP
CIP
(A0)
( (Ah) + j k m )
64
T Regs
(A0)
( (Ah) + j k m )
64
B Regs
S0
S1
S2
S3
S4
S5
S6
S7
A0
A1
A2
A3
A4
A5
A6
A7
Si
Tjk
Ai
Bjk
FP Add
FP Mul
FP Recip
Int Add
Int Logic
Int Shift
Pop Cnt
Sj
Si
Sk
Addr Add
Addr Mul
Aj
Ai
Ak
memory bank cycle 50 ns processor cycle 12.5 ns (80MHz)
V0
V1
V2
V3
V4
V5
V6
V7
Vk
Vj
Vi
V. Mask
V. Length
64 Element Vector Registers

## Slide 23: Vector Instruction Set Advantages
Compact
  one short instruction encodes N operations
Expressive, tells hardware that these N operations:
  are independent
  use the same functional unit
  access disjoint registers
  access registers in same pattern as previous instructions
  access a contiguous block of memory (unit-stride load/store)
  access memory in a known pattern (strided load/store)
Scalable
  can run same code on more parallel pipelines (lanes)

## Slide 24: Vector Arithmetic Execution
Use deep pipeline (=> fast clock) to execute element operations
Simplifies control of deep pipeline because elements in vector are independent (=> no hazards!)
V1
V2
V3
V3 <- v1 * v2
Six stage multiply pipeline

## Slide 25: Vector Instruction Execution
ADDV C,A,B
C[1]
C[2]
C[0]
A[3]
B[3]
A[4]
B[4]
A[5]
B[5]
A[6]
B[6]
Execution using one pipelined functional unit
C[4]
C[8]
C[0]
A[12]
B[12]
A[16]
B[16]
A[20]
B[20]
A[24]
B[24]
C[5]
C[9]
C[1]
A[13]
B[13]
A[17]
B[17]
A[21]
B[21]
A[25]
B[25]
C[6]
C[10]
C[2]
A[14]
B[14]
A[18]
B[18]
A[22]
B[22]
A[26]
B[26]
C[7]
C[11]
C[3]
A[15]
B[15]
A[19]
B[19]
A[23]
B[23]
A[27]
B[27]
Execution using four pipelined functional units

## Slide 26: How Do Vector Architectures Affect Memory?

## Slide 27: Interleaved Vector Memory System
0
1
2
3
4
5
6
7
8
9
A
B
C
D
E
F
+
Base
Stride
Vector Registers
Memory Banks
Address Generator
Cray-1, 16 banks, 4 cycle bank busy time, 12 cycle latency
  Bank busy time: Time before bank ready to accept next request

## Slide 28: Vector Unit Structure
Lane
Functional Unit
Vector
Registers
Memory Subsystem
Elements 0, 4, 8, …
Elements 1, 5, 9, …
Elements 2, 6, 10, …
Elements 3, 7, 11, …

## Slide 29: T0 Vector Microprocessor (UCB/ICSI, 1995)
Lane
Vector register elements striped over lanes
[0]
[8]
[16]
[24]
[1]
[9]
[17]
[25]
[2]
[10]
[18]
[26]
[3]
[11]
[19]
[27]
[4]
[12]
[20]
[28]
[5]
[13]
[21]
[29]
[6]
[14]
[22]
[30]
[7]
[15]
[23]
[31]

## Slide 30: Vector Instruction Parallelism
Can overlap execution of multiple vector instructions
  example machine has 32 elements per vector register and 8 lanes
load
load
mul
mul
add
add
Load Unit
Multiply Unit
Add Unit
time
Instruction issue
Complete 24 operations/cycle while issuing 1 short instruction/cycle

## Slide 31: Vector Chaining
Vector version of register bypassing
  introduced with Cray-1
Memory
V1
Load Unit
Mult.
V2
V3
Chain
Add
V4
V5
Chain
LV v1
MULV v3,v1,v2
ADDV v5, v3, v4

## Slide 32: Vector Chaining Advantage
With chaining, can start dependent instruction as soon as first result appears
Load
Mul
Add
Load
Mul
Add
Time
Without chaining, must wait for last element of result to be written before starting dependent instruction

## Slide 33: Vector Startup
Two components of vector startup penalty
  functional unit latency (time through pipeline)
  dead time or recovery time (time before another vector instruction can start down pipeline). Some pipelines reduce control logic by requiring dead time between instructions to the same vector unit
R
X
X
X
W
R
X
X
X
W
R
X
X
X
W
R
X
X
X
W
R
X
X
X
W
R
X
X
X
W
R
X
X
X
W
R
X
X
X
W
R
X
X
X
W
R
X
X
X
W
Functional Unit Latency
Dead Time
First Vector Instruction
Second Vector Instruction
Dead Time

## Slide 34: Dead Time and Short Vectors
Cray C90, Two lanes
4 cycle dead time
Maximum efficiency 94% with 128 element vectors
4 cycles dead time
T0, Eight lanes
No dead time
100% efficiency with 8 element vectors
No dead time
64 cycles active

## Slide 35: Vector Memory-Memory versus Vector Register Machines
Vector memory-memory instructions hold all vector operands in main memory
The first vector machines, CDC Star-100 (‘73) and TI ASC (‘71), were memory-memory machines
Cray-1 (’76) was first vector register machine
for (i=0; i<N; i++)
{
C[i] = A[i] + B[i];
D[i] = A[i] - B[i];
}
Example Source Code
ADDV C, A, B
SUBV D, A, B
Vector Memory-Memory Code
LV V1, A
LV V2, B
ADDV V3, V1, V2
SV V3, C
SUBV V4, V1, V2
SV V4, D
Vector Register Code

## Slide 36: Vector Memory-Memory vs. Vector Register Machines
Vector memory-memory architectures (VMMA) require greater main memory bandwidth, why?
  All operands must be read in and out of memory
VMMAs make if difficult to overlap execution of multiple vector operations, why?
  Must check dependencies on memory addresses
VMMAs incur greater startup latency
  Scalar code was faster on CDC Star-100 (VMM) for vectors < 100 elements
Apart from CDC follow-ons (Cyber-205, ETA-10) all major vector machines since Cray-1 have had vector register architectures
(we ignore vector memory-memory from now on)

## Slide 37: Automatic Code Vectorization
for (i=0; i < N; i++)
C[i] = A[i] + B[i];
load
load
add
store
load
load
add
store
Iter. 1
Iter. 2
Scalar Sequential Code
Vectorization is a massive compile-time reordering of operation sequencing
 requires extensive loop dependence analysis
Vector Instruction
load
load
add
store
load
load
add
store
Iter. 1
Iter. 2
Vectorized Code
Time

## Slide 38: Vector Stripmining
Problem: Vector registers have finite length
Solution: Break loops into pieces that fit in registers, “Stripmining”
ANDI R1, N, 63 # N mod 64
MTC1 VLR, R1 # Do remainder
loop:
LV V1, RA
DSLL R2, R1, 3 # Multiply by 8
DADDU RA, RA, R2 # Bump pointer
LV V2, RB
DADDU RB, RB, R2
ADDV.D V3, V1, V2
SV V3, RC
DADDU RC, RC, R2
DSUBU N, N, R1 # Subtract elements
LI R1, 64
MTC1 VLR, R1 # Reset full length
BGTZ N, loop # Any more to do?
for (i=0; i<N; i++)
C[i] = A[i]+B[i];
+
+
+
A
B
C
64 elements
Remainder

## Slide 39: Vector Conditional Execution
Problem: Want to vectorize loops with conditional code:
      for (i=0; i<N; i++)
      if (A[i]>0) then
      A[i] = B[i];
Solution: Add vector mask (or flag) registers
  vector version of predicate registers, 1 bit per element
…and maskable vector instructions
  vector operation becomes bubble (“NOP”) at elements where mask bit is clear
Code example:
  CVM # Turn on all elements
  LV vA, rA # Load entire A vector
  SGTVS.D vA, F0 # Set bits in mask register where A>0
  LV vA, rB # Load B vector into A under mask
  SV vA, rA # Store A back to memory under mask

## Slide 40: Masked Vector Instructions
C[4]
C[5]
C[1]
Write data port
A[7]
B[7]
M[3]=0
M[4]=1
M[5]=1
M[6]=0
M[2]=0
M[1]=1
M[0]=0
M[7]=1
Density-Time Implementation
  scan mask vector and only execute elements with non-zero masks
C[1]
C[2]
C[0]
A[3]
B[3]
A[4]
B[4]
A[5]
B[5]
A[6]
B[6]
M[3]=0
M[4]=1
M[5]=1
M[6]=0
M[2]=0
M[1]=1
M[0]=0
Write data port
Write Enable
A[7]
B[7]
M[7]=1
Simple Implementation
  execute all N operations, turn off result writeback according to mask

## Slide 41: Vector Reductions
Problem: Loop-carried dependence on reduction variables
  sum = 0;
  for (i=0; i<N; i++)
  sum += A[i]; # Loop-carried dependence on sum
Solution: Re-associate operations if possible, use binary tree to perform reduction
  # Rearrange as:
  sum[0:VL-1] = 0 # Vector of VL partial sums
  for(i=0; i<N; i+=VL) # Stripmine VL-sized chunks
  sum[0:VL-1] += A[i:i+VL-1]; # Vector sum
  # Now have VL partial sums in one vector register
  do {
  VL = VL/2; # Halve vector length
  sum[0:VL-1] += sum[VL:2*VL-1] # Halve no. of partials
  } while (VL>1)

## Slide 42: Vector Scatter/Gather
Want to vectorize loops with indirect accesses:
  for (i=0; i<N; i++)
  A[i] = B[i] + C[D[i]]
Indexed load instruction (Gather)
  LV vD, rD # Load indices in D vector
  LVI vC, rC, vD # Load indirect from rC base
  LV vB, rB # Load B vector
  ADDV.D vA,vB,vC # Do add
  SV vA, rA # Store result

## Slide 43: Vector Scatter/Gather
Histogram example:
  for (i=0; i<N; i++)
  A[B[i]]++;
Is following a correct translation?
  LV vB, rB # Load indices in B vector
  LVI vA, rA, vB # Gather initial A values
  ADDV vA, vA, 1 # Increment
  SVI vA, rA, vB # Scatter incremented values

## Slide 44: A Modern Vector Super: NEC SX-9 (2008)
65nm CMOS technology
Vector unit (3.2 GHz)
  8 foreground VRegs + 64 background VRegs (256x64-bit elements/VReg)
  64-bit functional units: 2 multiply, 2 add, 1 divide/sqrt, 1 logical, 1 mask unit
  8 lanes (32+ FLOPS/cycle, 100+ GFLOPS peak per CPU)
  1 load or store unit (8 x 8-byte accesses/cycle)
Scalar unit (1.6 GHz)
  4-way superscalar with out-of-order and speculative execution
  64KB I-cache and 64KB data cache
Memory system provides 256GB/s DRAM bandwidth per CPU
Up to 16 CPUs and up to 1TB DRAM form shared-memory node
  total of 4TB/s bandwidth to shared DRAM memory
Up to 512 nodes connected via 128GB/s network links (message passing between nodes)
Notes: Picture from NEC article “A hardware overview of SX-6 and SX-7 supercomputer”

## Slide 45: Multimedia Extensions (aka SIMD extensions)
Very short vectors added to existing ISAs for microprocessors
Use existing 64-bit registers split into 2x32b or 4x16b or 8x8b
  Lincoln Labs TX-2 from 1957 had 36b datapath split into 2x18b or 4x9b
  Newer designs have wider registers
    128b for PowerPC Altivec, Intel SSE2/3/4
    256b for Intel AVX
Single instruction operates on all elements within register
16b
16b
16b
16b
32b
32b
64b
8b
8b
8b
8b
8b
8b
8b
8b
16b
16b
16b
16b
16b
16b
16b
16b
16b
16b
16b
16b
+
+
+
+
4x16b adds

## Slide 46: Multimedia Extensions versus Vectors
Limited instruction set:
  no vector length control
  no strided load/store or scatter/gather
  unit-stride loads must be aligned to 64/128-bit boundary
Limited vector register length:
  requires superscalar dispatch to keep multiply/add/load units busy
  loop unrolling to hide latencies increases register pressure
Trend towards fuller vector support in microprocessors
  Better support for misaligned memory accesses
  Support of double-precision (64-bit floating-point)
  New Intel AVX spec (announced April 2008), 256b vector registers (expandable up to 1024b)

## Slide 47: Degree of Vectorization
Compilers are good at finding data-level parallelism

## Slide 48: Average Vector Length
Maximum depends on if becnhmarks use 16 bit or 32 bit operations

## Slide 49: Distribution of Instructions

## Slide 50: Question of the Day
Can Vector and VLIW combine?
Yes!
Fujitsy FR-V can process both VLIW and vector instructions
Exploits both instruction- and data-level parallelism

## Slide 51: Acknowledgements
These slides contain material developed and copyright by:
  Arvind (MIT)
  Krste Asanovic (MIT/UCB)
  Joel Emer (Intel/MIT)
  James Hoe (CMU)
  John Kubiatowicz (UCB)
  David Patterson (UCB)
MIT material derived from course 6.823
UCB material derived from course CS252
“Vector Vs. Superscalar and VLIW Architectures for Embedded Multimedia Benchmarks”. Christos Kozyrakis and David Patterson. MICRO-35. 2002