The problem sets are intended to help you learn the material, and we encourage you to collaborate with other students and to ask questions in discussion sections and office hours to understand the problems. However, each student must turn in his own solution to the problems.

|  | CS152 Computer Architecture and Engineering |  |
| --- | --- | --- |
|  | ISAs, Microprogramming and Pipelining |  |
| Assigned 1/24/2018 | Problem Set #1 | Due February 5 |

http://inst.eecs.berkeley.edu/~cs152/sp18

The problem sets also provide essential background material for the quizzes. The problem sets will be graded primarily on an effort basis, but if you do not work through the problem sets you are unlikely to succeed at the quizzes! We will distribute solutions to the problem sets on the day the problem sets are due to give you feedback.  Homework assignments are due at the beginning of class on the due date.  Late homework will not be accepted, except for extreme circumstances and with prior arrangement.

Problem 1: CISC, RISC, accumulator, and Stack: Comparing ISAs

In this problem, your task is to compare four different ISAs. x86 is an extended accumulator, CISC architecture with variable-length instructions.  RISC-V is a load-store, RISC architecture with fixed-length instructions (for this problem only consider the 32-bit form of its ISA). We will also look at a simple stack-based ISA and an accumulator architecture.

| Problem 1.A | CISC |
| --- | --- |

Let us begin by considering the following C code:

int b;  //a global variable

void multiplyByB(int a){

int i, result;

for(i = 0; i<b; i++){

result=result+a;

}

}

Using gcc and objdump on a Pentium III, we see that the above loop compiles to the following x86 instruction sequence.  (On entry to this code, register %ecx contains i, and register %edx contains result, and register %eax contains a.  b is stored in memory at location 0x8049580)

xor    %edx,%edx

xor    %ecx,%ecx

loop:      cmp    0x8049580,%ecx

jl     L1

jmp    done

L1:		add    %eax,%edx

inc    %ecx

jmp    loop

done:    ...

The meanings and instruction lengths of the instructions used above are given in the following table. Registers are denoted with RSUBSCRIPT, register contents with <RSUBSCRIPT>.

| Instruction | Operation | Length |
| --- | --- | --- |
| add RDEST, RSRC | RSRC <= <RSRC> + <RDST> | 2 bytes |
| cmp imm32, RSRC2 | Temp <= <RSRC2> - MEM[imm32] | 6 bytes |
| inc RDEST | RDEST <= <RDEST> + 1 | 1 byte |
| jmp label | jump to the address specified by label | 2 bytes |
| jl label | if (SF≠!= OF) jump to the address specified by label | 2 bytes |
| xor RDEST, RSRC | RDEST <= RDEST xor RSRC | 2 bytes |

Notice that the jump instruction jl (jump if less than) depends on SF and OF, which are status flags. Status flags are set by the instruction preceding the jump, based on the result of the computation. Some instructions, like the cmp instruction, perform a computation and set status flags, but do not return any result. The meanings of the status flags are given in the following table:

| Name | Purpose | Condition Reported |
| --- | --- | --- |
| OF | Overflow | Result exceeds positive or negative limit of number range |
| SF | Sign | Result is negative (less than zero) |

How many bytes is the program?  For the above x86 assembly code, how many bytes of instructions need to be fetched if b = 10?  Assuming 32-bit data values, how many bytes of data memory need to be fetched? Stored?

| Problem 1.B | RISC |
| --- | --- |

Translate each of the x86 instructions in the following table into one or more RISC-V instructions.  Place the L1 and loop labels where appropriate.  You should use the minimum number of instructions needed to translate each x86 instruction. Assume that upon entry, x1 contains b, x2 contains a, x3 contains i.  x4 should receive result. If needed, use x5 as a condition register, and x6, x7, etc., for temporaries. You should not need to use any floating-point registers or instructions in your code.  A description of the RISC-V instruction set architecture can be found in the class website, resources page.

| x86 instruction | label | RISC-V instruction sequence |
| --- | --- | --- |
| xor %edx,%edx |  |  |
| xor %ecx,%ecx |  |  |
| cmp 0x8049580,%ecx |  |  |
| jl L1 |  |  |
| jmp done |  |  |
| add %eax,%edx |  |  |
| inc %ecx |  |  |
| jmp loop |  |  |
| ... | done: | ... |

How many bytes is the RISC-V program using your direct translation?  How many bytes of RISC-V instructions need to be fetched for b = 10 using your direct translation? Assuming 32-bit data values, how many bytes of data memory need to be fetched? Stored?

| Problem 1.C | Stack |
| --- | --- |

In a stack architecture, all operations occur on top of the stack.  Only push and pop access memory, and all other instructions remove their operands from the stack and replace them with the result.  The hardware implementation we will assume for this problem set uses stack registers for the top two entries; accesses that involve other stack positions (e.g., pushing or popping something when the stack has more than two entries) use an extra memory reference.  The table below gives a subset of a simple stack-style instruction set.  Assume each opcode is a single byte.  Labels, constants, and addresses require two bytes.

| Example instruction | Meaning |
| --- | --- |
| PUSH A | push M[A] onto stack |
| POP A | pop stack and place popped value in M[A] |
| ADD | pop two values from the stack; ADD them; push result onto stack |
| SUB | pop two values from the stack; SUBtract top value from the 2nd; push result onto stack |
| ZERO | zeroes out the value at top of stack |
| INC | pop value from top of stack; increments value by one push new value back on the stack |
| BEQZ label | pop value from stack; if it’s zero, continue at label; else, continue with next instruction |
| BNEZ label | pop value from stack; if it’s not zero, continue at label; else, continue with next instruction |
| GOTO label | continue execution at location label |

Translate the multiplyByB loop to the stack ISA.  For uniformity, please use the same control flow as in parts a and b.  Assume that when we reach the loop, a is the only thing on the stack.  Assume b is still at address 0x8000 (to fit within a 2 byte address specifier).

How many bytes is your program?  Using your stack translations from part (c), how many bytes of stack instructions need to be fetched for b = 10? Assuming 32-bit data values, how many bytes of data memory need to be fetched? Stored?  If you could push and pop to/from a four-entry register file rather than memory (the Java virtual machine does this), what would be the resulting number of bytes fetched and stored?

| Problem 1.D | Accumulator |
| --- | --- |

In an accumulator ISA, one operand is implicitly a specific register (the same for all instructions), called the accumulator. For example, to execute C = A + B, the assembly code is:

Load A	Load A into the accumulator

Add B		Add B to the accumulator (which contains A’s value)

Store C	Store the accumulator’s value into the address contained in C

Notice that all instructions use the same accumulator. Also note that there are no registers in this example, but A, B, and C are all memory addresses. For this question, we will consider a modified architecture to make a solution possible. We will have accumulator instructions denoted by the postfix accumulator, and subtractor instructions which work the same way but reference a separate register. Therefore, a load can be either “load A accumulator” or “load A subtractor” depending on where the value of address A should be loaded. Using this ISA, and addition, subtraction, increment, decrement, zero, and branch instructions similar to the stack ISA, write the assembly for the program of this problem.

How many bytes is your program (assume same byte usage as the stack architecture and that the specifier for accumulator and subtractor requires no extra bytes)? Can the same program be implemented with just one accumulator (i.e., no subtractor)? If not, how would you extend this ISA to implement this program with just one accumulator?

| Problem 1.E | Conclusions |
| --- | --- |

In just a few sentences, compare the four ISAs you have studied with respect to code size, number of instructions fetched, and data memory traffic. Which one would you choose if you were to build a specialized processor to execute the code in this program, and why?

| Problem 1.F | Optimization |
| --- | --- |

To get more practice with RISC-V, optimize the code from part B so that it can be expressed in fewer instructions.  There are solutions more efficient than simply translating each individual x86 instruction as you did in part B. Your solution should contain commented assembly code, a paragraph that explains your optimizations, and a short analysis of the savings you obtained.

Problem 2:  Microprogramming and Bus-Based Architectures

In  this  problem,  we  explore  microprogramming  by  writing  microcode  for  the  bus-based implementation  of  the  RISC-V  machine  described  in  Handout  #1  (Bus-Based  RISC-V Implementation). Read the instruction fetch microcode in Table H1-3 of Handout #1.  Make sure that you understand how different types of data and control transfers are achieved by setting the appropriate control signals before attempting this problem.

In order to further simplify this problem, ignore the busy signal, and assume that the memory is as fast as the register file.

The final solution should be elegant and efficient (e.g. number of new states needed, amount of new hardware added).

| Problem 2.A | Implementing Memory-to-Memory Add |
| --- | --- |

For this problem, you are to implement a new memory-memory add operation.  The new instruction has the following format:

ADDm rd, rs, rt

ADDm performs the following operation:

M[rd] <= M[rs] + M[rt]

Fill in Worksheet 2.A with the microcode for ADDm.  Use don’t cares (*) for fields where it is safe to use don’t cares.  Study the hardware description well, and make sure all your microinstructions are legal.

Please comment your code clearly. If the pseudo-code for a line does not fit in the space provided, or if you have additional comments, you may write in the margins as long as you do it neatly.  Your code should exhibit “clean” behavior and not modify any registers (except rd) in the course of executing the instruction.

Finally, make sure that the instruction fetches the next instruction (i.e., by doing a microbranch to FETCH0 as discussed above).

You may want to consult the micro-code found in the micro-coded processor provided in Lab1, which can be viewed at ${LAB1ROOT}/src/rv32_ucode/micrcode.scala  for  guidance.  Warning:  While that micro-code passes  all  provided  assembly  tests  and  benchmarks,  no guarantees to  the  optimality of  the  code  can  be  assured,  and  there  may still  be  bugs in  the provided implementation.

| Problem 2.B | Implementing STRCPY Instruction |
| --- | --- |

In this question we ask you to implement a useful string instruction, string copy

(STRCPY). This instruction uses the same encoding as the other arithmetic instructions (R-type)

on RISC-V (note rs2 should always be 00000 as there’s only one source operand):

| rd | rs1 | rs2 | func | opcode |
| --- | --- | --- | --- | --- |
| 5 bits | 5 bits | 5 bits | 10 bits | 7 bits |  |

The STRCPY instruction provides the programmer the ability to copy a string directly from one location in memory (M[Rs]) to another location in memory (M[Rd]).

For this problem, think of a string as an array of 4-byte words, with the last element being zero (the string is “null terminated”).

Starting from the memory location addressed by Rs (M[Rs]), keep copying one 4-byte word at a time to an other  memory  location,  starting  at  the  address  M[Rd],  until  you  hit  the  null terminating character (zero). Do not forget to copy the null character too!

Finally, once STRCPY has finished, Rd and Rs will hold the address of the null character at the end of their respective strings.

The instruction definition for STRCPY requires that the strings pointed to by Rs and Rd do not overlap in memory.

Your task is to fill out Worksheet 2.B for STRCPY instruction. You should try to optimize your implementation for the minimal number of cycles necessary and for which signals can be set to don’t-cares.

| Problem 2.C | Instruction Execution Times |
| --- | --- |

How many cycles does it take to execute the following instructions in the microcoded RISC-V machine?  Use the states and control points from RISC-V-Controller-2 in Lecture 2 (or Lab 1, in

${LAB1ROOT}/src/rv32_ucode/micrcode.scala) and assume Memory will not assert its busy signal.

| Instruction | Cycles |
| --- | --- |
| ADD x3,x2,x1 |  |
| ADDI x2,x1,#4 |  |
| SW x1,0(x2) |  |
| BNE x1,x2,label #(x1 == x2) |  |
| BNE x1,x2,label #(x1 != x2) |  |
| BEQ x1,x2,label #(x1 == x2) |  |
| BEQ x1,x2,label #(x1 != x2) |  |
| J label |  |
| JAL label |  |
| JALR x1 |  |

Which instruction takes the most cycles to execute?  Which instruction takes the fewest cycles to execute?

Problem 3: 6-Stage Pipeline

In this problem, we consider a modification to the fully bypassed 5-stage RISC-V processor pipeline presented in Lecture 4.   Our new processor has a data cache with a two-cycle latency.  To accommodate this cache, the memory stage is pipelined into two stages, M1 and M2, as shown in Figure 1-A. Additional bypasses are added to keep the pipeline fully bypassed.

Suppose we are implementing this 6-stage pipeline in a technology in which register file ports are inexpensive but bypasses are costly. We wish to reduce cost by removing some of the bypass paths, but without increasing CPI. The proposal is for all integer arithmetic instructions to write their results to the register file at the end of the Execute stage, rather than waiting until the Writeback stage.  A second register file write port is added for this purpose.  Remember that register file writes occur on each rising clock edge, and values can be read in the next clock cycle.  The proposed change is shown in Figure 1-B.

In this problem, assume that the only exceptions that can occur in this pipeline are illegal opcodes (detected in the Decode stage) and invalid memory address (detected at the start of the M2 stage).  Additionally assume that the control logic is optimized to stall only when necessary.  You may ignore branch and jump instructions in this problem.

Figure 1-A.  6-stage pipeline.  For clarity, bypass paths are not shown.

Figure 1-B.  6-stage pipeline with proposed additional write port.

| Problem 3.A | Hazards: Second Write Port |
| --- | --- |

The second write port allows some bypass paths to be removed without adding stalls in the decode stage.  Explain how the second write port improves performance by eliminating such stalls and give a short code sequence that would have required an interlock to execute correctly with only a single write port and with the same bypass paths removed.

| Problem 3.B | Hazards: Bypasses Removed |
| --- | --- |

After the second write port is added, which bypass paths can be removed in this new pipeline without introducing additional stalls?  List each removed bypass individually.

| Problem 3.C | Precise Exceptions |
| --- | --- |

Without further modifications, this pipeline may not support precise exceptions.  Briefly explain why, and provide a minimal code sequence that will result in an imprecise exception.

| Problem 3.D | Precise Exceptions: Implemented using a Interlock |
| --- | --- |

Describe how precise exceptions can be implemented by adding a new interlock.  Provide a minimal code sequence that would engage this interlock.  Qualitatively, what is the performance impact of this solution?

| Problem 3.E | Precise Exceptions: Implemented using an Extra Read Port |
| --- | --- |

Suppose you are additionally given the budget to add a new register file read port.  Propose an alternative solution to implement precise exceptions in this pipeline without requiring any new interlocks.

Problem 4: CISC vs RISC

For each of the following questions, circle either CISC or RISC, depending on which ISA you feel would be best suited for the situation described.  Also, briefly explain your reasoning.

| Problem 4.A | Lack of Good Compilers I |
| --- | --- |

Assume that compiler technology is poor, and therefore your users are far more apt to write all of their code in assembly.  A _____ ISA would be best appreciated by these programmers.

CISC   										RISC

| Problem 4.B | Lack of Good Compilers II |
| --- | --- |

You desire to make compilers better at targeting your yet-to-be-designed machine. Therefore, you choose a _____ ISA, as it would be easiest for a compiler to target, thus allowing your users to write code in higher-level languages like C and Fortran and raise their productivity.

CISC   										RISC

| Problem 4.C | Fast Logic, Slow Memory |
| --- | --- |

Assume that CPU logic is fast, very fast, while instruction fetch accesses are at least 10x slower (say, you’re the lead architect of the “709”).  Which ISA style do you choose as a best match for the hardware’s limitations?

CISC   										RISC

| Problem 4.D | Higher Performance(?) |
| --- | --- |

Starting with a clean slate in the year 2016 (area/logic/memory is cheap), you think that a _____ ISA that would lend itself best to a very high performance processor (e.g., high frequency, highly pipelined).

CISC   										RISC

Problem 5: Iron Law of Processor Performance

Mark whether the following modifications will cause each of the first three categories to increase, decrease, or whether the modification will have no effect.  Explain your reasoning.

For the final column “Overall Performance”, mark whether the following modifications increase, decrease, have no effect, or whether the modification will have an ambiguous effect. Explain your reasoning.  If the modification has an ambiguous effect, describe the tradeoff in which it would be a beneficial modification or in which it would a detrimental modification (i.e., as an engineer would you suggest using the modification or not and why?).

|  |  | Instructions / Program | Cycles / Instruction | Seconds / Cycle | Overall Performance |
| --- | --- | --- | --- | --- | --- |
| a) | Adding a branch delay slot |  |  |  |  |
| b) | Adding a complex instruction |  |  |  |  |
| c) | Reduce number of registers in the ISA |  |  |  |  |
| d) | Improving memory access speed |  |  |  |  |
| e) | Adding 16-bit versions of the most common instructions in RISC-V (normally 32-bits in length) to the ISA (i.e., make RISC-V a variable length ISA) |  |  |  |  |
| f) | For a given CISC ISA, changing the implementation of the micro-architecture from a microcoded engine to a RISC pipeline (with a CISC-to-RISC decoder on the front-end) |  |  |  |  |

# Text boxes

Worksheet 2.A

Worksheet 2.B