## Slide 1: CS 152 Computer Architecture and Engineering CS252 Graduate Computer Architecture Lecture 5 – Memory
Krste Asanovic
Electrical Engineering and Computer Sciences
University of California at Berkeley
http://www.eecs.berkeley.edu/~krste
http://inst.eecs.berkeley.edu/~cs152

## Slide 2: Last time in Lecture 4
Handling exceptions in pipelined machines by passing exceptions down pipeline until instructions cross commit point in order
Can use values before commit through bypass network
Pipeline hazards can be avoided through software techniques: scheduling, loop unrolling
Decoupled architectures use queues between “access” and “execute” pipelines to tolerate long memory latency
Regularizing all functional units to have same latency simplifies more complex pipeline design by avoiding structural hazards, can be expanded to in-order superscalar designs

## Slide 3: Early Read-Only Memory Technologies
Punched cards, From early 1700s through Jaquard Loom, Babbage, and then IBM
Punched paper tape, instruction stream in Harvard Mk 1
IBM Card Capacitor ROS
IBM Balanced Capacitor ROS
Diode Matrix, EDSAC-2 µcode store

## Slide 4: Early Read/Write Main Memory Technologies
Williams Tube, Manchester Mark 1, 1947
Babbage, 1800s: Digits stored on mechanical wheels
Mercury Delay Line, Univac 1, 1951
Also, regenerative capacitor memory on Atanasoff-Berry computer, and rotating magnetic drum memory on IBM 650

## Slide 5: MIT Whirlwind Core Memory

## Slide 6: Core Memory
Core memory was first large scale reliable main memory
  invented by Forrester in late 40s/early 50s at MIT for Whirlwind project
Bits stored as magnetization polarity on small ferrite cores threaded onto two-dimensional grid of wires
Coincident current pulses on X and Y wires would write cell and also sense original state (destructive reads)
DEC PDP-8/E Board,
4K words x 12 bits, (1968)
Robust, non-volatile storage
Used on space shuttle computers
Cores threaded onto wires by hand (25 billion a year at peak production)
Core access time ~ 1µs
Notes: Early machines had things like mercury delay lines (jse)
Photo from David Gesswein djg@pdp8.net

## Slide 7: Semiconductor Memory
Semiconductor memory began to be competitive in early 1970s
  Intel formed to exploit market for semiconductor memory
  Early semiconductor memory was Static RAM (SRAM). SRAM cell internals similar to a latch (cross-coupled inverters).
First commercial Dynamic RAM (DRAM) was Intel 1103
  1Kbit of storage on single chip
  charge on a capacitor used to hold value
Semiconductor memory quickly replaced core in ‘70s

## Slide 8: One-Transistor Dynamic RAM [Dennard, IBM]
TiN top electrode (VREF)
Ta2O5 dielectric
W bottom
electrode
poly
word
line
access transistor
1-T DRAM Cell
word
bit
access transistor
Storage
capacitor (FET gate, trench, stack)
VREF

## Slide 9: Modern DRAM Structure
[Samsung, sub-70nm DRAM, 2004]

## Slide 10: DRAM Architecture
Row Address Decoder
Col.
1
Col. 2M
Row 1
Row 2N
Column Decoder & Sense Amplifiers
M
N
N+M
bit lines
word lines
Memory cell (one bit)
D
Data
Bits stored in 2-dimensional arrays on chip
Modern chips have around 4-8 logical banks on each chip
  each logical bank physically implemented as many smaller arrays

## Slide 11: DRAM Packaging (Laptops/Desktops/Servers)
DIMM (Dual Inline Memory Module) contains multiple chips with clock/control/address signals connected in parallel (sometimes need buffers to drive signals to all chips)
Data pins work together to return wide word (e.g., 64-bit data bus using 16x4-bit parts)
Address lines multiplexed row/column address
Clock and control signals
Data bus
(4b,8b,16b,32b)
DRAM chip
~12
~7

## Slide 12: DRAM Packaging, Mobile Devices
[ Apple A4 package cross-section, iFixit 2010 ]
Two stacked DRAM die
Processor plus logic die
[ Apple A4 package on circuit board]

## Slide 13: DRAM Packaging Apple A10

## Slide 14: DRAM Operation
Three steps in read/write access to a given bank
Row access (RAS)
  decode row address, enable addressed row (often multiple Kb in row)
  bitlines share charge with storage cell
  small change in voltage detected by sense amplifiers which latch whole row of bits
  sense amplifiers drive bitlines full rail to recharge storage cells
Column access (CAS)
  decode column address to select small number of sense amplifier latches (4, 8, 16, or 32 bits depending on DRAM package)
  on read, send latched bits out to chip pins
  on write, change sense amplifier latches which then charge storage cells to required value
  can perform multiple column accesses on same row without another row access (burst mode)
Precharge
  charges bit lines to known value, required before next row access
Each step has a latency of around 15-20ns in modern DRAMs
Various DRAM standards (DDR, RDRAM) have different ways of encoding the signals for transmission to the DRAM, but all share same core architecture
Notes: Use RAS/CAS to reduce average latency.

## Slide 15: Double-Data Rate (DDR2) DRAM
Row
Column
Precharge
Row’
Data
200MHz Clock
400Mb/s Data Rate
[ Micron, 256Mb DDR2 SDRAM datasheet ]

## Slide 16: CPU-Memory Bottleneck
Performance of high-speed computers is usually limited by memory bandwidth & latency
Latency (time for a single access)
  Memory access time >> Processor cycle time
Bandwidth (number of accesses per unit time)
  if fraction m of instructions access memory
   1+m memory references / instruction
   CPI = 1 requires 1+m memory refs / cycle (assuming RISC-V ISA)
Memory
CPU

## Slide 17: Processor-DRAM Gap (latency)
Time
µProc 60%/year
DRAM
7%/year
1
10
100
1000
1980
1981
1983
1984
1985
1986
1987
1988
1989
1990
1991
1992
1993
1994
1995
1996
1997
1998
1999
2000
DRAM
CPU
1982
Processor-Memory
Performance Gap: (growing 50%/yr)
Performance
Four-issue 3GHz superscalar accessing 100ns DRAM could execute 1,200 instructions during time for one memory access!
Notes: Why doesn’t DRAM get faster?

## Slide 18: Physical Size Affects Latency
Small Memory
CPU
Big Memory
CPU
Signals have further to travel
Fan out to more locations

## Slide 19: Relative Memory Cell Sizes
[ Foss, “Implementing Application-Specific Memory”, ISSCC 1996 ]
DRAM on memory chip
On-Chip SRAM in logic chip

## Slide 20: Memory Hierarchy
Small,
Fast Memory
(RF, SRAM)
capacity: Register << SRAM << DRAM
latency: Register << SRAM << DRAM
bandwidth: on-chip >> off-chip
On a data access:
  if data Î fast memory  low latency access (SRAM)
  if data Ï fast memory  high latency access (DRAM)
CPU
Big, Slow Memory
(DRAM)
A
B
holds frequently used data
Notes: Due to cost
Due to size of DRAM
Due to cost and wire delays (wires on-chip cost much less, and are faster)

## Slide 21: CS152 Administrivia

## Slide 22: CS252 Administrivia

## Slide 23: Management of Memory Hierarchy
Small/fast storage, e.g., registers
  Address usually specified in instruction
  Generally implemented directly as a register file
    but hardware might do things behind software’s back, e.g., stack management, register renaming
Larger/slower storage, e.g., main memory
  Address usually computed from values in register
  Generally implemented as a hardware-managed cache hierarchy (hardware decides what is kept in fast memory)
    but software may provide “hints”, e.g., don’t cache or prefetch
Notes: Secondary characteristic:
Some machines (PDP-10) have overlain the registers on memory (jse)

## Slide 24: Real Memory Reference Patterns
Donald J. Hatfield, Jeanette Gerald: Program Restructuring for Virtual Memory. IBM Systems Journal 10(3): 168-192 (1971)
Time
Memory Address (one dot per access)

## Slide 25: Typical Memory Reference Patterns
Address
Time
Instruction
fetches
Stack
accesses
Data
accesses
n loop iterations
subroutine call
subroutine return
argument access
vector access
scalar accesses

## Slide 26: Two predictable properties of memory references:
Temporal Locality: If a location is referenced it is likely to be referenced again in the near future.
Spatial Locality: If a location is referenced it is likely that locations near it will be referenced in the near future.

## Slide 27: Memory Reference Patterns
Donald J. Hatfield, Jeanette Gerald: Program Restructuring for Virtual Memory. IBM Systems Journal 10(3): 168-192 (1971)
Time
Memory Address (one dot per access)
Spatial
Locality
Temporal
Locality

## Slide 28: Caches exploit both types of predictability:
Exploit temporal locality by remembering the contents of recently accessed locations.
Exploit spatial locality by fetching blocks of data around recently accessed locations.

## Slide 29: Inside a Cache
CACHE
Processor
Main
Memory
Address
Address
Data
Data
Address
Tag
Data Block
Data
Byte
Data
Byte
Data
Byte
Line
100
304
6848
copy of main
memory
location 100
copy of main
memory
location 101
416
Notes: Tag only needs enough bits to uniquely identify the block (jse)

## Slide 30: Cache Algorithm (Read)
Look at Processor Address, search cache tags to find match. Then either
Found in cache
a.k.a. HIT
Return copy
of data from
cache
Not in cache
a.k.a. MISS
Read block of data from
Main Memory
Wait …
Return data to processor
and update cache
Q: Which line do we replace?

## Slide 31: Placement Policy
0 1 2 3 4 5 6 7
0 1 2 3
Set Number
Cache
Fully (2-way) Set Direct
Associative Associative Mapped
anywhere anywhere in only into
set 0 block 4
(12 mod 4) (12 mod 8)
0 1 2 3 4 5 6 7 8 9
1 1 1 1 1 1 1 1 1 1 0 1 2 3 4 5 6 7 8 9
2 2 2 2 2 2 2 2 2 2 0 1 2 3 4 5 6 7 8 9
3 3
0 1
Memory
Block Number
block 12
can be placed
Notes: Simplest scheme is to extract bits from ‘block number’ to determine ‘set’ (jse)
More sophisticated schemes will hash the block number ---- why could that be good/bad?

## Slide 32: Direct-Mapped Cache
Tag
Data Block
V
=
Block
Offset
Tag
Index
t
k
b
t
HIT
Data Word or Byte
2k
lines

## Slide 33: Direct Map Address Selection higher-order vs. lower-order address bits
Tag
Data Block
V
=
Block
Offset
Index
t
k
b
t
HIT
Data Word or Byte
2k
lines
Tag
Notes: Index and tag reversed

## Slide 34: 2-Way Set-Associative Cache
Tag
Data Block
V
=
Block
Offset
Tag
Index
t
k
b
HIT
Tag
Data Block
V
Data
Word
or Byte
=
t
Notes: Compare latency to direct mapped case? (jse)

## Slide 35: Fully Associative Cache
Tag
Data Block
V
=
Block
Offset
Tag
t
b
HIT
Data
Word
or Byte
=
=
t

## Slide 36: Replacement Policy
In an associative cache, which block from a set should be evicted when the set becomes full?
Random
Least-Recently Used (LRU)
  LRU cache state must be updated on every access
  true implementation only feasible for small sets (2-way)
  pseudo-LRU binary tree often used for 4-8 way
First-In, First-Out (FIFO) a.k.a. Round-Robin
  used in highly associative caches
Not-Most-Recently Used (NMRU)
  FIFO with exception for most-recently used block or blocks
This is a second-order effect. Why?
Replacement only happens on misses
Notes: NLRU used in Alpha TLBs (jse)

## Slide 37: Block Size and Spatial Locality
Word3
Word0
Word1
Word2
Larger block size has distinct hardware advantages
  less tag overhead
  exploit fast burst transfers from DRAM
  exploit fast burst transfers over wide busses
What are the disadvantages of increasing block size?
block address offsetb
2b = block size a.k.a line size (in bytes)
Split CPU address
b bits
32-b bits
Tag
Block is unit of transfer between the cache and memory
4 word block, b=2
Fewer blocks => more conflicts. Can waste bandwidth.
Notes: Larger block size will reduce compulsory misses (first miss to a block).
Larger blocks may increase conflict misses since the number of blocks
is smaller.

## Slide 38: Acknowledgements
This course is partly inspired by previous MIT 6.823 and Berkeley CS252 computer architecture courses created by my collaborators and colleagues:
  Arvind (MIT)
  Joel Emer (Intel/MIT)
  James Hoe (CMU)
  John Kubiatowicz (UCB)
  David Patterson (UCB)