## Slide 1: CS 152 Computer Architecture and Engineering CS252 Graduate Computer Architecture Lecture 16 – RISC-V Vectors
Krste Asanovic
Electrical Engineering and Computer Sciences
University of California at Berkeley
http://www.eecs.berkeley.edu/~krste
http://inst.eecs.berkeley.edu/~cs152

## Slide 2: Last Time in Lecture 15
Vector supercomputers
Vector register versus vector memory
Scaling performance with lanes
Stripmining
Chaining
Masking
Scatter/Gather

## Slide 3: New RISC-V Vector Standard
Being added as a standard extension to the RISC-V ISA
An updated form of Cray-style vectors for modern microprocessors
Still a work in progress, so details might change before being standardized
Today, a short tutorial on vector programming using the current draft standard
Assembly syntax will be changed, but concepts should be correct

## Slide 4: Quick Summary of RISC-V Vector ISA
32 vector registers, v0-v31 (no zero register)
Each vector register has associated type including:
  Number of bits in each element (8-bit, 16-bit, 32-bit, 64-bit, 128-bit, …)
  Representation (signed integer, unsigned integer, floating-point)
  Shape (scalar, 1D vector)
Number of vector registers, and their type are configured with special instructions before using vector unit
Vector instructions are polymorphic, operation depends on opcode and vector register operand types
Vector length register, vl , controls number of elements executed by each instruction
Instructions can be executed under mask
Vector arithmetic operations include all standard scalar operations
Vector memory operations include unit-stride, constant-stride, scatter-gather

## Slide 5: Vector Unit State
[0]
[1]
v0
[MAXVL-1]
[0]
[1]
v1
[MAXVL-1]
[0]
[1]
v31
[MAXVL-1]
vl
vtype0
vtype1
vtype31
Vector length register
Vector data registers
Vector configuration state
MAXVL depends on implementation and configuration

## Slide 6: Vector Configuration
Can be done by writing a number of control registers
Faster method is a special instruction that sets up standard patterns:
  vcfg N1*TYPE1, N2*TYPE2, N3*TYPE3,…
  v0..vN1-1 have TYPE1, vN1…v(N1+N2-1) have TYPE 2, …
Requested vector registers are zeroed
Unused vector registers are not accessible
MAXVL depends on number of vector registers and type, but can write assembly code without knowing MAXVL

## Slide 7: setvl instruction
setvl xregd, xregsrc
vl is set to MIN(MAXVL, xregsrc), also copied to xregd
E.g., setvl t0,a0 # vl, t0 = MIN(MAXVL,a0)

## Slide 8: Simple Example: Vector-vector add
for (i=0; i<N; i++)
{ C[i] = A[i] + B[i]; } // 32-bit ints
vcfg 3*V32bINT # Set up v0,v1,v2 to be 32-bit ints
Loop:
setvl t0, a0 # a0 holds N, t0 holds amount done
ld v0, a1 # load strip of A vector
ld v1, a2 # load strip of B vector
vadd v2, v0, v1 # add vectors
st v2, a3 # store strip of C vector
slli t1, t0, 2 # multiply by 4 to get bytes
add a1, a1, t1 # bump pointers
add a2, a2, t1
add a3, a3, t1
sub a0, a0, t0 # Subtract amount done
bnez a0, Loop

## Slide 9: Simple Example: Float vector-vector add
for (i=0; i<N; i++)
{ C[i] = A[i] + B[i]; } // 32-bit ints
vcfg 3*V32bFP # Set up v0,v1,v2 to be 32-bit floats
Loop:
setvl t0, a0 # a0 holds N, t0 holds amount done
ld v0, a1 # load strip of A vector
ld v1, a2 # load strip of B vector
vadd v2, v0, v1 # add vectors
st v2, a3 # store strip of C vector
slli t1, t0, 2 # multiply by 4 to get bytes
add a1, a1, t1 # bump pointers
add a2, a2, t1
add a3, a3, t1
sub a0, a0, t0 # Subtract amount done
bnez a0, Loop

## Slide 10: Vector-vector add, 32b+16b -> 32b integer
for (i=0; i<N; i++)
{ C[i] = A[i] + B[i]; } // 32-bit ints
vcfg 2*V32bINT, 1*V16bINT # v0,v1:32b, v2:16b
Loop:
setvl t0, a0 # a0 holds N, t0 holds amount done
ld v0, a1 # load strip of A vector
ld v2, a2 # load strip of B vector
vadd v1, v0, v2 # add vectors
st v1, a3 # store strip of C vector
slli t1, t0, 2 # multiply by 4 to get bytes
slli t2, t0, 1 # multiply by 2 to get bytes
add a1, a1, t1 # bump pointers
add a2, a2, t2
add a3, a3, t1
sub a0, a0, t0 # Subtract amount done
bnez a0, Loop

## Slide 11: Vector-scalar add
for (i=0; i<N; i++)
{ C[i] = A[i] + B; } // 32-bit ints
vcfg 2*V32bINT, 1*S32bINT #
vmv v2, a2 # Copy B to vector unit scalar
Loop:
setvl t0, a0 # a0 holds N, t0 holds amount done
ld v0, a1 # load strip of A vector
vadd v1, v0, v2 # add vectors
st v1, a3 # store strip of C vector
slli t1, t0, 2 # multiply by 4 to get bytes
add a1, a1, t1 # bump pointers
add a3, a3, t1
sub a0, a0, t0 # Subtract amount done
bnez a0, Loop

## Slide 12: Vector length < MAXVL
When vl is set to less than MAXVL, elements past end of vector are zeroed. This supports vector register renaming.
E.g., MAXVL=8, vl = 5, when execute add:
a
b
c
d
e
f
g
h
i
j
k
l
m
n
o
p
a+i
b+j
c+k
d+l
e+m
0
0
0
+
+
+
+
+
vl=5

## Slide 13: Vector masking
In base instruction set, instructions can be “unmasked” or masked by vector register v1, either true or complement
Least-significant bit of each element is used as mask
vadd v3,v0,v2,v1.t # Execute only if v1.LSB is set
a
b
c
d
e
f
g
h
i
j
k
l
m
n
o
p
a+i
0
c+k
0
e+m
0
0
0
+
+
+
1
0
1
0
1
1
1
0
v1
v0
v2
v3
vl=5
Zeros written to masked results

## Slide 14: CS152 Administrivia
PS 4 due Friday March 23 in section
  Can also turn in on class Wednesday, office hours, or can email pdf

## Slide 15: CS252 Administrivia