## Slide 1: CS 152 Computer Architecture and Engineering CS252 Graduate Computer Architecture Lecture 20 Synchronization
Krste Asanovic
Electrical Engineering and Computer Sciences
University of California at Berkeley
http://www.eecs.berkeley.edu/~krste
http://inst.eecs.berkeley.edu/~cs152

## Slide 2: Last Time in Lecture 19
Memory Consistency Model (MCM) describes what values are legal for a load to return
Sequential Consistency is most intuitive model, but almost never implemented in actual hardware
  Single global memory order where all individual thread memory operations appear in local program order
Stronger versus Weaker MCMs
  TSO is strongest common model, allows local hardware thread to see own stores before other hardware threads, but otherwise no visible reordering
  Weak multi-copy atomic model allows more reordering provided when a store is made visible to other threads, all threads can “see” at same time
  Very weak non-multi-copy atomic model allows stores from one thread to be observed in different orders by remote threads
Fences are used to enforce orderings within local thread, suffice for TSO and weak memory models
Heavyweight barriers are needed for non-multi-copy atomic, across multiple hardware threads

## Slide 3: Synchronization
The need for synchronization arises whenever there are concurrent processes in a system (even in a uniprocessor system).
Two classes of synchronization:
Producer-Consumer: A consumer process must wait until the producer process has produced data
Mutual Exclusion: Ensure that only one process uses a resource at a given time
producer
consumer
Shared Resource
P1
P2

## Slide 4: Simple Mutual-Exclusion Example
Memory
// Both threads execute:
ld xdata, (xdatap)
add xdata, 1
sd xdata, (xdatap)
data
Thread 1
Thread 2
Is this correct?
xdatap
xdatap

## Slide 5: Mutual Exclusion Using Load/Store (assume SC)
A protocol based on two shared variables c1 and c2.
Initially, both c1 and c2 are 0 (not busy)
What is wrong?
Process 1
  ...
  c1=1;
L: if c2=1 then go to L
  < critical section>
  c1=0;
Process 2
  ...
  c2=1;
L: if c1=1 then go to L
  < critical section>
  c2=0;
Deadlock!

## Slide 6: Mutual Exclusion: second attempt
To avoid deadlock, let a process give up the reservation
(i.e. Process 1 sets c1 to 0) while waiting.
Deadlock is not possible but with a low probability a livelock may occur.
An unlucky process may never get to enter the critical section starvation
Process 1
  ...
L: c1=1;
  if c2=1 then
{ c1=0; go to L}
  < critical section>
  c1=0
Process 2
  ...
L: c2=1;
  if c1=1 then
{ c2=0; go to L}
  < critical section>
  c2=0

## Slide 7: A Protocol for Mutual Exclusion T. Dekker, 1966
Process 1
  ...
  c1=1;
  turn = 1;
L: if c2=1 & turn=1
    then go to L
  < critical section>
  c1=0;
A protocol based on 3 shared variables c1, c2 and turn.
Initially, both c1 and c2 are 0 (not busy)
turn = i ensures that only process i can wait
variables c1 and c2 ensure mutual exclusion
Solution for n processes was given by Dijkstra
and is quite tricky!
Process 2
  ...
  c2=1;
  turn = 2;
L: if c1=1 & turn=2
then go to L
  < critical section>
  c2=0;

## Slide 8: Analysis of Dekker’s Algorithm
  ... Process 1
  c1=1;
  turn = 1;
L: if c2=1 & turn=1
    then go to L
  < critical section>
  c1=0;
  ... Process 2
  c2=1;
  turn = 2;
L: if c1=1 & turn=2
then go to L
  < critical section>
  c2=0;
Scenario 1
  ... Process 1
  c1=1;
  turn = 1;
L: if c2=1 & turn=1
    then go to L
  < critical section>
  c1=0;
  ... Process 2
  c2=1;
  turn = 2;
L: if c1=1 & turn=2
then go to L
  < critical section>
  c2=0;
Scenario 2

## Slide 9: ISA Support for Mutual-Exclusion Locks
Regular loads and stores in SC model (plus fences in weaker model) sufficient to implement mutual exclusion, but code is inefficient and complex
Therefore, atomic read-modify-write (RMW) instructions added to ISAs to support mutual exclusion
Many forms of atomic RMW instruction possible, some simple examples:
  Test and set (reg_x = M[a]; M[a]=1)
  Swap (reg_x=M[a]; M[a] = reg_y)

## Slide 10: Lock for Mutual-Exclusion Example
Release Lock
Acquire Lock
Critical Section
Memory
// Both threads execute:
li xone, 1
spin: amoswap xlock, xone, (xlockp)
bnez xlock, spin
ld xdata, (xdatap)
add xdata, 1
sd xdata, (xdatap)
sd x0, (xlockp)
data
Thread 1
Thread 2
xdatap
xdatap
lock
xlockp
xlockp
Assumes SC memory model

## Slide 11: Lock for Mutual-Exclusion with Relaxed MM
Release Lock
Acquire Lock
Critical Section
Memory
// Both threads execute:
li xone, 1
spin: amoswap xlock, xone, (xlockp)
bnez xlock, spin
fence r,rw
ld xdata, (xdatap)
add xdata, 1
sd xdata, (xdatap)
fence rw,w
sd x0, (xlockp)
data
Thread 1
Thread 2
xdatap
xdatap
lock
xlockp
xlockp

## Slide 12: CS152 Administrivia
Midterm 2 in class Wednesday April 11
  covers lectures 10-17, plus associated problem sets, labs, and readings
PS 5 out on Wednesday April 11
Lab 5 in section on Friday April 13

## Slide 13: CS252 Administrivia
Monday April 9th Project Checkpoint, 4-5pm, 405 Soda
  Prepare 10-minute presentation on current status

## Slide 14: RISC-V Atomic Memory Operations
Atomic Memory Operations (AMOs) have two ordering bits:
  Acquire (aq)
  Release (rl)
If both clear, no additional ordering implied
If aq set, then AMO “happens before” any following loads or stores
If rl set, then AMO “happens after” any earlier loads or stores
If both aq and rl set, then AMO happens in program order

## Slide 15: Lock for Mutual-Exclusion using RISC-V AMO
Release Lock
Acquire Lock
Critical Section
Memory
// Both threads execute:
li xone, 1
spin: amoswap.w.aq xlock, xone, (xlockp)
bnez xlock, spin
ld xdata, (xdatap)
add xdata, 1
sd xdata, (xdatap)
amoswap.w.rl x0, x0, (xlockp)
data
Thread 1
Thread 2
xdatap
xdatap
lock
xlockp
xlockp

## Slide 16: RISC-V FENCE versus AMO.aq/rl
sd x1, (a1) # Unrelated store
ld x2, (a2) # Unrelated load
li t0, 1
again:
amoswap.w.aq t0, t0, (a0)
bnez t0, again
# …
# critical section
# …
amoswap.w.rl x0, x0, (a0)
sd x3, (a3) # Unrelated store
ld x4, (a4) # Unrelated load
sd x1, (a1) # Unrelated store
ld x2, (a2) # Unrelated load
li t0, 1
again:
amoswap.w t0, t0, (a0)
fence r, rw
bnez t0, again
# …
# critical section
# …
fence rw, w
amoswap.w x0, x0, (a0)
sd x3, (a3) # Unrelated store
ld x4, (a4) # Unrelated load
AMOs only order the AMO w.r.t. other loads/stores/AMOs
FENCEs order every load/store/AMO before/after FENCE

## Slide 17: Executing Critical Sections without Locks
If a software thread is descheduled after taking lock, other threads cannot make progress inside critical section
“Non-blocking” synchronization allows critical sections to execute atomically without taking a lock

## Slide 18: Nonblocking Synchronization
Compare&Swap(m), Rt, Rs:
if (Rt==M[m])
then M[m]=Rs;
Rs=Rt ;
status success;
else status fail;
try: Load Rhead, (head)
spin: Load Rtail, (tail)
if Rhead==Rtail goto spin
Load R, (Rhead)
Rnewhead = Rhead+1
Compare&Swap(head), Rhead, Rnewhead
if (status==fail) goto try
process(R)
status is an implicit argument

## Slide 19: Compare-and-Swap Issues
Compare and Swap is a complex instruction
  Three source operands: address, comparand, new value
  One return value: success/fail or old value
ABA problem
  Load(A), Y=process(A), success=CAS(A,Y)
  What if different task switched A to B then back to A before process() finished?
Add a counter, and make CAS access two words
Double Compare and Swap
  Five source operands: one address, two comparands, two values
  Load(<A1,A2>), Z=process(A1), success=CAS(<A1,A2>,<Y,A2+1>)

## Slide 20: Load-reserve & Store-conditional
Special register(s) to hold reservation flag and address,
and the outcome of store-conditional
try: Load-reserve Rhead, (head)
spin: Load Rtail, (tail)
if Rhead==Rtail goto spin
Load R, (Rhead)
Rhead = Rhead + 1
Store-conditional (head), Rhead
if (status==fail) goto try
process(R)
Load-reserve R, (m):
  <flag, adr>  <1, m>;
  R  M[m];
Store-conditional (m), R:
  if <flag, adr> == <1, m>
  then cancel other procs’
  reservation on m;
    M[m] R;
    status succeed;
  else status fail;

## Slide 21: Load-Reserved/Store-Conditional using MESI Caches
CPU1
Memory
Bus
Main Memory (DRAM)
DMA
Snoopy Cache
CPU2
Snoopy Cache
CPU3
Snoopy Cache
Disk
DMA
Network
Bus Control
Load-Reserved ensures line in cache in Exclusive/Modified state
Store-Conditional succeeds if line still in Exclusive/Modified state

## Slide 22: LR/SC Issues
LR/SC does not suffer from ABA problem, as any access to addresses will clear reservation regardless of value
  CAS only checks stored values not intervening accesses
LR/SC non-blocking synchronization can livelock between two competing processors
  CAS guaranteed to make forward progress, as CAS only fails if some other thread succeeds
RISC-V LR/SC makes guarantee of forward progress provided code inside LR/SC pair obeys certain rules
  Can implement CAS inside RISC-V LR/SC

## Slide 23: RISC-V Atomic Instructions
Non-blocking “Fetch-and-op” with guaranteed forward progress for simple operations, returns original memory value in register
AMOSWAP M[a] = d
AMOADD M[a] += d
AMOAND M[a] &= d
AMOOR M[a] |= d
AMOXOR M[a] ^= d
AMOMAX M[a] = max(M[a],d)
AMOMIN M[a] = min(M[a],d)

## Slide 24: Transactional Memory
Proposal from Knight [‘80s], and Herlihy and Moss [’93]
    XBEGIN
    MEM-OP1
    MEM-OP2
    MEM-OP3
    XEND
Operations between XBEGIN instruction and XEND instruction either all succeed or are all squashed
Access by another thread to same addresses, cause transaction to be squashed
More flexible than CAS or LR/SC
Commercially deployed on IBM POWER8 and Intel TSX extension

## Slide 25: Acknowledgements
This course is partly inspired by previous MIT 6.823 and Berkeley CS252 computer architecture courses created by my collaborators and colleagues:
  Arvind (MIT)
  Joel Emer (Intel/MIT)
  James Hoe (CMU)
  John Kubiatowicz (UCB)
  David Patterson (UCB)