## Slide 1: Final Review part1
Howard Mao

## Slide 2: Pipelining

## Slide 3: “Iron Law” of Processor Performance
Instructions per program depends on source code, compiler technology, and ISA
Cycles per instructions (CPI) depends on ISA and µarchitecture
Time per cycle depends upon the µarchitecture and base technology
Time = Instructions Cycles Time
Program Program * Instruction * Cycle
Microarchitecture | CPI | cycle time
Microcoded | >1 | short
Single-cycle unpipelined | 1 | long
Pipelined | 1 | short

## Slide 4: Instructions interact with each other in pipeline
An instruction in the pipeline may need a resource being used by another instruction in the pipeline  structural hazard
An instruction may depend on something produced by an earlier instruction
  Dependence may be for a data value  data hazard
  Dependence may be for the next instruction’s address  control hazard (branches, exceptions)
Handling hazards generally introduces bubbles into pipeline and reduces ideal CPI > 1

## Slide 5: Interlocking Versus Bypassing
add x1, x3, x5
sub x2, x1, x4
F
add x1, x3, x5
D
F
X
D
F
sub x2, x1, x4
W
M
X
bubble
F
D
W
X
M
W
M
W
W
M
D
X
bubble
M
X
bubble
D
F
Instruction interlocked in decode stage
F
D
X
M
W
add x1, x3, x5
F
D
X
M
W
sub x2, x1, x4
Bypass around ALU with no bubbles

## Slide 6: Example Bypass Path
Memory
EXecute
Decode
Fetch
Registers
ALU
B
A
Data Cache
PC
Instruction Cache
Store
Imm
Inst. Register
Writeback

## Slide 7: Fully Bypassed Data Path
Memory
EXecute
Decode
Fetch
Registers
ALU
B
A
Data Cache
PC
Instruction Cache
Store
Imm
Inst. Register
Writeback
F
D
X
M
W
F
D
X
M
W
F
D
X
M
W
F
D
X
M
W
[ Assumes data written to registers in a W cycle is readable in parallel D cycle (dotted line). Extra write data register and bypass paths required if this is not possible. ]

## Slide 8: Exception Handling 5-Stage Pipeline
PC
Inst. Mem
D
Decode
E
M
Data Mem
W
+
Illegal Opcode
Overflow
Data address Exceptions
PC address Exception
Asynchronous
Interrupts
Exc
D
PC
D
Exc
E
PC
E
Exc
M
PC
M
Cause
EPC
Kill D Stage
Kill F Stage
Kill E Stage
Select Handler PC
Kill Writeback
Commit Point

## Slide 9: In-Order Superscalar Pipeline
Fetch two instructions per cycle; issue both simultaneously if one is integer/memory and other is floating point
Inexpensive way of increasing throughput, examples include Alpha 21064 (1992) & MIPS R5000 series (1996)
Same idea can be extended to wider issue by duplicating functional units (e.g. 4-issue UltraSPARC & Alpha 21164) but regfile ports and bypassing costs grow quickly
Commit Point
2
PC
Inst. Mem
D
Dual
Decode
X1
X2
Data Mem
W
+
GPRs
X2
W
FAdd
X3
X3
FPRs
X1
X2
FMul
X3
X2
FDiv
X3
Unpipelined divider

## Slide 10: Out-of-Order Processor

## Slide 11: Scoreboard for In-order Issues
Busy[FU#] : a bit-vector to indicate FU’s availability.
        (FU = Int, Add, Mult, Div)
  These bits are hardwired to FU's.
WP[reg#] : a bit-vector to record the registers for which writes are pending.
  These bits are set by Issue stage and cleared by WB stage
Issue checks the instruction (opcode dest src1 src2)
against the scoreboard (Busy & WP) to dispatch
    FU available?
    RAW?
    WAR?
    WAW?
Busy[FU#]
WP[src1] or WP[src2]
cannot arise
WP[dest]

## Slide 12: Renaming Structures
Renaming
table &
regfile
Reorder
buffer
Load
Unit
FU
FU
Store
Unit
< t, result >
Ins# use exec op p1 src1 p2 src2
t1
t2
.
.
tn
Instruction template (i.e., tag t) is allocated by the Decode stage, which also associates tag with register in regfile
When an instruction completes, its tag is deallocated
Replacing the
tag by its value
is an expensive
operation

## Slide 13: IBM 360/91 Floating-Point Unit R. M. Tomasulo, 1967
Mult
1
1
2
3
4
5
6
load
buffers
(from
memory)
1
2
3
4
Adder
1
2
3
Floating-Point
Regfile
store buffers
(to memory)
...
instructions
Common bus ensures that data is made available immediately to all the instructions waiting for it.
Match tag, if equal, copy value & set presence “p”.
Distribute
instruction
templates
by
functional
units
< tag, result >
p
tag/data
p
tag/data
p
tag/data
p
tag/data
p
tag/data
p
tag/data
p
tag/data
p
tag/data
p
tag/data
p
tag/data
p
tag/data
p
tag/data
p
tag/data
2
p
tag/data
p
tag/data
p
tag/data
p
tag/data
p
tag/data
p
tag/data
p
tag/data
p
tag/data
p
tag/data
p
tag/data

## Slide 14: In-Order Commit for Precise Traps
In-order instruction fetch and decode, and dispatch to reservation stations inside reorder buffer
Instructions issue from reservation stations out-of-order
Out-of-order completion, values stored in temporary buffers
Commit is in-order, checks for traps, and if none updates architectural state
Fetch
Decode
Execute
Commit
Reorder Buffer
In-order
In-order
Out-of-order
Trap?
Kill
Kill
Kill
Inject handler PC

## Slide 15: “Data-in-ROB” Design (HP PA8000, Pentium Pro, Core2Duo, Nehalem)
Managed as circular buffer in program order, new instructions dispatched to free slots, oldest instruction committed/reclaimed when done (“p” bit set on result)
Tag is given by index in ROB (Free pointer value)
In dispatch, non-busy source operands read from architectural register file and copied to Src1 and Src2 with presence bit “p” set. Busy operands copy tag of producer and clear “p” bit.
Set valid bit “v” on dispatch, set issued bit “i” on issue
On completion, search source tags, set “p” bit and copy data into src on tag match. Write result and exception flags to ROB.
On commit, check exception status, and copy result into architectural register file if no trap.
On trap, flush machine and ROB, set free=oldest, jump to handler
Tag
p
Src1
Tag
p
Src2
Reg
p
Result
Except?
i
v
Opcode
Tag
p
Src1
Tag
p
Src2
Reg
p
Result
Except?
i
v
Opcode
Tag
p
Src1
Tag
p
Src2
Reg
p
Result
Except?
i
v
Opcode
Tag
p
Src1
Tag
p
Src2
Reg
p
Result
Except?
i
v
Opcode
Tag
p
Src1
Tag
p
Src2
Reg
p
Result
Except?
i
v
Opcode
Oldest
Free

## Slide 16: Data Movement in Data-in-ROB Design
ROB
Architectural Register File
Read operands during decode
Read operands at issue
Functional Units
Read results for commit
Bypass newer values at dispatch
Result Data
Write results at completion
Write results at commit
Source Operands
Write sources in dispatch

## Slide 17: Unified Physical Register File (MIPS R10K, Alpha 21264, Intel Pentium 4 & Sandy/Ivy Bridge)
Rename all architectural registers into a single physical register file during decode, no register values read
Functional units read and write from single unified register file holding committed and temporary registers in execute
Commit only updates mapping of architectural register to physical register, no data movement
Unified Physical Register File
Read operands at issue
Functional Units
Write results at completion
Committed Register Mapping
Decode Stage Register Mapping

## Slide 18: Speculative Store Buffer
Just like register updates, stores should not modify the memory until after the instruction is committed. A speculative store buffer is a structure introduced to hold speculative store data.
During decode, store buffer slot allocated in program order
Stores split into “store address” and “store data” micro-operations
“Store address” execution writes tag
“Store data” execution writes data
Store commits when oldest instruction and both address and data available:
  clear speculative bit and eventually move data to cache
On store abort:
  clear valid bit
Data
Tags
Store Commit Path
Speculative Store Buffer
L1 Data Cache
Tag
Data
S
V
Tag
Data
S
V
Tag
Data
S
V
Tag
Data
S
V
Tag
Data
S
V
Tag
Data
S
V
Store Address
Store Data

## Slide 19: Conservative O-o-O Load Execution
sd x1, (x2)
ld x3, (x4)
Can execute load before store, if addresses known and x4 != x2
Each load address compared with addresses of all previous uncommitted stores
  can use partial conservative check i.e., bottom 12 bits of address, to save hardware
Don’t execute load if any previous store address not known
(MIPS R10K, 16-entry address queue)

## Slide 20: Address Speculation
sd x1, (x2)
ld x3, (x4)
Guess that x4 != x2
Execute load before store address known
Need to hold all completed but uncommitted load/store addresses in program order
If subsequently find x4==x2, squash load and all following instructions
=> Large penalty for inaccurate address speculation

## Slide 21: Branch Prediction

## Slide 22: Static Branch Prediction
Overall probability a branch is taken is ~60-70% but:
ISA can attach preferred direction semantics to branches, e.g., Motorola MC88110
  bne0 (preferred taken) beq0 (not taken)
ISA can allow arbitrary choice of statically predicted direction, e.g., HP PA-RISC, Intel IA-64 typically reported as ~80% accurate
backward
90%
forward
50%

## Slide 23: Branch Prediction Bits
Assume 2 BP bits per instruction
Change the prediction after two consecutive mistakes!
¬take
wrong
taken
¬ taken
taken
taken
taken
¬take
right
take
right
take
wrong
¬ taken
¬ taken
¬ taken
BP state:
(predict take/¬take) x (last prediction right/wrong)

## Slide 24: Branch History Table (BHT)
4K-entry BHT, 2 bits/entry, ~80-90% correct predictions
0
0
Fetch PC
Branch?
Target PC
+
I-Cache
Opcode
offset
Instruction
k
BHT Index
2k-entry
BHT,
2 bits/entry
Taken/¬Taken?

## Slide 25: Two-Level Branch Predictor
Pentium Pro uses the result from the last two branches
to select one of the four sets of BHT bits (~95% correct)
0
0
k
Fetch PC
Shift in Taken/¬Taken results of each branch
2-bit global branch history shift register
Taken/¬Taken?

## Slide 26: Branch Target Buffer (BTB)
Keep both the branch PC and target PC in the BTB
PC+4 is fetched if match fails
Only taken branches and jumps held in BTB
Next PC determined before branch fetched and decoded
2k-entry direct-mapped BTB
(can also be associative)
I-Cache
PC
k
Valid
valid
Entry PC
=
match
predicted
target
target PC

## Slide 27: Subroutine Return Stack
Small structure to accelerate JR for subroutine returns, typically much more accurate than BTBs.
&fb()
&fc()
Push call address when function call executed
Pop return address when subroutine return decoded
fa() { fb(); }
fb() { fc(); }
fc() { fd(); }
&fd()
k entries
(typically k=8-16)

## Slide 28: Multithreading

## Slide 29: Multithreading
How can we guarantee no dependencies between instructions in a pipeline?
One way is to interleave execution of instructions from different program threads on same pipeline
F
D
X
M
W
t0
t1
t2
t3
t4
t5
t6
t7
t8
T1:LD x1,0(x2)
T2:ADD x7,x1,x4
T3:XORI x5,x4,12
T4:SD 0(x7),x5
T1:LD x5,12(x1)
t9
F
D
X
M
W
F
D
X
M
W
F
D
X
M
W
F
D
X
M
W
Interleave 4 threads, T1-T4, on non-bypassed 5-stage pipe
Prior instruction in a thread always completes write-back before next instruction in same thread reads register file

## Slide 30: Thread Scheduling Policies
Fixed interleave (CDC 6600 PPUs, 1964)
  Each of N threads executes one instruction every N cycles
  If thread not ready to go in its slot, insert pipeline bubble
Software-controlled interleave (TI ASC PPUs, 1971)
  OS allocates S pipeline slots amongst N threads
  Hardware performs fixed interleave over S slots, executing whichever thread is in that slot
Hardware-controlled thread scheduling (HEP, 1982)
  Hardware keeps track of which threads are ready to go
  Picks next thread to execute based on hardware priority scheme
Notes: Software-controlled interleave, S > N. Wheel with the threads in each slot. If thread is ready to go
It goes, else NOP, I.e., pipeline bubble.

## Slide 31: Coarse-Grain Multithreading
Tera MTA designed for supercomputing applications with large data sets and low locality
  No data cache
  Many parallel threads needed to hide large memory latency
Other applications are more cache friendly
  Few pipeline bubbles if cache mostly has hits
  Just add a few threads to hide occasional cache miss latencies
  Swap threads on cache misses
Notes: Tera --- 256 mem-ops/cycle * 150 cycles/mem-op = 38K instructions-in-flight…
Tera not very successful, 2 machines sold.
Changed their name back to Cray!

## Slide 32: Superscalar Machine Efficiency
Issue width
Time
Completely idle cycle (vertical waste)
Instruction issue
Partially filled cycle, i.e., IPC < 4
(horizontal waste)
Notes: Focus is switching to function unit efficiency (as a measure of throughput).

## Slide 33: Vertical Multithreading
Cycle-by-cycle interleaving removes vertical waste, but leaves some horizontal waste
Issue width
Time
Second thread interleaved cycle-by-cycle
Instruction issue
Partially filled cycle, i.e., IPC < 4
(horizontal waste)

## Slide 34: Chip Multiprocessing (CMP)
What is the effect of splitting into multiple processors?
  reduces horizontal waste,
  leaves some vertical waste, and
  puts upper limit on peak throughput of each thread.
Issue width
Time

## Slide 35: SMT adaptation to parallelism type
For regions with high thread-level parallelism (TLP) entire machine width is shared by all threads
Issue width
Time
Issue width
Time
For regions with low thread-level parallelism (TLP) entire machine width is available for instruction-level parallelism (ILP)
Notes: Amdahl’s law…

## Slide 36: Icount Choosing Policy
Why does this enhance throughput?
Fetch from thread with the least instructions in flight.
Notes: Fetch unit that can keep up with the simultaneous multithreaded execution engine
have the fewest instructions waiting to be executed
making the best progress through the machine
40% increase in IPC over RR
Don’t want to clog instruction window with thread with many stalls  try to fetch from thread that has fewest insts in window

## Slide 37: Summary: Multithreaded Categories
Time (processor cycle)
Superscalar
Fine-Grained
Coarse-Grained
Multiprocessing
Simultaneous
Multithreading
Thread 1
Thread 2
Thread 3
Thread 4
Thread 5
Idle slot

## Slide 38: CS152 Administrivia
Lab 5 due Friday Aril 27
Friday April 27, discussion will cover multiprocessor review
Final exam, Tuesday May 8, 306 Soda, 11:30am-2:30pm

## Slide 39: CS252 Administrivia
Project presentations, May 2nd, 2:30pm-5pm, 511 Soda
Final project papers , May 11th

## Slide 40: final Review part2
Donggyu Kim

## Slide 41: Memory Hierarchy
Why does it matter?

## Slide 42: Processor-DRAM Gap (latency)
Time
µProc 60%/year
DRAM
7%/year
1
10
100
1000
1980
1981
1983
1984
1985
1986
1987
1988
1989
1990
1991
1992
1993
1994
1995
1996
1997
1998
1999
2000
DRAM
CPU
1982
Processor-Memory
Performance Gap: (growing 50%/yr)
Performance
Four-issue 3GHz superscalar accessing 100ns DRAM could execute 1,200 instructions during time for one memory access!
Notes: Why doesn’t DRAM get faster?

## Slide 43: Physical Size Affects Latency
Small Memory
CPU
Big Memory
CPU
Signals have further to travel
Fan out to more locations
More complex address decoder

## Slide 44: Memory Hierarchy
Small,
Fast Memory
(RF, SRAM)
capacity: Register << SRAM << DRAM
latency: Register << SRAM << DRAM
bandwidth: on-chip >> off-chip
On a data access:
  if data Î fast memory  low latency access (SRAM)
  if data Ï fast memory  high latency access (DRAM)
CPU
Big, Slow Memory
(DRAM)
A
B
holds frequently used data
Notes: Due to cost
Due to size of DRAM
Due to cost and wire delays (wires on-chip cost much less, and are faster)

## Slide 45: Performance Models
Average Memory Access Time(AMAT)
  Hit Time + Miss Rate Miss Penalty
Iron Law
Goal
  Reduce the hit time
  Reduce the miss rate
  Reduce the miss penalty
  Increase the cache bandwidth  effectively decrease the hit time

## Slide 46: Causes of Cache Misses: The 3+1 C’s
Compulsory: first reference to a line (a.k.a. cold start misses)
  misses that would occur even with infinite cache
Capacity: cache is too small to hold all data needed by the program
  misses that would occur even under perfect replacement policy
Conflict: misses that occur because of collisions due to line-placement strategy
  misses that would not occur with ideal full associativity
Coherence: misses that occur when a line is invalidated due to a remote write to another word (false sharing)
  misses that would not occur without shared lines

## Slide 47: Effect of Cache Parameters on Performance
Larger cache size
  reduces capacity and conflict misses
  hit time will increase
Higher associativity
  reduces conflict misses
  may increase hit time
Larger line size
  reduces compulsory misses
  increases conflict & coherence misses and miss penalty
Notes: Requested line first….
The following could be in the slide…
spatial locality reduces compulsory misses and capacity reload misses
  fewer lines may increase conflict miss rate
  larger lines may increase miss penalty

## Slide 48: Multilevel Caches
Problem: A memory cannot be large and fast
Solution: Increasing sizes of cache at each level
CPU
L1$
L2$
DRAM
Local miss rate = misses in cache / accesses to cache
Global miss rate = misses in cache / CPU memory accesses
Misses per instruction = misses in cache / number of instructions
Notes: MPI makes it easier to compute overall performance (jse)

## Slide 49: Hardware Instruction Prefetching
Instruction prefetch in Alpha AXP 21064
  Fetch two lines on a miss; the requested line (i) and the next consecutive line (i+1)
  Requested line placed in cache, and next line in instruction stream buffer
  If miss in cache but hit in stream buffer, move stream buffer line into cache and prefetch next line (i+2)
L1 Instruction
Unified L2 Cache
RF
CPU
Stream
Buffer
Prefetched
instruction line
Req
line
Req
line
Notes: Need to check the stream buffer if the requested line is in there.
Never more than one 32-byte line in the stream buffer.

## Slide 50: Reducing Write Hit Time (or Bandwidth)
Problem: Writes take two cycles in memory stage, one cycle for tag check plus one cycle for data write if hit
Solutions:
Design data RAM that can perform read and write in one cycle, restore old value after tag miss
Fully-associative (CAM Tag) caches: Word line only enabled if hit
Pipelined writes: Hold write data for store in single buffer ahead of cache, write cache data during next store’s tag check
Notes: Need to bypass from write buffer if read address matches write buffer tag!

## Slide 51: Write Buffer to Reduce Read Miss Penalty
Processor is not stalled on writes, and read misses can go ahead of write to main memory
Problem: Write buffer may hold updated value of location needed by a read miss
Simple solution: on a read miss, wait for the write buffer to go empty
Faster solution: Check write buffer addresses against read miss addresses, if no match, allow read miss to go ahead of writes, else, return value in write buffer
 This breaks sequential consistency (SC) !
Evicted dirty lines for writeback cache
OR All writes in writethrough cache
Data Cache
Unified L2 Cache
RF
CPU
Write
buffer
Notes: Deisgners of the MIPS M/1000 estimated that waiting for a four-word buffer to empty
increased the read miss penalty by a factor of 1.5.

## Slide 52: Cache Summary
Technique | Hit Time | Miss Penalty | Miss Rate | Hardware
Small and simple caches | Decrease | ⎯ | Increase (Capacity) | Decrease
Multi-level caches | ⎯ | Increase | Decrease | Increase
Pipelined writes | Decrease (Write BW) | ⎯ | ⎯ | Increase
Write buffer | ⎯ | Decrease | ⎯ | Increase
Sub-blocks | ⎯ | Decrease | Increase (Compulsory) | Increase
Code optimization | ⎯ | ⎯ | Decrease | ⎯
Compiler prefetching | ⎯ | ⎯ | Decrease (Compulsory, But possible cache / bandwidth pollution) | Increase (non-blocking cache, additional instructions)
Hardware prefetching (Stream buffer) | ⎯ | ⎯ | Decrease (Compulsory) | Increase
Victim cache | ⎯ | Increase | Decrease (Conflict, compared to direct-mapped) | Decrease (Compared to set-associative)

## Slide 53: Virtual Memory
Why do we care hardware support?

## Slide 54: Page Tables Live in Memory
Virtual Address Space Pages for Job 1
Physical Memory
Pages
0
1
2
3
Page Table
for Job 1
1
0
1
3
3
2
0
2
Virtual Address Space Pages for Job 2
0
1
2
3
Page Table
for Job 2
Simple linear page tables are too large, so hierarchical page tables are commonly used (see later)
Common for modern OS to place page tables in kernel’s virtual memory (page tables can be swapped to secondary storage)
How many memory accesses per instruction?
Notes: Relaxes the contiguous allocation requirement.

## Slide 55: Address Translation & Protection
Every instruction and data access needs address
translation and protection checks
A good VM design needs to be fast (~ one cycle) and space efficient
Physical Address
Virtual Address
Address
Translation
Virtual Page No. (VPN)
offset
Physical Page No. (PPN)
offset
Exception?
Kernel/User Mode
Read/Write
Protection Check

## Slide 56: Translation-Lookaside Buffers (TLB)
Address translation is very expensive!
  In a two-level page table, each reference becomes several memory accesses
Solution: Cache translations in TLB
TLB hit  Single-Cycle Translation
TLB miss  Page-Table Walk to refill
VPN offset
V R W D tag PPN
physical address
PPN offset
virtual address
hit?
(VPN = virtual page number)
(PPN = physical page number)
Notes: 3 memory references
2 page faults (disk accesses) + ..
Actually used in IBM before paged memory.

## Slide 57: Address Translation: putting it all together
Virtual Address
TLB
Lookup
Page Table
Walk
Update TLB
Page Fault
(OS loads page)
Protection
Check
Physical
Address
(to cache)
miss
hit
the page is
Ï memory Î memory
denied
permitted
Protection
Fault
hardware
hardware or software
software
SEGFAULT
Where?
Notes: Need to restart instruction.
Soft and hard page faults.

## Slide 58: Handling a TLB Miss
Software (MIPS, Alpha)
  TLB miss causes an exception and the operating system walks the page tables and reloads TLB. A privileged “untranslated” addressing mode used for walk.
  Software TLB miss can be very expensive on out-of-order superscalar processor as requires a flush of pipeline to jump to trap handler.
Hardware (SPARC v8, x86, PowerPC, RISC-V)
  A memory management unit (MMU) walks the page tables and reloads the TLB.
  If a missing (data or PT) page is encountered during the TLB reloading, MMU gives up and signals a Page Fault exception for the original instruction.
NOTE: A given ISA can use either TLB miss strategy

## Slide 59: Virtual-Address Caches
one-step process in case of a hit (+)
cache needs to be flushed on a context switch unless address space identifiers (ASIDs) included in tags (-)
aliasing problems due to the sharing of pages (-)
maintaining cache coherence (-)
CPU
Physical
Cache
TLB
Primary
Memory
VA
PA
PA
Alternative: place the cache before the TLB
Virtual Cache
CPU
VA
(StrongARM)
PA
TLB
Primary
Memory
VA

## Slide 60: Concurrent Access to TLB & Cache (Virtual Index/Physical Tag)
Index L is available without consulting the TLB
   cache and TLB accesses can begin simultaneously!
Tag comparison is made after both accesses are completed
Condition: L + b <= k
VPN L b
TLB
Direct-map Cache
2L blocks
2b-byte block
PPN Page Offset
=
hit?
Data
Physical Tag
Tag
VA
PA
Virtual
Index
k

## Slide 61: VLIW Machine
Simple HW + Smart Compilers

## Slide 62: Performance Models, Again
Goal
  Take advance of instruction-level parallelism (ILP)
    Limited by data dependencies
    Varies across applications
  Reschedule instructions
    By hardware (OoO processors)
    By software (compiler optimizations)

## Slide 63: Out-of-Order Control Complexity: MIPS R10000
Control Logic
[ SGI/MIPS Technologies Inc., 1995 ]

## Slide 64: VLIW: Very Long Instruction Word
Multiple operations packed into one instruction
Each operation slot is for a fixed function
Constant operation latencies are specified
HW doesn’t check data dependencies across instructions (no pipeline stalls)
Two Integer Units,
Single-Cycle Latency
Two Load/Store Units,
Three-Cycle Latency
Two Floating-Point Units,
Four-Cycle Latency
Int Op 2
Mem Op 1
Mem Op 2
FP Op 1
FP Op 2
Int Op 1

## Slide 65: VLIW Compiler Responsibilities
Schedule operations to maximize parallel execution
Guarantees intra-instruction parallelism
Schedule to avoid data hazards (no interlocks)
  Typically separates operations with explicit NOPs

## Slide 66: Loop Execution
How many FP ops/cycle?
for (i=0; i<N; i++)
B[i] = A[i] + C;
Int1
Int 2
M1
M2
FP+
FPx
loop:
fld
add x1
fadd
fsd
add x2
bne
1 fadd / 8 cycles = 0.125
loop: fld f1, 0(x1)
add x1, 8
fadd f2, f0, f1
fsd f2, 0(x2)
add x2, 8
bne x1, x3, loop
Compile
Schedule

## Slide 67: Scheduling Loop Unrolled Code
loop: fld f1, 0(x1)
fld f2, 8(x1)
fld f3, 16(x1)
fld f4, 24(x1)
add x1, 32
fadd f5, f0, f1
fadd f6, f0, f2
fadd f7, f0, f3
fadd f8, f0, f4
fsd f5, 0(x2)
fsd f6, 8(x2)
fsd f7, 16(x2)
fsd f8, 24(x2)
add x2, 32
bne x1, x3, loop
Schedule
Int1
Int2
M1
M2
FP+
FPx
loop:
Unroll 4 ways
fld f1
fld f2
fld f3
fld f4
add x1
fadd f5
fadd f6
fadd f7
fadd f8
fsd f5
fsd f6
fsd f7
fsd f8
add x2
bne
How many FLOPS/cycle?
4 fadds / 11 cycles = 0.36

## Slide 68: Dependence Graph
for (i=0; i<N; i++)
B[i] = A[i] + C;
loop: fld f1, 0(x1)
add x1, 8
fadd f2, f0, f1
fsd f2, 0(x2)
add x2, 8
bne x1, x3, loop
Compile
fld
fadd
fsd
Iteration i:
Iteration i+1:
fld
fadd
fsd
Iteration i+2:
fld
fadd
fsd
loop:
prologue
epilogue

## Slide 69: Software Pipelining
How many FLOPS/cycle?
Int1
Int 2
M1
M2
FP+
FPx
fld f1
fsd f5
add x1
add x2
bne
fld f1
add x1
add x2
loop:
prolog
epilog
1 fadd / 3 cycles = 0.333
loop: fld f1, 0(x1)
add x1, 8
fadd f2, f0, f1
fsd f2, 0(x2)
add x2, 8
bne x1, x3, loop
fadd f5
fadd f5
fld f1
add x1
fadd f5
fsd f5
fsd f5
add x2

## Slide 70: Software Pipelining + Loop Unrolling
How many FLOPS/cycle?
loop: fld f1, 0(x1)
fld f2, 8(x1)
fld f3, 16(x1)
fld f4, 24(x1)
add x1, 32
fadd f5, f0, f1
fadd f6, f0, f2
fadd f7, f0, f3
fadd f8, f0, f4
fsd f5, 0(x2)
fsd f6, 8(x2)
fsd f7, 16(x2)
add x2, 32
fsd f8, -8(x2)
bne x1, x3, loop
Int1
Int 2
M1
M2
FP+
FPx
Unroll 4 ways first
fld f1
fld f2
fld f3
fld f4
fadd f5
fadd f6
fadd f7
fadd f8
fsd f5
fsd f6
fsd f7
fsd f8
add x1
add x2
bne
fld f1
fld f2
fld f3
fld f4
fadd f5
fadd f6
fadd f7
fadd f8
fsd f5
fsd f6
fsd f7
fsd f8
add x1
add x2
bne
fld f1
fld f2
fld f3
fld f4
fadd f5
fadd f6
fadd f7
fadd f8
fsd f5
add x1
loop:
iterate
prolog
epilog
4 fadds / 4 cycles = 1

## Slide 71: Trace Scheduling [ Fisher,Ellis]
Pick string of basic blocks, a trace, that represents most frequent branch path
Use profiling feedback or compiler heuristics to find common branch paths
Schedule whole “trace” at once
Add fixup code to cope with branches jumping out of trace

## Slide 72: Limits of Static Scheduling
Unpredictable branches
Variable memory latency (unpredictable cache misses)
Code size explosion
Compiler complexity (compiler runtime)
Despite several attempts, VLIW has failed in general-purpose computing arena (so far).
  More complex VLIW architectures are close to in-order superscalar in complexity, no real advantage on large complex apps.
Successful in embedded DSP market
  Simpler VLIWs with more constrained environment, friendlier code.

## Slide 73: SIMD vs. Vector vs. GPU
Towards Data-Level Parallelism (DLP)

## Slide 74: Performance Models, Again
Goal
  Take advantage of data-level parallelism
    Same operations on large data arrays
    Present in scientific/machine-learning applications
  Increase the bandwidth of each instruction
    Less dynamic instruction counts while keeping CPI & cycle time constant

## Slide 75: Vector Programming Model
+
+
+
+
+
+
[0]
[1]
[vl-1]
Vector Arithmetic Instructions
vadd v3, v1, v2
v3
v2
v1
Scalar Registers
x0
x31
Vector Registers
v0
v31
[0]
[1]
[2]
[MAXVL-1]
vl
Vector Length Register
v1
Vector Load and Store Instructions
vlds v1, x1, x2
Base, x1
Stride, x2
Memory
Vector Register

## Slide 76: Vector Code Example
# Scalar Code
li x4, 64
loop:
fld f1, 0(x1)
fld f2, 0(x2)
fadd.d f3,f1,f2
fsd f3, 0(x3)
addi x1, 8
addi x2, 8
addi x3, 8
subi x4, 1
bnez x4, loop
# Vector Code
li x4, 64
setvl x5, x4
vld v1, x1
vld v2, x2
vadd v3,v1,v2
vst v3, x3
# C code
for (i=0; i<64; i++)
C[i] = A[i] + B[i];

## Slide 77: Vector Instruction Set Advantages
Compact
  one short instruction encodes N operations
Expressive
  Unit-stride load/store for a contiguous block
  Strided load/store for a known pattern
  Indexed load/store for indirect accesses
Scalable
  Same code on more parallel pipelines (lanes)

## Slide 78: T0 Vector Microprocessor (UCB/ICSI, 1995)
Lane
Vector register elements striped over lanes
[0]
[8]
[16]
[24]
[1]
[9]
[17]
[25]
[2]
[10]
[18]
[26]
[3]
[11]
[19]
[27]
[4]
[12]
[20]
[28]
[5]
[13]
[21]
[29]
[6]
[14]
[22]
[30]
[7]
[15]
[23]
[31]
Built by Prof. Krste Asanovic

## Slide 79: Interleaved Vector Memory System
Bank busy time: Time before bank ready to accept next request
Cray-1, 16 banks, 4 cycle bank busy time, 12 cycle latency
0
1
2
3
4
5
6
7
8
9
A
B
C
D
E
F
+
Base
Stride
Vector Registers
Memory Banks
Address Generator

## Slide 80: HW/SW Techniques for Vector Machine
Chaining
  Bypassing the results to the dependent instructions to start the following instructions as soon as possible
Stripmining
  Compiler optimization that breaks loops to fit in vector registers
Vector masks
  To support conditional code for vectorizable loop
Vector reduction
  For reduction operations across vector elements
Gather/Scatter
  To support indirect (indexed) memory operations for vectorizable loop

## Slide 81: RISC-V Vector ISA
Enjoy Lab4?
Ready for another coding question?

## Slide 82: Packed SIMD vs. Vectors?
Big problem of SIMD
  Vector lengths are encoded in instructions
  Need different instructions for different vector lengths (recall 61C labs)
  Rewrite your code for wider vectors!
  Vector: the VL register + stripmining

## Slide 83: GPU vs. Vectors?
 | GPU | Vector
Programing Model | SPMD(CUDA, OpenCL) Should reason threads | C code + Auto Vectorization SPMD(OpenCL) (RISC-V Vector Assembly)
Execution Model | SIMT (Single instruction Multiple threads)  Context-switching overhead | SIMD
Memory Hierarchy | Scratchpad + Caches | Transparent Caches
Memory Operations | Scatter/Gather + Hardware Coalescing Unit | Unit-stride, Strided, Scatter/gather
Conditional Execution | Thread Mask + Divergence Stack | Vector mask
Hardware Complexity | High | Low

## Slide 84: Summary
Memory hierarchy
  To cope with the speed gap between CPU and main memory
  Various cache optimizations
Virtual memory (paging)
  No programs run in bare-metal
  Each program runs as if it has its own contiguous memory space
  OS + HW (TLB, virtually-indexed physically-tagged)
Very Long Instruction Word (VLIW)
  Simple HW + very smart compilers
  Loop unrolling, SW pipelining, trace scheduling
  Predictability: variable memory latency, branches, exceptions
Data-level Parallelism
  Vector Processor vs. SIMD vs. GPU
  HW & SW techniques for vector machines
  RISC-V Vector Programming