## Slide 1: CS 152 Computer Architecture and Engineering CS252 Graduate Computer Architecture Lecture 4 – Pipelining Part II
Krste Asanovic
Electrical Engineering and Computer Sciences
University of California at Berkeley
http://www.eecs.berkeley.edu/~krste
http://inst.eecs.berkeley.edu/~cs152

## Slide 2: Last Time in Lecture 3
Iron law of performance:
  time/program = insts/program * cycles/inst * time/cycle
Classic 5-stage RISC pipeline
Structural, data, and control hazards
Structural hazards handled with interlock or more hardware
Data hazards include RAW, WAR, WAW
  Handle data hazards with interlock, bypass, or speculation
Control hazards (branches, interrupts) most difficult as change which is next instruction
  Branch prediction commonly used
Precise traps: stop cleanly on one instruction, all previous instructions completed, no following instructions have changed architectural state

## Slide 3: Recap: Trap: altering the normal flow of control
Ii-1
HI1
HI2
HIn
Ii
Ii+1
program
trap
handler
An external or internal event that needs to be processed by another (system) program. The event is usually unexpected or rare from program’s point of view.

## Slide 4: Recap: Trap Handler
Saves EPC before enabling interrupts to allow nested interrupts 
  need an instruction to move EPC into GPRs
  need a way to mask further interrupts at least until EPC can be saved
Needs to read a status register that indicates the cause of the trap
Uses a special indirect jump instruction ERET (return-from-environment) which
  enables interrupts
  restores the processor to the user mode
  restores hardware status and control state

## Slide 5: Recap: Synchronous Trap
A synchronous trap is caused by an exception on a particular instruction
In general, the instruction cannot be completed and needs to be restarted after the exception has been handled
  requires undoing the effect of one or more partially executed instructions
In the case of a system call trap, the instruction is considered to have been completed
  a special jump instruction involving a change to a privileged mode

## Slide 6: Recap: Exception Handling 5-Stage Pipeline
How to handle multiple simultaneous exceptions in different pipeline stages?
How and where to handle external asynchronous interrupts?
PC
Inst. Mem
D
Decode
E
M
Data Mem
W
+
Illegal Opcode
Overflow
Data address Exceptions
PC address Exception
Asynchronous Interrupts

## Slide 7: Recap: Exception Handling 5-Stage Pipeline
PC
Inst. Mem
D
Decode
E
M
Data Mem
W
+
Illegal Opcode
Overflow
Data address Exceptions
PC address Exception
Asynchronous
Interrupts
Exc
D
PC
D
Exc
E
PC
E
Exc
M
PC
M
Cause
EPC
Kill D Stage
Kill F Stage
Kill E Stage
Select Handler PC
Kill Writeback
Commit Point

## Slide 8: Recap: Exception Handling 5-Stage Pipeline
Hold exception flags in pipeline until commit point (M stage)
Exceptions in earlier pipe stages override later exceptions for a given instruction
Inject external interrupts at commit point (override others)
If trap at commit: update Cause and EPC registers, kill all stages, inject handler PC into fetch stage

## Slide 9: Recap: Speculating on Exceptions
Prediction mechanism
  Exceptions are rare, so simply predicting no exceptions is very accurate!
Check prediction mechanism
  Exceptions detected at end of instruction execution pipeline, special hardware for various exception types
Recovery mechanism
  Only write architectural state at commit point, so can throw away partially executed instructions after exception
  Launch exception handler after flushing pipeline
Bypassing allows use of uncommitted instruction results by following instructions

## Slide 10: Deeper Pipelines: MIPS R4000
Figure C.36 The eight-stage pipeline structure of the R4000 uses pipelined instruction and data caches. The pipe stages are labeled and their detailed function is described in the text. The vertical dashed lines represent the stage boundaries as well as the location of pipeline latches. The instruction is actually available at the end of IS, but the tag check is done in RF, while the registers are fetched. Thus, we show the instruction memory as operating through RF. The TC stage is needed for data memory access, because we cannot write the data into the register until we know whether the cache access was a hit or not.
© 2018 Elsevier Inc. All rights reserved.
Commit Point
Direct-mapped I$ allows use of instruction before tag check complete

## Slide 11: R4000 Load-Use Delay
Figure C.37 The structure of the R4000 integer pipeline leads to a x1 load delay. A x1 delay is possible because the data value is available at the end of DS and can be bypassed. If the tag check in TC indicates a miss, the pipeline is backed up a cycle, when the correct data are available.
© 2018 Elsevier Inc. All rights reserved.
Direct-mapped D$ allows use of data before tag check complete

## Slide 12: R4000 Branches
Figure C.39 The basic branch delay is three cycles, because the condition evaluation is performed during EX.
© 2018 Elsevier Inc. All rights reserved.

## Slide 13: Simple vector-vector add code example
# for(i=0; i<N; i++)
# A[i] = B[i]+C[i];
loop: fld f0, 0(x2) // x2 points to B
fld f1, 0(x3) // x3 points to C
fadd.d f2, f0, f1
fsd f2, 0(x1) // x1 points to A
addi x1, x1, 8 // Bump pointer
addi x2, x2, 8 // Bump pointer
addi x3, x3, 8 // Bump pointer
bne x1, x4, loop // x4 holds end

## Slide 14: Simple Pipeline Scheduling
Can reschedule code to try to reduce pipeline hazards
loop: fld f0, 0(x2) // x2 points to B
fld f1, 0(x3) // x3 points to C
addi x3, x3, 8 // Bump pointer
addi x2, x2, 8 // Bump pointer
fadd.d f2, f0, f1
addi x1, x1, 8 // Bump pointer
fsd f2, -8(x1) // x1 points to A
bne x1, x4, loop // x4 holds end
Long latency loads and floating-point operations limit parallelism within a single loop iteration

## Slide 15: One way to reduce hazards: Loop Unrolling
Can unroll to expose more parallelism, reduce dynamic instruction count
loop: fld f0, 0(x2) // x2 points to B
fld f1, 0(x3) // x3 points to C
fld f10, 8(x2)
fld f11, 8(x3)
addi x3,x3,16 // Bump pointer
addi x2,x2,16 // Bump pointer
fadd.d f2, f0, f1
fadd.d f12, f10, f11
addi x1,x1,16 // Bump pointer
fsd f2, -16(x1) // x1 points to A
fsd f12, -8(x1)
bne x1, x4, loop // x4 holds end
Unrolling limited by number of architectural registers
Unrolling increases instruction cache footprint
More complex code generation for compiler, has to understand pointers
Can also software pipeline, but has similar concerns

## Slide 16: Alternative Approach: Decoupling (lookahead, runahead) in µarchitecture
Can separate control and memory address operations from data computations:
loop: fld f0, 0(x2) // x2 points to B
fld f1, 0(x3) // x3 points to C
fadd.d f2, f0, f1
fsd f2, 0(x1) // x1 points to A
addi x1,x1,8 // Bump pointer
addi x2,x2,8 // Bump pointer
addi x3,x3,8 // Bump pointer
bne x1, x4, loop // x4 holds end
The control and address operations do not depend on the data computations, so can be computed early relative to the data computations, which can be delayed until later.

## Slide 17: Simple Decoupled Machine
F
D
X
M
W
X1
X2
X3
W
µOp Queue
R
Load Data Queue
Store Address Queue
Store Data Queue
Integer Pipeline
Floating-Point Pipeline
Load Address
Check
Load Data
{Load Data Writeback µOp}
{Compute µOp}
{Store Data Read µOp}

## Slide 18: Decoupled Execution
fld f0
fld f1
Send load to memory, queue up write to f0
Send load to memory, queue up write to f1
fadd.d
Queue up fadd.d
fsd f2
Queue up store address, wait for store data
addi x1
Bump pointer
addi x2
Bump pointer
addi x3
Bump pointer
bne
Take branch
fld f0
fld f1
Send load to memory, queue up write to f0
Send load to memory, queue up write to f1
fadd.d
Queue up fadd.d
fsd f2
Queue up store address, wait for store data
…
Check load address against queued pending store addresses
Many writes to f0 can be in queue at same time

## Slide 19: Simple Decoupled Machine
F
D
X
M
W
X1
X2
X3
W
µOp Queue
R
Load Data Queue
Store Address Queue
Store Data Queue
Integer Pipeline
Floating-Point Pipeline
Load Address
Check
Load Data
{Load Data Writeback µOp}
{Compute µOp}
{Store Data Read µOp}

## Slide 20: CS152 Administrivia
PS 1 is due at start of class on Monday Feb 11
Lab 1 due at start of class Wednesday Feb 20

## Slide 21: CS252 Administrivia
Project proposals due Wed Feb 27th
Use Krste’s office hours Wed 10-11am to get feedback on ideas

## Slide 22: IBM 7030 “Stretch” (1954-1961)
Original goal was to use new transistor technology to give 100x performance of tube-based IBM 704.
Design based around 4 stages of “lookahead” pipelining
More than just pipelining, a simple form of decoupled execution with indexing and branch operations performed speculatively ahead of data operations
Also had a simple store buffer
Very complex design for the time, difficult to explain to users performance of pipelined machine
When finally delivered in 1961, was benchmarked at only 30x 704 and embarrassed IBM, causing price to drop from $13.5M to $7.8M, and withdrawal after initial deliveries
But technologies lived on in later IBM computers, 360 and POWER
© IBM

## Slide 23: Supercomputers
Definitions of a supercomputer:
Fastest machine in world at given task
A device to turn a compute-bound problem into an I/O bound problem
Any machine costing $30M+
Any machine designed by Seymour Cray
CDC6600 (Cray, 1964) regarded as first supercomputer

## Slide 24: CDC 6600 Seymour Cray, 1964
A fast pipelined machine with 60-bit words
  128 Kword main memory capacity, 32 banks
Ten functional units (parallel, unpipelined)
  Floating Point: adder, 2 multipliers, divider
  Integer: adder, 2 incrementers, ...
Hardwired control (no microcoding)
Scoreboard for dynamic scheduling of instructions
Ten Peripheral Processors for Input/Output
  a fast multi-threaded 12-bit integer ALU
Very fast clock, 10 MHz (FP add in 4 clocks)
>400,000 transistors, 750 sq. ft., 5 tons, 150 kW, novel freon-based technology for cooling
Fastest machine in world for 5 years (until 7600)
  over 100 sold ($7-10M each)

## Slide 25: CDC 6600: A Load/Store Architecture
Separate instructions to manipulate three types of reg.
  8x60-bit data registers (X)
  8x18-bit address registers (A)
  8x18-bit index registers (B)
All arithmetic and logic instructions are register-to-register
Only Load and Store instructions refer to memory!
Touching address registers 1 to 5 initiates a load
6 to 7 initiates a store
        - very useful for vector operations
opcode i j k Ri  Rj op Rk
opcode i j disp Ri M[Rj + disp]
6
3
3
3
6
3
3
18

## Slide 26: CDC 6600: Datapath
Address Regs Index Regs
8 x 18-bit 8 x 18-bit
Operand Regs
8 x 60-bit
Inst. Stack
8 x 60-bit
IR
10 Functional
Units
Central
Memory
128K words,
32 banks,
1µs cycle
result
addr
result
operand
operand
addr

## Slide 27: CDC6600 ISA designed to simplify high-performance implementation
Use of three-address, register-register ALU instructions simplifies pipelined implementation
  Only 3-bit register-specifier fields checked for dependencies
  No implicit dependencies between inputs and outputs
Decoupling setting of address register (Ar) from retrieving value from data register (Xr) simplifies providing multiple outstanding memory accesses
  Software can schedule load of address register before use of value
  Can interleave independent instructions inbetween
CDC6600 has multiple parallel but unpipelined functional units
  E.g., 2 separate multipliers
Follow-on machine CDC7600 used pipelined functional units
  Foreshadows later RISC designs

## Slide 28: CDC6600: Vector Addition
    B0 ← - n
loop: JZE B0, exit
    A0 ← B0 + a0 load X0
    A1 ← B0 + b0 load X1
    X6 ← X0 + X1
    A6 ← B0 + c0 store X6
    B0 ← B0 + 1
    jump loop
Ai = address register
Bi = index register
Xi = data register

## Slide 29: Issues in Complex Pipeline Control
IF
ID
WB
ALU
Mem
Fadd
Fmul
Fdiv
Issue
GPRs
FPRs
Structural conflicts at the execution stage if some FPU or memory unit is not pipelined and takes more than one cycle
Structural conflicts at the write-back stage due to variable latencies of different functional units
Out-of-order write hazards due to variable latencies of different functional units
How to handle exceptions?

## Slide 30: CDC6600 Scoreboard
Instructions dispatched in-order to functional units provided no structural hazard or WAW
  Stall on structural hazard, no functional units available
  Only one pending write to any register
Instructions wait for input operands (RAW hazards) before execution
  Can execute out-of-order
Instructions wait for output register to be read by preceding instructions (WAR)
  Result held in functional unit until register free

## Slide 31
[© IBM]

## Slide 32: IBM Memo on CDC6600
Thomas Watson Jr., IBM CEO, August 1963:
  “Last week, Control Data ... announced the 6600 system. I understand that in the laboratory developing the system there are only 34 people including the janitor. Of these, 14 are engineers and 4 are programmers... Contrasting this modest effort with our vast development activities, I fail to understand why we have lost our industry leadership position by letting someone else offer the world's most powerful computer.”
To which Cray replied: “It seems like Mr. Watson has answered his own question.”

## Slide 33: More Complex In-Order Pipeline
Delay writeback so all operations have same latency to W stage
  Write ports never oversubscribed (one inst. in & one inst. out every cycle)
  Stall pipeline on long latency operations, e.g., divides, cache misses
  Handle exceptions in-order at commit point
Commit Point
PC
Inst. Mem
D
Decode
X1
X2
Data Mem
W
+
GPRs
X2
W
FAdd
X3
X3
FPRs
X1
X2
FMul
X3
X2
FDiv
X3
Unpipelined divider
How to prevent increased writeback latency from slowing down single cycle integer operations?
Bypassing

## Slide 34: In-Order Superscalar Pipeline
Fetch two instructions per cycle; issue both simultaneously if one is integer/memory and other is floating point
Inexpensive way of increasing throughput, examples include Alpha 21064 (1992) & MIPS R5000 series (1996)
Same idea can be extended to wider issue by duplicating functional units (e.g. 4-issue UltraSPARC & Alpha 21164) but regfile ports and bypassing costs grow quickly
Commit Point
2
PC
Inst. Mem
D
Dual
Decode
X1
X2
Data Mem
W
+
GPRs
X2
W
FAdd
X3
X3
FPRs
X1
X2
FMul
X3
X2
FDiv
X3
Unpipelined divider

## Slide 35: In-Order Pipeline with two ALU stages
[ © Motorola 1994 ]
Address calculate before memory access
Integer ALU after memory access

## Slide 36: MC68060 Dynamic ALU Scheduling
EA
MEM
ALU
EA
MEM
ALU
EA
MEM
ALU
EA
MEM
ALU
add x1,x1,24(x2)
lw x4, 16(x5)
x2+24
x1+M[x2+24]
Using RISC-V style assembly code for MC68060
EA
MEM
ALU
add x3,x1,x6
x1+x6
addi x5,x2,12
x2+12
x5+16
lw x8, 16(x3)
x3+16
Common trick used in modern in-order RISC pipeline designs, even without reg-mem operations

## Slide 37: Acknowledgements
This course is partly inspired by previous MIT 6.823 and Berkeley CS252 computer architecture courses created by my collaborators and colleagues:
  Arvind (MIT)
  Joel Emer (Intel/MIT)
  James Hoe (CMU)
  John Kubiatowicz (UCB)
  David Patterson (UCB)