## Slide 1: CS 152 Computer Architecture and Engineering CS252 Graduate Computer Architecture Lecture 16 – RISC-V Vectors
Krste Asanovic
Electrical Engineering and Computer Sciences
University of California at Berkeley
http://www.eecs.berkeley.edu/~krste
http://inst.eecs.berkeley.edu/~cs152

## Slide 2: Last Time in Lecture 16
GPU architecture
Evolved from graphics-only, to more general-purpose computing
GPUs programmed as attached accelerators, with software required to separate GPU from CPU code, move memory
Many cores, each with many lanes
  thousands of lanes on current high-end GPUs
SIMT model has hardware management of conditional execution
  code written as scalar code with branches, executed as vector code with predication

## Slide 3: New RISC-V “V” Vector Extension
Being added as a standard extension to the RISC-V ISA
  An updated form of Cray-style vectors for modern microprocessors
Today, a short tutorial on current draft standard, v0.7
  v0.7 is intended to be close to final version of RISC-V vector extension
  Still a work in progress, so details might change before standardization
  https://github.com/riscv/riscv-v-spec
WARNING: Lab 4 uses older version of vector ISA, since new tools not available yet
  Most concepts carry over, if not programming details

## Slide 4: RISC-V Scalar State
Program counter (pc)
32x32/64-bit integer registers (x0-x31)
x0 always contains a 0
Floating-point (FP), adds 32 registers (f0-f31)
each can contain a single- or double-precision FP value (32-bit or 64-bit IEEE FP)
FP status register (fcsr), used for FP rounding mode & exception reporting
ISA string options:
RV32I (XLEN=32, no FP)
RV32IF (XLEN=32, FLEN=32)
RV32ID (XLEN=32, FLEN=64)
RV64I (XLEN=64, no FP)
RV64IF (XLEN=64, FLEN=32)
RV64ID (XLEN=64, FLEN=64)

## Slide 5: Vector Extension Additional State
32 vector data registers, v0-v31, each VLEN bits long
Vector length register vl
Vector type register vtype
Other control registers:
  vstart
    For trap handling
  vrm/vxsat
    Fixed-point rounding mode/saturation
    Also appear in fcsr
v31
vl
vtype
Vector length register
Vector data registers
VLEN bits per vector register, (implementation-dependent)
v0
Vector type register

## Slide 6: Vector Type Register
vsew[2:0] field encodes standard element width (SEW) in bits of elements in vector register (SEW = 8*2vsew )
vlmul[1:0] encodes vector register length multiplier (LMUL = 2vlmul = 1-8)
vediv[1:0] encodes how vector elements are divided into equal sub-elements (EDIV = 2vediv = 1-8)

## Slide 7: Example Vector Register Data Layouts (LMUL=1)

## Slide 8: Setting vector configuration, vsetvli/vsetvl
vsetvli rd, rs1, e8 # Set SEW=8, vl=min(VLEN/SEW,rs1), rd=vl
Requested application vector length
Resulting machine vector length setting
vtype parameters (SEW,LMUL,EDIV) encoded as immediate in instruction
The vsetvl{i} configuration instructions set the vtype register, and also set the vl register, returning the vl value in a scalar register
Usually use immediate form, vsetvli, to set vtype parameters.
The register version vsetvl is usually used for context save/restore
Instruction encoding

## Slide 9: vsetvl{i} operation
The first scalar register argument, rs1, is the requested application vector length (AVL)
The type argument (either immediate or second register) indicates how the vector registers should be configured
  Configuration includes size of each element
The vector length is set to the minimum of requested AVL and the maximum supported vector length (VLMAX) in the new configuration
  VLMAX = LMUL*VLEN/SEW
  vl = min(AVL, VLMAX)
The value placed in vl is also written to the scalar destination register rd

## Slide 10: Simple stripmined vector memcpy example
Unit-stride vector load bytes
Unit-stride vector store bytes
Set configuration, calculate vector strip length
Binary machine code can run on machines with any VLEN!

## Slide 11: Vector Load Instructions
Scalar base address
Scalar stride (bytes)
Vector of offsets (bytes)
Vector destination

## Slide 12: Vector Store Instructions
Vector store data

## Slide 13: Vector Unit-Stride Loads/Stores

## Slide 14: Vector Strided Load/Store Instructions

## Slide 15: Vector Indexed Loads/Stores

## Slide 16: Vector Length Multiplier, LMUL
Set by vlmul[1:0]field in vtype during setvli
LMUL=2
LMUL=4
Gives fewer but longer vector registers

## Slide 17: LMUL=8 stripmined vector memcpy example
Unit-stride vector load bytes
Unit-stride vector store bytes
Set configuration, calculate vector strip length
Binary machine code can run on machines with any VLEN!
Combine eight vector registers into group
(v0,v1,…,v7)

## Slide 18: Mixed-Width Loops
Have different element widths in one loop, even in one instruction
Want same number of elements in each vector register, even if different bits/element
Solution: Keep SEW/LMUL constant

## Slide 20: CS152 Administrivia
PS 4 due Friday April 5 in Section
Lab 4 out on Friday
Lab 3 due Monday April 8

## Slide 21: CS252 Administrivia
Next week readings: Cray-1, VLIW & Trace Scheduling