## Slide 1: CS 152 Computer Architecture and Engineering CS252 Graduate Computer Architecture Lecture 18 Cache Coherence
Krste Asanovic
Electrical Engineering and Computer Sciences
University of California at Berkeley
http://www.eecs.berkeley.edu/~krste
http://inst.eecs.berkeley.edu/~cs152

## Slide 2: Last Time in Lecture 17
RISC-V Standard Vectors
  Note slides from last year available on website to help with Lab 4

## Slide 3: Bus Management
A “bus” is a collection of shared wires
  Newer “busses” use point-point links
Only one “master” can initiate a transaction by driving wires at any one time
Multiple “slaves” can observe and conditionally respond to the transaction on the wires
  slaves decode address on bus to see if they should respond (memory is most common slave)
  some masters can also act as slaves
Masters arbitrate for access with requests to bus “controller”
  Some busses only allow one master (in which case, it’s also the controller)
Master 0
Master 1
Slave 0
Slave 1
Bus Controller
Clock/Control
Address
Data
Request
Grant

## Slide 4: Shared-Memory Multiprocessor
CPU1
Use snoopy mechanism to keep all processors’ view of memory coherent
Memory
Bus
Main Memory (DRAM)
DMA
Snoopy Cache
CPU2
Snoopy Cache
CPU3
Snoopy Cache
Disk
DMA
Network
Bus Control

## Slide 5: Snoopy Cache, Goodman 1983
Idea: Have cache watch (or snoop upon) other memory transactions, and then “do the right thing”
Snoopy cache tags are dual-ported
Proc.
Cache
Snoopy read port
attached to Memory
Bus
Data
(lines)
Tags and
State
A
D
R/W
Used to drive Memory Bus
when Cache is Bus Master
A
R/W

## Slide 6: Snoopy Cache-Coherence Protocols
Write miss:
  the address is invalidated in all other caches before the write is performed
Read miss:
  if a dirty copy is found in some cache, a write-back is performed before the memory is read
Notes: Update protocols, or write broadcast. Latency between writing a word in one processor
and reading it in another is usually smaller in a write update scheme.
But since bandwidth is more precious, most multiprocessors use a write invalidate scheme.

## Slide 7: Cache State-Transition Diagram The MSI protocol
M
S
I
M: Modified
S: Shared
I: Invalid
Each cache line has state bits
Address tag
state
bits
Write miss
(P1 gets line from memory)
Other processor
intent to write (P1 writes back)
Read miss
(P1 gets line from memory)
P1 intent to write
Other processor
intent to write
Read by any
processor
P1 reads
or writes
Cache state in processor P1
Other processor reads
(P1 writes back)

## Slide 8: Two-Processor Example (Reading and writing the same cache line)
M
S
I
Write miss
Read
miss
P1 intent to write
P2 intent to write
P2 reads,
P1 writes back
P1 reads
or writes
P2 intent to write
P1
M
S
I
Write miss
Read
miss
P2 intent to write
P1 intent to write
P1 reads,
P2 writes back
P2 reads
or writes
P1 intent to write
P2
P1 reads
P1 writes
P2 reads
P2 writes
P1 writes
P2 writes
P1 reads
P1 writes

## Slide 9: Observation
If a line is in the M state then no other cache can have a copy of the line!
Memory stays coherent, multiple differing copies cannot exist
M
S
I
Write miss
Other processor
intent to write
Read
miss
P1 intent to write
Other processor
intent to write
Read by any
processor
P1 reads
or writes
Other processor reads
P1 writes back

## Slide 10: MESI: An Enhanced MSI protocol increased performance for private data
M
E
S
I
M: Modified Exclusive
E: Exclusive but unmodified
S: Shared
I: Invalid
Each cache line has a tag
Address tag
state
bits
Write miss
Other processor
intent to write
Read miss,
shared
Other processor
intent to write
P1 write
Read by any
processor
Other processor reads
P1 writes back
P1 read
P1 write
or read
Cache state in processor P1
P1 intent to write
Read miss, not shared
Other processor
reads
Other processor intent to write, P1 writes back

## Slide 11: Optimized Snoop with Level-2 Caches
Processors often have two-level caches
  small L1, large L2 (usually both on chip now)
Inclusion property: entries in L1 must be in L2
  Miss in L2 ⇒ Not present in L1
  Only if invalidation hits in L2 ⇒ probe and invalidate in L1
Snooping on L2 does not affect CPU-L1 bandwidth
Snooper
Snooper
Snooper
Snooper
CPU
L1 $
L2 $
CPU
L1 $
L2 $
CPU
L1 $
L2 $
CPU
L1 $
L2 $
Notes: Interlocks are required when both CPU-L1 and L2-Bus interactions involve
the same address.

## Slide 12: Intervention
When a read-miss for A occurs in cache-2,
a read request for A is placed on the bus
  Cache-1 needs to supply & change its state to shared
  The memory may respond to the request also!
Does memory know it has stale data?
Cache-1 needs to intervene through memory controller to supply correct data to cache-2
cache-1
A 200
CPU-Memory bus
CPU-1
CPU-2
cache-2
memory (stale data)
A 100

## Slide 13: False Sharing
state line addr data0 data1 ... dataN
A cache line contains more than one word
Cache-coherence is done at the line-level and not word-level
Suppose M1 writes wordi and M2 writes wordk and
i ≠ k but both words have the same line address.
What can happen?
Notes: The block may be invalidated many times unnecessarily because
the addresses share a common block.

## Slide 14: Performance of Symmetric Multiprocessors (SMPs)
Cache performance is combination of:
Uniprocessor cache miss traffic
Traffic caused by communication
  Results in invalidations and subsequent cache misses
Coherence misses
  Sometimes called a Communication miss
  4th C of cache misses along with Compulsory, Capacity, & Conflict.

## Slide 15: Coherency Misses
True sharing misses arise from the communication of data through the cache coherence mechanism
  Invalidates due to 1st write to shared line
  Reads by another CPU of modified line in different cache
  Miss would still occur if line size were 1 word
False sharing misses when a line is invalidated because some word in the line, other than the one being read, is written into
  Invalidation does not cause a new value to be communicated, but only causes an extra cache miss
  Line is shared, but no word in line is actually shared  miss would not occur if line size were 1 word

## Slide 16: Example: True v. False Sharing v. Hit?
Time | P1 | P2 | True, False, Hit? Why?
1 | Write x1 |  | 
2 |  | Read x2 | 
3 | Write x1 |  | 
4 |  | Write x2 | 
5 | Read x2 |  | 
Assume x1 and x2 in same cache line. P1 and P2 both read x1 and x2 before.
True miss; invalidate x1 in P2
False miss; x1 irrelevant to P2
False miss; x1 irrelevant to P2
True miss; x2 not writeable
True miss; invalidate x2 in P1

## Slide 17: MP Performance 4-Processor Commercial Workload: OLTP, Decision Support (Database), Search Engine
Uniprocessor cache misses improve with cache size increase (Instruction, Capacity/Conflict, Compulsory)
True sharing and false sharing unchanged going from 1 MiB to 8 MiB (L3 cache)

## Slide 18: MP Performance 2MiB Cache Commercial Workload: OLTP, Decision Support (Database), Search Engine
True sharing, false sharing increase going from 1 to 8 CPUs

## Slide 19: CS152 Administrivia
Midterm 2 in class Wednesday April 17
  covers lectures 10-17, plus associated problem sets, labs, and readings

## Slide 20: CS252 Administrivia
Monday April 15th Project Checkpoint, 11am-noon, 405 Soda
  Prepare 10-minute presentation on current status

## Slide 21: Scaling Snoopy/Broadcast Coherence
When any processor gets a miss, must probe every other cache
Scaling up to more processors limited by:
  Communication bandwidth over bus
  Snoop bandwidth into tags
Can improve bandwidth by using multiple interleaved buses with interleaved tag banks
  E.g, two bits of address pick which of four buses and four tag banks to use – (e.g., bits 7:6 of address pick bus/tag bank, bits 5:0 pick byte in 64-byte line)
Buses don’t scale to large number of connections, so can use point-to-point network for larger number of nodes, but then limited by tag bandwidth when broadcasting snoop requests.
Insight: Most snoops fail to find a match!

## Slide 22: Scalable Approach: Directories
Every memory line has associated directory information
  keeps track of copies of cached lines and their states
  on a miss, find directory entry, look it up, and communicate only with the nodes that have copies if necessary
  in scalable networks, communication with directory and copies is through network transactions
Many alternatives for organizing directory information

## Slide 23: Directory Cache Protocol
Assumptions: Reliable network, FIFO message delivery between any given source-destination pair
CPU
Cache
Interconnection Network
Directory Controller
DRAM Bank
Directory Controller
DRAM Bank
CPU
Cache
CPU
Cache
CPU
Cache
CPU
Cache
CPU
Cache
Directory Controller
DRAM Bank
Directory Controller
DRAM Bank
Data
Tag
Stat.
Each line in cache has state field plus tag
Data
Stat.
Directry
Each line in memory has state field plus bit vector directory with one bit per processor
Notes: Delay is a fact of life
Serialization by directory, no longer the bus
SC not guarantied

## Slide 24: Cache States
For each cache line, there are 4 possible states:
  C-invalid (= Nothing): The accessed data is not resident in the cache.
  C-shared (= Sh): The accessed data is resident in the cache, and possibly also cached at other sites. The data in memory is valid.
  C-modified (= Ex): The accessed data is exclusively resident in this cache, and has been modified. Memory does not have the most up-to-date data.
  C-transient (= Pending): The accessed data is in a transient state (for example, the site has just issued a protocol request, but has not received the corresponding protocol reply).
Notes: - common cases
- read miss to private (victim clean or dirty)
- write miss to private
- read miss to shared
- write miss to shared

## Slide 25: Home directory states
For each memory line, there are 4 possible states:
  R(dir): The memory line is shared by the sites specified in dir (dir is a set of sites). The data in memory is valid in this state. If dir is empty (i.e., dir = ε), the memory line is not cached by any site.
  W(id): The memory line is exclusively cached at site id, and has been modified at that site. Memory does not have the most up-to-date data.
  TR(dir): The memory line is in a transient state waiting for the acknowledgements to the invalidation requests that the home site has issued.
  TW(id): The memory line is in a transient state waiting for a line exclusively cached at site id (i.e., in C-modified state) to make the memory line at the home site up-to-date.

## Slide 26: Read miss, to uncached or shared line
Directory Controller
DRAM Bank
CPU
Cache
1
Load request at head of CPU->Cache queue.
2
Load misses in cache.
3
Send ShReq message to directory.
4
Message received at directory controller.
5
Access state and directory for line. Line’s state is R, with zero or more sharers.
6
Update directory by setting bit for new processor sharer.
7
Send ShRep message with contents of cache line.
8
ShRep arrives at cache.
9
Update cache tag and data and return load data to CPU.
Interconnection Network
Notes: Delay is a fact of life
Serialization by directory, no longer the bus
SC not guarantied

## Slide 27: Write miss, to read shared line
Directory Controller
DRAM Bank
CPU
Cache
1
Store request at head of CPU->Cache queue.
2
Store misses in cache.
3
Send ExReq message to directory.
4
ExReq message received at directory controller.
5
Access state and directory for line. Line’s state is R, with some set of sharers.
6
Send one InvReq message to each sharer.
11
ExRep arrives at cache
12
Update cache tag and data, then store data from CPU
Interconnection Network
CPU
Cache
7
InvReq arrives at cache.
8
Invalidate cache line. Send InvRep to directory.
9
InvRep received. Clear down sharer bit.
10
When no more sharers, send ExRep to cache.
Multiple sharers
CPU
Cache
CPU
Cache
Notes: Delay is a fact of life
Serialization by directory, no longer the bus
SC not guarantied

## Slide 28: Concurrency Management
Protocol would be easy to design if only one transaction in flight across entire system
But, want greater throughput and don’t want to have to coordinate across entire system
Great complexity in managing multiple outstanding concurrent transactions to cache lines
  Can have multiple requests in flight to same cache line!

## Slide 29: Acknowledgements
This course is partly inspired by previous MIT 6.823 and Berkeley CS252 computer architecture courses created by my collaborators and colleagues:
  Arvind (MIT)
  Joel Emer (Intel/MIT)
  James Hoe (CMU)
  John Kubiatowicz (UCB)
  David Patterson (UCB)