## Slide 1: CS 152 Computer Architecture and Engineering CS252 Graduate Computer Architecture Lecture 19 Memory Consistency Models
Krste Asanovic
Electrical Engineering and Computer Sciences
University of California at Berkeley
http://www.eecs.berkeley.edu/~krste
http://inst.eecs.berkeley.edu/~cs152

## Slide 2: Last Time in Lecture 18
Cache coherence, making sure every store to memory is eventually visible to any load to same memory address
Cache line states: M,S,I or M,E,S,I
Cache miss if tag not present, or line has wrong state
  Write to a shared line is handled as a miss
Snoopy coherence:
  Broadcast updates and probe all cache tags on any miss of any processor, used to be bus connection now often broadcast over point-to-point iinks
  Lower latency, but consumes lots of bandwidth on both the communication bus and for probing the cache tags
Directory coherence:
  Structure keeps track of which caches can have copies of data, and only send messages/probes to those caches
  Complicated to get right with all the possible overlapping cache transactions

## Slide 3: Synchronization
The need for synchronization arises whenever there are concurrent processes in a system (even in a uniprocessor system).
Two classes of synchronization:
Producer-Consumer: A consumer process must wait until the producer process has produced data
Mutual Exclusion: Ensure that only one process uses a resource at a given time
producer
consumer
Shared Resource
P1
P2

## Slide 4: Simple Producer-Consumer Example
Shared Memory
sw xdata, (xdatap)
li xflag, 1
sw xflag, (xflagp)
spin: lw xflag, (xflagp)
beqz xflag, spin
lw xdata, (xdatap)
data
flag
Is this correct?
xflagp
xdatap
xflagp
xdatap
Initially flag=0
Producer processor
Consumer processor

## Slide 5: Memory Consistency Model
Sequential ISA only specifies that each processor sees its own memory operations in program order
Memory consistency model describes what values can be returned by load instructions across multiple hardware threads
Coherence describes the legal values a single memory address should return
Consistency describes properties across all memory addresses

## Slide 6: Simple Producer-Consumer Example
sw xdata, (xdatap)
li xflag, 1
sw xflag, (xflagp)
spin: lw xflag, (xflagp)
beqz xflag, spin
lw xdata, (xdatap)
data
flag
Producer
Consumer
Can consumer read flag=1 before data written by producer visible to consumer?
Initially flag=0

## Slide 7: Sequential Consistency (SC) A Memory Model
“ A system is sequentially consistent if the result of any execution is the same as if the operations of all the processors were executed in some sequential order, and the operations of each individual processor appear in the order specified by the program”
Leslie Lamport
Sequential Consistency = arbitrary order-preserving interleaving of memory references of sequential programs
M
P
P
P
P
P
P

## Slide 8: Simple Producer-Consumer Example
sw xdata, (xdatap)
li xflag, 1
sw xflag, (xflagp)
spin: lw xflag, (xflagp)
beqz xflag, spin
lw xdata, (xdatap)
data
flag
Producer
Consumer
Initially flag =0
Dependencies from sequential ISA
Dependencies added by sequentially consistent memory model

## Slide 9: Most real machines are not SC
Only a few commercial ISAs require SC
  Neither x86 nor ARM are SC
Originally, architects developed uniprocessors with optimized memory systems (e.g., store buffer)
When uniprocessors were lashed together to make multiprocessors, resulting machines were not SC
Requiring SC would make simpler machines slower, or requires adding complex hardware to retain performance
Architects/language designers/applications developers work hard to explain weak memory behavior
Resulted in “weak” memory models with fewer guarantees

## Slide 10: Store Buffer Optimization
Common optimization allows stores to be buffered while waiting for access to shared memory
Load optimizations:
  Later loads can go ahead of buffered stores if to different address
  Later loads can bypass value from earlier buffered store if to same address
CPU
Store Buffer
Shared Memory
CPU
Store Buffer

## Slide 11: TSO example
Allows local buffering of stores by processor
Initially M[X] = M[Y] = 0
P1:
li x1, 1
sw x1, X
lw x2, Y
P2:
li x1, 1
sw x1, Y
lw x2, X
P1.x2 | P2.x2 | SC | TSO
0 | 0 | N | Y
0 | 1 | Y | Y
1 | 0 | Y | Y
1 | 1 | Y | Y
Possible Outcomes
TSO is the strongest memory model in common use

## Slide 12: Strong versus Weak Memory Consistency Models
Stronger models provide more guarantees on ordering of loads and stores across different hardware threads
  Easier ISA-level programming model
  Can require more hardware to ensure orderings (e.g., MIPS R10K was SC, with hardware to speculate on load/stores and squash when ordering violations detected across cores)
Weaker models provide fewer guarantees
  Much more complex ISA-level programming model
    Extremely difficult to understand, even for experts
  Simpler to achieve high performance, as weaker models allow many reorderings to be exposed to software
  Additional instructions (fences) are provided to allow software to specify which orderings are required

## Slide 13: Fences in Producer-Consumer Example
sd xdata, (xdatap)
li xflag, 1
fence w,w //Write-write fence
sd xflag, (xflagp)
spin: ld xflag, (xflagp)
beqz xflag, spin
fence r,r // Read-read fence
ld xdata, (xdatap)
data
flag
Producer
Consumer
Initially flag =0

## Slide 14: CS152 Administrivia
Midterm 2 in class Wednesday April 17
  covers lectures 10-17, plus associated problem sets, labs, and readings
Lab 4 due Friday April 19
Lab 5 out on Friday, covered in Section

## Slide 15: CS252 Administrivia
Will try to schedule makeup slot for class readings

## Slide 16: Range of Memory Consistency Models
SC “Sequential Consistency”
  MIPS R10K
TSO “Total Store Order”
  processor can see its own writes before others do (store buffer)
  IBM-370 TSO, x86 TSO, SPARC TSO (default), RISC-V RVTSO (optional)
Weak, multi-copy-atomic memory models
  all processors see writes by another processor in same order
  Revised ARM v8 memory model
  RISC-V RVWMO, baseline weak memory model for RISC-V
Weak, non-multi-copy-atomic memory models
  processors can see another’s writes in different orders
  ARM v7, original ARM v8
  IBM POWER
  Digital Alpha
  Recent consensus is that this appears to be too weak

## Slide 17: Multi-Copy Atomic models
Each hardware thread must view its own memory operations in program order, but can buffer these locally and reorder accesses around the buffer
But once a local store is made visible to one other hardware thread in system, all other hardware threads must also be able to observe it (this is what is meant by “atomic”)
CPU
Buffer
Shared Memory
CPU
Buffer
Point of global visibility

## Slide 18: Hierarchical Shared Buffering
Common in large systems to have shared intermediate buffers on path between CPUs and global memory
Potential optimization is to allow some CPUs see some writes by a CPU before other CPUs
Shared memory stores are not seen to happen atomically by other threads (non multi-copy atomic)
CPU
Intermediate Buffer
Shared Memory
CPU
CPU
Intermediate Buffer
CPU

## Slide 19: Non-Multi-Copy Atomic
In general, Non-MCA is very difficult to reason about
Software in one thread cannot assume all data it sees is visible to other threads, so how to share data structures?
Adding local fences to require ordering of each thread’s accesses is insufficient – need a more global memory barrier to ensure all writes are made visible
Initially M[X] = M[Y] = 0
P1:
li x1, 1
sw x1, X
P2:
lw x1, X
sw x1, Y
Can P3.x1 = 1, and P3.x2 = 0 ?
P3:
lw x1, Y
fence r,r
lw x2, X

## Slide 20: Relaxed Memory Models
Not all dependencies assumed by SC are supported, and software has to explicitly insert additional dependencies were needed
Which dependencies are dropped depends on the particular memory model
  IBM370, TSO, PSO, WO, PC, Alpha, RMO, …
  Some ISAs allow several memory models, some machines have switchable memory models
How to introduce needed dependencies varies by system
  Explicit FENCE instructions (sometimes called sync or memory barrier instructions)
  Implicit effects of atomic memory instructions
How on earth are programmers supposed to work with this????

## Slide 21: But compilers reorder too!
Compiler can reorder/remove memory operations:
  Instruction scheduling, move loads before stores if to different address
  Register allocation, cache load value in register, don’t check memory
Prohibiting these optimizations would result in very poor performance
//Producer code
*datap = x/y;
*flagp = 1;
//Consumer code
while (!*flagp)
;
d = *datap;

## Slide 22: Language-Level Memory Models
Programming languages have memory models too
Hide details of each ISA’s memory model underneath language standard
  c.f. C function declarations versus ISA-specific subroutine linkage convention
Language memory models: C/C++, Java
Describe legal behaviors of threaded code in each language and what optimizations are legal for compiler to make
E.g., C11/C++11: atomic_load(memory_order_seq_cst) maps to RISC-V fence rw,rw; lw; fence r,rw

## Slide 23: Release Consistency
Observation that consistency only matters when processes communicate data
Only need to have consistent view when one process shares its updates to other processes
Other processes only need to ensure they receive updates after they acquire access to shared data
Release
Acquire
Critical
Release
Acquire
Critical
Other Code
Other Code
P1
P2
Ensure critical section updates visible before release visible
Ensure acquire happened before critical section reads data

## Slide 24: Release Consistency Adopted
Memory model for C/C++ and Java uses release consistency
Programmer has to identify synchronization operations, and if all data accesses are protected by synchronization, appears like SC to programmer
ARM v8.1 and RISC-V ISA adopt release consistency semantics on AMOs

## Slide 25: Acknowledgements
This course is partly inspired by previous MIT 6.823 and Berkeley CS252 computer architecture courses created by my collaborators and colleagues:
  Arvind (MIT)
  Joel Emer (Intel/MIT)
  James Hoe (CMU)
  John Kubiatowicz (UCB)
  David Patterson (UCB)