## Slide 1: CS 152 Computer Architecture and Engineering CS252 Graduate Computer Architecture Lecture 9 – Virtual Memory
Krste Asanovic
Electrical Engineering and Computer Sciences
University of California at Berkeley
http://www.eecs.berkeley.edu/~krste
http://inst.eecs.berkeley.edu/~cs152

## Slide 2: Last time in Lecture 8
Protection and translation required for multiprogramming
  Base and bounds was early simple scheme
Page-based translation and protection avoids need for memory compaction, easy allocation by OS
  But need to indirect in large page table on every access
Address spaces accessed sparsely
  Can use multi-level page table to hold translation/protection information, but implies multiple memory accesses per reference
Address space access with locality
  Can use “translation lookaside buffer” (TLB) to cache address translations (sometimes known as address translation cache)
  Still have to walk page tables on TLB miss, can be hardware or software talk
Virtual memory uses DRAM as a “cache” of disk memory, allows very cheap main memory

## Slide 3: Modern Virtual Memory Systems Illusion of a large, private, uniform store
Protection & Privacy
  several users, each with their private address space and one or more shared address spaces
page table  name space
Demand Paging
  Provides the ability to run programs larger than the primary memory
  Hides differences in machine configurations
The price is address translation on
each memory reference
OS
useri
Primary
Memory
Secondary
Storage
VA
PA
mapping
TLB
Notes: Portability on machines with different memory configurations.

## Slide 4: Recap: Hierarchical Page Table
Level 1
Page Table
Level 2
Page Tables
Data Pages
page in primary memory
page in secondary memory
Root of Current
Page Table
p1
offset
p2
Virtual Address from CPU
(Processor
Register, satp in RISC-V)
PTE of a nonexistent page
p1 p2 offset
0
11
12
21
22
31
10-bit
L1 index
10-bit
L2 index
Physical Memory
RISC-V Sv32 Virtual Memory Scheme

## Slide 5: Recap: Page-Based Virtual-Memory Machine (Hardware Page-Table Walk)
Assumes page tables held in untranslated physical memory
PC
Inst. TLB
Inst. Cache
D
Decode
E
M
Data Cache
W
+
Page Fault?
Protection violation?
Page Fault?
Protection violation?
Data TLB
Main Memory (DRAM)
Memory Controller
Physical Address
Physical Address
Physical Address
Physical Address
Page-Table Base Register
Virtual Address
Physical Address
Virtual Address
Hardware Page Table Walker
Miss?
Miss?

## Slide 6: Address Translation: putting it all together
Virtual Address
TLB
Lookup
Page Table
Walk
Update TLB
Page Fault
(OS loads page)
Protection
Check
Physical
Address
(to cache)
miss
hit
the page is
Ï memory Î memory
denied
permitted
Protection
Fault
hardware
hardware or software
software
SEGFAULT
Where?
Notes: Need to restart instruction.
Soft and hard page faults.

## Slide 7: Page-Fault Handler
When the referenced page is not in DRAM:
  The missing page is located (or created)
  It is brought in from disk, and page table is updated
    Another job may be run on the CPU while the first job waits for the requested page to be read from disk
  If no free pages are left, a page is swapped out
    Pseudo-LRU replacement policy, implemented in software
Since it takes a long time to transfer a page (msecs), page faults are handled completely in software by the OS
  Untranslated addressing mode is essential to allow kernel to access page tables

## Slide 8: Handling VM-related exceptions
Handling a TLB miss needs a hardware or software mechanism to refill TLB
Handling page fault (e.g., page is on disk) needs restartable exception so software handler can resume after retrieving page
  Precise exceptions are easy to restart
  Can be imprecise but restartable, but this complicates OS software
A protection violation may abort process
  But often handled the same as a page fault
PC
Inst TLB
Inst. Cache
D
Decode
E
M
Data TLB
Data Cache
W
+
TLB miss? Page Fault?
Protection violation?
TLB miss? Page Fault?
Protection violation?

## Slide 9: Address Translation in CPU Pipeline
Need to cope with additional latency of TLB:
  slow down the clock?
  pipeline the TLB and cache access?
  virtual address caches
  parallel TLB/cache access
PC
Inst TLB
Inst. Cache
D
Decode
E
M
Data TLB
Data Cache
W
+
TLB miss? Page Fault?
Protection violation?
TLB miss? Page Fault?
Protection violation?

## Slide 10: Virtual-Address Caches
one-step process in case of a hit (+)
cache needs to be flushed on a context switch unless address space identifiers (ASIDs) included in tags (-)
aliasing problems due to the sharing of pages (-)
maintaining cache coherence (-)
CPU
Physical
Cache
TLB
Primary
Memory
VA
PA
PA
Alternative: place the cache before the TLB
Virtual Cache
CPU
VA
(StrongARM)
PA
TLB
Primary
Memory
VA

## Slide 11: Virtually Addressed Cache (Virtual Index/Virtual Tag)
PC
Inst. TLB
Inst. Cache
D
Decode
E
M
Data Cache
W
+
Data TLB
Main Memory (DRAM)
Memory Controller
Physical Address
Instruction data
Physical Address
Physical Address
Page-Table Base Register
Virtual Address
Virtual Address
Hardware Page Table Walker
Miss?
Miss?
Translate on miss

## Slide 12: Aliasing in Virtual-Address Caches
VA1
VA2
Page Table
Data Pages
PA
VA1
VA2
1st Copy of Data at PA
2nd Copy of Data at PA
Tag
Data
Two virtual pages share one physical page
Virtual cache can have two copies of same physical data. Writes to one copy not visible to reads of other!
General Solution: Prevent aliases coexisting in cache
Software (i.e., OS) solution for direct-mapped cache
  VAs of shared pages must agree in cache index bits; this ensures all VAs accessing same PA will conflict in direct-mapped cache (early SPARCs)
Notes: Two processes sharing the same file,
Map the same memory segment to different
Parts of their address space.

## Slide 13: Concurrent Access to TLB & Cache (Virtual Index/Physical Tag)
Index L is available without consulting the TLB
  → cache and TLB accesses can begin simultaneously!
Tag comparison is made after both accesses are completed
Cases: L + b = k, L + b < k, L + b > k
VPN L b
TLB
Direct-map Cache
2L blocks
2b-byte block
PPN Page Offset
=
hit?
Data
Physical Tag
Tag
VA
PA
Virtual
Index
k

## Slide 14: Virtual-Index Physical-Tag Caches: Associative Organization
How does this scheme scale to larger caches?
VPN a L = k-b b
TLB
Direct-map
2L blocks
PPN Page Offset
=
hit?
Data
Phy.
Tag
Tag
VA
PA
Virtual
Index
k
Direct-map
2L blocks
2a
=
2a
After the PPN is known, 2a physical tags are compared
Notes:   Consider 4-Kbyte pages and caches with 32-byte blocks
  32-Kbyte cache  2a = 8
    4-Mbyte cache  2a =1024 No !

## Slide 15: CS152 Administrivia
PS 2 due Wednesday Feb 26
Midterm in class Monday March 2
  Covers lectures 1 – 9, plus assigned problem sets, labs, book readings
Lab 2 due Monday March 9

## Slide 16: CS252 Administrivia
Start thinking of class projects and forming teams of two
Proposal due Wednesday February 26th
Proposal should be one page PDF including:
  Title
  Team member names
  What are you trying to do?
  How is it done today?
  What is your idea for improvement and why do you think you’ll be successful
  What infrastructure are you going to use for your project?
  Project timeline with milestones
Mail PDF of proposal to instructors
Give a <5-minute presentation in class in discussion section time on March 11th
No discussion on Mnoday March 4th – midterm!

## Slide 17: Concurrent Access to TLB & Large L1 The problem with L1 > Page size
Can VA1 and VA2 both map to PA ?
VPN a Page Offset b
TLB
PPN Page Offset b
Tag
VA
PA
Virtual Index
L1 PA cache
Direct-map
=
hit?
PPNa Data
PPNa Data
VA1
VA2
Notes: If they differ in the lower ‘a’ bits alone, and share a physical page.

## Slide 18: A solution via Second-Level Cache
Usually a common L2 cache backs up both Instruction and Data L1 caches
L2 is “inclusive” of both Instruction and Data caches
  Inclusive means L2 has copy of any line in either L1
CPU
L1 Data Cache
L1 Instruction Cache
Unified L2 Cache
RF
Memory
Memory
Memory
Memory

## Slide 19: Anti-Aliasing Using L2 [MIPS R10000,1996]
Suppose VA1 and VA2 both map to PA and VA1 is already in L1, L2 (VA1  VA2)
After VA2 is resolved to PA, a collision will be detected in L2.
VA1 will be purged from L1 and L2, and VA2 will be loaded  no aliasing !
VPN a Page Offset b
TLB
PPN Page Offset b
Tag
VA
PA
Virtual Index
L1 PA cache
Direct-map
=
hit?
PPNa Data
PPNa Data
VA1
VA2
Direct-Mapped L2
PA a1 Data
PPN
into L2 tag

## Slide 20: Anti-Aliasing using L2 for a Virtually Tagged L1
VPN Page Offset b
TLB
PPN Page Offset b
Tag
VA
PA
Virtual
Index & Tag
Physical
Index & Tag
L1 VA Cache
L2 PA Cache
L2 “contains” L1
PA VA1 Data
VA1 Data
VA2 Data
“Virtual Tag”
Physically-addressed L2 can also be used to avoid aliases in virtually-addressed L1

## Slide 21: Atlas Revisited
One PAR for each physical page
PAR’s contain the VPN’s of the pages resident in primary memory
Advantage: The size is proportional to the size of the primary memory
What is the disadvantage ?
VPN
PAR’s
PPN

## Slide 22: Hashed Page Table: Approximating Associative Addressing
Hashed Page Table is typically 2 to 3 times larger than the number of PPN’s to reduce collision probability
It can also contain DPN’s for some non-resident pages (not common)
If a translation cannot be resolved in this table then the software consults a data structure that has an entry for every existing page (e.g., full page table)
hash
Offset
Base of Table
+
PA of PTE
Primary
Memory
VPN PID PPN
Page Table
VPN d
Virtual Address
VPN PID DPN
VPN PID
PID

## Slide 23: Power PC: Hashed Page Table
Each hash table slot has 8 PTE's <VPN,PPN> that are searched sequentially
If the first hash slot fails, an alternate hash function is used to look in another slot
All these steps are done in hardware!
Hashed Table is typically 2 to 3 times larger than the number of physical pages
The full backup Page Table is managed in software
Base of Table
hash
Offset
+
PA of Slot
Primary
Memory
VPN PPN
Page Table
VPN d
80-bit VA
VPN

## Slide 24: VM features track historical uses:
Bare machine, only physical addresses
  One program owned entire machine
Batch-style multiprogramming
  Several programs sharing CPU while waiting for I/O
  Base & bound: translation and protection between programs (supports swapping entire programs but not demand-paged virtual memory)
  Problem with external fragmentation (holes in memory), needed occasional memory defragmentation as new jobs arrived
Time sharing
  More interactive programs, waiting for user. Also, more jobs/second.
  Motivated move to fixed-size page translation and protection, no external fragmentation (but now internal fragmentation, wasted bytes in page)
  Motivated adoption of virtual memory to allow more jobs to share limited physical memory resources while holding working set in memory
Virtual Machine Monitors
  Run multiple operating systems on one machine
  Idea from 1970s IBM mainframes, now common on laptops
    e.g., run Windows on top of Mac OS X
  Hardware support for two levels of translation/protection
    Guest OS virtual -> Guest OS physical -> Host machine physical

## Slide 25: Virtual Memory Use Today - 1
Servers/desktops/laptops/smartphones have full demand-paged virtual memory
  Portability between machines with different memory sizes
  Protection between multiple users or multiple tasks
  Share small physical memory among active tasks
  Simplifies implementation of some OS features
Vector supercomputers have translation and protection but rarely complete demand-paging
(Older Crays: base&bound, Japanese & Cray X1/X2: pages)
  Don’t waste expensive CPU time thrashing to disk (make jobs fit in memory)
  Mostly run in batch mode (run set of jobs that fits in memory)
  Difficult to implement restartable vector instructions
Modern GPUs operate similarly to vector supercomputers, with translation and protection but not demand paging

## Slide 26: Virtual Memory Use Today - 2
Most embedded processors and DSPs provide physical addressing only
  Can’t afford area/speed/power budget for virtual memory support
  Often there is no secondary storage to swap to!
  Programs custom written for particular memory configuration in product
  Difficult to implement precise or restartable exceptions for exposed architectures

## Slide 27: Acknowledgements
This course is partly inspired by previous MIT 6.823 and Berkeley CS252 computer architecture courses created by my collaborators and colleagues:
  Arvind (MIT)
  Joel Emer (Intel/MIT)
  James Hoe (CMU)
  John Kubiatowicz (UCB)
  David Patterson (UCB)