## Slide 1: CS 152 Computer Architecture and Engineering CS252 Graduate Computer Architecture Lecture 11 – Out-of-Order Execution
Krste Asanovic
Electrical Engineering and Computer Sciences
University of California at Berkeley
http://www.eecs.berkeley.edu/~krste
http://inst.eecs.berkeley.edu/~cs152

## Slide 2: Last Time in Lecture 10
Pipelining is complicated by multiple and/or variable latency functional units
Out-of-order and/or pipelined execution requires tracking of dependencies (RAW, WAR, WAW)
OoO issue limited by WAR and WAW hazards caused by reuse of architectural register names, removed by register renaming
OoO issue and register renaming invented in mid-1960s but disappeared in practice until 1990s, as simpler architecture approaches (pipelining, caches) could more easily take advantage of technology scaling
Also, two important problems had to be solved:
  Control hazards
  Precise traps and interrupts

## Slide 3: Recap: In-Order Commit for Precise Traps
In-order instruction fetch and decode, and dispatch to reservation stations inside reorder buffer
Instructions issue from reservation stations out-of-order
Out-of-order completion, values stored in temporary buffers
Commit is in-order, checks for traps, and if none updates architectural state
Fetch
Decode
Execute
Commit
Reorder Buffer
In-order
In-order
Out-of-order
Trap?
Kill
Kill
Kill
Inject handler PC

## Slide 4: Recap: Separating Completion from Commit
Re-order buffer holds register results from completion until commit
  Entries allocated in program order during decode
  Buffers completed values and exception state until in-order commit point
  Completed values can be used by dependents before committed (bypassing)
  Each entry holds program counter, instruction type, destination register specifier and value if any, and exception status (info often compressed to save hardware)
Memory reordering needs special data structures
  Speculative store address and data buffers
  Speculative load address and data buffers

## Slide 5: Recap: Phases of Instruction Execution
Fetch: Instruction bits retrieved from instruction cache.
I-cache
Fetch Buffer
Issue Buffer
Functional Units
Architectural
State
Execute: Instructions and operands issued to functional units. When execution completes, all results and exception flags are available.
Decode: Instructions dispatched to appropriate issue buffer
Result Buffer
Commit: Instruction irrevocably updates architectural state (aka “graduation”), or takes precise trap/interrupt.
PC
Commit
Decode/Rename

## Slide 6: In-Order versus Out-of-Order Phases
Instruction fetch/decode/rename always in-order
  Need to parse ISA sequentially to get correct semantics
  CS252:Proposals for speculative OoO instruction fetch, e.g., Multiscalar. Predict control flow and data dependencies across sequential program segments fetched/decoded/executed in parallel, fixup if prediction wrong
Dispatch (place instruction into machine buffers to wait for issue) also always in-order
  Some use “Dispatch” to mean “Issue”, but not in these lectures

## Slide 7: In-Order Versus Out-of-Order Issue
In-order (InO) issue:
  Issue stalls on RAW dependencies or structural hazards, or possibly WAR/WAW hazards
  Instruction cannot issue to execution units unless all preceding instructions have issued to execution units
Out-of-order (OoO) issue:
  Instructions dispatched in program order to reservation stations (or other forms of instruction buffer) to wait for operands to arrive, or other hazards to clear
  While earlier instructions wait in issue buffers, following instructions can be dispatched and issued out-of-order

## Slide 8: In-Order versus Out-of-Order Completion
All but simplest machines have out-of-order completion, due to different latencies of functional units and desire to bypass values as soon as available
Classic RISC 5-stage integer pipeline just barely has in-order completion
  Load takes two cycles, but following one-cycle integer op completes at same time, not earlier
  Adding pipelined FPU immediately brings OoO completion

## Slide 9: In-Order versus Out-of-Order Commit
In-order commit supports precise traps, standard today
  CS252: Some proposals to reduce the cost of in-order commit by retiring some instructions early to compact reorder buffer, but this is just an optimized in-order commit
Out-of-order commit was effectively what early OoO machines implemented (imprecise traps) as completion irrevocably changed machine state
  i.e., complete == commit in these machines

## Slide 10: OoO Design Choices
Where are reservation stations?
  Part of reorder buffer, or in separate issue window?
  Distributed by functional units, or centralized?
How is register renaming performed?
  Tags and data held in reservation stations, with separate architectural register file
  Tags only in reservation stations, data held in unified physical register file

## Slide 11: “Data-in-ROB” Design (HP PA8000, Pentium Pro, Core2Duo, Nehalem)
Managed as circular buffer in program order, new instructions dispatched to free slots, oldest instruction committed/reclaimed when done (“p” bit set on result)
Tag is given by index in ROB (Free pointer value)
In dispatch, non-busy source operands read from architectural register file and copied to Src1 and Src2 with presence bit “p” set. Busy operands copy tag of producer and clear “p” bit.
Set valid bit “v” on dispatch, set issued bit “i” on issue
On completion, search source tags, set “p” bit and copy data into src on tag match. Write result and exception flags to ROB.
On commit, check exception status, and copy result into architectural register file if no trap.
On trap, flush machine and ROB, set free=oldest, jump to handler
Tag
p
Src1
Tag
p
Src2
Reg
p
Result
Except?
i
v
Opcode
Tag
p
Src1
Tag
p
Src2
Reg
p
Result
Except?
i
v
Opcode
Tag
p
Src1
Tag
p
Src2
Reg
p
Result
Except?
i
v
Opcode
Tag
p
Src1
Tag
p
Src2
Reg
p
Result
Except?
i
v
Opcode
Tag
p
Src1
Tag
p
Src2
Reg
p
Result
Except?
i
v
Opcode
Oldest
Free

## Slide 12: Managing Rename for Data-in-ROB
If “p” bit set, then use value in architectural register file
Else, tag field indicates instruction that will/has produced value
For dispatch, read source operands <p,tag,value> from arch. regfile, then also read <p,result> from producing instruction in ROB at tag index, bypassing as needed. Copy operands to ROB.
Write destination arch. register entry with <0,Free,_>, to assign tag to ROB index of this instruction
On commit, update arch. regfile with <1, _, Result>
On trap, reset table (All p=1)
Tag
p
Value
Tag
p
Value
Tag
p
Value
Tag
p
Value
One entry per arch. register
Rename table associated with architectural registers, managed in decode/dispatch

## Slide 13: Data Movement in Data-in-ROB Design
ROB
Architectural Register File
Read operands during decode
Read operands at issue
Functional Units
Read results for commit
Bypass newer values at dispatch
Result Data
Write results at completion
Write results at commit
Source Operands
Write sources in dispatch

## Slide 14: CS152 Administrivia
PS 3 out today, due Monday March 16
Lab 2 due Monday March 9
  Lab 2 takes time to run, so please get started ASAP
  Don’t wait till Sunday!
  Can share directed simulation results but must do own analysis.
  Look at pinned README on Piazza
Lab 3 out Friday, due Monday April 6
Exams handed back next week Wednesday
  One week to submit regrade requests (score might go up or down with regrade requests)

## Slide 15: CS252 Administrivia
Project proposal presentations March in discussion section, maybe rescheduled to Friday March 13

## Slide 16: Unified Physical Register File (MIPS R10K, Alpha 21264, Intel Pentium 4 & Sandy/Ivy Bridge)
Rename all architectural registers into a single physical register file during decode, no register values read
Functional units read and write from single unified register file holding committed and temporary registers in execute
Commit only updates mapping of architectural register to physical register, no data movement
Unified Physical Register File
Read operands at issue
Functional Units
Write results at completion
Committed Register Mapping
Decode Stage Register Mapping

## Slide 17: Lifetime of Physical Registers
ld x1, (x3)
addi x3, x1, #4
sub x6, x7, x9
add x3, x3, x6
ld x6, (x1)
add x6, x6, x3
sd x6, (x1)
ld x6, (x11)
ld P1, (Px)
addi P2, P1, #4
sub P3, Py, Pz
add P4, P2, P3
ld P5, (P1)
add P6, P5, P4
sd P6, (P1)
ld P7, (Pw)
Rename
When can we reuse a physical register?
When next writer of same architectural register commits
Physical regfile holds committed and speculative values
Physical registers decoupled from ROB entries (no data in ROB)

## Slide 18: Physical Register Management
op
p1
PR1
p2
PR2
ex
use
Rd
PRd
LPRd
<x6>
P5
<x7>
P6
<x3>
P7
P0
Pn
P1
P2
P3
P4
x5
P5
x6
P6
x7
x0
P8
x1
x2
P7
x3
x4
ROB
Rename Table
Physical Regs
Free List
ld x1, 0(x3)
addi x3, x1, #4
sub x6, x7, x6
add x3, x3, x6
ld x6, 0(x1)
p
p
p
P0
P1
P3
P2
P4
(LPRd requires third read port on Rename Table for each instruction)
<x1>
P8
p

## Slide 19: Physical Register Management
op
p1
PR1
p2
PR2
ex
use
Rd
PRd
LPRd
ROB
ld x1, 0(x3)
addi x3, x1, #4
sub x6, x7, x6
add x3, x3, x6
ld x6, 0(x1)
Free List
P0
P1
P3
P2
P4
<x6>
P5
<x7>
P6
<x3>
P7
P0
Pn
P1
P2
P3
P4
Physical Regs
p
p
p
<x1>
P8
p
x ld p P7 x1 P0
x5
P5
x6
P6
x7
x0
P8
x1
x2
P7
x3
x4
Rename Table
P0
P8

## Slide 20: Physical Register Management
op
p1
PR1
p2
PR2
ex
use
Rd
PRd
LPRd
ROB
ld x1, 0(x3)
addi x3, x1, #4
sub x6, x7, x6
add x3, x3, x6
ld x6, 0(x1)
Free List
P0
P1
P3
P2
P4
<x6>
P5
<x7>
P6
<x3>
P7
P0
Pn
P1
P2
P3
P4
Physical Regs
p
p
p
<R1>
P8
p
x ld p P7 x1 P0
x5
P5
x6
P6
x7
x0
P8
x1
x2
P7
x3
x4
Rename Table
P0
P8
P7
P1
x addi P0 x3 P1

## Slide 21: Physical Register Management
op
p1
PR1
p2
PR2
ex
use
Rd
PRd
LPRd
ROB
ld x1, 0(x3)
addi x3, x1, #4
sub x6, x7, x6
add x3, x3, x6
ld x6, 0(x1)
Free List
P0
P1
P3
P2
P4
<x6>
P5
<x7>
P6
<x3>
P7
P0
Pn
P1
P2
P3
P4
Physical Regs
p
p
p
<R1>
P8
p
x ld p P7 x1 P0
x5
P5
x6
P6
x7
x0
P8
x1
x2
P7
x3
x4
Rename Table
P0
P8
P7
P1
x addi P0 x3 P1
P5
P3
x sub p P6 p P5 x6 P3

## Slide 22: Physical Register Management
op
p1
PR1
p2
PR2
ex
use
Rd
PRd
LPRd
ROB
ld x1, 0(x3)
addi x3, x1, #4
sub x6, x7, x6
add x3, x3, x6
ld x6, 0(x1)
Free List
P0
P1
P3
P2
P4
<x6>
P5
<x7>
P6
<x3>
P7
P0
Pn
P1
P2
P3
P4
Physical Regs
p
p
p
<x1>
P8
p
x ld p P7 x1 P0
x5
P5
x6
P6
x7
x0
P8
x1
x2
P7
x3
x4
Rename Table
P0
P8
P7
P1
x addi P0 x3 P1
P5
P3
x sub p P6 p P5 x6 P3
P1
P2
x add P1 P3 x3 P2

## Slide 23: Physical Register Management
op
p1
PR1
p2
PR2
ex
use
Rd
PRd
LPRd
ROB
ld x1, 0(x3)
addi x3, x1, #4
sub x6, x7, x6
add x3, x3, x6
ld x6, 0(x1)
Free List
P0
P1
P3
P2
P4
<x6>
P5
<x7>
P6
<x3>
P7
P0
Pn
P1
P2
P3
P4
Physical Regs
p
p
p
<x1>
P8
p
x ld p P7 x1 P0
x5
P5
x6
P6
x7
x0
P8
x1
x2
P7
x3
x4
Rename Table
P0
P8
P7
P1
x addi P0 x3 P1
P5
P3
x sub p P6 p P5 x6 P3
P1
P2
x add P1 P3 x3 P2
x ld P0 x6 P4
P3
P4

## Slide 24: Physical Register Management
op
p1
PR1
p2
PR2
ex
use
Rd
PRd
LPRd
ROB
x ld p P7 x1 P0
x addi P0 x3 P1
x sub p P6 p P5 x6 P3
x ld p P7 x1 P0
ld x1, 0(x3)
addi x3, x1, #4
sub x6, x7, x6
add x3, x3, x6
ld x6, 0(x1)
Free List
P0
P1
P3
P2
P4
<x6>
P5
<x7>
P6
<x3>
P7
P0
Pn
P1
P2
P3
P4
Physical Regs
p
p
p
<x1>
P8
p
x5
P5
x6
P6
x7
x0
P8
x1
x2
P7
x3
x4
Rename Table
P0
P8
P7
P1
P5
P3
P1
P2
x add P1 P3 x3 P2
x ld P0 x6 P4
P3
P4
Execute & Commit
p
p
p
<x1>
P8
x

## Slide 25: Physical Register Management
op
p1
PR1
p2
PR2
ex
use
Rd
PRd
LPRd
ROB
x sub p P6 p P5 x6 P3
x addi P0 x3 P1
x addi P0 x3 P1
ld x1, 0(x3)
addi x3, x1, #4
sub x6, x7, x6
add x3, x3, x6
ld x6, 0(x1)
Free List
P0
P1
P3
P2
P4
<x6>
P5
<x7>
P6
<x3>
P7
P0
Pn
P1
P2
P3
P4
Physical Regs
p
p
p
P8
x x ld p P7 x1 P0
x5
P5
x6
P6
x7
x0
P8
x1
x2
P7
x3
x4
Rename Table
P0
P8
P7
P1
P5
P3
P1
P2
x add P1 P3 x3 P2
x ld P0 x6 P4
P3
P4
Execute & Commit
p
p
p
<x1>
P8
x
p
p
<x3>
P7

## Slide 26: Repairing Rename at Traps
MIPS R10K rename table is repaired by unrenaming instructions in reverse order using the PRd/LPRd fields
Alpha 21264 had similar physical register file scheme, but kept complete rename table snapshots for each instruction in ROB (80 snapshots total)
  Flash copy all bits from snapshot to active table in one cycle

## Slide 27: Reorder Buffer Holds Active Instructions (Decoded but not Committed)
(Older instructions)
(Newer instructions)
Cycle t
…
ld x1, (x3)
add x3, x1, x2
sub x6, x7, x9
add x3, x3, x6
ld x6, (x1)
add x6, x6, x3
sd x6, (x1)
ld x6, (x1)
…
Commit
Fetch
Cycle t + 1
Execute
…
ld x1, (x3)
add x3, x1, x2
sub x6, x7, x9
add x3, x3, x6
ld x6, (x1)
add x6, x6, x3
sd x6, (x1)
ld x6, (x1)
…
ROB contents

## Slide 28: Separate Issue Window from ROB
Reorder buffer used to hold exception information for commit.
The issue window holds only instructions that have been decoded and renamed but not issued into execution. Has register tags and presence bits, and pointer to ROB entry.
op
p1
PR1
p2
PR2
PRd
use
ex
ROB#
ROB is usually several times larger than issue window – why?
Rd
LPRd
PC
Except?
Oldest
Free
Done?

## Slide 29: Superscalar Register Renaming
During decode, instructions allocated new physical destination register
Source operands renamed to physical register with newest value
Execution unit only sees physical register numbers
Rename Table
Op
Src1
Src2
Dest
Op
Src1
Src2
Dest
Register Free List
Op
PSrc1
PSrc2
PDest
Op
PSrc1
PSrc2
PDest
Update
Mapping
Does this work?
Inst 1
Inst 2
Read Addresses
Read Data
Write Ports

## Slide 30: Superscalar Register Renaming
Rename Table
Op
Src1
Src2
Dest
Op
Src1
Src2
Dest
Register Free List
Op
PSrc1
PSrc2
PDest
Op
PSrc1
PSrc2
PDest
Update
Mapping
Inst 1
Inst 2
Read Addresses
Read Data
Write Ports
=?
=?
Must check for RAW hazards between instructions issuing in same cycle. Can be done in parallel with rename lookup.
MIPS R10K renames 4 serially-RAW-dependent insts/cycle
Notes: Doesn’t show that update reflects last dest. (jse)

## Slide 31: Acknowledgements
This course is partly inspired by previous MIT 6.823 and Berkeley CS252 computer architecture courses created by my collaborators and colleagues:
  Arvind (MIT)
  Joel Emer (Intel/MIT)
  James Hoe (CMU)
  John Kubiatowicz (UCB)
  David Patterson (UCB)