## Slide 1: CS 152 Computer Architecture and Engineering CS252 Graduate Computer Architecture Lecture 14 – Multithreading
Krste Asanovic
Electrical Engineering and Computer Sciences
University of California at Berkeley
http://www.eecs.berkeley.edu/~krste
http://inst.eecs.berkeley.edu/~cs152

## Slide 2: Last Time Lecture 13: VLIW
In a classic VLIW, compiler is responsible for avoiding all hazards -> simple hardware, complex compiler. Later VLIWs added more dynamic hardware interlocks
Use loop unrolling and software pipelining for loops, trace scheduling for more irregular code
Static scheduling difficult in presence of unpredictable branches and variable latency memory

## Slide 3: Multithreading
Difficult to continue to extract instruction-level parallelism (ILP) from a single sequential thread of control
Many workloads can make use of thread-level parallelism (TLP)
  TLP from multiprogramming (run independent sequential jobs)
  TLP from multithreaded applications (run one job faster using parallel threads)
Multithreading uses TLP to improve utilization of a single processor

## Slide 4: Multithreading
How can we guarantee no dependencies between instructions in a pipeline?
One way is to interleave execution of instructions from different program threads on same pipeline
F
D
X
M
W
t0
t1
t2
t3
t4
t5
t6
t7
t8
T1:LD x1,0(x2)
T2:ADD x7,x1,x4
T3:XORI x5,x4,12
T4:SD 0(x7),x5
T1:LD x5,12(x1)
t9
F
D
X
M
W
F
D
X
M
W
F
D
X
M
W
F
D
X
M
W
Interleave 4 threads, T1-T4, on non-bypassed 5-stage pipe
Prior instruction in a thread always completes write-back before next instruction in same thread reads register file

## Slide 5: CDC 6600 Peripheral Processors (Cray, 1964)
First multithreaded hardware
10 “virtual” I/O processors
Fixed interleave on simple pipeline
Pipeline has 100ns cycle time
Each virtual processor executes one instruction every 1000ns
Accumulator-based instruction set to reduce processor state
Notes: Was objective was to cope with long I/O latencies?

## Slide 6: Simple Multithreaded Pipeline
Have to carry thread select down pipeline to ensure correct state bits read/written at each pipe stage
Appears to software (including OS) as multiple, albeit slower, CPUs
+1
2
Thread select
PC
1
PC
1
PC
1
PC
1
I$
IR
GPR1
GPR1
GPR1
GPR1
X
Y
2
D$

## Slide 7: Multithreading Costs
Each thread requires its own user state
  PC
  GPRs
Also, needs its own system state
  Virtual-memory page-table-base register
  Exception-handling registers
Other overheads:
  Additional cache/TLB conflicts from competing threads
  (or add larger cache/TLB capacity)
  More OS overhead to schedule more threads (where do all these threads come from?)

## Slide 8: Thread Scheduling Policies
Fixed interleave (CDC 6600 PPUs, 1964)
  Each of N threads executes one instruction every N cycles
  If thread not ready to go in its slot, insert pipeline bubble
Software-controlled interleave (TI ASC PPUs, 1971)
  OS allocates S pipeline slots amongst N threads
  Hardware performs fixed interleave over S slots, executing whichever thread is in that slot
Hardware-controlled thread scheduling (HEP, 1982)
  Hardware keeps track of which threads are ready to go
  Picks next thread to execute based on hardware priority scheme
Notes: Software-controlled interleave, S > N. Wheel with the threads in each slot. If thread is ready to go
It goes, else NOP, I.e., pipeline bubble.
Biancolin: For students: benefits of software-controlled interleave?

## Slide 9: Denelcor HEP (Burton Smith, 1982)
First commercial machine to use hardware threading in main CPU
  120 threads per processor
  10 MHz clock rate
  Up to 8 processors
  precursor to Tera MTA (Multithreaded Architecture)
Notes: Would be nice to add a slide on the implementation…

## Slide 10: Tera MTA (1990-)
Up to 256 processors
Up to 128 active threads per processor
Processors and memory modules populate a sparse 3D torus interconnection fabric
Flat, shared main memory
  No data cache
  Sustains one main memory access per cycle per processor
GaAs logic in prototype, 1KW/processor @ 260MHz
  Second version CMOS, MTA-2, 50W/processor
  Newer version, XMT, fits into AMD Opteron socket, runs at 500MHz
  Newest version, XMT2, has higher memory bandwidth and capacity
Notes: Biancolin:
Interconnect: 16 x 16 x 16 (4096 nodes)
XMT -> aka. Threadstorm (Max 8192 processors, 512 TB of memory)

## Slide 11: MTA Pipeline
A
W
C
W
M
Inst Fetch
Memory Pool
Retry Pool
Interconnection Network
Write Pool
W
Memory pipeline
Issue Pool
Every cycle, one VLIW instruction from one active thread is launched into pipeline
Instruction pipeline is 21 cycles long
Memory operations incur ~150 cycles of latency
Assuming a single thread issues one instruction every 21 cycles, and clock rate is 260 MHz…
What is single-thread performance?
  Effective single-thread issue rate is 260/21 = 12.4 MIPS
Notes: Memory unit is busy, or sync operation failed retry.
Just goes around the memory pipeline.
Biancolin notes:
Lookahead -> specify number of instructions later load data will be used (hide memory latency; esp. when we don’t have 128 threads)

## Slide 12: Coarse-Grain Multithreading
Tera MTA designed for supercomputing applications with large data sets and low locality
  No data cache
  Many parallel threads needed to hide large memory latency
Other applications are more cache friendly
  Few pipeline bubbles if cache mostly has hits
  Just add a few threads to hide occasional cache miss latencies
  Swap threads on cache misses
Notes: Tera --- 256 mem-ops/cycle * 150 cycles/mem-op = 38K instructions-in-flight…
Tera not very successful, 2 machines sold.
Changed their name back to Cray!

## Slide 13: MIT Alewife (1990)
Modified SPARC chips
  register windows hold different thread contexts
Up to four threads per node
Thread switch on local cache miss

## Slide 14: IBM PowerPC RS64-IV (2000)
Commercial coarse-grain multithreading CPU
Based on PowerPC with quad-issue in-order five-stage pipeline
Each physical CPU supports two virtual CPUs
On L2 cache miss, pipeline is flushed and execution switches to second thread
  short pipeline minimizes flush penalty (4 cycles), small compared to memory access latency
  flush pipeline to simplify exception handling

## Slide 15: Oracle/Sun Niagara processors
Target is datacenters running web servers and databases, with many concurrent requests
Provide multiple simple cores each with multiple hardware threads, reduced energy/operation though much lower single thread performance
Niagara-1 [2004], 8 cores, 4 threads/core
Niagara-2 [2007], 8 cores, 8 threads/core
Niagara-3 [2009], 16 cores, 8 threads/core
T4 [2011], 8 cores, 8 threads/core
T5 [2012], 16 cores, 8 threads/core
M5 [2012], 6 cores, 8 threads/core
M6 [2013], 12 cores, 8 threads/core
Notes: Biancolin:
T4: First to use OoO (advertised 5x single-threaded improvement over T3)

## Slide 16: Oracle/Sun Niagara-3, “Rainbow Falls” 2009

## Slide 17: Oracle M6 - 2013
Notes: T4;

## Slide 18: Oracle M6 - 2013

## Slide 19: Oracle M6 - 2013
Notes: Biancolin: M8 (2017): 32 Sparc V9 cores; Quad issue; 8 threads per core; @ 5GHz Shared 256 KB L2 instruction cache (per four cores), private 128K L2 data cache per core 64 MB L3

## Slide 20: CS152 Administrivia
PS 3 due today
PS 4 out Wednesday March 18, due Friday April 3
Lab 3 due Monday April 6

## Slide 21: CS252 Administrivia
Reading today 3:30 on Zoom, link on piazza

## Slide 22: Simultaneous Multithreading (SMT) for OoO Superscalars
Techniques presented so far have all been “vertical” multithreading where each pipeline stage works on one thread at a time
SMT uses fine-grain control already present inside an OoO superscalar to allow instructions from multiple threads to enter execution on same clock cycle. Gives better utilization of machine resources.

## Slide 23: For most apps, most execution units lie idle in an OoO superscalar
From: Tullsen, Eggers, and Levy,
“Simultaneous Multithreading: Maximizing On-chip Parallelism”, ISCA 1995.
For an 8-way superscalar.

## Slide 24: Superscalar Machine Efficiency
Issue width
Time
Completely idle cycle (vertical waste)
Instruction issue
Partially filled cycle, i.e., IPC < 4
(horizontal waste)
Notes: Focus is switching to function unit efficiency (as a measure of throughput).

## Slide 25: Vertical Multithreading
Cycle-by-cycle interleaving removes vertical waste, but leaves some horizontal waste
Issue width
Time
Second thread interleaved cycle-by-cycle
Instruction issue
Partially filled cycle, i.e., IPC < 4
(horizontal waste)
Notes: Two flavours: Fine grained (per-vertical slot(cycle)) vs coarse-grained (multiple cycles)

## Slide 26: Chip Multiprocessing (CMP)
What is the effect of splitting into multiple processors?
  reduces horizontal waste,
  leaves some vertical waste, and
  puts upper limit on peak throughput of each thread.
Issue width
Time

## Slide 27: Ideal Superscalar Multithreading [Tullsen, Eggers, Levy, UW, 1995]
Interleave multiple threads to multiple issue slots with no restrictions
Issue width
Time

## Slide 28: O-o-O Simultaneous Multithreading [Tullsen, Eggers, Emer, Levy, Stamm, Lo, DEC/UW, 1996]
Add multiple contexts and fetch engines and allow instructions fetched from different threads to issue simultaneously
Utilize wide out-of-order superscalar processor issue queue to find instructions to issue from multiple threads
OOO instruction window already has most of the circuitry required to schedule from multiple threads
Any single thread can utilize whole machine

## Slide 29: SMT adaptation to parallelism type
For regions with high thread-level parallelism (TLP) entire machine width is shared by all threads
Issue width
Time
Issue width
Time
For regions with low thread-level parallelism (TLP) entire machine width is available for instruction-level parallelism (ILP)
Notes: Amdahl’s law…

## Slide 30: Pentium-4 Hyperthreading (2002)
First commercial SMT design (2-way SMT)
Logical processors share nearly all resources of the physical processor
  Caches, execution units, branch predictors
Die area overhead of hyperthreading ~ 5%
When one logical processor is stalled, the other can make progress
  No logical processor can use all entries in queues when two threads are active
Processor running only one active software thread runs at approximately same speed with or without hyperthreading
Hyperthreading dropped on OoO P6 based followons to Pentium-4 (Pentium-M, Core Duo, Core 2 Duo), until revived with Nehalem generation machines in 2008.
Intel Atom (in-order x86 core) has two-way vertical multithreading
  Hyperthreading == (SMT for Intel OoO & Vertical for Intel InO)
Notes: Load-store buffer in L1 cache doesn’t behave like that, and hence 15% slowdown.

## Slide 31: IBM Power 4
Single-threaded predecessor to Power 5.
8 execution units in out-of-order engine, each may issue an instruction each cycle.

## Slide 32
Power 4
Power 5
2 fetch (PC), 2 initial decodes
2 commits (architected register sets)

## Slide 33: Power 5 data flow ...
Why only 2 threads? With 4, one of the shared resources (physical registers, cache, memory bandwidth) would be prone to bottleneck

## Slide 34: Initial Performance of SMT
Pentium-4 Extreme SMT yields 1.01 speedup for SPECint_rate benchmark and 1.07 for SPECfp_rate
  Pentium-4 is dual-threaded SMT
  SPECRate requires that each SPEC benchmark be run against a vendor-selected number of copies of the same benchmark
Running on Pentium-4 each of 26 SPEC benchmarks paired with every other (262 runs) speed-ups from 0.90 to 1.58; average was 1.20
Power 5, 8-processor server 1.23 faster for SPECint_rate with SMT, 1.16 faster for SPECfp_rate
Power 5 running 2 copies of each app speedup between 0.89 and 1.41
  Most gained some
  Fl.Pt. apps had most cache conflicts and least gains

## Slide 35: SMT Performance: Application Interaction
Bulpin et al, “Multiprogramming Performance of Pentium 4 with Hyper-Threading”
So long as they aren’t banging on the L2 too.
Not affected by other programs
Your favorite benchmark from Lab2

## Slide 36: SMT Performance: Application Interaction
Bulpin et al, “Multiprogramming Performance of Pentium 4 with Hyper-Threading”
Doesn’t play nice
Your favorite benchmark from Lab2

## Slide 37: SMT Performance: Application Interaction
Bulpin et al, “Multiprogramming Performance of Pentium 4 with Hyper-Threading”
Very sensitive to second program

## Slide 38: Icount Choosing Policy
Why does this enhance throughput?
Fetch from thread with the least instructions in flight.
Notes: Fetch unit that can keep up with the simultaneous multithreaded execution engine
have the fewest instructions waiting to be executed
making the best progress through the machine
40% increase in IPC over RR
Don’t want to clog instruction window with thread with many stalls  try to fetch from thread that has fewest insts in window

## Slide 39: Summary: Multithreaded Categories
Time (processor cycle)
Superscalar
Fine-Grained
Coarse-Grained
Multiprocessing
Simultaneous
Multithreading
Thread 1
Thread 2
Thread 3
Thread 4
Thread 5
Idle slot

## Slide 40: Multithreaded Design Discussion
Want to build a multithreaded processor, how should each component be changed and what are the tradeoffs?
  L1 caches (instruction and data)
  L2 caches
  Branch predictor
  TLB
  Physical register file

## Slide 41: SMT & Security
Most hardware attacks rely on shared hardware resources to establish a side-channel
  Eg. Shared outer caches, DRAM row buffers
SMT gives attackers high-BW access to previously private hardware resources that are shared by co-resident threads:
TLBs: TLBleed (June, ‘18)
L1 caches: CacheBleed (2016)
Functional unit ports: PortSmash (Nov, ’18)
OpenBSD 6.4  Disabled HT in BIOS, AMD SMT to follow

## Slide 42: Acknowledgements
This course is partly inspired by previous MIT 6.823 and Berkeley CS252 computer architecture courses created by my collaborators and colleagues:
  Arvind (MIT)
  Scott Beamer (UCB)
  Joel Emer (Intel/MIT)
  James Hoe (CMU)
  John Kubiatowicz (UCB)
  David Patterson (UCB)